## Slide 1: Processing-in-Memory in the Wild
Sasha Fedorova
University of British Columbia
MongoDB

## Slide 2: Acknowledgments
Students
Andrada Zoltan
Craig Mustard
Jacob Grossbard
Joel Nider
John Ramsden
Larry Liu
Mohammad Dashti
Niloo Zarif
Collaborators (UPMEM)
Alexandre Ghiti
Jordi Chauzi
Rémy Cimadomo
Fabrice Devaux
Romaric Jodin
Julien Legriel
Vincent Palatin
UBC
Systopia

## Slide 3: PIM: Now commercially available
UPMEM PIM-capable DRAM commercially available today
  DDR4-compatible DRAM with small general-purpose processors
  Integrated into standard off-the-shelf servers
Samsung Function in Memory Architecture (FIMA) – coming up
  Processors near HBM memory
  Execute 32-instruction snippets, total of nine instructions available

## Slide 4: UPMEM Overview
Looks and can be used like regular DRAM
Drop-in replacement for DDR4 DRAM
Each chip is equipped with small processors
Can be used in off-the-shelf servers
regular DRAM
UPMEM DRAM

## Slide 5: UPMEM architecture
UPMEM DRAM
DRAM Slice
64MB
DRAM Processing UNIT
General-purpose processor
Simple, in-order, 267-500MHz
No cache, only scratchpad memory
One DPU per 64MB slice of DRAM
8GB DIMM: 128 DPUs
Each DPU has its own DMA engine
Many DPUs can achieve very high DRAM bandwidth together

## Slide 6: PIM superpower: High DRAM bandwidth
DPUs running at 267 MHz
Only 32GB PIM DRAM
Sequentially read every byte of memory
128GB DRAM, 500MHz DPUs: 2TB/sec bandwidth
J. Nider, C. Mustard, A. Zoltan, J. Ramsden, L. Liu, J. Grossbard, M. Dashti, R. Jodin, A. Ghiti, J. Chauzi, A. Fedorova
A Case Study of Processing-in-Memory in off-the-Shelf Systems, USENIX ATC 2021

## Slide 7: Total cost of ownership
You can also get high memory bandwidth
  On high-end CPUs
  HBM (high-bandwidth memory)
  GPUs
PIM can deliver high bandwidth at a lower cost ($$ and Watts)
…if you are able to use it efficiently

## Slide 8: PIM superpower: Low TCO
Price:
8GB UPMEM DIMM: ~$300
More CPUs adds memory channels, but requires expensive high-end CPUs
Processor (Intel Xeon) | DRAM | PIM | Max. memory bandwidth (PIM or DRAM) | Cost
Low-bandwidth system |  |  |  | 
4110 | 48GB |  | 115GB/s | $860
4110 | 48GB | 24GB | 134GB/s | $1,760
Medium-bandwidth system |  |  |  | 
4110 | 48GB | 144GB | 806GB/s | $6,260
5318H | 192GB |  | 511GB/s | $6,532
High-bandwidth system |  |  |  | 
4110 | 64GB | 256GB | 1434GB/s | $10,580
8380 | 448GB |  | 1434GB/s | $83,580+
*Prices include just CPU and memory
Power:
Typical server with DRAM: about 400W
A server with 128GB PIM DRAM: 700W

## Slide 9: PIM performance: hyper-dimensional computing
Speedup over a single host CPU
End-to-end measurements
J. Nider, C. Mustard, A. Zoltan, J. Ramsden, L. Liu, J. Grossbard, M. Dashti, R. Jodin, A. Ghiti, J. Chauzi, A. Fedorova
A Case Study of Processing-in-Memory in off-the-Shelf Systems, to appear in USENIX ATC 2021
Number of DPUs
More data  more DPUs  more throughput

## Slide 10: PIM performance: compression
J. Nider, C. Mustard, A. Zoltan, J. Ramsden, L. Liu, J. Grossbard, M. Dashti, R. Jodin, A. Ghiti, J. Chauzi, A. Fedorova
A Case Study of Processing-in-Memory in off-the-Shelf Systems, to appear in USENIX ATC 2021
Snappy compression
Speedup over a single CPU
End-to-end measurements
Number of DPUs
More data  more DPUs  more throughput
Different input files

## Slide 11: Image Processing on PIM
lower is better
Motivation: pre-process images for ML training
PIM

## Slide 12: Moving data back-and-forth
copy overhead

## Slide 13: PIM limitations
UPMEM DRAM
DRAM Slice
64MB
DPUs can’t talk to each other
Each DPU sees data only in its slice
DPUs store data in different format than the CPU expects:
Has to do with interleaving
CPU has to de-interleave the data used by DPU
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
First 8-bytes of cache line
CPU splits a cache line across slices for better performance

## Slide 14: Deep Learning Recommendation Models in PIM
Problem
DNN-trained models
Inference done on CPUs
Models can be very large (even terabytes1)
Inference is bandwidth intensive
Can this be done?
Parts of DLRM inference were done in-memory2 and in-storage1
CPU Nodes
[1] Wilkening et al. RecSSD…, ASPLOS 2021
[2] Ke et al. RecNMP…, ISCA 2020
In-memory DLRM inference
Challenges
Some DLRM inference phases are compute-intensive
Skewed workload: balanced parallelism may be difficult to achieve

## Slide 15: DLRM Inference in PIM
RMC2 model
Latency of a single reference cycle. Larger batch size – more work.
lower is better
Notes: Total Embedding size 4 GB Per DPU Embedding data: 2 MB Per rank embedding data: 128 MB number of DPUs used: 2048 which is 32 ranks with 64 DPUs per rank. (edited)

## Slide 16: Where does the time go?
Useful work on PIM

## Slide 17: Low IPC when inference done on CPU
Inference done on CPU

## Slide 18: CPU implementation hits the memory wall
CPU cache hit – inference on CPU
CPU cache hit – inference on PIM

## Slide 19: Key-value store (in-memory cache) in PIM
DB
DB
DB
DB
memcached
memcached
memcached
memcached
Application Servers
Cache servers
Database servers
Benefits:
Cache servers use general-purpose CPUs
Get rid of expensive CPUs
Save money and power
Can this be done?
Get/put interface to memory
Hashtable and a memory allocator inside PIM
Data already sharded across cache servers – no communication needed!
Challenges
Difficult to buffer get requests; executing one at a time may be inefficient
get/put API
[1] LightStore (ASPLOS’19) – a key value store in SSD

## Slide 20: Filtering-in-memory
Key-value store with a column-store architecture
30MB of data per DPU
20 tasklets
Notes: Question: How do DPUs compare to CPU for a typical column-store workload: filtration?
PIM Setup: Each DPU is assigned 30MB of data. This data is divided among tasklets. Tasklets use a global lock to copy once a chunk (2048 bytes) of output data is ready. An optimum number of tasklets (20) is used for this experiment. The experiment assumes that data is already resident in the PIM-enabled DRAM. In other words, the runtime consists of DPU execution time and the time it takes to copy out the result.
CPU Setup: The experiment uses Intel Xeon Silver 4110 which has 2 CPUs, each containing 8 physical cores. There is 128 GB of memory on this server. Cache sizes are:
L1d cache: 32KB
L2 cache: 1MB
L3 cache: 11MB
There is a thread for each physical core that performs the filtering for a portion of the input data.
Each thread processes 240 MB of data.

## Slide 21: Filtering on PIM vs on CPU
As selectivity increases, we need to copy more data to back to the CPU

## Slide 22
Disaggregation
Blending
Disaggregation Meets Near-Data Processing

## Slide 23: Disaggregated memory meets PIM
PIM-enabled memory blades

## Slide 24: Memory management
Each DPU can run its own memory allocator
Keep a local page table
Can even compress pages on the fly

## Slide 25: Disaggregated memory meets PIM
100s ns
~10s of µs
Let memory run applications!
CPUs use load/store interface to access memory

## Slide 26: Disaggregated Memory Runs Applications
Disaggregated memory consists of CPU-less PIM blades
PIM array runs an entire application
CPU blades access memory via a higher-level API
Similar ideas:
  AIFM (OSDI 2020): Application-integrated far memory
  KV-Direct (SOSP 2017): key-value API to memory via a smart NIC and RDMA
  StRoM (EuroSys 2020): Smart Remote Memory
load/store
Higher-level interface