## Slide 1
Dr. Juan Gómez Luna
Professor Onur Mutlu
PIM Adoption Issues
How to Enable PIM Adoption?
ASPLOS 2023 Tutorial
Real-world Processing-in-Memory Systems for Modern Workloads
Sunday, March 26, 2023

## Slide 2: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 3: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 4: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 6: PIM Review and Open Problems (II)
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "Processing Data Where It Makes Sense: Enabling In-Memory Computation" Invited paper in Microprocessors and Microsystems (MICPRO), June 2019. [arXiv version]
https://arxiv.org/pdf/1903.03988.pdf

## Slide 7: PIM Review and Open Problems (III)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 8: Real PIM Hardware Systems and Prototypes

## Slide 9: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/
CPU
(x86, ARM, RV…)
DDR
Data bus

## Slide 10: Samsung Function-in-Memory DRAM (2021)

## Slide 11: AiM: Chip Implementation
4 Gb AiM die with 16 processing units (PUs)
Lee et al., A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications, ISSCC 2022
Notes: * The operating voltage is 1.25V: - Lowered from 1.35V of the normal GDDR6, for bank parallel operation.
* 16Gb/s is reached at 1.25V in DL operation.
Flat-lid package for lower thermal resistance.
Tested in a prototype system with an FPGA (connected to host CPU via PCIe).

## Slide 12: Samsung AxDIMM (2021)
DIMM-based PIM
  DLRM recommendation system
Baseline System
AxDIMM System
Ke et al. "Near-Memory Processing in Action: Accelerating Personalized Recommendation with AxDIMM", IEEE Micro (2021)

## Slide 13: HB-PNM: Overall Architecture
3D-stacked logic die and DRAM die vertically bonded by hybrid bonding (HB)
Niu et al., 184QPS/W 64Mb/mm2 3D Logic-to-DRAM Hybrid Bonding with Process-Near-Memory Engine for Recommendation System, ISSCC 2022

## Slide 14: AMD GPU with HBM-PIM
AMD Instinct Mi100 + HBM-PIM
https://semiconductor.samsung.com/newsroom/tech-blog/samsung-electronics-semiconductor-unveils-cutting-edge-memory-technology-to-accelerate-next-generation-ai/

## Slide 15: Compute Express Link (CXL)
Compute Express Link (CXL) is an open industry standard interconnect offering high-bandwidth, low-latency connectivity between host processor and devices such as accelerators, memory buffers, and smart I/O devices
https://www.computeexpresslink.org/_files/ugd/0c1418_14c5283e7f3e40f9b2955c7d0f60bebe.pdf

## Slide 16: CXL and PIM
CXL, as a high-bandwidth and low-latency interconnect, is a perfect complement for near-data processing
https://semiconductor.samsung.com/newsroom/tech-blog/samsung-electronics-semiconductor-unveils-cutting-edge-memory-technology-to-accelerate-next-generation-ai/

## Slide 17: Programming Models and Code Generation for PIM

## Slide 18: UPMEM System Organization
A UPMEM DIMM contains 8 or 16 chips
  Thus, 1 or 2 ranks of 8 chips each
Inside each PIM chip there are:
  8 64MB banks per chip: Main RAM (MRAM) banks
  8 DRAM Processing Units (DPUs) in each chip, 64 DPUs per rank

## Slide 19: Accelerator Model (I)
UPMEM DIMMs coexist with conventional DIMMs
Integration of UPMEM DIMMs in a system follows an accelerator model
UPMEM DIMMs can be seen as a loosely coupled accelerator
  Explicit data movement between the main processor (host CPU) and the accelerator (UPMEM)
  Explicit kernel launch onto the UPMEM processors
This resembles GPU computing

## Slide 20: Accelerator Model (II)
FIG. 6 is a flow diagram representing operations in a method of delegating a processing task to a DRAM processor according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 21: Inter-DPU Communication
There is no direct communication channel between DPUs
Inter-DPU communication takes places via the host CPU using CPU-DPU and DPU-CPU transfers
Example communication patterns:
  Merging of partial results to obtain the final result
    Only DPU-CPU transfers
  Redistribution of intermediate results for further computation
    DPU-CPU transfers and CPU-DPU transfers

## Slide 22: Lecture on Programming UPMEM PIM
https://youtu.be/RaOIoOQ5EgE

## Slide 23: SIMDRAM Framework
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
Notes: SIMDRAM is an end-to-end framework that provides the user with
the ability to implement an arbitrary operation in DRAM
The framework is composed of three main steps which are illustrated in this picture.
[CLICK] It takes as user input input the AND/OR/NOT representation of a desired operation.
[CLICK] Step 1 builds an efficient MAJ/NOT representation of a given desired operation from its AND/OR/NOT-based implementation. Specifically, this step takes as input a desired
operation and uses logic optimization to minimize the number of logic primitives (and, therefore, the computation latency) required to perform the operation.
[CLICK] The second step allocates DRAM rows to the operation’s inputs and outputs and generates the required sequence of DRAM commands to execute the desired operation.
[CLICK] This step’s output is a μProgram, i.e., the optimized sequence of DRAM commands that is stored in main memory and will be used to execute the operation at runtime. The uProgram
[CLICK] is stored in main memory and will be used to execute the operation at runtime
[CLICK] and a new SIMDRAM instruction called bbop is created as an interface to the uProgram, and then added to the CPU ISA
[CLICK] The third step executes the μProgram to perform the operation. SIMDRAM uses a control unit in the memory controller that transparently issues the sequence of commands to DRAM, as dictated by the μProgram. Once the μProgram is complete, the result of the operation is held in DRAM.
[NEXT]

## Slide 24: Programming Interface
Four new SIMDRAM ISA extensions
Type | ISA Format
Initialization | bbop_trsp_init address, size, n
1-Input Operation | bbop_op dst, src, size, n
2-Input Operation | bbop_op dst, src_1, src_2, size, n
Predication | bbop_if_else dst, src_1, src_2, select, size, n

## Slide 25: Code Using SIMDRAM Instructions
1 | int size = 65536;
2 | int elm_size = sizeof (uint8_t);
3 | uint8_t *A , *B , *C = (uint8_t *) malloc(size * elm_size);
4 | uint8_t *pred = (uint8_t *) malloc(size * elm_size);
5 | …
6 | for (int i = 0; i < size ; ++ i){
7 | bool cond = A[i] > pred[i];
8 | if (cond)
9 | C [i] = A[i] + B[i];
10 | else
11 | C [i] = A[i] - B [i];
12 | }
1 | int size = 65536;
2 | int elm_size = sizeof(uint8_t);
3 | uint8_t *A , *B , *C = (uint8_t *) malloc(size * elm_size);
4 | 
5 | bbop_trsp_init(A , size , elm_size);
6 | bbop_trsp_init(B , size , elm_size);
7 | bbop_trsp_init(C , size , elm_size);
8 | uint8_t *pred = (uint8_t *) malloc(size * elm_size);
9 | // D, E, F store intermediate data
10 | uint8_t *D , *E = (uint8_t *) malloc (size * elm_size);
11 | bool *F = (bool *) malloc (size * sizeof(bool));
12 | …
13 | bbop_add(D , A , B , size , elm_size);
14 | bbop_sub(E , A , B , size , elm_size);
15 | bbop_greater(F , A , pred , size , elm_size);
16 | bbop_if_else(C , D , E , F , size , elm_size);
← C code for vector add/sub
with predicated execution
Equivalent code using SIMDRAM operations →
Notes: Discuss manual vs automatic programming

## Slide 26: Lecture on SIMDRAM
https://youtu.be/pmZoAAhvkRQ

## Slide 27: PIM Runtime: Scheduling and Data Mapping

## Slide 28: Simple PIM Operations as ISA Extensions (I)
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture
PageRank algorithm (Page et al. 1999)

## Slide 29: Simple PIM Operations as ISA Extensions (II)
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)
PageRank algorithm (Page et al. 1999)

## Slide 30: Example PEI Microarchitecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
3D-stacked Memory
…
PCU (PEI Computation Unit)
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU (PEI
Mgmt Unit)
Example PEI uArchitecture

## Slide 31: PEI Performance Delta: Large Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: CPU-Only)
GeoMean
Percentage of Performance Improvement
wrt Baseline (CPU-only)
Locality-Aware = PIM or CPU depending on data location

## Slide 32: PEI Energy Consumption
Chart: 
| Small | Medium | Large
Cache | 0.27613 | 0.22974 | 0.2138
HMC Link | 0.50415 | 0.51297 | 0.51397
DRAM | 0.21457 | 0.25453 | 0.26887
Host-side PCU | 0.0043662 | 0.0036967 | 0.0030358
Memory-side PCU | 0 | 0 | 0
PMU | 7.7323e-05 | 6.4146e-05 | 5.4225e-05
계열 7 | 0.29322 | 0.18897 | 0.14107
계열 8 | 0.68428 | 0.4834 | 0.36147
계열 9 | 0.46391 | 0.35056 | 0.26204
계열 10 | 0 | 0 | 0
계열 11 | 0.015795 | 0.011518 | 0.0085371
계열 12 | 0.0053637 | 0.0036921 | 0.0027686
Host-Only (CPU)
PIM-Only
Locality-Aware
Total Energy Consumption
Breakdown of Energy Consumption on Different System Components

## Slide 33: More on PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 34: Key Challenge 1: Code Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
?
Main GPU
3D-stacked memory
(memory stack)
Challenge 1: Which operations should be executed in memory vs. in CPU?
?
SM (Streaming Multiprocessor)

## Slide 35: Key Challenge 2: Data Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
Challenge 2: How should data be mapped to different 3D memory stacks?
SM (Streaming Multiprocessor)

## Slide 36: How to Do the Code and Data Mapping?
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 37: How to Schedule Code? (I)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 38: How to Schedule Code? (II)
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 39: How to Schedule Code? (III)
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 40: Research Questions
What are simple mechanisms to enable and disable PIM execution? How can PIM execution be throttled for highest performance gains? How should data locations and access patterns affect where/whether PIM execution should occur?
Which parts of a given application’s code should be executed on PIM? What are simple mechanisms to identify when those parts of the application code can benefit from PIM?
What are scheduling mechanisms to share PIM engines between multiple requesting cores to maximize benefits obtained from PIM?
What are simple mechanisms to manage access to a memory that serves both CPU requests and PIM requests?

## Slide 41: Memory Coherence

## Slide 42: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 43: How to Maintain Coherence? (I)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 44: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 45: CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators
Amirali Boroumand
Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Rachata Ausavarungnirun, Kevin Hsieh, Nastaran Hajinazar, Krishna Malladi, Hongzhong Zheng, Onur Mutlu

## Slide 46: Specialized Accelerators
ASIC
FPGA
GPU
NDA
ASIC
ASIC
  Specialized accelerators are now everywhere!
Recent advancement in 3D-stacked technology enabled Near-Data Accelerators (NDA)
CPU
DRAM
NDA
Notes: Specialized accelerators are now every where, and they are widely used to improve the performance and energy efficiency of computing systems.
At the same time, recent advancement in 3D-stacked technology enabled near data acceleartors. These accelerators can further boost the benefits of specialized accelerator by moving computation close to data and getting rid of data movement.

## Slide 47: Coherence For NDAs
ASIC
  Challenge: Coherence between NDAs and CPUs
DRAM
L2
L1
CPU
CPU
CPU
CPU
NDA
Compute Unit
(1) Large cost of off-chip communication
It is impractical to use traditional coherence protocols
(2) NDA applications generate a large amount of off-chip data movement
Notes: However, one of the major system challenges for adopting near data accelartors into computing system is coherence. Maintainig coherence between NDAs and CPUs is very challenging because of two reasons: First, the cost of off-chip communication between NDAs and CPUs is very high. Second, NDA applications typically have poor locality, and generate a large amount of off-chip data movement which leads to a large number of coherence misses. Because of these challenges, it is
Impractical use traditional coherence protocols for coherence, because that leads to a large amount of off-chip coherence messages, which can eliminate a significant portion of NDA benefits

## Slide 48: Existing Coherence Mechanisms
ASIC
  We extensively study existing NDA coherence mechanisms and make three key observations:
These mechanisms eliminate a significant portion of NDA’s benefits
1
The majority of off-chip coherence traffic generated by these mechanisms is unnecessary
2
Much of the off-chip traffic can be eliminated if the coherence mechanism has insight into the memory accesses
3
Notes: In this work, We extensively study existing NDA coherence mechanisms and make three key observations:
First, these mechanisms eliminate a significant portion of NDA’s benefits as they generate a large amount of off-chip coherence traffic, Second, … Finally, we find that a significant portion of off-chip traffic can be eliminated if the coherence mechanism has insight into
which memory accesses actually require a coherence operation (what part of the shared data is actually accessed)

## Slide 49: An Optimistic Approach
ASIC
1
Gain insights before any coherence checks happens
  We find that an optimistic approach to coherence can address the challenges related to NDA coherence
2
Perform only the necessary coherence requests
Notes: Based on these observations, we find that an optimistic approach to coherence can address the challenges of NDA coherence. We find that an optimistic execution model for NDA enables us to gain insight into the memory accesses before any coherence permissions are
checked, and as a result, enforce coherence with only the necessary data movement/coherence requests.
We propose CoNDA, a new coherence mechanism that optimistically executes code on an NDA to gather information on memory
accesses. Optimistic execution enables CoNDA to identify and avoid performing unnecessary coherence requests
Our evaluation shows that CoNDA consistency retain the benefit of NDA across all of the workloads and …

## Slide 50: CoNDA
Time
Optimistic execution
CPU
NDA
Concurrent CPU + NDA Execution
Offload NDA kernel
Signature
Signature
Send signatures
  Coherence Resolution
Commit or Re-execute
CPU Thread Execution
  We propose CoNDA, a mechanism that uses optimistic NDA execution to avoid unnecessary coherence traffic
No Coherence Request
Notes: So, based on the execution model I just explained, we propose a coherence mechanism, which uses that execution model to avoid unnecessary coherence traffic.
Basically, in Conda, CPU offload the kernel to NDA. NDA starts executing in optimistic mode. During optimistic execution
CoNDA efficiently tracks the addresses of all NDA reads, NDA writes, and CPU write using compressed signatures. When optimistic mode is done, NDA send these signaturs to CPU and CoNDA use these signatures to resolve coherence violations.
If CoNDA detects any coherence violation (1) the NDA invalidates all
Of updates; (2) the CPU resolves the coherence
requests, performing only the necessary coherence operations (including
any cache line updates); and (3) the NDA re-executes the
uncommitted portion of the kernel.
Otherwise, CoNDA performs the necessary coherence operations, clears the uncommitted flag
for all data updates in the NDA L1 cache, and resumes optimistic execution if
the NDA kernel is not finished.

## Slide 51: CoNDA
Time
Optimistic execution
CPU
NDA
Concurrent CPU + NDA Execution
Offload NDA kernel
Signature
Signature
Send signatures
  Coherence Resolution
Commit or Re-execute
CPU Thread Execution
  We propose CoNDA, a mechanism that uses optimistic NDA execution to avoid unnecessary coherence traffic
No Coherence Request
  CoNDA comes within 10.4% and 4.4% of performance and energy of an ideal NDA coherence mechanism
Notes: So, based on the execution model I just explained, we propose a coherence mechanism, which uses that execution model to avoid unnecessary coherence traffic.
Basically, in Conda, CPU offload the kernel to NDA. NDA starts executing in optimistic mode. During optimistic execution
CoNDA efficiently tracks the addresses of all NDA reads, NDA writes, and CPU write using compressed signatures. When optimistic mode is done, NDA send these signaturs to CPU and CoNDA use these signatures to resolve coherence violations.
If CoNDA detects any coherence violation (1) the NDA invalidates all
Of updates; (2) the CPU resolves the coherence
requests, performing only the necessary coherence operations (including
any cache line updates); and (3) the NDA re-executes the
uncommitted portion of the kernel.
Otherwise, CoNDA performs the necessary coherence operations, clears the uncommitted flag
for all data updates in the NDA L1 cache, and resumes optimistic execution if
the NDA kernel is not finished.

## Slide 52: CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators
Amirali Boroumand
Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Rachata Ausavarungnirun, Kevin Hsieh, Nastaran Hajinazar, Krishna Malladi, Hongzhong Zheng, Onur Mutlu

## Slide 53: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 54: Synchronization Support

## Slide 55: How to Support Synchronization?
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 56
SynCron
Efficient Synchronization Support
for Near-Data-Processing Architectures
Christina Giannoula
Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas
Ivan Fernandez, Juan Gómez Luna, Lois Orosa
Nectarios Koziris, Georgios Goumas, Onur Mutlu

## Slide 57
Problem:
Synchronization support is challenging for NDP systems
Prior schemes are not suitable or efficient for NDP systems
Contribution:
SynCron: the first end-to-end synchronization solution for NDP architectures
Key Results:
SynCron comes within 9.5% and 6.2% of performance and energy of an Ideal zero-overhead synchronization scheme
Executive Summary

## Slide 58
Single Source Shortest Path (SSSP)
for v in Graph:
for u in neighbors[v]:
if distance[v] + edge_weight[v, u] < distance[u]
if distance[v] + edge_weight[v, u] < distance[u]
distance[u] = distance[v] + edge_weight[v, u]
Locks
Barriers
Graph Analytics
Bioinformatics
Concurrent
Data Structures
Databases
Image Processing
Synchronization is Necessary
lock_acquire(u)
lock_release(u)

## Slide 59
Synchronization challenges in NDP systems:
(1) Lack of hardware cache coherence support
(2) Expensive communication across NDP units
(3) Lack of a shared level of cache memory
Main Memory
NDP Core
NDP Core
NDP Core
NDP Unit
Programmable Core / Accelerator
Private Cache
NDP System
Baseline NDP Architecture

## Slide 60
NDP Synchronization Solution Space
(1) Shared Memory
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
NDPs:
SynCron [HPCA’21]
SynCron’s Key Techniques:
1. Hardware support for synchronization acceleration
2. Direct buffering of synchronization variables
3. Hierarchical message-passing communication
4. Integrated hardware-only overflow management
(2) Message-passing

## Slide 61
NDP Unit 0
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 0
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
`````
ISA
  No Complex Cache Coherence Protocols
  No Expensive Atomic Operations
  Low Hardware Cost
1. Hardware Synchronization Support
Local
lock acquire

## Slide 62
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
Indexing Counters
Synchronization
Processing Unit
Address
…
--
…
--
…
--
…
--
…
Synchronization
Table
2. Direct Buffering of Variables
Local
lock acquire

## Slide 63
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
Indexing Counters
Synchronization
Processing Unit
Synchronization
Table
2. Direct Buffering of Variables
Local
lock acquire
Address
…
0x33A9
…
--
…
--
…
--
…
      No Costly Memory Accesses
      Low Latency

## Slide 64
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
syncronVar
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication

## Slide 65
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
syncronVar
Master
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication
Local
lock acquire

## Slide 66
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
syncronVar
Master
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication
Global
lock acquire
Minimize Expensive Traffic

## Slide 67
SynCron’s Benefits:
High System Performance
Low Hardware Cost
Programming Ease
General Synchronization Support
The first end-to-end synchronization solution for NDP architectures
SynCron
SynCron comes within 9.5% and 6.2% of performance and energy of Ideal zero-overhead synchronization

## Slide 68
SynCron
Efficient Synchronization Support
for Near-Data-Processing Architectures
Christina Giannoula
Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas
Ivan Fernandez, Juan Gómez Luna, Lois Orosa
Nectarios Koziris, Georgios Goumas, Onur Mutlu

## Slide 69: How to Support Synchronization?
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 70: Lecture on Synchronization Support for PIM
https://youtu.be/GHZkRHp_AG0

## Slide 71: How to Design Data Structures for PIM?
Zhiyu Liu, Irina Calciu, Maurice Herlihy, and Onur Mutlu, "Concurrent Data Structures for Near-Memory Computing" Proceedings of the 29th ACM Symposium on Parallelism in Algorithms and Architectures (SPAA), Washington, DC, USA, July 2017. [Slides (pptx) (pdf)]

## Slide 72: Virtual Memory Support

## Slide 73: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 74: Executive Summary
Our Goal: Accelerating pointer chasing inside main memory
Challenges: Parallelism challenge and Address translation challenge
Our Solution: In-Memory PoInter Chasing Accelerator (IMPICA)
  Address-access decoupling: enabling parallelism in the accelerator with low cost
  IMPICA page table: low cost page table in logic layer
Key Results:
  1.2X – 1.9X speedup for pointer chasing operations, +16% database throughput
  6% - 41% reduction in energy consumption

## Slide 75: Linked Data Structures
Linked data structures are widely used in many important applications
Database
B-Tree
Hash Table
Key-value stores
Linked data structures are
connected by pointers

## Slide 76: The Problem: Pointer Chasing
Traversing linked data structures requires chasing pointers
MEM
H
E
A
F
Q
M
Find(A)
Addr (H)
Data (H)
Addr (E)
Data (E)
Addr (A)
Data (A)
Serialized and irregular access pattern
6X cycles per instruction in real workloads

## Slide 77: Our Goal
DRAM layers
Accelerating pointer chasing inside main memory
H
E
A
F
Q
M
Find(A)
MEM
Data (A)
Logic layer
Find
(A)

## Slide 78: Parallelism Challenge
Time
Memory
access
CPU core
In-Memory Accelerator
Comp
Memory access
CPU core
Comp
Comp
Comp
Memory
access
Comp
Comp
Comp
Memory access
Comp
Faster for one operation
Slower for two operations

## Slide 79: Parallelism Challenge and Opportunity
A simple in-memory accelerator can still be slower than multiple CPU cores
Opportunity: a pointer-chasing accelerator spends a long time waiting for memory
CPU core
Accelerator
CPU core
CPU core
Comp
Memory access (10-15X of Comp)
Comp

## Slide 80: Our Solution: Address-Access Decoupling
Time
Comp
Memory access
Comp
Comp
Address Engine
Access Engine
Comp
Memory access
Memory
access
CPU core
CPU core
Comp
Comp
Memory
access
Comp
Comp
Address-access decoupling enables parallelism in both engines with low cost

## Slide 81: IMPICA Core Architecture
DRAM Dies
Address
Engine
Access
Engine
Memory Controller
DRAM
Logic Layer
DRAM Layers
Request Queue
To/From CPU
Access Queue
Response Queue
IMPICA Cache
Traversal 1
Traversal 2

## Slide 82: Address Translation Challenge
TLB/MMU
Pointer (VA)
Pointer (PA)
Page table walk
PTW
PTW
PTW
PTW
PTW
No TLB/MMU on the memory side
Duplicating it is costly and creates compatibility issue
The page table walk requires multiple memory accesses

## Slide 83: Our Solution: IMPICA Page Table
Completely decouple the page table of IMPICA from the page table of the CPUs
IMPICA Region
Physical Address Space
Virtual Page
Physical Page
Physical Page
Virtual Page
CPU Page Table
Virtual Address Space
IMPICA Page Table
Map linked data structure into IMPICA regions
IMPICA page table is a partial-to-any mapping

## Slide 84: IMPICA Page Table: Mechanism
Bit [47:41]
Bit [40:21]
Bit [20:12]
Bit [11:0]
Region Table
Flat Page Table (2MB)
Small Page Table (4KB)
+
+
Virtual Address
+
Physical Address
Tiny region table is almost always in the cache
Flat page table
saves one memory access
84

## Slide 85: Evaluation Methodology
Simulator: gem5
System Configuration
  CPU
    4 OoO cores, 2GHz
    Cache: 32KB L1, 1MB L2
  IMPICA
    1 core, 500MHz, 32KB Cache
  Memory Bandwidth
    12.8 GB/s for CPU, 51.2 GB/s for IMPICA
Our simulator code is open source
  https://github.com/CMU-SAFARI/IMPICA

## Slide 86: Result – Microbenchmark Performance
Chart: Speedup
| Linked List | Hash Table | B-Tree
Baseline + extra 128KB L2 | 1.0261 | 1.0135 | 1.0205
IMPICA | 1.9236 | 1.2865 | 1.1848
1.9X
1.3X
1.2X

## Slide 87: Result – Database Performance
Chart: Database Throughput
| Baseline + extra 128KB L2 | Baseline + extra 1MB L2 | IMPICA
Throughput | 1.0101 | 1.054 | 1.1601
+2%
+5%
+16%
Chart: Database Latency
| Baseline + extra 128KB L2 | Baseline + extra 1MB L2 | IMPICA
Latency | 1.001 | 0.95911 | 0.86934
-4%
-13%
-0%

## Slide 88: System Energy Consumption
Chart: Normalized Energy
| Linked List | Hash Table | B-Tree | DBx1000
Baseline + extra 128KB L2 | 0.97087 | 0.99077 | 0.98072 | 0.9731
IMPICA | 0.59474 | 0.77144 | 0.90116 | 0.94365
-41%
-24%
-6%
-10%

## Slide 89: Area and Power Overhead
Power overhead: average power increases by 5.6%
CPU (Cortex-A57) | 5.85 mm2 per core
L2 Cache | 5 mm2 per MB
Memory Controller | 10 mm2
IMPICA (+32KB cache) | 0.45 mm2

## Slide 90: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 91: Rethinking Virtual Memory
Nastaran Hajinazar, Pratyush Patel, Minesh Patel, Konstantinos Kanellopoulos, Saugata Ghose, Rachata Ausavarungnirun, Geraldo Francisco de Oliveira Jr., Jonathan Appavoo, Vivek Seshadri, and Onur Mutlu, "The Virtual Block Interface: A Flexible Alternative to the Conventional Virtual Memory Framework" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Virtual, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [ARM Research Summit Poster (pptx) (pdf)] [Talk Video (26 minutes)] [Lightning Talk Video (3 minutes)] [Lecture Video (43 minutes)]

## Slide 92: VBI: Overview
92
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
VBI
Conventional Virtual Memory
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes

## Slide 93: Lecture on Virtual Block Interface
https://www.youtube.com/watch?v=2RhGMpY18zw&list=PL5PHm2jkkXmi5CxxI7b3JCL1TWybTDtKq&index=22

## Slide 94: Security Considerations

## Slide 95: DRAM Latency PUF Key Idea
Row Decoder
A cell’s latency failure probability is inherently related to random process variation from manufacturing
We can provide repeatable and unique device signatures using latency error patterns
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Notes: Our key idea is to reduce DRAM read access latency below the reliable datasheet specifications using software-only system calls in order to exploit the resulting error patterns as unique identifiers.
[CLICK] We find that the probability that a cell will result in a latency failure due to a reduced-tRCD access, is inherently related to random process variation from manufacturing [CLICK] This knowledge enables us to provide a repeatable and unique device signature with these patterns of latency failures.
[CLICK] Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing.
The Key Idea is to generate a PUF response using the locations of cells that have a high percentage chance of failing with a tRCD value reduced below manufacturer-recommended values.

## Slide 96: DRAM Latency Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 97: D-RaNGe Key Idea
Row Decoder
A cell’s latency failure probability is inherently related to random process variation from manufacturing
We can extract random values by observing DRAM cells’ latency failure probabilities
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Notes: Our key idea is to reduce DRAM read access latency below the reliable datasheet specification values using software-only system calls in order to exploit the resulting error patterns as true random numbers
[CLICK] We find that the probability that a cell will result in a latency failure due to a reduced-tRCD access, is inherently related to random process variation from manufacturing [CLICK] This knowledge enables us to provide random values by observing DRAM cells’ latency failure probabilities.
[CLICK] Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing.

## Slide 98: DRAM Latency True Random Number Generator
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 99: Quadruple Activation (QUAC)
New Observation
Carefully-engineered DRAM commands can activate four rows in real DRAM chips
Activate four rows with two ACT commands
ACT
PRE
ACT
<3ns
<3ns
35ns
14ns
Violated
Default

## Slide 100: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
Ready to Sense
Voltage Level
VTH
-VTH
0
Sense Amplifier
VDD/2
VDD/2
Enable
Logic-1
R0
R1
R2
R3

## Slide 101: Generating Random Values via QUAC
Vdd
-Vdd
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Voltage Difference
VTH
-VTH
0
Time
R0
R1
R2
R3
Sense Amplifier

## Slide 102: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
VTH
-VTH
0
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Enable Sense Amplifiers
Sense Amplifier
R0
R1
R2
R3
Random perturbation

## Slide 103: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
R0
R1
R2
R3
DRAM Segment
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Random Values
Logic-1
Logic-0

## Slide 104: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Step 3 Read
SHA-256
Memory Controller
256-bit Shannon Entropy Blocks
Step 4 Post-process
256-bit TRN

## Slide 105: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Step 3 Read
SHA-256
Memory Controller
Step 4 Post-process
256-bit TRN
Generates a 256-bit random number for every 256-bit Shannon Entropy block

## Slide 106: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 107: Benchmarks and Simulation Infrastructures

## Slide 108: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 109: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 110: Lecture on PrIM Benchmarks
https://youtu.be/S1h1yw-94iw

## Slide 111: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 112: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
16
Notes: Our methodology has three steps.
[CLICK] It takes as input an application’s source code and its input datasets.
[CLICK] In Step 1, we use a hardware profiling tool to identify memory-bound functions across many applications. This step allows for a quick first-level identification of many applications that suffer from memory bottlenecks and functions that cause these bottlenecks.
[CLICK] We utilize a new simulator, called DAMOV-SIM to collect key metrics and execute performance analysis of the functions identified in Step 1.
[CLICK] In Step 2, we use the architecture-independent profiling tool to collect metrics that provide insights about the memory access behavior of the memory-bottlenecked functions.
[CLICK] In Step 3, we collect architecture-dependent metrics and analyze the performance and energy of each function in an application when each of our three candidate data movement mitigation mechanisms is applied to the system.
[CLICK] By combining the data obtained from all three steps, we can systematically classify the leading causes of data movement bottlenecks in an application or function into different bottleneck classes
[NEXT]

## Slide 113: More on DAMOV
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan Fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" Preprint in arXiv, 8 May 2021. [arXiv preprint] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 114: Lecture on DAMOV
https://youtu.be/8OYGTIR07uA

## Slide 115: Simulation Infrastructures for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator-pim
  https://github.com/CMU-SAFARI/ramulator
  [Source Code for Ramulator-PIM]

## Slide 116: Simulation Infrastructures for PIM (in SSDs)
Arash Tavakkol, Juan Gomez-Luna, Mohammad Sadrosadati, Saugata Ghose, and Onur Mutlu, "MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices" Proceedings of the 16th USENIX Conference on File and Storage Technologies (FAST), Oakland, CA, USA, February 2018. [Slides (pptx) (pdf)] [Source Code]

## Slide 117: NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira,
Stefano Corda, Sander Stuijk, Onur Mutlu, Henk Corporaal
56th Design Automation Conference (DAC), Las Vegas
4th-June-2019
Funded by the Horizon 2020 Framework Programme of the European Union
MSCA-ITN-EID

## Slide 118: Executive Summary
Motivation: A promising paradigm to alleviate data movement bottleneck is near-memory computing (NMC), which consists of placing compute units close to the memory subsystem
Problem: Simulation times are extremely slow, imposing long run-time especially in the early-stage design space exploration
Goal: A quick high-level performance and energy estimation framework for NMC architectures
Our contribution: NAPEL
  Fast and accurate performance and energy prediction for previously-unseen applications using ensemble learning
  Use intelligent statistical techniques and micro-architecture-independent application features to minimize experimental runs
Evaluation
  NAPEL is, on average, 220x faster than state-of-the-art NMC simulator
  Error rates (average) of 8.5% and 11.5% for performance and energy estimation
We open source Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 119: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 120: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
Simulation of real workloads can be 10000x slower than native-execution!!!
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 121: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
Idea: Leverage ML with statistical techniques for quick NMC performance/energy prediction
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 122: NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning
NAPEL Model Training

## Slide 123: Phase 1: LLVM Analyzer

## Slide 124: Phase 2: Microarchitecture Simulation
Central composite design of experiments technique to minimize the number of experiments while data collection

## Slide 125: Phase 3: Ensemble ML Training
Application Features
Instruction Mix
ILP
Reuse distance
Memory traffic
Register traffic
Memory footprint
Architecture Features
Core type
#PEs
Core frequency
Cache line size
DRAM layers
Cache access fraction
DRAM access fraction

## Slide 126: NAPEL Framework

## Slide 127: NAPEL Prediction

## Slide 128: Experimental Setup
Host System
  IBM POWER9
  Power: AMESTER
NMC Subsystem
  Ramulator-PIM1
Workloads
  PolyBench and Rodinia
  Heterogeneous workloads such as image processing, machine learning, graph processing etc.
Accuracy in terms of mean relative error (MRE)
1https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 129: NAPEL Accuracy: Performance and Energy Estimates
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 18 | 49 | 64.4 | 17.5 | 27 | 54.5 | 45 | 79 | 19.5 | 89 | 12 | 10 | 40.4083
ANN | 19 | 22 | 24 | 13.52 | 15.5 | 27.15 | 15.47 | 26 | 6 | 15.2 | 6.18 | 6.05 | 16.3392
NAPEL | 10.1 | 15 | 17 | 5 | 17 | 12 | 15 | 14.5 | 12 | 8.1 | 3.62 | 10.1 | 11.6183
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 16.5 | 60 | 37.65 | 10.92 | 32.5 | 41 | 19.2 | 14.74 | 23.16 | 32 | 25 | 13.14 | 27.1508
ANN | 13.44 | 26 | 21 | 12 | 11.29 | 19.78 | 9.97 | 8.83 | 10.05 | 22.24 | 11.27 | 11 | 14.7392
NAPEL | 5.86 | 19 | 14 | 5 | 9.28 | 6.6 | 5.68 | 12.36 | 5.67 | 4.63 | 6.23 | 8.05 | 8.53
(a) Performance prediction
(b) Energy prediction

## Slide 130: NAPEL Accuracy: Performance and Energy Estimates
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 18 | 49 | 64.4 | 17.5 | 27 | 54.5 | 45 | 79 | 19.5 | 89 | 12 | 10 | 40.4083
ANN | 19 | 22 | 24 | 13.52 | 15.5 | 27.15 | 15.47 | 26 | 6 | 15.2 | 6.18 | 6.05 | 16.3392
NAPEL | 10.1 | 15 | 17 | 5 | 17 | 12 | 15 | 14.5 | 12 | 8.1 | 3.62 | 10.1 | 11.6183
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 16.5 | 60 | 37.65 | 10.92 | 32.5 | 41 | 19.2 | 14.74 | 23.16 | 32 | 25 | 13.14 | 27.1508
ANN | 13.44 | 26 | 21 | 12 | 11.29 | 19.78 | 9.97 | 8.83 | 10.05 | 22.24 | 11.27 | 11 | 14.7392
NAPEL | 5.86 | 19 | 14 | 5 | 9.28 | 6.6 | 5.68 | 12.36 | 5.67 | 4.63 | 6.23 | 8.05 | 8.53
(a) Performance prediction
(b) Energy prediction
MRE of 8.5% and 11.6% for performance and energy

## Slide 131: Speed of Evaluation
Chart: DoE configurations
256 DoE configurations for 12 evaluated applications
256
1

## Slide 132: Speed of Evaluation
Chart: DoE configurations
256 DoE configurations for 12 evaluated applications
256
1
220x (up to 1039x) faster than NMC simulator

## Slide 133: Use Case: NMC Suitability Analysis
Chart: EDP Reduction
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm
Actual | 1.2825 | 4.5336 | 5.1644 | 4.9851 | 0.61146 | 0.2095 | 2.5023 | 2.1933 | 0.66969 | 0.16452 | 0.08306 | 0.029039
NAPEL | 1.5154 | 4.5901 | 3.8068 | 4.5216 | 0.48655 | 0.24709 | 2.0589 | 1.7048 | 0.63388 | 0.1711 | 0.091906 | 0.02441
Assess the potential of offloading a workload to NMC
NAPEL provides accurate prediction of NMC suitability
MRE between 1.3% to 26.3% (average 14.1%)

## Slide 134: Performance & Energy Models for PIM
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira, Stefano Corda, Sander Stujik, Onur Mutlu, and Henk Corporaal, "NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning" Proceedings of the 56th Design Automation Conference (DAC), Las Vegas, NV, USA, June 2019. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code for Ramulator-PIM]

## Slide 135: Applications that Benefit from PIM

## Slide 136: New Applications and Use Cases for PIM
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. arxiv.org Version (pdf)

## Slide 137: Genome Read In-Memory (GRIM) Filter: Fast Seed Location Filtering in DNA Read Mapping using Processing-in-Memory Technologies
Jeremie Kim,
Damla Senol, Hongyi Xin, Donghyuk Lee,
Saugata Ghose, Mohammed Alser, Hasan Hassan,
Oguz Ergin, Can Alkan, and Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be presenting Genome Read In-Memory Filter which will also be referred to as GRIM-Filter for short.
[CLICK]

## Slide 138: Executive Summary
Genome Read Mapping is a very important problem and is the first step in many types of genomic analysis
  Could lead to improved health care, medicine, quality of life
Read mapping is an approximate string matching problem
  Find the best fit of 100 character strings into a 3 billion character dictionary
  Alignment is currently the best method for determining the similarity between two strings, but is very expensive
We propose an in-memory processing algorithm GRIM-Filter for accelerating read mapping, by reducing the number of required alignments
We implement GRIM-Filter using in-memory processing within 3D-stacked memory and show up to 3.7x speedup.

## Slide 139: Accelerating Approximate String Matching
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 140: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 141: Accelerating Climate Modeling
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (23 minutes)] Nominated for the Stamatis Vassiliadis Memorial Award.

## Slide 142: Accelerating Time Series Analysis
Ivan Fernandez, Ricardo Quislant, Christina Giannoula, Mohammed Alser, Juan Gómez-Luna, Eladio Gutiérrez, Oscar Plata, and Onur Mutlu, "NATSA: A Near-Data Processing Accelerator for Time Series Analysis" Proceedings of the 38th IEEE International Conference on Computer Design (ICCD), Virtual, October 2020.

## Slide 143: Epilogue

## Slide 144: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 146: PIM Review and Open Problems (II)
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "Processing Data Where It Makes Sense: Enabling In-Memory Computation" Invited paper in Microprocessors and Microsystems (MICPRO), June 2019. [arXiv version]
https://arxiv.org/pdf/1903.03988.pdf

## Slide 147: PIM Review and Open Problems (III)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 148: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 149: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 150: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 151: A Tutorial on Memory-Centric Systems
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 153: Real PIM Tutorial (ISCA 2023)
https://events.safari.ethz.ch/isca-pim-tutorial/doku.php?id=start
Lectures + Hands-on labs + Invited lectures

## Slide 154: Processing-in-Memory Course (Fall 2022)
https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=processing_in_memory
https://youtube.com/playlist?list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy
Short weekly lectures
Hands-on projects

## Slide 155: Processing-in-Memory Course (Spring 2023)
Short weekly lectures
Hands-on projects

## Slide 156: Introducción al Procesamiento en Memoria (en Español)
https://youtu.be/QixM8UUwGi8

## Slide 157: Análisis de una Arquitectura Real de Procesamiento en Memoria (en Español)

## Slide 158
Dr. Juan Gómez Luna
Professor Onur Mutlu
PIM Adoption Issues
How to Enable PIM Adoption?
ASPLOS 2023 Tutorial
Real-world Processing-in-Memory Systems for Modern Workloads
Sunday, March 26, 2023