## Slide 1: PiDRAM An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques
Ataberk Olgun
Juan Gomez Luna
Konstantinos Kanellopoulos
Hasan Hassan
Behzad Salami
Oğuz Ergin
Onur Mutlu
Notes: Hi, I am Ataberk and I will present PiDRAM: An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques. This work was done in a collaboration of SAFARI and Kasirga Research groups in ETH Zurich and TOBB University of Economics and technology.

## Slide 2: Executive Summary
Motivation: Commodity DRAM based PiM techniques improve the performance and energy efficiency of computing systems at no additional DRAM hardware cost
Problem: Challenges of integrating these PiM techniques into real systems are not solved
General-purpose computing systems, special-purpose testing platforms, and system simulators cannot be used to efficiently study system integration challenges
Goal: Design and implement a flexible framework that can be used to:
solve system integration challenges
analyze trade-offs of end-to-end implementations of commodity DRAM-based-PiM techniques
Key idea: PiDRAM, an FPGA-based framework that enables:
system integration studies
end-to-end evaluations of PIM techniques using real unmodified DRAM chips
Evaluation: End-to-end integration of two PiM techniques on PiDRAM’s FPGA prototype
Case Study #1 – RowClone: In-DRAM bulk data copy operations
119x speedup for copy operations compared to CPU-copy with system support
198 lines of Verilog and 565 lines of C++ code over PiDRAM’s flexible codebase
Case Study #2 – D-RaNGe: DRAM-based random number generation technique
8.30 Mb/s true random number generator (TRNG) throughput, 220 ns TRNG latency
190 lines of Verilog and 78 lines of C++ code over PiDRAM’s flexible codebase
PiDRAM: https://github.com/CMU-SAFARI/PiDRAM
Notes: I will start with an executive summary
[CLICK] Commodity DRAM-based PIM techniques improve the performance and energy efficiency of computing systems without incurring any DRAM hardware cost
[CLICK] However, challenges of integrating these techniques into real systems are not yet solved.
[CLICK] Moreover, these challenges cannot be efficiently studied using existing computing systems, special-purpose DRAM testing platforms or system simulators
[CLICK] Our goal is to design and implement a flexible framework that can be used to [CLICK] solve the important system integration challenges and [CLICK] analyze the trade-offs of end-to-end implementations of commodity DRAM based PiM techniques
[CLICK] Our key idea is to develop PiDRAM, an FPGA-based framework that enables such studies using real unmodified DRAM chips
[CLICK] Using our framework, we conduct two case studies on two recent commodity DRAM based PiM techniques on a real FPGA prototype of a full system
[CLICK] In our first case study about in-DRAM bulk data copy operations, we show that in-DRAM data copy operations provide 119 times speedup over CPU-copy operations including system support. To conduct this case study over PiDRAM’s extensible code base, we add only 198 lines of Verilog and only 565 lines of C++ code.
[CLICK] In our second case study about an in-DRAM true random number generation technique, we show that an end-to-end implementation of a DRAM-based true random number generator can provide high throughput true random numbers at low latency. Implementing the true random number generator takes us only 190 additional lines of Verilog and 78 additional lines of C++ code over PiDRAM’s code base.

## Slide 3: Outline
Background
  Commodity DRAM Based PiM Techniques
PiDRAM
  Overview
  Hardware & Software Components
  FPGA Prototype
Case Studies
  Case Study #1 – RowClone Case Study #2 – D-RaNGe
Conclusion
Notes: Here is the outline of my talk. I will start by quickly introducing commodity DRAM based PuM techniques

## Slide 4: Processing-in-Memory Techniques
Use operational principles of memory to perform bulk data movement and computation
Commodity DRAM chips can already perform:
Row-copy: In-DRAM bulk data copy (or initialization) at DRAM row granularity
True random number generation
Physical uncloneable functions
Majority operation
[Gao+, MICRO’19]-[Gao+, MICRO’22]
(e.g., [Kim+, HPCA’19]-[Olgun+, ISCA’21])
(e.g., [Kim+, HPCA’18])
[Gao+, MICRO’19]-[Gao+, MICRO’22]
Notes: Commodity DRAM based PiM techniques use operational principles of commodity DRAM chips to move data and perform computation inside the DRAM chip.
[CLICK] Two examples of such techniques relevant to our work are in-DRAM data copy or initialization and [CLICK] in-DRAM true random number generation.

## Slide 5: Row-Copy: Key Idea (RowClone)
r
c
r
o
w
s
s
t
o
w
d
r
1. Source row to sense amplifiers
2. Sense amplifiers to destination row
Sense Amplifiers
r
c
r
o
w
s
s
r
c
r
o
w
?

[Seshadri+ MICRO’13]
Notes: I will describe the key idea of in-DRAM copy operations over this diagram. The diagram shows a simplified view of a DRAM subarray with a set of DRAM rows and sense amplifiers. To copy the orange source row to the gray destination row:
[CLICK] First, we copy the source row to row buffer
[CLICK] Second, we move the data from the sense amplifiers to the destination row
[CLICK] Current DRAM chips already support the first step of this operation. We can use activate commands to copy the source row to the destination row
[CLICK] I will describe how we can move data back from the sense amplifiers to the destination row later in my presentation

## Slide 6: RowClone in Real DRAM Chips
Key Idea: Use carefully created DRAM command sequences
ACT  PRE  ACT command sequence with greatly reduced DRAM timing parameters
ComputeDRAM [Gao+, MICRO’19] demonstrates in-DRAM copy operations in real DDR3 chips
ACT S
PRE
ACT D
ACT S
PRE
ACT D
Standard DRAM Timings
Violated DRAM Timings
“activate row S, precharge, then activate row D”
“activate row S, then activate row D”
Notes: The key idea in our RowClone implementation is to perform in-DRAM copy operations by using carefully crafted DRAM command sequences.

## Slide 7: Row-copy in ComputeDRAM
[Gao+, MICRO’19]
Notes: Simplified diagram of two cells on the same bitline
Top box: bitline voltage
R1 and R2 are two cells from two rows. Color of cells indicate their voltage level. We want to copy R1 to R2.
T1 and T2 around 10 nanoseconds (which is below standard timings) work

## Slide 8: More in ComputeDRAM
Majority Function
Row-copy/Majority Characterization
32 DDR3 Modules
~256 DRAM Chips

## Slide 9: In-DRAM TRNG: Key Idea (D-RaNGe)
Row Decoder
High % chance to fail with reduced access latency
Low % chance to fail with reduced access latency
SA
SA
SA
SA
SA
SA
SA
[Kim+ HPCA’19]
Commodity DRAM chips can already perform D-RaNGe
50% chance to fail
Notes: The key idea of D-RaNGe, or the in-DRAM true random number generation technique that we are interested in is to reduce DRAM read access latency below manufacturer-recommended values and exploit the resulting error patterns as true random numbers. I will describe this over a diagram:
[CLICK] This diagram depicts a DRAM bank. We color and size the cells according to their failure probabilities when they are accessed with reduced access latency values.
[CLICK] Red cells fail with a high probability
[CLICK] and green cells fail with a low probability when accessed with reduced latency
[CLICK] D-RaNGe identifies cells that fail with a probability close to 50% and repeatedly accesses these cells with reduced access latency to generate true random numbers in DRAM

## Slide 10: System Support for PiM
bulk data initialization
DRAM Chip
support for custom timing parameters
control logic for PiM operations
software interface to execute PiM ops.
supervisor for basic system support
Micro-architecture
SW/HW Interface
Program/Language
Application
Logic
Devices
System Software
Electrons

## Slide 11: PiDRAM
bulk data initialization
DRAM Chip
support for custom timing parameters
control logic for PiM operations
software interface to execute PiM ops.
supervisor for basic system support
Bridge the “system gap” with customizable HW/SW components
rapidly implement PiM techniques,
solve system integration challenges,
analyze end-to-end implementations
in doing so, allow users to

## Slide 12: PiDRAM: Key Components
Hardware
Software
Control PiM operation
Memory controller for
custom timing parameters
Interface for
Applications
Supervisor software
for basic system support
Notes: PiDRAM’s goal is to provide a flexible framework that is useful for studies on commodity DRAM based PiM techniques, such as the ones I described in the previous slides.
[CLICK] To guide our design, we look at the system requirements shared by the PiM techniques that we are interested in.
[CLICK] Then, we develop these key components as customizable modules to provide modularity and enhance the extensibility of PiDRAM
[CLICK] Overall, these components provide a common basis for developers of the framework to implement and enable system support for PiM techniques

## Slide 13: PiDRAM: System Design
Key components attached to a real computing system
Notes: We attach the key components to a real RISC-V based computing system to develop PiDRAM’s system design.
[CLICK] In the system, we implement PiM Operations Controller and PiDRAM memory controller as hardware modules in the hardware system
[CLICK] the custom supervisor software runs on the hardware system
[CLICK] and the extensible software library is used by the supervisor software and runs on the hardware system
[CLICK] I will describe each component using this diagram

## Slide 14: PiM Operations Controller (POC)
Decode & execute PiDRAM instructions (e.g., in-DRAM copy)
Receive instructions over memory-mapped interface
Simple interface to the PiDRAM memory controller (i) send request, (ii) wait until completion, (iii) read results
Notes: The PiM Operations Controller
[CLICK] decodes and executes PiDRAM instructions to perform PiM operations
[CLICK] It is connected to the hardware system as a memory mapped module, meaning that it receives the PiDRAM instructions over the memory bus from the RISC-V CPU core. The three registers, depicted as instruction, flag, and data registers in the figure are accessible over the memory bus. This makes it easy to port PiM operations controller to another system that uses a different CPU ISA.
[CLICK] PiM operations controller communicates with the PiDRAM memory controller over a simple interface where it sends a request for a PiM operation to the memory controller, waits until the operation is complete, and reads the results from the memory controller to perform a PiM operation.

## Slide 15: PiDRAM Memory Controller
Perform PiM operations by violating DRAM timing parameters
Support conventional memory operations (e.g., LOAD/STORE) One state machine per operation (e.g., LOAD/STORE, in-DRAM copy)
Easily replicate a state machine to implement a new operation
Controls the physical DDR3 interface Receives commands from command scheduler & operates DDR3 pins
Notes: The PiDRAM memory controller performs PiM operations by using timing parameters smaller than manufacturer-recommended values.
[CLICK] The command scheduler supports conventional memory operations like stores and loads. We implement one state machine in its command scheduler to control the execution per each memory operation. [CLICK] This makes PiDRAM memory controller easy to extend to support new PiM operations or new DRAM commands by replicating the state machines.
[CLICK] The physical interface controls the physical signals on the DDR3 interface. It receives DRAM commands from the command scheduler and drives the DDR3 interface signals.

## Slide 16: PiM Operations Library (pimolib)
Contains customizable functions that interface with the POC Software interface for performing PiM operations
Executes LOAD & STORE requests to communicate with the POC
Notes: The PiM operations library or pimolib encapsulates customizable functions that interface with the pim operations controller to perform pim operations. We expose the PIM functionality to software using pimolib.
[CLICK] To perform a PiM operation, a typical function in pimolib executes LOAD&STORE requests to access the memory mapped registers of the Pim operations controller
I will later describe the communication protocol that pimolib obeys while communicating with the pim operations controller

## Slide 17: Custom Supervisor Software
Exposes PiM operations to the user application via system calls
Contains the necessary OS primitives to develop end-to-end PiM techniques (e.g., memory management and allocation for RowClone)
Notes: The last component, custom supervisor software, exposes PiM oeprations to user applications via system calls
[CLICK] We implement the necessary OS primitivies to develop end-to-end PiM techniques in the custom supervisor software such as memory management and allocation for in-DRAM copy or RowClone operations)

## Slide 18: PiM Operation Execution Flow
Copy() function called by the user to perform a RowClone-Copy operation in DRAM
1
Application makes a system call: Copy(A, B, N bytes)
2
Custom Supervisor Software calls the Copy() pimolib function
Copy (S, D)
S: source DRAM row
D: destination DRAM row
Notes: I will describe the execution flow for a PiM operation in our PiDRAM framework
As an example, we will look at what happens when the user calls the copy() function to perform an in-DRAM copy operation
[CLICK] The user first makes a system call to the copy function to copy N bytes from array A to array B
[CLICK] The custom supervisor software find the physical addresses corresponding to arrays A and B, and then calls the copy() function in the pimolib with the semantics that I show here
[CLICK] It takes two arguments, S is the address of the source DRAM row, and D is the address of the destination DRAM row

## Slide 19: PiM Operation Execution Flow
3
Copy(S, D) executes two store instructions in the CPU
4
The first store updates the instruction register with Copy(S, D)
5
The second store sets the “Start” flag in the flag register
1
Start (S)
Start the execution of PiM operation
Notes: The Copy function executes two store instrutions in the CPU
[CLICK] The first store instruction updates the instruction register with a PiDRAM instruction that instructs the Pim operations controller to perform in-DRAM copy from row S to row D
[CLICK] The second store instruction sets the start flag in the flag register [CLICK] to initiate the PiM operation

## Slide 20: PiM Operation Execution Flow
6
POC instructs the memory controller to perform RowClone
7
POC resets the “Start” flag, and sets the “Ack” flag
8
PiDRAM memory controller issues commands with violated timing parameters to the DDR3 module
Notes: When the start flag is set, the Pim operations controller instructs the memory controller to perform an in-DRAM copy operation from row S to row D
[CLICK] When the memory controller acknowledges the Pim operations controller’s request, the Pim operations controller resets the start flag and sets the ack. flag. This indicates that the PiDRAM memory controller has started executing the last valid PiM operation.
[CLICK] To execute the PiM operation, the PiDRAM memory controller issues DRAM commands with violated timing parameters to the DDR3 module

## Slide 21: PiM Operation Execution Flow
9
The memory controller sets the “Fin.” flag
10
Copy(S, D) periodically checks either “Ack” or “Fin.” flags using LOAD instructions
Copy(S, D)returns when the periodically checked flag is set
Notes: When the memory controller issues the last DRAM command to perform the operation, it sets the Fin. Flag. This indicates that the memory controller has finished executing the last valid PiM operation
[CLICK] The pimolib copy function periodically checks either the ACK or the FIN flags, based on a user-specified argument, to block until either the start or the end of the PiM operation. [CLICK] In other words, the pimolib function returns when either the ACK or the FIN flag is set.

## Slide 22: PiM Operation Execution Flow
Data Register is not used in RowClone operations because the result is stored in memory
It is used to read true random numbers generated by D-RaNGe
Notes: In this example, we did not make use of the data register in the pim operations controller. This register was not useful because the in-DRAM copy operation’s result is already stored in memory.
[CLICK] However, we use this register in our in-DRAM true random number generator implementation in which case the random number generation function in the pimolib accesses the data register using LOAD instructions

## Slide 23: PiDRAM Components Summary
Four key components orchestrate PiM operation execution
Notes: [CLICK] In short, we implement four key components that together orchestrate the execution of PiM operations.

## Slide 24: PiDRAM’s FPGA Prototype
Full system prototype on Xilinx ZC706 FPGA board
RISC-V System: In-order, pipelined RISC-V Rocket CPU core, L1D/I$, TLB
PiM-Enabled DIMM (Commodity): Micron MT8JTF12864, 1 GiB, 8 banks
Notes: We develop a prototype of PiDRAM’s full system on a Xilinx ZC706 FPGA board
[CLICK] The RISC-V system comprises an in-order pipelined RISC-V core and level 1 data and instruction caches as well as a translation lookaside buffer
[CLICK] and we enable PIM operations in the DRAM module under the metal cage in the photograph

## Slide 25: Outline
Background
  DRAM Organization and Operation
  Commodity DRAM Based PiM Techniques
PiDRAM
  Overview
  Hardware & Software Components
  FPGA Prototype
Case Studies
  Case Study #1 – RowClone Case Study #2 – D-RaNGe
Conclusion
Notes: I will continue with the case studies we performed on our full system prototype

## Slide 26: RowClone Implementation
Extend the PiDRAM memory controller to support the DRAM command sequence
Expose the operation to pimolib by implementing the copy() PiDRAM instruction
1
2
Only 198 lines of Verilog code
ACT S
PRE
ACT D
ACT S
PRE
ACT D
Standard DRAM Timings
“activate row S, precharge, then activate row D”
“activate row S, then activate row D”
Violated DRAM Timings
Notes: [CLICK] We extend the PiDRAM memory controller with a new state machine that controls the activate precharge activate command sequence
[CLICK] and expose the operation to pimolib by implementing the copy() PiDRAM instruction in the pim operations controller
[CLICK] These modifications take us only 198 lines of Verilog code over PiDRAM’s flexible code base

## Slide 27: RowClone System Integration
Identify two challenges in end-to-end RowClone
1
Memory allocation (intra-subarray operation)
2
Memory coherency (computation in DRAM)
Implement CLFLUSH instruction in the RISC-V CPU Evict a cache block from the CPU caches to the DRAM module
Notes: We then study the challenges in integrating RowClone end-to-end in a real system
[CLICK] The first challenge we identify is proper memory allocation for RowClone operations. Because RowClone operations can only copy data inside a subarray, the data structures must be allocated properly to benefit from fast bulk-data copy operations in DRAM.
[CLICK] The second challenge is maintaining memory coherency. Because data movement, or computation is done inside memory, any cached copies of the data we operate on needs to be evicted and the data must be up to date in DRAM.
[CLICK] To address the second challenge, we implement the CLFLUSH instruction in the RISC-V CPU. This instruction allows us to evict a cache block, given its address as an argument, from CPU caches to the DRAM module. We use CLFLUSH instructions to evict data to DRAM prior to ROwClone operations.
[CLICK] I will now explain the first challenge in more detail

## Slide 28: RowClone Memory Allocation (I)
Memory allocation requirements
Granularity: Operands must occupy DRAM rows fully
1
Notes: We identify three memory allocation requirements for operands of RowClone operations
[CLICK] This is a simplified diagram of a DRAM chip with two banks on two columns and two subarrays (depicted as SA W and SA Z) on two rows.
[CLICK] The first requirement is the granularity requirement. Operands must occupy their DRAM rows fully. Otherwise, RowClone operations may overwrite data on the destination row.

## Slide 29: RowClone Memory Allocation (I)
Memory allocation requirements
Alignment: Operands must be placed at the same offset
2
Notes: The second requirement is called alignment. Operands must be placed at the same offsets in their respective DRAM rows. This is because in-DRAM the operand can be copied to the other operand only if their bits share the same set of sense amplifiers.

## Slide 30: RowClone Memory Allocation (I)
Memory allocation requirements
Mapping: Operands must be placed in the same subarray
3
Notes: The third requirement is called mapping. Because ROwClone operations can only be performed within a DRAM subarray, the operands must be placed or allocated in the same DRAM subarray in the same DRAM bank.

## Slide 31: RowClone Memory Allocation (I)
Memory allocation requirements
Satisfies all three requirements
4
Notes: In contrast to previous operand allocations, the allocation for source four and target four satisfy all three requirements and can be used in RowClone operations.

## Slide 32: RowClone Memory Allocation (II)
Implement a new memory allocation function to overcome the memory allocation challenges
Goal: Allocate virtual memory pages that are mapped to the same DRAM subarray and aligned with each other
virtual_address = alloc_align(int size, int id) size: # of bytes allocated id: allocations with the same id go to the same subarray
alloc_align( 4 KiB, “Subarray 0”)
Subarray Mapping Table
Page Table
1
2
Get physical address pointing to a DRAM row in subarray 0
Update the page table to map virtual address to subarray 0
1
2
Notes: We implement a new memory allocation function in the custom supervisor software to overcome the memory allocation challenges of RowClone
[CLICK] The goal of this function is to allow programmers to allocate virtual memory pages that are mapped to the same DRAM subarray in an aligned way
[CLICK] The key mechanism of our function is to distribute the allocated virtual pages to different banks, but also map the virtual pages to different rows in the same DRAM subarray in those banks.
[CLICK] We implement alloc_align with the semantics I show here. It takes two arguments. The size arguments tells it the amount of data it needs to allocate in bytes, and the id argument is supplied by the programmer to collect data structures that are allocated with different alloc_align calls under the same subarray, such that they can be copied to and from each other.

## Slide 33: RowClone Memory Allocation (II)
Implement a new memory allocation function to overcome the memory allocation challenges
Goal: Allocate virtual memory pages that are mapped to the same DRAM subarray and aligned with each other
virtual_address = alloc_align(int size, int id) size: # of bytes allocated id: allocations with the same id go to the same subarray
alloc_align( 4 KiB, “Subarray 0”)
Subarray Mapping Table
Page Table
1
2
Get physical address pointing to a DRAM row in subarray 0
Update the page table to map virtual address to subarray 0
1
2
https://arxiv.org/abs/2111.00082

## Slide 34: Evaluation: Methodology
Microbenchmarks
CPU-Copy (using LOAD/STORE instructions)
RowClone-Copy (using in-DRAM copy operations) with and without CLFLUSH
Copy/Initialization Heavy Workloads
forkbench (copy)
compile (initialization)
SPEC2006 libquantum: replace “calloc()” with in-DRAM initialization
in-DRAM copy/initialization granularity
Notes: We evaluate the performance of RowClone operations with system support in our PiDRAM prototype.
[CLICK] This table shows the configuration of our prototyped system
[CLICK] We run two sets of microbenchmarks called CPU-Copy and RowClone-Copy. To perform bulk data copy, in the CPU-Copy microbenchmark we execute load and store instructions in the RISC-V core, and in the RowCLone-Copy microbenchmark we execute in-DRAM copy instructions
[CLICK] We estimate the performance improvements provided by RowClone-Copy and Initialization operations using two copy/initialization heavy workloads
[CLICK] and we run the libquantum workload from SPEC2006 end-to-end on our prototype

## Slide 35: Microbenchmark Copy/Initialization Throughput Improvement
In-DRAM Copy and Initialization improve throughput by 119x and 89x, respectively
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 36: CLFLUSH Overhead
CLFLUSH dramatically reduces the potential throughput improvement
Notes: Now I will discuss the overheads of CLFLUSH operations. The plot shows the throughput improvement provided by in-DRAM copy and initialization over CPU-based copy and initialization when we copy 8 megabytes of data and all data is cached. The x-axis shows the proportion of the modified cache blocks among all cache blocks of the data being copied.
[CLICK] We observe that CLFLUSH operations dramatically reduce the potential copy throughput improvement provided by in-DRAM copy operations.

## Slide 37: Other Workloads
forkbench (copy-heavy workload)
compile (initialization-heavy workload)
9% execution time reduction by in-DRAM initialization
  17% of compile’s execution time is spent on initialization
SPEC2006 libquantum
1.3% end-to-end execution time reduction
  2.3% of libquantum’s time is spent on initialization
Performance improvement increases
Notes: I will summarize our results for other workloads in this slide
[CLICK] This plot shows the Speedup provided by rowclone-copy operations for the forkbench workload when the rowclone copy operations are used instead of CPU-based copy operations. The x-axis shows different configurations of the forkbench workload where the number after the hyphen indicates the amount of 4 KiB pages copied after each fork call.
We observe that as the fraction of time spent on copy operations increase, indicated by the blue curve, the speedup provided by RowClone increases, up to 42.9% for the fork-2K configuration
[CLICK] We observe 9% reduction in execution time for the initialization-heavy compile workload, which is expected as compile spends 17% of its execution time on initialization.
[CLICK] Finally, we observe 1.3% end-to-end execution time reduction for libquantum. Similarly this is because in our experiments libquantum spends only 2.3% of its time on bulk data initialization.

## Slide 38: Outline
Background
  DRAM Organization and Operation
  Commodity DRAM Based PiM Techniques
PiDRAM
  Overview
  Hardware & Software Components
  FPGA Prototype
Case Studies
  Case Study #1 – RowClone Case Study #2 – D-RaNGe
Conclusion
Notes: Now I will describe our second key study

## Slide 39: Recall: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced access latency
Low % chance to fail with reduced access latency
SA
SA
SA
SA
SA
SA
SA
[Kim+ HPCA’19]
Commodity DRAM chips can already perform D-RaNGe
50% chance to fail
Notes: The key idea of D-RaNGe, or the in-DRAM true random number generation technique that we are interested in is to reduce DRAM read access latency below manufacturer-recommended values and exploit the resulting error patterns as true random numbers. I will describe this over a diagram:
[CLICK] This diagram depicts a DRAM bank. We color and size the cells according to their failure probabilities when they are accessed with reduced access latency values.
[CLICK] Red cells fail with a high probability
[CLICK] and green cells fail with a low probability when accessed with reduced latency
[CLICK] D-RaNGe identifies cells that fail with a probability close to 50% and repeatedly accesses these cells with reduced access latency to generate true random numbers in DRAM

## Slide 40: D-RaNGe Implementation
Identify four DRAM cells that fail randomly in a cache block
1 0 1 0 1 0 0 1 0 0
1 0010110100110011101000110101
1
RNG Cell
SA
[Kim+ HPCA’19]
Notes: To implement the D-RaNGe true random number generation technique
[CLICK] We first identify a DRAM cache block that contains four cells with a failure probability of 50% when accessed with a reduced access latency value.
[CLICK] Then, we use these cells to produce true random numbers as accessing them with a reduced access latency will output random values.

## Slide 41: D-RaNGe Implementation
Periodically generate true random numbers by accessing the identified cache block
Reduce access latency
1 KiB random number buffer in POC
Programmers read random numbers from the data register using the rand_dram() function call
190 lines of Verilog code 74 lines of C++ code
Notes: We periodically generate true random numbers by accessing these four cells.
[CLICK] To store the periodically generated random numbers, we implement a one kilobyte random number buffer in the pim operations controller
[CLICK] The programmer reads a random number from the data register using the rand_dram() function call
[CLICK] Modifying PiDRAM to implement D-RaNGe takes us only 190 lines of Verilog and 74 lines of C++ code

## Slide 42: Evaluation
Methodology: Microbenchmark that reads true random numbers
PiDRAM’s D-RaNGe generates true random numbers at 8.30 Mb/s throughput
Notes: To evaluate our implementation of D-RaNGe, we run a microbenchmark that continuously reads true random numbers using the rand_dram() function.
[CLICK] This plot shows the true random number generation throughput we observe. On the x-axis, we show the true random number generation period which we can dynamically configure for PiDRAM’s D-RaNGe implementation.
[CLICK] We observe that our D-RaNGE implementation can generate true random numbers at high throughput.

## Slide 43: Outline
Background
  DRAM Organization and Operation
  Commodity DRAM Based PiM Techniques
PiDRAM
  Overview
  Hardware & Software Components
  FPGA Prototype
Case Studies
  Case Study #1 – RowClone Case Study #2 – D-RaNGe
Conclusion
Notes: I will conclude with a summary

## Slide 44: Executive Summary
Motivation: Commodity DRAM based PiM techniques improve the performance and energy efficiency of computing systems at no additional DRAM hardware cost
Problem: Challenges of integrating these PiM techniques into real systems are not solved
General-purpose computing systems, special-purpose testing platforms, and system simulators cannot be used to efficiently study system integration challenges
Goal: Design and implement a flexible framework that can be used to:
solve system integration challenges
analyze trade-offs of end-to-end implementations of commodity DRAM-based-PiM techniques
Key idea: PiDRAM, an FPGA-based framework that enables:
system integration studies
end-to-end evaluations of PIM techniques using real unmodified DRAM chips
Evaluation: End-to-end integration of two PiM techniques on PiDRAM’s FPGA prototype
Case Study #1 – RowClone: In-DRAM bulk data copy operations
119x speedup for copy operations compared to CPU-copy with system support
198 lines of Verilog and 565 lines of C++ code over PiDRAM’s flexible codebase
Case Study #2 – D-RaNGe: DRAM-based random number generation technique
8.30 Mb/s true random number generator (TRNG) throughput, 220 ns TRNG latency
190 lines of Verilog and 74 lines of C++ code over PiDRAM’s flexible codebase
PiDRAM: https://github.com/CMU-SAFARI/PiDRAM
Notes: I will start with an executive summary
[CLICK] Commodity DRAM-based PIM techniques improve the performance and energy efficiency of computing systems without incurring any DRAM hardware cost
[CLICK] However, challenges of integrating these techniques into real systems are not yet solved.
[CLICK] Moreover, these challenges cannot be efficiently studied using existing computing systems, special-purpose DRAM testing platforms or system simulators
[CLICK] Our goal is to design and implement a flexible framework that can be used to [CLICK] solve the important system integration challenges and [CLICK] analyze the trade-offs of end-to-end implementations of commodity DRAM based PiM techniques
[CLICK] Our key idea is to develop PiDRAM, an FPGA-based framework that enables such studies using real unmodified DRAM chips
[CLICK] Using our framework, we conduct two case studies on two recent commodity DRAM based PiM techniques on a real FPGA prototype of a full system
[CLICK] In our first case study about in-DRAM bulk data copy operations, we show that in-DRAM data copy operations provide 119 times speedup over CPU-copy operations including system support. To conduct this case study over PiDRAM’s extensible code base, we add only 198 lines of Verilog and only 565 lines of C++ code.
[CLICK] In our second case study about an in-DRAM true random number generation technique, we show that an end-to-end implementation of a DRAM-based true random number generator can provide high throughput true random numbers at low latency. Implementing the true random number generator takes us only 190 additional lines of Verilog and 78 additional lines of C++ code over PiDRAM’s code base.

## Slide 45: PiDRAM is Open Source
https://github.com/CMU-SAFARI/PiDRAM
Notes: PiDRAM is openly and freely available on Github. If you are interested in PiDRAM, please use it and feel free to contribute to it.

## Slide 46: Extended Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 47: Long Talk + Tutorial on Youtube
https://youtu.be/s_z_S6FYpC8
Notes: I also describe PiDRAM in more detail and give a tutorial on how to use our framework in this SAFARI live seminar talk.

## Slide 48: PiDRAM An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques
Ataberk Olgun
Juan Gomez Luna
Konstantinos Kanellopoulos
Hasan Hassan
Behzad Salami
Oğuz Ergin
Onur Mutlu
Notes: Thank you very much for listening to my presentation. I am happy to take your questions.

## Slide 49: BACKUP SLIDES

## Slide 50: Accessing a DRAM Cell
Sense Amp
enable
bitline
wordline
capacitor
access transistor
[Seshadri+ MICRO’17]
Notes: Here is how we access this DRAM cell. This is a diagram showing how a DRAM cell is connected to a sense amplifier.
[CLICK] A DRAM cell contains two components, the capacitor stores data and the access transistor determines if the cell is being accessed.
[CLICK] The access transistor is controlled by the wordline, which is enabled to
[CLICK] connect the DRAM cell to its bitline
[CLICK] The bitline bar is esentially the inverse of the bitline
[CLICK] The DRAM sense amplifier has an enable signal which determines if the sense amplifier is currently active.

## Slide 51: Accessing a DRAM Cell
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
½ VDD
VDD
enable wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell charge restored
Sense Amp
deviation in bitline voltage
[Seshadri+ MICRO’17]
1
2
3
4
5
6
Notes: Initially, both the access transistor and the sense amplifier are disabled and both ends of the sense amplifier are maintained at half vdd. In this example, the capacitor is fully charged. To access the cell
[CLICK] we first enable the wordline, [CLICK] this connects the capacitor to its bitline.
[CLICK] Since the capacitor has a voltage level higher than the bitline, the charge starts flowing from the capacitor to the bitline, [CLICK] resulting in the bitline voltage to deviate slightly towards Vdd.
[CLICK] When we enable the sense amplifier, it will compare the voltage levels of bitline and bitline bar, and [CLICK] amplify the deviation until bitline voltage reaches Vdd.
[CLICK] Since the capacitor is still connected to the bitline, the amplification process also restores the charge in the capacitor.

## Slide 52: alloc_align() function
SubArray Mapping Table (SAMT) enables alloc_align()
SAMT
Subarray 0
Subarray 1
Subarray N
…
SAMT Entry
Physical addresses of DRAM rows
alloc_align( 4 KiB, “Subarray 0”)
SAMT
Page Table
1
2
Retrieve a physical address pointing to a DRAM row in subarray 0
Update the page table to map programmer-allocated address to subarray 0
1
2
Notes: We implement a key structure in the supervisor software called subarray mapping table, to enable alloc_align().
[CLICK] SAMT is organized as a table of entries per DRAM subarray
[CLICK] Each SAMT entry contains a list of physical addresses that point to the DRAM rows in that subarray
[CLICK] An example alloc align call to allocate four kibs of data in subarray 0 [CLICK] accesses SAMT to retrieve a physical address pointing to a DRAM row in subarray 0, and then [CLICK] updates the page table to map the virtual address allocated for the programmer to subarray 0
This way, we allocate different virtual pages to the same DRAM subarray, such that we can use in-DRAM copy operations to copy data from and to these pages

## Slide 53: Initializing SAMT
SAMT
Subarray 0
Subarray 1
Subarray N
…
SAMT Entry
Physical addresses of DRAM rows
?
Perform in-DRAM copy using every DRAM row address as source and destination rows
If the in-DRAM copy operation succeeds source and destination rows are in the same subarray
Notes: [CLICK] To find physical addresses of the DRAM rows that map to a subarray,
[CLICK] We perform an experiment in our prototype where we try to copy data in-DRAM from every row address to every other row address.
[CLICK] We conclude that if the operation succeeds, the source and the destination row addresses we used must belong in the same subarray.
[CLICK] Please read our full paper in arXiv for more details on how our allocation mechanism works

## Slide 60: DRAM Organization
…
…
…
[Olgun+ ISCA’21]
Notes: A processor’s memory controller
[CLICK] communicates with a set of DRAM chips within a DRAM module through a memory channel.
[CLICK] Each DRAM chip contains multiple banks that share a common chip I/O interface.
[CLICK] DRAM banks are organized into subarrays that consists of a set of wordline drivers and sense amplifiers
[CLICK] Subarrays are partitioned into DRAM MATs which are collections of DRAM cells that are separated from each other by wordline drivers.
[CLICK] DRAM cells are laid out onto a two-dimensional array of wordlines and bitlines within
a DRAM MAT. A row of DRAM cells is a DRAM row.
[CLICK] Here is a simplified diagram of a DRAM cell.

## Slide 61: DRAM Operation
…
…
…
…
…
Sense Amplifiers
Sense Amplifiers
Cache line
READ
…
READ
READ
Wordline Drivers
Sense Amplifiers
READ
READ
READ
ACT R0
RD
PRE R0
RD
RD
ACT R1
RD
RD
RD
time
DRAM Command Sequence
(Activation Latency)
(Precharge Latency)
[Kim+ HPCA’19]
(Access Latency)
Notes: Now we will look at how DRAM operates at the scope of a single subarray.
[CLICK] Because memory controllers typically access DRAM cells in the granularity of a cache line or a cache block we combine consecutive DRAM cells to form cache lines in this diagram.
[CLICK] On the bottom we have a timeline of DRAM commands.
[CLICK] First, we activate the first row to [CLICK] copy its cache lines to the sense amplifiers
[CLICK] At this point we can read data [CLICK] in cache line granularity from the sense [CLICK] amplifiers by sending READ commands
[CLICK] To access another row, we must first precharge the DRAM bank which closes the open DRAM row and sets the bitline voltage to half Vdd.
[CLICK] We can now activate the [CLICK] second row before [CLICK] [CLICK] [CLICK] reading data from it.
[CLICK] To ensure correct operation, we must obey certain timing parameters that define intervals between DRAM command pairs.
Three important timing parameters are tRAS, tRP, and tRCD
[CLICK] tRAS is the time required for the charge to become restored in the capacitors on the open row. tRAS dictates the amount of time we need to wait between successive activate and precharge commands
[CLICK] tRP is the time it takes for a bitline to become precharged to half Vdd such that a new activate command can be issued to open a DRAM row. Successive precharge and activate commands must be separated on the command bus by at least a tRP amount of time.
[CLICK] tRCD is the time it takes for sense amplifiers to amplify the bitline voltage to an I/O readable value. Successive activate and read commands must be separated by a tRCD amount of time.