## Slide 1
AiM : Accelerator-in-Memory
System Architecture and Software Stack for GDDR6-AiM
Yongkee Kwon and Chanwook Park
SK hynix inc.

## Slide 2
AiM FPGA Platform (w/ CPU Host)
AiM Subsystem and Software Stack
AiM Concept
The Accelerator-in-Memory (AiM) is a GDDR6-based Processing-in-Memory device designed to accelerate memory-intensive Machine Learning applications in memory.
Conventional System vs. AiM System

## Slide 3
CONTENTS
GDDR6-AiM Overview
AiM Subsystem
AiM Software Stack
Performance Evaluation
Ⅰ
Ⅱ
Ⅲ
IV

## Slide 4
CACM’20: Domain Specific Accelerators

## Slide 5
AiM as a Domain Specific Memory
Accelerator-in-Memory
Efficiency: specialization for a particular domain of applications
Target domain: memory bound DNN applications
Main goals:
1) Performance: high degrees of bank-level parallelism
2) Power: reduce significant data movement
3) Cost: commodity DRAM-based (GDDR6)

## Slide 6
GDDR6-AiM Key Operation: Matrix × Vector
MAC and Activation Function operations can be performed in all banks in parallel.
Weight matrix data is sourced from Banks; Vector data is sourced from the Global Buffer.
MAC results are stored in latches collectively referred to as MAC_REG.
Activation Function results are stored in latches collectively referred to as AF_REG.
W[0]
V[0]
W[1]
V[1]
W[14]
V[14]
W[15]
V[15]
MAC_REG
ACCUMULATOR
Multiply-And-Accumulate (MAC)
Performs MAC operation on sixteen BF16 weight matrix and vector elements (corresponds to a single DRAM column access, i.e. 32B).
Computation results are stored in a dedicated MAC_REG set and can be later accessed by the user.
GLOBAL_BUFFER
BANK0
W
BANK1
W
BANK15
W
Weights
Activations
V
MAC
x
MAC
MAC
MAC_REG
AF(x)
AF
AF
AF_REG
32B
2KB
2KB
Activation Function Module
Performs Activation Function (AF) computation by linearly interpolating pre-stored AF template data using MAC calculation results.
Interpolation results are stored in a dedicated AF_REG set and can be later accessed by the user.
LUT[0]
LUT[1]
LUT[2]
MAC Result
AF Result
×
+
f
=
Weight Matrix
Activation
Vector
32B

## Slide 7
GDDR6-AiM Key Operation: Matrix × Vector
MAC and Activation Function operations can be performed in all banks in parallel.
Weight matrix data is sourced from Banks; Vector data is sourced from the Global Buffer.
MAC results are stored in latches collectively referred to as MAC_REG.
Activation Function results are stored in latches collectively referred to as AF_REG.
W[0]
V[0]
W[1]
V[1]
W[14]
V[14]
W[15]
V[15]
MAC_REG
ACCUMULATOR
Multiply-And-Accumulate (MAC)
Performs MAC operation on sixteen BF16 weight matrix and vector elements (corresponds to a single DRAM column access, i.e. 32B).
Computation results are stored in a dedicated MAC_REG set and can be later accessed by the user.
GLOBAL_BUFFER
BANK0
W
BANK1
W
BANK15
W
Weights
Activations
V
MAC
x
MAC
MAC
MAC_REG
AF(x)
AF
AF
AF_REG
32B
2KB
2KB
Activation Function Module
Performs Activation Function (AF) computation by linearly interpolating pre-stored AF template data using MAC calculation results.
Interpolation results are stored in a dedicated AF_REG set and can be later accessed by the user.
LUT[0]
LUT[1]
LUT[2]
MAC Result
AF Result
×
+
f
=
Weight Matrix
Activation
Vector
32B

## Slide 8
GDDR6-AiM Key Operation: Matrix × Vector
MAC and Activation Function operations can be performed in all banks in parallel.
Weight matrix data is sourced from Banks; Vector data is sourced from the Global Buffer.
MAC results are stored in latches collectively referred to as MAC_REG.
Activation Function results are stored in latches collectively referred to as AF_REG.
W[0]
V[0]
W[1]
V[1]
W[14]
V[14]
W[15]
V[15]
MAC_REG
ACCUMULATOR
Multiply-And-Accumulate (MAC)
Performs MAC operation on sixteen BF16 weight matrix and vector elements (corresponds to a single DRAM column access, i.e. 32B).
Computation results are stored in a dedicated MAC_REG set and can be later accessed by the user.
GLOBAL_BUFFER
BANK0
W
BANK1
W
BANK15
W
Weights
Activations
V
MAC
x
MAC
MAC
MAC_REG
AF(x)
AF
AF
AF_REG
32B
2KB
2KB
Activation Function Module
Performs Activation Function (AF) computation by linearly interpolating pre-stored AF template data using MAC calculation results.
Interpolation results are stored in a dedicated AF_REG set and can be later accessed by the user.
LUT[0]
LUT[1]
LUT[2]
MAC Result
AF Result
×
+
f
=
Weight Matrix
Activation
Vector
32B

## Slide 9
GDDR6-AiM Feature Summary
SK hynix’s very first GDDR6-based processing-in-memory (PIM) product sample, called Accelerator-in-Memory (AiM)
GDDR6-AiM* | 
DRAM Type | GDDR6
Process Technology | 1y
Memory Density | 8Gb (4Gb DDP)
Organization | 2CH/Chip, x16 mode only
IO Data rate | 16 Gb/s/pin (@1.25V)
Bandwidth | 64 GB/s
Processing Unit (PU) | 16 PU/die, 32 PU/Chip
Operating Speed | 1 GHz
Compute Throughput | 1TFLOPS/Chip
Numeric Precision | Brain Floating Point 16 (BF16)
Activation Function support** | Sigmoid, tanh, GELU, ReLU, Leaky ReLU, …
Targets | Memory-bound DNN applications
* S. Lee, et al. “A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications”, 2022 INTERNATIONAL SOLID-STATE CIRCUITS CONFERENCE (ISSCC). IEEE, 2022
** With using internal lookup table and linear interpolation unit. Any customized function may apply with accuracy limitation.
[GDDR6-AiM Floorplan]

## Slide 10
GDDR6-AiM Feature Summary
SK hynix’s very first GDDR6-based processing-in-memory (PIM) product sample, called Accelerator-in-Memory (AiM)
GDDR6-AiM* | 
DRAM Type | GDDR6
Process Technology | 1y
Memory Density | 8Gb (4Gb DDP)
Organization | 2CH/Chip, x16 mode only
IO Data rate | 16 Gb/s/pin (@1.25V)
Bandwidth | 64 GB/s
Processing Unit (PU) | 16 PU/die, 32 PU/Chip
Operating Speed | 1 GHz
Compute Throughput | 1TFLOPS/Chip
Numeric Precision | Brain Floating Point 16 (BF16)
Activation Function support** | Sigmoid, tanh, GELU, ReLU, Leaky ReLU, …
Targets | Memory-bound DNN applications
* S. Lee, et al. “A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications”, 2022 INTERNATIONAL SOLID-STATE CIRCUITS CONFERENCE (ISSCC). IEEE, 2022
** With using internal lookup table and linear interpolation unit. Any customized function may apply with accuracy limitation.
[GDDR6-AiM Floorplan]
No compromise on
parallelism = performance

## Slide 11
Bank Activation | 
ACT4, ACT16 | Activate four/sixteen banks in parallel
ACTAF4, ACTAF16 | Activate rows storing Activation Functions LUTs in four/sixteen banks in parallel
Compute Commands | 
MACSB, MAC4B, MACAB | Perform MAC in one/four/sixteen banks in parallel
AF | Compute Activation Function in all banks
EWMUL | Perform element-wise multiplication
Data Commands | 
RDCP | Copy data from a bank to the Global Buffer
WRCP | Copy data from the Global Buffer to a bank
WRGB* | Write to Global Buffer (often Activation vector data)
RDMAC* | Read from MAC result register
RDAF* | Read from Activation Function result register
WRMAC* | Write to MAC result register (or WRBIAS as often BIAS data is written)
WRBK | Write to all activated banks in parallel
Commands marked as CMD* require a special Mode Register set to be recognized.
New Commands introduced in AiM

## Slide 12
GDDR6-AiM Overview
AiM Subsystem
AiM Software Stack
Performance Evaluation
Ⅰ
Ⅱ
Ⅲ
IV
CONTENTS

## Slide 13
AiM Subsystem: High-Performance Scalable Reference Design
PCIe/DMA
x86
CPU
ARM,
RISC-V,
…
AI
Accelerator
AXI
AXI
AXI
AiM Subsystem is a hardware bridge between the host and the AiM devices. It is designed to 1) maximize compute throughput for a set of AiM devices and to 2) minimize software stack overhead.
1
2
3
GDDR6-AiM
FMC Extension Card
Xilinx VCU118

## Slide 14
AiM Subsystem: High-Performance Scalable Reference Design
AiM Command/Data DMA engine
AiM Multicasting Interconnect
AiM Controller
PCIe/DMA
x86
CPU
ARM,
RISC-V,
…
AI
Accelerator
AXI
AXI
AXI
1
2
3
Enables efficient workload distribution through flexible instruction parallelism. Supports unicast, multicast, and broadcast modes.
Decodes AiM instructions from software and provides direct memory access for the host.
Generates and schedules low-level AiM and typical DRAM commands.
AiM Subsystem is a hardware bridge between the host and the AiM devices. It is designed to 1) maximize compute throughput for a set of AiM devices and to 2) minimize software stack overhead.
1
2
3

## Slide 15
1) AiM Command/Data DMA engine
Operations Engine
Interprets AXI operations from the host and accordingly generates either memory access or AiM compute requests. Memory requests are passed to the memory directly, while AiM requests are additionally processed by the dedicated FSM called ISR.
AXI Packet Decoder performs host (software) packet interpretation.
General Purpose Register (GPR) is an SRAM used for 1) holding bias data to be rewritten multiple times during GEMV computation, 2) holding activation results to be used as vectors for the following layers, 3) holding diagnostic and debugging data, e.g. temperature.
Instruction Set Register (ISR) FSM generates streams of low-level AiM requests based on the higher-level software commands. See next slide for an example.
Response Ordering Engine
An optional block used for restoring the order of DRAM read transactions, which can be reordered by the AiM controllers.
1
2
1
2

## Slide 16
3) AiM Controller
GDDR6-AiM Controller = GDDR6 Controller + AiM Command Scheduling
Scheduler
FR-FCFS Arbiter rearranges memory requests to reduce the number of row activations. AiM requests are always scheduled in-order.
Bank Engines and AiM Engine generate and schedule DRAM commands (ACT, PREPB, MAC, …) from the memory requests.
Refresh Engine periodically generates and schedules refresh commands.
Engine Arbiter multiplexes between the engines and issues prioritized DRAM commands to PHY.
1
2
PHY
A standard GDDR6 DRAM PHY block. Details depend on the selected implementation technology (e.g. FPGA).
1
2

## Slide 17
AiM Host (Macro) Instruction
AiM
AiM (Micro) Command
(PCIe Protocol)
AiM
Controller
Micro
Command
Generator
Host
Processor
ISR Instructions
AiM Command
New commands named AiM commands are introduced to control computing operations in AiM
AiM software stack generates AiM Host (Macro) Instructions and each Macro Instruction is converted into the corresponding multiple AiM (Micro) commands by the Command Generator and AiM Controller
* AiM Controller = GDDR6 Controller + AiM Command Scheduling
Bank Activation | 
ACT4, ACT16 | Activate four/sixteen banks in parallel
ACTAF4, ACTAF16 | Activate rows storing Activation Functions LUTs in four/sixteen banks in parallel
Compute Commands | 
MACSB, MAC4B, MACAB | Perform MAC in one/four/sixteen banks in parallel
AF | Compute Activation Function in all banks
EWMUL | Perform element-wise multiplication
Data Commands | 
RDCP | Copy data from a bank to the Global Buffer
WRCP | Copy data from the Global Buffer to a bank
WRGB* | Write to Global Buffer (often Activation vector data)
RDMAC* | Read from MAC result register
RDAF* | Read from Activation Function result register
WRMAC* | Write to MAC result register (or WRBIAS as often BIAS data is written)
WRBK | Write to all activated banks in parallel
…
(DRAM Command Protocol)
FPGA
Single Instruction
Multiple Commands (Max 64)
x86 Server
x64
AiM Control Flow from Host Processor

## Slide 18
AiM FPGA Platform: AiM Subsystem Prototyped in Xilinx FPGA
GDDR6-AiM
FMC Extension Card
Xilinx VCU118
PHY is implemented by using configurable source-synchronous interface technology (SelectIO) available in Xilinx FPGAs.
Interface calibration is performed by a specialized RTL FSM (Calibration Handler) controlled by an MCS microcontroller.

## Slide 19
GDDR6-AiM Overview
AiM Subsystem
AiM Software Stack
Performance Evaluation
Ⅰ
Ⅱ
Ⅲ
IV
CONTENTS

## Slide 20
Motivation
In order to increase the value of new memory solutions such as AiM, expanding the ecosystem is of paramount importance.
To achieve this goal, we have developed an SDK to allow any DNN models to be easily adapted by operator-level APIs.
The proposed API abstracts the functionality of PIM operations and provides ease of programmability to users.
AiM SDK
+
(AiM HW Platform)
Expanding
Ecosystem
distribute

## Slide 21
Weight
Matrix
Vector
Result
Bias
GLOBAL_BUFFER
BANK0
BANK1
BANK15
Weights
Vector
MAC
MAC
MAC
ACC_REG
AF
AF
AF
RESULT_REG
STORE
ISR_WR_GB
(Macro CMD)
ISR_WR_BIAS
ISR_RD_AF
WR
WR_VECTOR
(Micro CMD)
WR_BIAS
RD_AF
ISR_MAC_ABK
(Macro CMD)
RUN_MAC
(Micro CMD)
ISR_AF
RUN_AF
Weight
Vector
Bias
Result
AiM Host Instructions
AiM Commands
Weight
Matrix
Vector
X
Result
=
Bias
+
(
)
GDDR6-AiM
f
MAC
AF
x64
x64
* AF : Activation Function
AiM Execution Sequence for Fully Connected Layer

## Slide 22
SK hynix has implemented full software stack (device drivers, runtime library, frameworks and applications)
Supports an AiM software emulator that allows users to develop AI applications without evaluation board
AiM Software Stack
Application (GPT-2, LSTM, …)
Deep Learning Frameworks
AiM Runtime Library
Memory
Management
AiM OP
Kernel
ISR Instruction
Generator
AiM Device Driver
Memory
Allocator
Instruction
Dispatcher
DMA
Device Driver
AiM Extension
AiM Execution Provider
AiM Software Emulator
AiM
Function Simulator
AiM
Performance Model
Software
Hardware
User Space
Kernel Space
User Space
Hardware

## Slide 23
CreateAiMLinearOp
RunAiMLinearOp
CreateAiMSeqOp
RunAiMSeqOp
CreateAiMRNNOp
RunAiMRNNOp
CreateAiMLSTMOp
RunAiMLSTMOp
CreateAiMGRUOp
RunAiMGRUOp
Basic RNN
LSTM
GRU
CreateAiMCustomOp
RunAiMCustomOp
…
AiM OP Kernel API
AiM OP Kernel API
The AiM Runtime Library provides a number of AiM OP kernels for Deep Learning Frameworks and AI Applications by exposing operator-level APIs.
AiM Operation Kernels

## Slide 24
DNN Application
Conversion API (to_aim())
PyTorch Custom Ops
AiM Extension (C++)
AiM Runtime Library
PyTorch
torch.nn.LSTM
AiMLSTM
RunAiMLSTMOp
RunAiMLSTMOp()
Python
C++
The framework provides abstraction functions for various PIM operations and easy programmability for developers.
If users simply apply “to_aim” API to any PyTorch operations, the runtime library will convert them to the operator-level AiM APIs defined in the runtime library.
AiM Integration on PyTorch

## Slide 25
Graph Partitioner
Distributed
Graph Runner
AiM
Execution Provider
CPU
Execution Provider
…
Execution Providers
ONNX Model (.onnx)
Provider
Registry
In-Memory
Graph
AiM
Runtime Library
ONNX Runtime
ONNX Graph Partitioning
In order to run ONNX Runtime applications on AiM, developers simply add “AiMExecutionProvider” to the “EP_List”, which will make the AiM execution provider the default provider, and some nodes in the ONNX graph will be offloaded to AiM.
AiM Integration on ONNX Runtime

## Slide 26
AiM Memory Allocator
Back-End Allocator
Host Memory Allocator
Chunk Pool
Buddy Allocator
Shared Buffer
Between Kernel and User
Data Buffer
Vector, Bias, Etc.
SLAB Allocator
AiM
Runtime Lib
AiM
GPR in FPGA
Host DRAM
Kernel Space
User Space
HW
Heap Allocator
Weight
Matrix
SLAB Allocator
Device Memory Allocator
Heap Allocator
AiM
Device Driver
Linux
Kernel
For Host Memory
For Device Memory
AiMMalloc
AiMMatrixMalloc
AiMMemcpy
AiMFree
AiM Memory Allocator API
The memory allocator allocates buffers from the AiM and host DRAM, and manages the virtual address of each buffer for each process. This allocator manages three types of memory (Host DRAM, AiM, and FPGA GPR) and has a hierarchical structure.
AiM Memory Allocator

## Slide 27
Weight Matrix
Vector
Bias
Result
Weight
Matrix
vector
X
Result
=
Host (Macro) Instructions
DL Frameworks
(e.g. PyTorch)
Runtime Lib
Generate ISR Instruction Stream
DMA
1
2
3
RunAiMLinearOp
4
Bias
+
Host DRAM
Tile0
(Job0)
Tile2
(Job2)
Tile3
(Job3)
Tile1
(Job1)
f (
)
V0
X
R0
=
B0
+
f (
)
CreateAiMLinearOp
V1
B1
R1
ISR_WR_BIAS (B0)
ISR_WR_GB (V0)
ISR_MAC_ABK
ISR_RD_MAC (B0’)
ISR_WR_BIAS (B1)
ISR_MAC_ABK
ISR_RD_MAC (B1’)
ISR_WR_BIAS (B0’)
ISR_WR_GB (V1)
ISR_MAC_ABK
ISR_AF
ISR_RD_AF (R0)
ISR_WR_BIAS (B1’)
ISR_MAC_ABK
ISR_AF
ISR_RD_AF (R1)
Tile0
Tile1
Tile2
Tile3
Hardware
Only once at Application Initialization Time
at Every Inference Time
The process of generating the host instructions and dispatching them to the hardware.
AiM Host (ISR) Instruction Generator

## Slide 28
With the AiM performance model, users can estimate not only the total execution time of AI applications but also the execution time of each individual host instruction.
The other benefit of using the software emulator is the flexibility of the hardware.
AiM Software Emulator
Configuration File
Estimated Performance from Analytical Model
AiM Software Emulator
AiM Software Emulator
Function Simulator Interface
512 KB
SRAM
AiM Functional Model
GDDR6-AiM Model
(CH 0)
AiM CTRL
Model
(CH 0)
AiM DMA
Model
AiM
Performance
Model
AiM Evaluation Board

## Slide 29
GDDR6-AiM Overview
AiM Subsystem
AiM Software Stack
Performance Evaluation
Ⅰ
Ⅱ
Ⅲ
IV
CONTENTS

## Slide 30
Chart: Execution Time (s)
| 93.6GB/s | 16GB/s | 128GB/s
AiM offloadable | 10.539 | 2.787 | 0.853
Others | 3.091 | 3.086 | 3.086
Data Movement | 0 | 0.48 | 0.48
Chart: Execution Time (s)
| 93.6GB/s | 16GB/s | 128GB/s
AiM offloadable | 78.956 | 18.921 | 4.5379
Others | 3.283 | 3.081 | 3.081
Data Movement | 0 | 0.545 | 0.545
Peak BW
(External)
Offloaded to AiM
Performance Evaluation on GPT-2 and GPT-3 (Memory intensive workload)
Higher gains are expected if AiM is directly deployed on the memory channels running at 16Gb/s/pin, as demonstrated by “AiM Projected” with our performance analytical model
By having a more memory intensive workload, AiM will be more effective
Performance on GPT-2 XL
Performance on GPT-3 13B Configuration
GPT-2 Model Architecture
Peak BW
(External)
Parameter Size : 1.5B
Parameter Size : 13B
3.1x
2.2x
CPU (FP32)
AiM (BF16)
Measured
(4ch,@2Gbps)
AiM (BF16)
Projected
(4ch,@16Gbps)
CPU (FP32)
AiM (BF16)
Measured
(4ch,@2Gbps)
AiM (BF16)
Projected
(4ch,@16Gbps)
10x
3.7x
Perfomance Evaluation: GPT-2 and GPT-3

## Slide 31
ㅡ
AiM Platform Distribution
SKhynix_PIM@skhynix.com
SK hynix can provide the following items for your research
  AiM SDK (including AiM Software Emulator)
  [Optional] AiM FMC card × 2
Please contact us at

## Slide 32
Circuit-level
  [ISSCC’22] A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications
    ISSCC’22 demo. (short video): https://www.youtube.com/watch?v=3LbvwrJFYoA
  [JSSC’23] A 1ynm 1.25V 8Gb 16Gb/s/Pin GDDR6-Based Accelerator-in-Memory Supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep Learning Application
Architectures/Software stack
  [Hot Chips’22] System Architecture and Software Stack for GDDR6-AiM
  White papers (released with AI Hardware Summit’22):
    (1) Accelerator-in-Memory: SK hynix’s GDDR6-based Processing-in-Memory Device
    (2) Accelerator-in-Memory Platform: Hardware Perspective
    (3) Accelerator-in-Memory Platform: Software Perspective
    (From https://product.skhynix.com)
References