## Slide 1: 1st Workshop on Memory-Centric Computing: Processing-Near-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025

## Slide 2: Processing in Memory: Two Approaches
1. Processing near Memory
2. Processing using Memory

## Slide 3: When to Employ PNM
Processing-near-Memory
Mobile consumer workloads
(GoogleWL2)
Neural networks
(GoogleWL2)
Graph processing
(Tesseract1)
Time series analysis
(NATSA6)
DNA
sequence mapping
(GenASM3; GRIM-Filter4)
...
[1] Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing," ISCA, 2015
[2] Boroumand+, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
[3] Cali+, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis,” MICRO, 2020
[4] Kim+, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies,” BMC Genomics, 2018
[5] Boroumand+, "Polynesia: Enabling High-Performance and Energy-Efficient Hybrid Transactional/Analytical Databases with Hardware/Software Co-Design,” ICDE, 2022
[6] Fernandez+, “NATSA: A Near-Data Processing Accelerator for Time Series Analysis,” ICCD, 2020
Databases
(Polynesia5)

## Slide 4: Processing Near-Memory (PNM)
Processing Near-Memory (PNM)
  Move computation closer to where the data resides
Logic layer
3D stacked DRAM
Memory module (DIMM)
Memory controller

## Slide 5: PNM: Design Challenges
Limited power & area budget with 3D-stacked memories
  e.g., area and power budget of the vault’s underlying logic layer is just 4.4mm2 and 312mW (circa HMC 2.0)
Strict thermal constraints
  It requires cooling solutions to remove heat throughout a 3D stack (i.e., volume-wise) instead of a 2D surface
Challenging manufacturing of logic+DRAM
  Logic process has been developed for speed performance, DRAM process for density and memory reliability
  e.g., Logic gates implemented with memory process slowdowns by ~21.5% [Kim+, Integration'99]

## Slide 6: Tesseract System for Graph Processing
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Top Picks Honorable Mention by IEEE Micro. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 7: Accelerating Neural Network Inference
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]

## Slide 8: PIM for Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Lightning Talk Video (2 minutes)] [Full Talk Video (21 minutes)]

## Slide 9: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 10: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 11: Accelerating In-Memory Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 12: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 13: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 14: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
14

## Slide 15: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Top Picks Honorable Mention by IEEE Micro. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 16: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 17: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/
CPU
(x86, ARM, RV…)
DDR
Data bus

## Slide 18: Accelerator Model (I)
UPMEM DIMMs coexist with conventional DIMMs
Integration of UPMEM DIMMs in a system follows an accelerator model
UPMEM DIMMs can be seen as a loosely coupled accelerator
  Explicit data movement between the main processor (host CPU) and the accelerator (UPMEM)
  Explicit kernel launch onto the UPMEM processors
This resembles GPU computing

## Slide 19: System Organization (I)
FIG. 1 schematically illustrates a computing system comprising DRAM circuits having integrated processors according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 20: System Organization (II)
In a UPMEM-based PIM system UPMEM DIMMs coexist with regular DDR4 DIMMs
Notes: P21 DIMMs.
DPUs cannot be shared. There is a large number of DPUs.
No need for OS.
This simplifies security implications. No side channels.

## Slide 21: System Organization (III)
A UPMEM DIMM contains 8 or 16 chips
  Thus, 1 or 2 ranks of 8 chips each
Inside each PIM chip there are:
  8 64MB banks per chip: Main RAM (MRAM) banks
  8 DRAM Processing Units (DPUs) in each chip, 64 DPUs per rank

## Slide 22: 2,560-DPU System (II)

## Slide 23: DRAM Processing Unit (I)
FIG. 4 schematically illustrates part of the computing system of FIG. 1 in more detail according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 24: DRAM Processing Unit (II)

## Slide 25: DPU: Arithmetic Throughput vs. Operational Intensity

## Slide 26: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 27: DPU Instruction Set Architecture
Specific 32-bit ISA
  Aiming at scalar, in-order, and multithreaded implementation
  Allowing compilation of 64-bit C code
  LLVM/Clang compiler
https://sdk.upmem.com/2021.2.0/201_IS.html#

## Slide 28: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 29: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 30: Recent SRC TECHCON Presentation
Dr. Juan Gomez-Luna
  Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware
  Based on two major works
    https://arxiv.org/pdf/2105.03814.pdf
    https://arxiv.org/pdf/2207.07886.pdf
https://www.youtube.com/watch?v=nphV36SrysA

## Slide 31: UPMEM PIM System Summary & Analysis
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware" Invited Paper at Workshop on Computing with Unconventional Technologies (CUT), Virtual, October 2021. [arXiv version] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Talk Video (37 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 32: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 33: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 34: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 35: Understanding a Modern PIM Architecture
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 36: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 37: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 38: ML Training on Real PIM Systems
Juan Gómez Luna, Yuxin Guo, Sylvan Brocard, Julien Legriel, Remy Cimadomo, Geraldo F. Oliveira, Gagandeep Singh, and Onur Mutlu, "Evaluating Machine Learning Workloads on Memory-Centric Computing Systems" Proceedings of the 2023 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Raleigh, North Carolina, USA, April 2023. [arXiv version, 16 July 2022.] [PIM-ML Source Code] Best paper session.
https://arxiv.org/pdf/2207.07886.pdf
https://github.com/CMU-SAFARI/pim-ml

## Slide 39: ML Training on a Real PIM System
Short version: https://arxiv.org/pdf/2206.06022.pdf
Long version: https://arxiv.org/pdf/2207.07886.pdf
https://www.youtube.com/watch?v=qeukNs5XI3g&t=11226s

## Slide 40: ML Training on a Real PIM System
Need to optimize data representation
  (1) fixed-point
  (2) quantization
  (3) hybrid precision
Use lookup tables (LUTs) to implement complex functions (e.g., sigmoid)
Optimize data placement & layout for streaming
Large speedups: 2.8X/27X vs. CPU, 1.3x/3.2x vs. GPU

## Slide 41: ML Training on Real PIM Talk Video
https://www.youtube.com/watch?v=qeukNs5XI3g&t=11226s

## Slide 42: SpMV Multiplication on Real PIM Systems
Appears at SIGMETRICS 2022
https://arxiv.org/pdf/2201.05072.pdf
https://github.com/CMU-SAFARI/SparseP
https://www.youtube.com/watch?v=5kaOsJKlGrE

## Slide 43: Transcendental Functions on Real PIM Systems
Maurus Item, Juan Gómez Luna, Yuxin Guo, Geraldo F. Oliveira, Mohammad Sadrosadati, and Onur Mutlu, "TransPimLib: Efficient Transcendental Functions for Processing-in-Memory Systems" Proceedings of the 2023 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Raleigh, North Carolina, USA, April 2023. [arXiv version] [Slides (pptx) (pdf)] [TransPimLib Source Code] [Talk Video (17 minutes)]
https://arxiv.org/pdf/2304.01951.pdf
https://github.com/CMU-SAFARI/transpimlib

## Slide 44: Sequence Alignment on Real PIM Systems
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez Luna, Onur Mutlu, and Izzat El Hajj, "A Framework for High-throughput Sequence Alignment using Real Processing-in-Memory Systems" Bioinformatics, [published online on] 27 March 2023. [Online link at Bioinformatics Journal] [arXiv preprint] [AiM Source Code]
https://arxiv.org/pdf/2208.01243.pdf
https://github.com/CMU-SAFARI/alignment-in-memory

## Slide 45: Homomorphic Operations on Real PIM Systems
Harshita Gupta, Mayank Kabra, Juan Gómez-Luna, Konstantinos Kanellopoulos, and Onur Mutlu, "Evaluating Homomorphic Operations on a Real-World Processing-In-Memory System" Proceedings of the 2023 IEEE International Symposium on Workload Characterization Poster Session (IISWC), Ghent, Belgium, October 2023. [arXiv version] [Lightning Talk Slides (pptx) (pdf)] [Poster (pptx) (pdf)]
https://arxiv.org/pdf/2309.06545.pdf

## Slide 46: Accelerating Reinforcement Learning
Kailash Gogineni, Sai Santosh Dayapule, Juan Gomez-Luna, Karthikeya Gogineni, Peng Wei, Tian Lan, Mohammad Sadrosadati, Onur Mutlu, Guru Venkataramani, "SwiftRL: Towards Efficient Reinforcement Learning on Real Processing-In-Memory Systems" Proceedings of the 2024 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Indianapolis, Indiana, May 2024. [Slides (pptx) (pdf)] [arXiv version]
https://arxiv.org/pdf/2405.03967

## Slide 47: Accelerating ML Training on Real PIM Systems
https://arxiv.org/pdf/2404.07164
Steve Rhyner, Haocong Luo, Juan Gómez-Luna, Mohammad Sadrosadati, Jiawei Jiang, Ataberk Olgun, Harshita Gupta, Ce Zhang, and Onur Mutlu, "PIM-Opt: Demystifying Distributed Optimization Algorithms on a Real-World Processing-In-Memory System" Proceedings of the 33rd International Conference on Parallel Architectures and Compilation Techniques (PACT), Long Beach, CA, USA, October 2024. [Preliminary arXiv version]

## Slide 48: Accelerating GNNs on Real PIM Systems
https://arxiv.org/pdf/2402.16731

## Slide 49: SpMV Multiplication on Real PIM Systems
Appears in SIGMETRICS 2022
https://arxiv.org/pdf/2201.05072.pdf
https://github.com/CMU-SAFARI/SparseP
https://www.youtube.com/watch?v=5kaOsJKlGrE

## Slide 50: Sequence Alignment on Real PIM Systems
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez Luna, Onur Mutlu, and Izzat El Hajj, "A Framework for High-throughput Sequence Alignment using Real Processing-in-Memory Systems" Bioinformatics, [published online on] 27 March 2023. [Online link at Bioinformatics Journal] [arXiv preprint] [AiM Source Code]
https://arxiv.org/pdf/2208.01243.pdf
https://github.com/CMU-SAFARI/alignment-in-memory

## Slide 51
Sequence alignment on traditional systems is limited by the memory bandwidth bottleneck
Processing-in-memory (PIM) overcomes this bottleneck by placing cores near the memory
Our framework, Alignment-in-Memory (AIM), is a PIM framework that supports multiple alignment algorithms (NW, SWG, GenASM, WFA)
  Implemented on UPMEM, the first real PIM system
Results show substantial speedups over both CPUs (1.8X-28X) and GPUs (1.2X-2.7X)
AIM is available at:
  https://github.com/CMU-SAFARI/alignment-in-memory
Summary
51

## Slide 52: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 53: Drawbacks and Limitations of PIM
PIM designs are restricted by low area and power budgets, manufacturing challenges, and limited clock frequencies
To avoid subpar performance, an efficient PIM architecture needs to take into consideration PIM constraints
Co-designing hardware and software to take advantage of PIM properties while mitigating its shortcomings can lead to a better system design
Chart: Normalized Runtime
| Texture Tiling | Color Blitting | Comp- ression | Decomp- ression | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation | TensorFlow | Chrome Browser | Video Playback and Capture | TensorFlow Mobile | GMean
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.43478 | 0.64516 | 0.76336 | 0.76923 | 0.72464 | 0.8 | 0.84746 | 0.63694 | 0.69027
PIM-Acc | 0.4 | 0.57803 | 0.47619 | 0.5 | 0.5814 | 0.70423 | 0.47619 | 0.50505 | 0.5209
+17%
[2]

## Slide 54: HW/SW Co-Design for PIM
We follow a two-step approach to co-design software and hardware to efficiently take advantage of PIM paradigm
Step 1:
Application Profiling
performance
bottleneck
HW/SW requirements
energy
bottleneck
high-performance and energy-efficient PIM architecture
Step 2:
Co-design SW and HW
Target Application
  We showcase our two-step approach for several applications:
1
Machine learning inference models for edge devices
54
2
Genome sequence alignment & filtering

## Slide 55: HW/SW Co-Design for PIM
We follow a two-step approach to co-design software and hardware to efficiently take advantage of PIM paradigm
Step 1:
Application Profiling
performance
bottleneck
HW/SW requirements
energy
bottleneck
high-performance and energy-efficient PIM architecture
Step 2:
Co-design SW and HW
Target Application
  We showcase our two-step approach for several applications:
1
Machine learning inference models for edge devices
55
2
Genome sequence alignment & filtering

## Slide 56: Google Edge Neural Network Models
  We analyze inference execution using 24 edge NN models
13 CNN
Face Detection
6 RNN Transducers
Speech Recognition
2 LSTMs
Language Translation
Image Captioning
3 RCNN
Google Edge TPU
56
Notes: [CLICK] We analyze inference execution on the accelerator using 24 edge NN models that serve as internal benchmarks for the Google Edge TPU, including
[CLICK] 6 RNN Transducers, used for applications such as automatic speech recognition.
[CLICK] 13 convolutional neural networks (CNNs), typically used for applications such as image classification and object detection
[CLICK] 2 long short-term memories (LSTMs), used for applications such as language translation and and handwriting recognition, and
[CLICK] 3 recurrent convolutional neural networks (RCNNs), used for applications such as image captioning
[NEXT]

## Slide 57: Diversity Across the Models
Insight 1: there is significant variation in terms of layer characteristics across the models
Chart: Parameter Footprint (MB)
| 1.0986329999999999E-3
CNN3 | 22201
CNN3 | 21609
CNN3 | 11025
CNN3 | 1225
CNN4 | 5329
CNN4 | 5041
CNN4 | 5329
CNN4 | 2628
CNN11 | 3136
CNN11 | 12544
CNN3 | 1
CNN4 | 1
Layers from LSTMs and Transducers
Layers from CNNs and RCNNs
57
Notes: We draw key two insights from our model analysis
[CLICK] First, we observe a large variation in terms of layer characteristics across different models.
[CLICK] To illustrate, the figure shows the total parameter footprint vs. the FLOP/B ratio (or reuse) across the layers of representative CNNs, LSTMs, and Transducers
[CLICK] We observe from the figure that that layers from LSTMs and Transducers have larger parameter footprints and lower reuse than layers from CNNs.
[NEXT]

## Slide 58: Diversity Within the Models
For example, our analysis of edge CNN models shows:
1
2
Insight 2: even within each model, layers exhibit
significant variation in terms of layer characteristics
Chart: CNN5
 | 150.0625 | 12.25 | 110.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 95.7031 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 13.7812 | 13.7812 | 24.5 | 24.5 | 12.25 | 110.25
Chart: CNN13
Variation in FLOP/Byte: up to 244x across layers
Variation in MAC intensity: up to 200x across layers
58
Notes: [CLICK] Second, even within a single model, layers show variation in terms of layer characteristics
[CLICK] For example, we observe that layers in a single CNN models show
[CLICK] a varying MAC intensity of up to 200x across different layers
and
[CLICK] a varying flop/byte ratio of up to 244x across different layers
[NEXT]

## Slide 59: Mensa High-Level Overview
Edge TPU Accelerator
Mensa
Monolithic Accelerator
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Model A
Model B
Model C
Model A
Model B
Model C
Acc. 1
Acc. 2
Family 2
Family 3
Runtime
Family 1
Acc. 3
CPU
3D-Stacked DRAM
Buffer
Buffer
Buffer
NoC
NoC
NoC
Heterogeneous Accelerators
59
Notes: [CLICK ] In a baseline system, different machine learning models are execute in a single, monolithic edge accelerator, which leads to performance and energy issues.
[CLICK] On the other hand, Mensa distributes the layers from an NN model using a runtime scheduler across a collection of smaller hardware accelerators that are catered the properties of different layer types. By specializing each accelerator to a subset of layers, Mensa avoids the shortcomings of current monolithic edge ML accelerators, resulting in a highly-efficient and high-performance accelerator with a much smaller area.
Next I will give an brief overview of Mensa’s ruy
[NEXT]

## Slide 60: Identifying Layer Families
Chart: Parameter Footprint
| 1.0986329999999999E-3
CNN3 | 22201
CNN3 | 21609
CNN3 | 11025
CNN3 | 1225
CNN4 | 5329
CNN4 | 5041
CNN4 | 5329
CNN4 | 2628
CNN11 | 3136
CNN11 | 12544
CNN3 | 1
CNN4 | 1
Chart: MAC (Millions)
| 24.3907470703125
CNN3 | 22201
CNN3 | 21609
CNN3 | 11025
CNN3 | 1225
CNN4 | 5329
CNN4 | 5041
CNN4 | 5329
CNN4 | 2628
CNN11 | 3136
CNN11 | 12544
CNN3 | 1
CNN4 | 1
  Key observation: the majority of layers group into
  a small number of layer families
Family 1
Family 2
Family 3
Family 4
Family 5
Family 1
Family 2
Family 3
Family 4
Family 5
  Families 1 & 2: low parameter footprint, high data reuse and MAC intensity
  → compute-centric layers
  Families 3, 4 & 5: high parameter footprint, low data reuse and MAC intensity
  → data-centric layers
60
Notes: First, we need to decide how many accelerators we need based on the key characteristics of our NN models.
[CLICK] We make a key observation that the majority of the layers we target fall into five major families in terms key characteristics that impact hardware design
[CLICK] First, we find two Families of layers (families 1 and 2) that have low parameter footprint and high data reuse and MAC intensity. We call such layers compute-centric layers.
[CLICK] Second, we find three families of layers (families, 3, 4 and 5) that have high parameter footprint , low data reuse and MAC intensity. We call such layers data-centric layers.
[NEXT]

## Slide 61: Mensa Runtime Scheduler
Accelerator characteristics
Layer characteristics
Scheduler
NN model
Layer Mapping
  The goal of Mensa’s software runtime scheduler is to identify which accelerator each layer in an NN model should run on
Generated once during initial setup
of a system
Layers tend to group together into a small number of families
Each of the accelerators caters to a specific family of layers
Notes: [CLICK] The goal of Mensa’s software runtime scheduler is to identify which accelerator each layer in an NN model should run on. It works as follows
[CLICK] The scheduler gets a NN model as an input.
[CLICK] It also has two other pieces of information: (1) the characteristics of each layer; and (2) the key characteristics of the available hardware accelerators.
[CLICK] As I will show next, different layers tend to group into a smaller set of layer families with sharing key properties
[CLICK] In this way we can have a small pool of edge accelerators where each accelerator caters to a specific family of layers
[CLICK] We collect the characteristics of the accelerators and layers once prior to inference execution
[CLICK] With all this information, the scheduler generates a per-layer mapping between layers and accelerators by utilizing a mapping heuristic.
[NEXT].

## Slide 62: Mensa: Energy Reduction
Chart: Normalized Energy
| Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | LSTM1 | Transd.1 | Transd.2 | CNN5 | CNN9 | CNN10 | CNN12 | RCNN1 | RCNN3 | Average
Total Static | 0.18337 | 0.028807 | 0.0016648 | 0.18261 | 0.050529 | 0.0029202 | 0.18196 | 0.049265 | 0.0028471 | 0.1816 | 0.17419 | 0.045879 | 0.22843 | 0.2123 | 0.033445 | 0.10425 | 0.071167 | 0.013518 | 0.23801 | 0.21307 | 0.037237 | 0.1827 | 0.083929 | 0.018429 | 0.13761 | 0.059899 | 0.030616 | 0.16493 | 0.086827 | 0.024117
PE | 0.0090239 | 0.0090239 | 0.0090239 | 0.0089025 | 0.0089025 | 0.0089025 | 0.0089121 | 0.0089121 | 0.0089121 | 0.30265 | 0.30265 | 0.30265 | 0.21111 | 0.21111 | 0.21111 | 0.078692 | 0.078692 | 0.078692 | 0.19984 | 0.19984 | 0.19984 | 0.12035 | 0.12035 | 0.12035 | 0.24015 | 0.24015 | 0.24015 | 0.19822 | 0.19822 | 0.19822
Param Buffer+NoC | 0.011732 | 0.011732 | 0 | 0.012646 | 0.012646 | 0 | 0.01223 | 0.01223 | 0 | 0.35617 | 0.35617 | 0.0066224 | 0.3645 | 0.3645 | 0.008601 | 0.62157 | 0.62157 | 0.011434 | 0.35462 | 0.35462 | 0.0081578 | 0.14233 | 0.14233 | 0.0025231 | 0.15703 | 0.15703 | 0.0025904 | 0.19173 | 0.19173 | 0.0038425
Act Buffer+NoC | 0.00029556 | 0.00029556 | 9.2361e-06 | 0.00050107 | 0.00050107 | 1.5659e-05 | 0.00047681 | 0.00047681 | 1.49e-05 | 0.011178 | 0.011178 | 0.00020783 | 0.013214 | 0.013214 | 0.0003118 | 0.024601 | 0.024601 | 0.00046662 | 0.013074 | 0.013074 | 0.00030238 | 0.0044216 | 0.0044216 | 8.4817e-05 | 0.005467 | 0.005467 | 9.3264e-05 | 0.0064591 | 0.0064591 | 0.00013406
Off-chip Interconnect | 0.31791 | 0.31791 | 0 | 0.31782 | 0.31782 | 0 | 0.31825 | 0.31825 | 0 | 0.059303 | 0.059303 | 0.028786 | 0.073025 | 0.073025 | 0.010856 | 0.068287 | 0.068287 | 0.0068711 | 0.077702 | 0.077702 | 0.008003 | 0.21986 | 0.21986 | 0.010914 | 0.18371 | 0.18371 | 0.018103 | 0.19266 | 0.19266 | 0.012536
DRAM | 0.47767 | 0.47767 | 0.16611 | 0.47752 | 0.47752 | 0.16606 | 0.47817 | 0.47817 | 0.16629 | 0.089103 | 0.089103 | 0.030986 | 0.10972 | 0.10972 | 0.038156 | 0.1026 | 0.1026 | 0.03568 | 0.11675 | 0.11675 | 0.040599 | 0.33034 | 0.33034 | 0.11488 | 0.27602 | 0.27602 | 0.095989 | 0.28948 | 0.28948 | 0.10101
Mensa-G reduces energy consumption by 3.0X
compared to the baseline Edge TPU
62
Notes: [CLICK] Fist, Mensa-G placement of accelerators and careful dataflow design enables to reduce the energy consumed by on-chip and off-chip parameter traffic by 15.3x on average compared to the baseline.
[CLICK] Second, Mensa-G reduces the dynamic energy of on-chip buffers and Noc by almost 50x compared to the Baseline system with high bw memory.
[CLICK] We conclude that Mensa-G reduces energy by 66% and improves inference energy efficiency by 3.0x compared to the baseline edge TPU.
[NEXT]

## Slide 63: Mensa: Throughput Improvement
Chart: Normalized Throughput
| LSTM1 | Trans.1 | Trans.2 | CNN5 | CNN9 | CNN10 | CNN12 | RCNN1 | RCNN3 | Average
Base | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Base+HB | 6.3653 | 3.6139 | 3.6935 | 1.6198 | 1.764 | 1.4649 | 1.646 | 2.1768 | 2.2974 | 2.5183
Mensa | 8.0452 | 4.5676 | 4.6683 | 1.9824 | 2.183 | 1.7926 | 2.0494 | 2.757 | 2.6132 | 3.1173
Mensa-G improves inference throughput by 3.1X
compared to the baseline Edge TPU
63
Notes: [CLICK] We also analyze Mensa-G’s throughput compared to the Baseline edge TPU and Baseline edge TPU with the high bandwidth off-chip memory
[CLICK] We observe that Mensa-G’s improve throughput compared to the baseline edge TPU by 3.1X on average
[NEXT]

## Slide 64: Mensa: Highly-Efficient ML Inference
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]

## Slide 65: HW/SW Co-Design for PIM
We follow a two-step approach to co-design software and hardware to efficiently take advantage of PIM paradigm
Step 1:
Application Profiling
performance
bottleneck
HW/SW requirements
energy
bottleneck
high-performance and energy-efficient PIM architecture
Step 2:
Co-design SW and HW
Target Application
  We showcase our two-step approach for several applications:
1
Machine learning inference models for edge devices
65
2
Genome sequence alignment & filtering

## Slide 66: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 67: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 68: Samsung Function-in-Memory DRAM (2021)

## Slide 69: Samsung Function-in-Memory DRAM (2021)

## Slide 70: Samsung Function-in-Memory DRAM (2021)

## Slide 71: Samsung Function-in-Memory DRAM (2021)

## Slide 72: Samsung PNM Solutions for Generative AI (2023)
Main target: transformer decoders used in ChatGPT, GPT-3
  Compute-bound step: Summarization
  Memory-bound step: Generation
    Most of the execution time is spent on the memory copy from the host CPU memory to the CPU memory
GEMV portion can be 60%-80% of total generation latency, which is the target of PIM/PNM
[J. H. Kim+ HC, 2023]

## Slide 73: Solution I: Samsung’s HBM-PIM (2023)
AMD MI100 GPUs fabricated with HBM-PIM
Experimental setup: GPT-J (6B, 32 input tokes), single AMD MI100-PIM GPU
GPT can be accelerated by more than 2x over baseline
[J. H. Kim+ HC, 2023]

## Slide 74: Solution II: Samsung’s LPDDR-PIM (2023)
PIM for on-device generative AI
  Datacenter costs and power consumption are increasing due to the growing demand for cloud AI
LPDDR-PIM improves battery life by preventing memory over-provisioning just for bandwidth
4.47x performance gains and 70.6% energy reduction in GPT-2
[J. H. Kim+ HC, 2023]

## Slide 75: Solution III: Samsung’s CXL-PNM (2023)
A CXL-based processing-near-memory solution
  Improves capacity, bandwidth, and power
  Large-scale large-language models are often capacity-bound
Multiple CXL-PNM can offer 4.4x higher energy efficiency and 53% higher throughput than multiple GPUs
[J. H. Kim+ HC, 2023]

## Slide 76: SK hynix AiM: Chip Implementation (2022)
4 Gb AiM die with 16 processing units (PUs)
Lee et al., A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications, ISSCC 2022
Notes: * The operating voltage is 1.25V: - Lowered from 1.35V of the normal GDDR6, for bank parallel operation.
* 16Gb/s is reached at 1.25V in DL operation.
Flat-lid package for lower thermal resistance.
Tested in a prototype system with an FPGA (connected to host CPU via PCIe).

## Slide 77: SK hynix AiM: System Organization (2022)
GDDR6-based AiM architecture
Lee et al., A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications, ISSCC 2022

## Slide 78: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 79: FPGA-based Processing Near Memory
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020.

## Slide 80: Heterogeneous System: CPU+FPGA
POWER9 AC922
DDR4-based AD9V3 board
CAPI2
Source: AlphaData
Source: IBM
  2. DDR4-based board AD9V3
  Xilinx Virtex Ultrascale+™ XCVU3P-2
We evaluate two POWER9+FPGA systems:
  1. HBM-based board AD9H7
  Xilinx Virtex Ultrascale+™ XCVU37P-2
Notes: and the second is alphadata 9v3 with DDR4
Our CPU-FPGA heterogeneous platform offloads the rep-ri-zen-tuh-tiv weather kernels onto the FPGA
% with 98% of stencil execution time
%In the execution flow of our application:
Application data is stored in the HOST DRAM
Since our platform offers memory-coherent access of FPGA to the system memory, we build a pipelined execution, where communication time for transferring data from host to FPGA memory is masked with the actual FPGA processing
%Despite the low computational complexity, we were able to hide the memory access latency with the CAPI2 interface

## Slide 81: NERO Design Flow
Notes: This is the complete design flow. All the tasks execute in a dataflow manner that enables task-level parallelism.
%Note that we show only a single port-based PE operation. However, for multiple PEs, we enable multiple HBM ports.

## Slide 82: NERO Performance Analysis
Horizontal Diffusion
Vertical Advection
NERO is 4.2x and 8.3x faster than
a complete POWER9 socket
Notes: By carefully designing the micro-archictecture architecture with application specific heterogeneous memory hierarchy, NERO is 4.2 times and 8.3 times faster for vertical advection and horizontal diffusion respectively than a complete~POWER9~socket.

## Slide 83: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 84: Samsung AxDIMM (2021)
https://news.samsung.com/global/samsung-brings-in-memory-processing-power-to-wider-range-of-applications

## Slide 85: Samsung AxDIMM (2021)
DIMM-based PIM
  DLRM recommendation system
Baseline System
AxDIMM System
[Ke+, IEEE Micro’2021]

## Slide 86: AxDIMM Design: Hardware Architecture
FPGA board with standard DIMM interface:
It serves as a real-system
near-memory processing implementation
[Ke+, IEEE Micro’2021]

## Slide 87: AxDIMM Design: Hardware Architecture
Two execution modes:
non-acceleration mode
acceleration mode (blocking)
[Ke+, IEEE Micro’2021]
Notes: Blocking = No concurrent access from host.

## Slide 88: Sparse Length Sum with AxDIMM (IEEE Micro 2021)
https://doi.org/10.1109/MM.2021.3097700

## Slide 89: Sparse Length Sum with AxDIMM (AICAS 2022)
https://doi.org/10.1109/AICAS54282.2022.9869896

## Slide 90: Database Operations with AxDIMM (DaMoN 2022)
https://doi.org/10.1145/3533737.3535093

## Slide 91: Longer Lecture on AxDIMM
https://youtu.be/SXdzQZAKG-Y

## Slide 92: Another Longer Lecture on AxDIMM
https://youtu.be/2FMQg786GKs

## Slide 93: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
This does not include many experimental chips and startups
[Alibaba 2022]

## Slide 94: Possible PNM Designs
Fixed-function units
  Hardware/software co-designed PIM for efficiency
  E.g. from academia: Mensa for NN Edge Inference
  E.g. from industry: Samsung HBM-PIM, SK hynix AiM
PIM-Accelerator 1
PIM-Accelerator N
…
Reconfigurable architectures
  PNM cores coupled with FPGAs, CGRA
  E.g. from academia: NERO for Weather Prediction
  E.g. from industry: Samsung AxDIMM
Reconfigurable Accelerator
General-purpose programmable cores
  Wimpy cores (possibility of running any workload)
  E.g. from academia: Tesseract PIM for Graph Processing
  E.g. from industry: UPMEM PIM
Cache
PIM Core

## Slide 95: Research Tools PNM: DAMOV-SIM
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 96: Step 3: Memory Bottleneck Classification (2/2)
Goal: identify the specific sources of data movement bottlenecks
DAMOV-SIM Simulator
# Cores
Scalability Analysis
Integrated ZSim and Ramulator
Scalability Analysis:
  1, 4, 16, 64, and 256 out-of-order/in-order host and NDP CPU cores
  3D-stacked memory as main memory
Configuration 2: NDP System
Off-chip link
DRAM
CPU
CPU
CPU
L2
L1
L3
L2
L1
L2
L1
L2
L1
CPU
Configuration 1: Host CPU System
Off-chip link
272
DAMOV-SIM: https://github.com/CMU-SAFARI/DAMOV
…
Logic Layer
CPU
CPU
CPU
L1
L1
L1
L1
CPU
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Notes: [CLICK] The goal of the scalability analysis we perform is to nail down the specific sources of data movement bottlenecks in the application.
In this analysis, we evaluate the performance and energy scaling of an application in three different system configurations; and collect the key metrics for our bottleneck classification
[CLICK] During scalability analysis, we simulate three system configurations of a general-purpose multicore processor. To this end, we build a framework that integrates the ZSim CPU simulator with the Ramulator memory simulator to produce a fast, scalable, and cycle-accurate open-source simulator called DAMOV-SIM. We use ZSim to simulate the core microarchitecture, cache hierarchy, coherence protocol, and prefetchers. We use Ramulator to simulate the DRAM architecture, memory controllers, and memory accesses.
[CLICK] The first configuration we evaluate is of a host CPU with a deep cache hierarchy, with a 32 KB, private L1 cache, a 256 KB private L2 cache, and a shared 8MB L3 cache.
[CLICK] The second configuration is of an NDP CPU with only a private read-only L1 cache of 32 KB.
In our paper we evaluate an third configuration that includes hardware prefetcher on top of configuration 1. However, we omit such configuration in this talk.
The remaining components of the processor configuration are kept the same to isolate the impact of only the caches, prefetchers, and NDP.
This way, we expect that the performance and energy differences between the three configurations to come exclusively from the different data movement requirements.
[CLICK] For all configurations, we sweep the number of CPU cores in our analysis from 1 to 256, as previous works show that large core counts are necessary to saturate the bandwidth provided by modern high-bandwidth memories, and because modern CPUs and NDP proposals can have varying core counts.
[CLICK] We simulate a memory architecture similar to the Hybrid Memory Cube device where the host CPU accesses memory through a high-speed off-chip link,
[CLICK] and the NDP logic resides in the logic layer of the memory chip and has direct access to the DRAM banks, thus taking advantage of higher memory bandwidth and lower memory latency.
[NEXT]

## Slide 97: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 98: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 99: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 100: More on DAMOV Methods & Benchmarks
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 101: Research Tools PNM: Samsung HBM-PIM
https://github.com/SAITPublic/PIMSimulator

## Slide 102: Research Tools PNM: UPMEM PIM (I)
https://github.com/VIA-Research/uPIMulator

## Slide 103: Research Tools PNM: UPMEM PIM (II)
https://ieeexplore.ieee.org/document/10476411/

## Slide 104: 1st Workshop on Memory-Centric Computing: Processing-Near-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025