## Slide 1: 1st Workshop on Memory-Centric Computing: Programming PNM Systems
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025

## Slide 2: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 3: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 4: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 5: Adoption: How to Keep It Simple?
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 6: Adoption: How to Ease Programmability? (I)
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu, “DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” in PACT SRC Student Competition, Vienna, Austria, October 2023.

## Slide 7: Adoption: How to Ease Programmability? (II)
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, YuXin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 8: The Programmability Barrier: Overview
  Programming the UPMEM-based system requires:
1
Splitting input data and computation across PIM chips
2
Transferring input data from main memory to PIM chips
3
Manually handling caching in PIM’s scratchpad memory
4
Transferring output data from PIM chips to main memory
Programming a general-purpose PIM architecture leads to non-trivial effort → requires knowledge of the underlying hardware and manual fine-grained data movement handling
1
2
3
4
1
2
3
4
Notes: In order to program the UPMEM system, the programmer needs to perform four main operations.
[CLICK] First, it needs to split input data across PIM chips
[CLICK] Second, it needs to transfer input data from main memory to PIM chips
[CLICK] Third, it needs to manually handle caching inside the PIM’s scratchpad memory
[CLICK] and fourth, it needs to transfer output data from PIM chips to main memory
[NEXT]

## Slide 9: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Notes: Let’s see how such four tasks translate into code.
Next, I will show code snippets of a vector addition implemented using the UPMEM programming model.
[NEXT]

## Slide 10: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
const unsigned int input_size = 1073741824; // Example value
const unsigned int input_size_8bytes =
((input_size * sizeof(T)) % 8) != 0
? roundup(input_size, 8) : input_size;
const unsigned int input_size_dpu = divceil(input_size, nr_of_dpus);
const unsigned int input_size_dpu_8bytes =
((input_size_dpu * sizeof(T)) % 8) != 0
? roundup(input_size_dpu, 8) : input_size_dpu;
Notes: The programmer has several tasks that need to be translated into code, including aligning data within PIM chips
[NEXT]

## Slide 11: The Programmability Barrier: Vector Addition Example
unsigned int kernel = 0;
dpu_arguments_t input_arguments[NR_DPUS];
for(i=0; i<nr_of_dpus-1; i++) {
input_arguments[i].size = input_size_dpu_8bytes * sizeof(T);
input_arguments[i].transfer_size = input_size_dpu_8bytes * sizeof(T);
input_arguments[i].kernel = kernel;
}
input_arguments[nr_of_dpus-1].size =
(input_size_8bytes - input_size_dpu_8bytes * (NR_DPUS-1)) * sizeof(T);
input_arguments[nr_of_dpus-1].transfer_size = input_size_dpu_8bytes * sizeof(T);
input_arguments[nr_of_dpus-1].kernel = kernel;
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Notes: Collect input parameters
[NEXT]

## Slide 12: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
DPU_ASSERT(dpu_push_xfer(dpu_set, DPU_XFER_TO_DPU, "DPU_INPUT_ARGUMENTS",
0, sizeof(input_arguments[0]), DPU_XFER_DEFAULT));
DPU_FOREACH(dpu_set, dpu, i) {
DPU_ASSERT(dpu_prepare_xfer(dpu, bufferA + input_size_dpu_8bytes * i));
}
DPU_ASSERT(dpu_push_xfer(dpu_set, DPU_XFER_TO_DPU, DPU_MRAM_HEAP_POINTER_NAME,
0, input_size_dpu_8bytes * sizeof(T), DPU_XFER_DEFAULT));
DPU_FOREACH(dpu_set, dpu, i) {
DPU_ASSERT(dpu_prepare_xfer(dpu, bufferB + input_size_dpu_8bytes * i));
}
DPU_ASSERT(dpu_push_xfer(dpu_set, DPU_XFER_TO_DPU, DPU_MRAM_HEAP_POINTER_NAME,
input_size_dpu_8bytes * sizeof(T),
input_size_dpu_8bytes * sizeof(T), DPU_XFER_DEFAULT));
Notes: Distribute input parameters across PIM cores
[NEXT]

## Slide 13: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
DPU_ASSERT(dpu_launch(dpu_set, DPU_SYNCHRONOUS));
Notes: Launch PIM computation
[NEXT]

## Slide 14: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
i = 0;
DPU_FOREACH(dpu_set, dpu, i) {
DPU_ASSERT(dpu_prepare_xfer(dpu, bufferC + input_size_dpu_8bytes * i));
}
DPU_ASSERT(dpu_push_xfer(dpu_set, DPU_XFER_FROM_DPU, DPU_MRAM_HEAP_POINTER_NAME,
input_size_dpu_8bytes * sizeof(T),
input_size_dpu_8bytes * sizeof(T), DPU_XFER_DEFAULT));
Notes: Collect PIM results
[NEXT]

## Slide 15: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
barrier_wait(&my_barrier);
uint32_t input_size_dpu_bytes = DPU_INPUT_ARGUMENTS.size;
uint32_t input_size_dpu_bytes_transfer = DPU_INPUT_ARGUMENTS.transfer_size;
uint32_t base_tasklet = tasklet_id << BLOCK_SIZE_LOG2;
uint32_t mram_base_addr_A = (uint32_t)DPU_MRAM_HEAP_POINTER;
uint32_t mram_base_addr_B = (uint32_t)(DPU_MRAM_HEAP_POINTER
+ input_size_dpu_bytes_transfer);
T *cache_A = (T *) mem_alloc(BLOCK_SIZE);
T *cache_B = (T *) mem_alloc(BLOCK_SIZE);
Notes: Manage the PIM scratchpad memory
[NEXT]

## Slide 16: The Programmability Barrier: Vector Addition Example
for (int byte_index = base_tasklet; byte_index < input_size_dpu_bytes;
byte_index += BLOCK_SIZE * NR_TASKLETS){
uint32_t l_size_bytes = (byte_index + BLOCK_SIZE >= input_size_dpu_bytes)
? (input_size_dpu_bytes - byte_index) : BLOCK_SIZE;
mram_read((__mram_ptr void const*)(mram_base_addr_A + byte_index),
cache_A, l_size_bytes);
mram_read((__mram_ptr void const*)(mram_base_addr_B + byte_index),
cache_B, l_size_bytes);
vector_addition(cache_B, cache_A, l_size_bytes >> DIV);
mram_write(cache_B, (__mram_ptr void*)(mram_base_addr_B + byte_index)
l_size_bytes);
}
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Notes: Orchestrate data movement and computation across PIM cores
[NEXT]

## Slide 17: The Programmability Barrier: Vector Addition Example
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Goal:
static void vector_addition(T *bufferB, T *bufferA, int l_size){
for (unsigned int i = 0; i < l_size; i++){
bufferB[i] += bufferA[i];
}
}
Notes: However, the programmer’s main goal is to just perform a simple vector addition
[NEXT]

## Slide 18: The Programmability Barrier: Summary
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Goal:
static void vector_addition(T *bufferB, T *bufferA, int l_size){
for (unsigned int i = 0; i < l_size; i++){
bufferB[i] += bufferA[i];
}
}
Programming the UPMEM system leads to non-trivial effort → requires knowledge of the underlying hardware and manual fine-grained data movement handling
Problem
Notes: We conclude that programming the UPMEM system leads to non-trivial effort by the programmer since it requires knowledge of the underlying hardware and manual data movement handling
[NEXT[

## Slide 19: Our Goal
To ease programmability for the UPMEM system, allowing a programmer to write efficient PIM-friendly code
without the need to explicitly manage hardware resources
Goal
Notes: Therefore, our goal in this work is to ease programmability for the UPMEM system, allowing the programmer to write PIM-friendly code efficiently.
[NEXT]

## Slide 20: Outline
The Programmability Barrier
2
Introduction
1
Conclusion
5
SimplePIM Overview
3
Management, Communication & Processing Interfaces
Evaluation Results
DaPPA Overview
4
DaPPA Main Components
Evaluation Results
Notes: This is the outline for my talk. First, I will give a brief introduction to PIM architectures. Second, I will talk about the problem our paper aims to solve and then on our solution. Fourth, I will briefly showcase our key results and then conclude.
[NEXT]

## Slide 21: SimplePIM: A Software Framework for Productive and Efficient Processing in Memory
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, Yuxin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023. [Slides (pptx) (pdf)] [SimplePIM Source Code]

## Slide 22: SimplePIM Programming Framework: Overview
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
1
  Management interface → Metadata for PIM-resident arrays
2
  Communication interface → Abstractions for host-PIM and PIM-PIM communication
3
  Processing interface → Iterators (map, reduce, zip) to implement workloads
Notes: [CLICK] Our software framework, SimplePIM, leverages the massive memory bandwidth and parallelism offered by PIM hardware to operate on arrays of arbitrary size and dimensions. SimplePIM offers three key interfaces to support PIM systems like UPMEM.
[CLICK] The management interface stores metadata for the PIM-resident arrays, which can be accessed by the programmer and other parts of SimplePIM as needed.
[CLICK] The communication interface provides abstractions for both Host-PIM and PIM-PIM communication patterns.
These patterns are similar to communication patterns in other distributed frameworks such as MPI [71], which makes it easier for SimplePIM to be adopted.
[CLICK] The processing interface leverages PIM’s high memory bandwidth and parallelism to execute map, reduce, and zip iterators on PIM arrays.
Programmers can combine these iterators to implement many widely-used workloads ranging from simple vector addition to complex machine learning model training.
[CLICK] Let’s check each one of these interfaces next
[NEXT]

## Slide 23: SimplePIM Programming Framework: Management Interface
Metadata for PIM-resident arrays
  array_meta_data_t describes a PIM-resident array
  simple_pim_management_t for managing PIM-resident arrays
lookup: Retrieves all relevant information of an array
register: Registers the metadata of an array
free: Removes the metadata of an array
void simple_pim_array_free(const char* id, simple_pim_management_t* management);
array_meta_data_t* simple_pim_array_lookup(const char* id,
simple_pim_management_t* management);
void simple_pim_array_register(array_meta_data_t* meta_data,
simple_pim_management_t* management);

## Slide 24: SimplePIM Programming Framework: Communication Interface (I)
SimplePIM Host-to-CPU Broadcast
  Transfers a host array to all PIM cores in the system
void simple_pim_array_broadcast(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 25: SimplePIM Programming Framework: Communication Interface (II)
Host-to-PIM SimplePIM Scatter
  Distributes an array to PIM DRAM banks
Host-to-PIM SimplePIM Gather
  Collects portions of an array from PIM DRAM banks
void* simple_pim_array_gather(char* const id, simple_pim_management_t* management);
void simple_pim_array_scatter(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 26: SimplePIM Programming Framework: Communication Interface (III)
PIM-to-PIM Communication: AllReduce
  Used for algorithm synchronization
  The programmer specifies an accumulative function
void simple_pim_array_allreduce(char* const id, handle_t* handle,
simple_pim_management_t* management);

## Slide 27: SimplePIM Programming Framework: Communication Interface (IV)
PIM-to-PIM Communication: AllGather
  Combines array pieces and distributes the complete array to all PIM cores
void simple_pim_array_allgather(char* const id, char* new_id,
simple_pim_management_t* management);

## Slide 28: SimplePIM Programming Framework: Processing Interface (I)
Array Map
  Applies map_func to every element of the data array
void simple_pim_array_map(const char* src_id, const char* dest_id,
uint32_t output_type, handle_t* handle, simple_pim_management_t* management);

## Slide 29: SimplePIM Programming Framework: Processing Interface (II)
Array Reduction
  The map_to_val_func function transforms an input element to an output value and an output index
  The acc_func function accumulates the output values onto the output array
void simple_pim_array_red(const char* src_id, const char* dest_id,
uint32_t output_type, uint32_t output_len, handle_t* handle,
simple_pim_management_t* management);

## Slide 30: SimplePIM Programming Framework: Processing Interface (III)
Array Zip
  Takes two input arrays and combines their elements into an output array
void simple_pim_array_zip(const char* src1_id, const char* src2_id,
const char* dest_id, simple_pim_management_t* management);

## Slide 31: SimplePIM Programming Framework: General Code Optimizations
Strength reduction
Loop unrolling
Avoiding boundary checks
Function inlining
Adjustment of data transfer sizes

## Slide 32: Evaluation Results: Evaluation Methodology
Evaluated system
  UPMEM PIM system with 2,432 PIM cores with 159 GB of PIM DRAM
Real-world Benchmarks
  Vector addition
  Reduction
  Histogram
  K-Means
  Linear regression
  Logistic regression
Comparison to hand-optimized codes in terms of programming productivity and performance

## Slide 33: Evaluation Results: Productive Improvement (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 34: Evaluation Results: Productive Improvement (II)
Example: SimplePIM histogram
// Programmer-defined functions in the file "histo_filepath"
void init_func (uint32_t size, void* ptr) {
char* casted_value_ptr = (char*) ptr;
for (int i = 0; i < size; i++)
casted_value_ptr[i] = 0;
}
void acc_func (void* dest, void* src) {
*(uint32_t*)dest += *(uint32_t*)src;
}
void map_to_val_func (void* input, void* output, uint32_t* key) {
uint32_t d = *((uint32_t*)input);
*(uint32_t*)output = 1;
*key = d * bins >> 12;
}
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);

## Slide 35: Evaluation Results: Productive Improvement (III)
Lines of code (LoC) reduction
 | SimplePIM | Hand-optimized | LoC Reduction
Reduction | 14 | 83 | 5.93×
Vector Addition | 14 | 82 | 5.86×
Histogram | 21 | 114 | 5.43×
Linear Regression | 48 | 157 | 3.27×
Logistic Regression | 59 | 176 | 2.98×
K-Means | 68 | 206 | 3.03×
SimplePIM reduces the number of lines of effective code by a factor of 2.98× to 5.93×

## Slide 36: Evaluation Results: Weak Scaling Analysis
SimplePIM achieves comparable performance for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 10%-37%

## Slide 37: Evaluation Results: Strong Scaling Analysis
SimplePIM scales better than hand-optimized implementations for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression, and k-means by 15%-43%

## Slide 38: Source Code
https://github.com/CMU-SAFARI/SimplePIM

## Slide 39: SimplePIM: A Software Framework for Productive and Efficient Processing in Memory
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, Yuxin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023. [Slides (pptx) (pdf)] [SimplePIM Source Code]

## Slide 40: DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu ”DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” arXiv:2310.10168 [cs.AR] 2nd Place ACM Student Research Competition at the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 41: DaPPA: Key Idea & Overview
Leverage an intuitive data-parallel pattern-based interface for PIM programming
Key Idea
DaPPA , a Data-Parallel PIM Architecture that automatically distributes input and gathers output data, handles memory management, and parallelizes work across PIM cores
1
Data-Parallel Pattern APIs
2
Dataflow Programming Interface
3
Dynamic Template-Based Compilation
  DaPPA is composed of three main components:
Notes: The key idea behind DaPPA is to use an intuitive data-parallel pattern Based programming interface for PIM
[CLICK] DaPPA uses such an interface to automatically distribute and gather data across PIM chips, handle memory management and to parallelism computation across PIM cores
[CLICK] DaPPA is composed of three main components.
[CLICK] A collection of data-parallel pattern APIs
[CLICK] A dataflow programming interface
[CLICK] and a dynamic template-based compilation
[NEXT]

## Slide 42: DaPPA: Data-Parallel Pattern APIs
Skeleton and pattern-based parallel programming are a common abstraction for parallel architectures
  M. Cole, “Bringing Skeletons Out of the Closet: A Pragmatic Manifesto for Skeletal Parallel Programming,” Parallel Computing, 2004
DaPPA supports five primary data-parallel patterns
Pre-defined functions that implement high-level data-parallel pattern primitives
The user can combine all five data-parallel primitives to describe complex data transformations
f
f
f
f
map
f
reduce
f
f
f
f
filter
f
f
f
f
window
f
f
group
Notes: The data parallel pattern APIs are a collection of pre-defined functions that implement high-level data-parallel pattern priorities.
[CLICK] DaPPA uses such APIs to implement a skeleton programming model, which is a common approach to abstract hardware components of parallel architectures, including multi-processor systems, GPUs, and custom accelerators.
[CLICK] DaPPA supports five primary data-parallel patterns, including map, reduce, filter, window, and group
[CLICK] The user can combine all five primitives for more complex patterns
[NEXT]

## Slide 43: DaPPA: Dataflow Programming Interface
DaPPA exposes to the user a dataflow-based programming interface
x
input
output
Pipeline
defines a collection of transformations over the input data
each stage represents a parallel pattern
data flows sequentially across each stage
stage 1
f
f
x
stage 2
f
f
x
stage N
f
Notes: DaPPA exposes a dataflow-based programming interface to the users. The interface has three main components.
[CLICK] First, a Pipeline defines a collection of transformations over the input data
[CLICK] Second, a stage defines a parallel pattern-based data transformation
[CLICK] Third, stage communication happens sequentially, with data following from one stage to another within the pipeline
[NEXT]

## Slide 44: DaPPA: Dynamic Template-Based Compilation
Templating: DaPPA creates a base UPMEM code based on a basic skeleton of a UPMEM application
  We use the Inja C++ templating engine
Optimizations: DaPPA uses a series of transformations to
  extract data required by the UPMEM code template
  calculate the memory offsets for MRAMs and WRAMs
  divide computation between CPU and PIM cores
DaPPA uses a dynamic template-based compilation to generate PIM code in two main steps
1
2
DaPPA compiles and executes each stage in a Pipeline per time → allows for runtime optimizations
Notes: DaPPA uses a dynamic template-based compilation to generate PIM code in two main steps
[CLICK] First, DaPPA creates UPMEM code using a template engine called Inja
[CLICK] Second, DaPPA applies a series of transformations to the code to extract the information required to feed the UPMEM code template from the Pipeline model, calculates memory offsets for automatically data handling, and divides computation between CPU and PIM cores, even allowing for collaborative execution between host cores and PIM cores
[CLICK] During the dynamic template-based compilation, DaPPA compiles and executes each Pipeline stage once per time, allowing for runtime optimizations based on output data
[NEXT]

## Slide 45: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Let’s see how DaPPA can be used to implement a simple dot product operation in the UPMEM system
[NEXT]

## Slide 46: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: First, the programmer chooses suitable data parallel patterns to represent the computation. In this case, a map and reduce patterns
[NEXT]

## Slide 47: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Second, the user creates two pipeline stages in C++ to implement the computation. Note that there is no hardware specific code required here.
[NEXT]

## Slide 48: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Finally, DaPPA takes the C++-based pipeline, and dynamically compiles and executes each stage in the UPMEM system.
[NEXT]

## Slide 49: Evaluation: Methodology Overview
Evaluation Setup
  Host CPU: 2-socket Intel® Xeon Silver 4110 CPU
  PIM Cores: 20 UPMEM PIM DIMMs (160 GB PIM memory)
  2560 DPUs in total
Workloads: 6 workloads from the PrIM benchmark suite
  Vector addition (VA); Select (SEL); Unique (UNI); Reduce (RED); General matrix-vector multiply (GEMV); Histogram small (HST-S)
Metrics
  End-to-end execution time (average of 10 runs)
  Programming complexity (in lines of code)
Notes: We evaluate DaPPA using a real UPMEM system with more than 2000 PIM cores
[CLICK] We use six workloads from the PrIM benchmark suite
[CLICK] We compare DaPPA’s performance and programming complexity against the hand-tuned PrIM workloads
[NEXT]

## Slide 50: Evaluation: Performance Analysis
Chart: Normalized Performance
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 1 | 1 | 1 | 1 | 1 | 1 | 1
DaPPA | 1.125 | 10 | 10 | 1.1 | 0.93333 | 0.93333 | 2.1
Large performance improvement due to parallel data transfers & host+PIM collaborative exec.
Notes: In this plot, we show DaPPA’s performance normalized to the hand-tuned PrIM implementations.
[CLICK] We observe a large performance improvement for some workloads, due to DAPPA usage of parallel data transfers and collaborative host and PIM execution
[NEXT[

## Slide 51: Evaluation: Performance Analysis
Chart: Normalized Performance
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 1 | 1 | 1 | 1 | 1 | 1 | 1
DaPPA | 1.125 | 10 | 10 | 1.1 | 0.93333 | 0.93333 | 2.1
2.1x
DaPPA significantly improves end-to-end performance
compared to hand-tuned implementations
Notes: Overall, DAPPA provides 2.1x the performance of hand-tuned code.
[NEXT]

## Slide 52: Evaluation: Programming Complexity Analysis
DaPPA significantly reduces programming complexity
by abstracting hardware components
Chart: Lines of Code (LOC)
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 78 | 120 | 155 | 123 | 180 | 113 | 123.9683
DaPPA | 6 | 6 | 6 | 6 | 9 | 8 | 6.7348
Reduction | 0.92308 | 0.95 | 0.96129 | 0.95122 | 0.95 | 0.9292 | 0.94404
94.4%
Notes: Next, we evaluate programming complexity measured in lines of code.
[CLICK] On average, DaPPA reduces the required lines of code by 94% compared to PrIM.
[NEXT]

## Slide 53: Evaluation: Comparison to State-of-the-Art
SimplePIM [Chen+, PACT’23]: a framework that uses (1) iterator functions and (2) primitives for communication to aid PIM programmability Compared to SimplePIM, DaPPA provides three key benefits
  Higher abstraction level → The programmer does not need to manually specify communication patterns used during computation
  Support for more parallel patterns → DaPPA supports two more parallel primitives (window and group), and allows the mixing of parallel patterns
  Further execution optimizations → DaPPA allows using idle host resources for collaborative execution
DaPPA improves state-of-the-art frameworks for PIM programmability
Notes: We briefly compared DaPPA to a previously proposed framework for PIM programmability called SimplePIM.
Compared to SimplePIM, DaPPA provides
[CLICK] A higher abstraction level, where the user does not need to manually specific communication across PIM cores as in SIMPLE PIM; two more parallel patterns, and further optimizations as colloborative PIM+host execution.
[CLICK] We conclude that DaPPA improves the state-of-the-art in PIM programmability
[NEXT]

## Slide 54: DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu ”DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” arXiv:2310.10168 [cs.AR] 2nd Place ACM Student Research Competition at the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 55: 1st Workshop on Memory-Centric Computing: Programming PNM Systems
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025