## Slide 1: 1st Workshop on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025

## Slide 2: Brief Review: Inside A DRAM Chip

## Slide 3: Background: DRAM Hierarchical Organization
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows/columns)
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 4: Background: DRAM Hierarchical Organization
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 5: Background: DRAM Operation – Row Access (ACTIVATE)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: To access data, the memory controller executes two main operations.
[CLICK] To access a DRAM row, the memory controller issues an ACTIVATE command to DRAM. On receiving an ACT, the global and local row decoder assess the wordline of the target row, connecting the DRAM cells to the bitlines
[CLICK] Then, the sense amplifier senses the perturbation caused in the bitline, amplifying and latching the data from the DRAM cells
[NEXT]

## Slide 6: Background: DRAM Operation – Column Access (READ)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
column
to memory channel
global wordline
Notes: Then, the memory controller issues a read command to read a column of data from the previously latched DRAM row.
[CLICK] The read command moves the target DRAM column from the local sense amplifiers to the global sense amplifier and finally to the memory channel via the I/O interface
[NEXT]

## Slide 7: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
← src
← dst
Notes: The operating principles of DRAM can be used to implement bulk-bitwise operations inside DRAM. For example, RowClone implements in-DRAM row copy operation by issuing back-to-back ACTIVATE commands to DRAM
[CLICK] The first activate copies the source row into the local sense amplifier
[NEXT]

## Slide 8: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 9: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 10: Background: PUD in Commodity Off-the-Shelf DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 11: PUD in COTS DRAM: Summary of Results
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 12: More on: Functionally-Complete DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024.

## Slide 13: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 14: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 15: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← tmp
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
A
Sum
MAJ
Cout
MAJ
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 16: Background: Bulk Bitwise Arithmetic Operations
← A
← tmp
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 17: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 18: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 19: Evaluation: Methodology Overview (I)
Simulator: gem5
Baselines:
  A multi-core CPU (Intel Skylake)
  A high-end GPU (NVidia Titan V)
  Ambit: a state-of-the-art in-memory computing mechanism
Evaluated SIMDRAM configurations (all using a DDR4 device):
  1-bank: SIMDRAM exploits 65’536 SIMD lanes (an 8 kB row buffer)
  4-banks: SIMDRAM exploits 262’144 SIMD lanes
  16-banks: SIMDRAM exploits 1’048’576 SIMD lanes
Notes: [CLICK] We implement SIMDRAM using gem5 simulator
[CLICK] We compare SIMDRAM against three baselines
[CLICK] a multi-core CPU
[CLICK] a high-end GPU
[CLICK] and, Ambit, an state-of-the-art in-DRAM computing mechanism
[CLICK] We evaluate three different configurations of SIMDRAM
[CLICK] 1-bank configuration, where a single DRAM bank is extended to enable SIMDRAM computation. This enables SIMDRAM to execute operations over 64K SIMD lanes
[CLICK] We also evaluate SIMDRAM with four in-DRAM computation enabled banks
[CLICK] And 16 in-DRAM computation enabled banks.
[NEXT]

## Slide 20: Evaluation: Methodology Overview (II)
16 complex in-DRAM operations:
  Absolute - Predication
  Addition/Subtraction - ReLU
  BitCount - AND-/OR-/XOR-Red
  Equality/ Greater/Greater Equal - Division/Multiplication
7 real-world applications
  BitWeaving (databases) - LeNET (Neural Networks)
  TPC-H (databases) - VGG-13/VGG-16 (NNs)
  kNN (machine learning) - brightness (graphics)
Notes: [CLICK] To demonstrate its generality, we evaluate SIMDRAM using
[CLICK] 16 complex in-DRAM operations
And [CLICK] 7 commonly-used real-world applications from various domains
[NEXT]

## Slide 21: Evaluation: Throughput Analysis
Chart: Average Normalized Throughput (GOPS/s) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 5.5 | 0.36 | 1.98
SIMDRAM - 4 Banks | 22 | 1.5 | 7.9
SIMDRAM - 16 Banks | 88.01 | 5.82 | 31.61
SIMDRAM significantly outperforms
all state-of-the-art baselines for a wide range of operations
Average normalized throughput across all 16 SIMDRAM operations
Notes: First, we compare the throughput across all 16 SIMDRAM operations, normalized to the three baselines.
[CLICK] Here, the X axis shows each one of the three baselines we evaluated, and the Y axis shows the average normalized throughput in GigaOPerations per second. We make the following observations.
[CLICK] First, SIMDRAM with a single bank provides 5.5x the throughput of the baseline CPU
[CLICK] This value increases to 22x the throughput of the baseline CPU using four DRAM banks
[CLICK] and to 88x the throughput of the CPU using 16 DRAM banks.
[CLICK] Second, SIMDRAM with a single bank is not enough to outperform the throughput of the GPU.
[CLICK] However, with four DRAM banks, SIMDRAM provides 1.5x the throughput of the GPU
[CLICK] which scales to 5.8x when using 16 DRAM banks.
[CLICK] Third, compared to Ambit, SIMDRAM 1 bank provides 2x Ambit's throughput of Ambit.
[CLICK] While SIMDRAM 4 banks provides 7.9x
[CLICK] And SIMDRAM 16 banks provides 31.6x the throughput of Ambit.
[CLICK] We conclude that SIMDRAM can largely outperform all three state-of-the-art baselines for a wide range of operations
[NEXT]

## Slide 22: Evaluation: Energy Analysis
Average normalized energy efficiency across all 16 SIMDRAM operations
Chart: Average Energy Efficiency (GOPS/s/Watt) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 257 | 31 | 2.6
SIMDRAM - 4 Banks | 257 | 31 | 2.6
SIMDRAM - 16 Banks | 257 | 31 | 2.6
SIMDRAM is more energy-efficient than
all state-of-the-art baselines for a wide range of operations
Notes: Second, we compare the energy efficiency across all 16 SIMDRAM operations, normalized to the three baselines.
[CLICK] Here, the X axis shows each one of the three baselines we evaluated, and the Y axis shows the average normalized energy efficiency in Throughput per Watt. We make the following observations.
[CLICK] SIMDRAM provides 257x the energy efficiency of the CPU baseline,
[CLICK] 31x the energy efficiency of the high-end GPU
[CLICK] And 2.6x the energy efficiency of Ambit
[CLICK] We conclude that SIMDRAM is more energy efficient than all state-of-the-art baselines
[NEXT]

## Slide 23: Evaluation: Real-World Applications
Chart: Average Speedup -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 3 | 0.30612 | 2.5
SIMDRAM - 4 Banks | 8.7 | 0.88776 | 7.25
SIMDRAM - 16 Banks | 21 | 2.1429 | 17.5
SIMDRAM effectively and efficiently accelerates
many commonly-used real-world applications
Average speedup across 7 real-world applications
Notes: Third, we compare the speedup across all 7 real-world applications,
[CLICK] First, SIMDRAM with a single bank provides 3x speedup compared to the baseline CPU
[CLICK] which scales to 8.7x using four DRAM banks and
[CLICK] 21x using all 16 SIMDRAM-capable banks
[CLICK] Second, SIMDRAM with a single bank and
[CLICK] with four banks is not enough to outperform the GPU.
[CLICK] However, by using all 16 SIMDRAM-capable banks, SIMDRAM provides an average speedup of 2.1x compared to the GPU
CLICK] Third, SIMDRAM with a single bank provides 2.5x speedup compared to Ambit
[CLICK] which scales to 7.3x using four DRAM banks and
[CLICK] 17.5x using all 16 SIMDRAM-capable banks
[CLICK] We conclude that SIMDRAM can effectively and efficiently accelerate many commonly used real-world applications.

## Slide 24: Frameworks for PUM: SIMDRAM
Geraldo F. Oliveira, Nastaran Hajinazar, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021.

## Slide 25: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 26: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Starting with the SIMD underutilization
[NEXT]

## Slide 27: Limitations of PUD Systems: Underutilization of SIMD Lanes (I)
Ideal maximum vectorization factor = # DRAM columns (e.g., 65,536)
Application Analysis: quantify the fraction of SIMD parallelism in real applications
Maximum Vectorization Factor:
maximum number of scalar operands that fit into a SIMD register
row decoder
global sense amplifier
Notes: In order to understand the amount of data parallelism a processing-using-DRAM architecture can leverage, we quantify the SIMD parallelism in real applications
[CLICK] To do so, we use the maximum vectorization factor metric, which is the maximum number of scalar operands that fit into a SIMD register a given loop
[CLICK] To achieve high SIMD utilization, the ideal maximum vectorization factor of a loop should match the number of DRAM columns in a DRAM subarray
[NEXT]

## Slide 28: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: In our application analysis, we collect the maximum vectorization of all vectorizable loops in twelve applications, and report their distribution using box plots, where whiskers extend to the maximum and minimum values, and a bubble depicts averages
[CLICK] As a reference, any value above the green line represents high SIMD utilization for a PUD system.
We draw two key observations.
[NEXT]

## Slide 29: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
SIMD parallelism significantly varies within a single application and across different applications
Takeaway
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: [CLICK] First, SIMD parallelism significantly varies within and across applications
[NEXT]

## Slide 30: Limitations of PUD Systems: Underutilization of SIMD Lanes (III)
A small fraction of vectorized loops have a large enough maximum vectorization factor to fully exploit the SIMD parallelism of PUD systems
Takeaway
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: Second, only very few loops have enough data parallelism to achieve high SIMD utilization of the processing-using-DRAM architecture.
[NEXT]

## Slide 31: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Let’s now look at the second issue.
[NEXT]

## Slide 32: Limitations of PUD Systems: Limited Computation Support
row decoder
PUD systems do not support vector reduction at low area cost since data movement is bounded to within a DRAM column
Directly connecting all DRAM columns
using a custom all-to-all interconnect
leads to large (i.e., 21%) area cost
Takeaway
no direct communication path across columns
global sense amplifier
Notes: Processing-using-DRAM can only support parallel map operations. Unfortunally, this limits processing-using-DRAM applicability, since commonly used reduction operations cannot be implemented natively.
The limiting factor to implement in-DRAM vector reduction is the lack of direct communication path across the many DRAM columns in a subarray
[CLICK] directly connecting all DRAM columns using custom fabric leads to large area costs
[NEXT]

## Slide 33: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Third, processing-using-DRAM suffers from a challenging programming model

## Slide 34: Limitations of PUD Systems: Challenging Programming Model
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
 |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Currently, processing-using-DRAM pototypes use assembly-like programming models, which leaves several key tasks for the programmer to manually handle. I will illustrate such tasks with a simple predicated addition/subtraction operation
[NEXT]

## Slide 35: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: A programmer needs to map and align the data structures involved in the computation respecting DRAM’s organization.

## Slide 36: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Identify the array boundaries of the target loops

## Slide 37: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions |  | Just write my kernel
Programmer’s Tasks:
Goal:
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Manually vectorize the target loop, while worrying to feed as many data operands to the DRAM array as possible, for high utilization
[NEXT]

## Slide 38: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: and manually orchestrate data movement across dependent operands.
[NEXT]

## Slide 39: Limitations of PUD Systems: Challenging Programming Model
bbop_trsp_init(A , size , elm_size);
bbop_trsp_init(B , size , elm_size);
bbop_trsp_init(C , size , elm_size);
bbop_add(D , A , B , size , elm_size);
bbop_sub(E , A , B , size , elm_size);
bbop_greater(F , A , pred , size , elm_size);
bbop_if_else(C , D , E , F , size , elm_size);
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
PUD’s assembly-like code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: As a result, the produced processing-using-DRAM code is often complicated and potentially inefficient
[NEXT]

## Slide 40: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 41: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 42: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 43: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 44: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 45: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 46: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 47: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 48: MIMDRAM: Modifications to DRAM Chip
inter-mat
interconnect
row decoder
global wordline
mat range
mat selector
isolation transistors
row decoder latch
IO interface
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 49: MIMDRAM: Control Unit Design
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 50: MIMDRAM: Compiler Support
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 51: MIMDRAM: Compiler Support (I)
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 52: MIMDRAM: Compiler Support (II)
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The first pass is responsible for identifying SIMD parallelism in a code, using LLVM’s auto-vectorization engine, generate PUD instructions and set the best vectorization factor for such PUD instruction
[NEXT]

## Slide 53: MIMDRAM: Compiler Support (II)
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The second pass is responsible for scheduling and mapping computation. Our pass uses metadata to mark independent PUD instructions that should be executed concurrently across mats
[NEXT]

## Slide 54: MIMDRAM: Compiler Support (III)
Generate the appropriate binary for data allocation and PUD instructions
Goal
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: Finally, the third pass is responsible for code generation and data allocation for PUD instructions
[NEXT]

## Slide 55: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware-side
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Our compiler pass relies on the system support we implement for PUD instructions
[NEXT]

## Slide 56: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Notes: Such system support includes ISA extensions, execution and data transposition, data coherence, address translation, data allocation and alignment, and metadata translation
[NEXT]

## Slide 57: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Notes: I will brief discuss our data allocation & alignment routine
[NEXT]

## Slide 58: MIMDRAM: Data Allocation & Alignment
PUD systems require OS support to guarantee that data is properly mapped and aligned within bank/subarray/mat a
→ not a natively supported operation
Virtual Memory
Physical Memory
Operating System
Memory Controller
Pages
Frames
DRAM Rows
Memory Allocator
DRAM Interleaving
huge pages
memalign
malloc
Notes: MIMDRAM requires data from PUD operations to map to the target DRAM mats correctly.
To allow the memory allocator to influence the physical data location for PUD operations, we implement a new memory allocator that leverages huge pages and reversed-engineered DRAM inter;eaving information for PUD memory objects.

## Slide 59: MIMDRAM: Data Allocation & Alignment
MIMDRAM’s memory allocator uses a pool of huge pages and reversed-engineered DRAM interleaving information for PUD memory objects
Notes: MIMDRAM requires data from PUD operations to map to the target DRAM mats correctly.
To allow the memory allocator to influence the physical data location for PUD operations, we implement a new memory allocator that leverages huge pages and reversed-engineered DRAM inter;eaving information for PUD memory objects.

## Slide 60: MIMDRAM: More in the Paper & GitHub
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
https://arxiv.org/pdf/2402.19080.pdf
https://github.com/CMU-SAFARI/MIMDRAM
Notes: For more details, please, check our paper
[NEXT]

## Slide 61: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 62: More on MIMDRAM
Geraldo F. Oliveira, Ataberk Olgun, Abdullah Giray Yağlıkçı, F. Nisa Bostancı, Juan Gómez-Luna, Saugata Ghose, and Onur Mutlu " MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.19080.pdf

## Slide 63: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: reduce the bit-precision of a PUD operation
2
Throughput-Oriented Execution
failing to reduce the latency of a single PUD operations
opportunity 2: use SALP to concurrently execute PUD primitives
3
High-Precision Computation
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: use alternative data representation for high-precision PUD operations

## Slide 64: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: reduce the bit-precision of a PUD operation
2
Throughput-Oriented Execution
failing to reduce the latency of a single PUD operations
opportunity 2: use SALP to concurrently execute PUD primitives
3
High-Precision Computation
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: use alternative data representation for high-precision PUD operations

## Slide 65: Limitations of PUD Systems: Static Data Representation (I)
Application Analysis: quantify the required bit-precision in real applications
Applications display a significant amount of narrow values → bit-precision can be reduced from 32-bit to 20-bit (min. 8-bit, max. 30 bit) on average
Takeaway
Notes: By
doing so, the performance of the underlying PUD architecture
can improve by 1.6×, in case the application utilizes linearlyscaling PUD operations (such as addition), or 2.6×, in case the
application utilizes quadratically-scaling PUD operations (such
as multiplication).

## Slide 66: Limitations of PUD Systems: Static Data Representation (II)
Application Analysis: quantify the required bit-precision in real applications
Bit-precision significantly varies for a given application → indicates the need for a mechanism that can dynamically identify the target bit-precision
Takeaway
Notes: In order to understand the amount of data parallelism a processing-using-DRAM architecture can leverage, we quantify the SIMD parallelism in real applications
[CLICK] To do so, we use the maximum vectorization factor metric, which is the maximum number of scalar operands that fit into a SIMD register a given loop
[CLICK] To achieve high SIMD utilization, the ideal maximum vectorization factor of a loop should match the number of DRAM columns in a DRAM subarray
[NEXT]

## Slide 67: Limitations of PUD Systems: Static Data Representation (III)
Application Analysis: quantify the required bit-precision in real applications
By dynamically adjusting the bit-precision of a PUD operation, we can improve the performance of bit-serial PUD operations (by 1.6x to 2.6x)
Key Idea
Notes: In order to understand the amount of data parallelism a processing-using-DRAM architecture can leverage, we quantify the SIMD parallelism in real applications
[CLICK] To do so, we use the maximum vectorization factor metric, which is the maximum number of scalar operands that fit into a SIMD register a given loop
[CLICK] To achieve high SIMD utilization, the ideal maximum vectorization factor of a loop should match the number of DRAM columns in a DRAM subarray
[NEXT]

## Slide 68: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: reduce the bit-precision of a PUD operation
2
Throughput-Oriented Execution
failing to reduce the latency of a single PUD operations
opportunity 2: use SALP to concurrently execute PUD primitives
3
High-Precision Computation
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: use alternative data representation for high-precision PUD operations

## Slide 69: Limitations of PUD Systems: Throughput-Oriented Execution
PUD architectures favor a throughput-oriented execution, as DRAM parallelism can partially hide the latency of DRAM ACTs
Notes: By
doing so, the performance of the underlying PUD architecture
can improve by 1.6×, in case the application utilizes linearlyscaling PUD operations (such as addition), or 2.6×, in case the
application utilizes quadratically-scaling PUD operations (such
as multiplication).

## Slide 70: Limitations of PUD Systems: Throughput-Oriented Execution
PUD architectures favor a throughput-oriented execution, as DRAM parallelism can partially hide the latency of DRAM ACTs
Several primitives in a PUD operation can be executed concurrently, as they are independent of one another
Key Idea
Notes: By
doing so, the performance of the underlying PUD architecture
can improve by 1.6×, in case the application utilizes linearlyscaling PUD operations (such as addition), or 2.6×, in case the
application utilizes quadratically-scaling PUD operations (such
as multiplication).

## Slide 71: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: reduce the bit-precision of a PUD operation
2
Throughput-Oriented Execution
failing to reduce the latency of a single PUD operations
opportunity 2: use SALP to concurrently execute PUD primitives
3
High-Precision Computation
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: use alternative data representation for high-precision PUD operations

## Slide 72: Limitations of PUD Systems: High-Precision Computation
For operations that require high precision, PUD architectures suffer from high latency
Notes: By
doing so, the performance of the underlying PUD architecture
can improve by 1.6×, in case the application utilizes linearlyscaling PUD operations (such as addition), or 2.6×, in case the
application utilizes quadratically-scaling PUD operations (such
as multiplication).

## Slide 73: Limitations of PUD Systems: High-Precision Computation
For operations that require high precision, PUD architectures suffer from high latency
Use a positional number system representation, i.e., the redundant binary representation (RBR) for high-precision PUD operations:
the operation no longer needs to propagate carry bits
the operation latency is independent of the data precision
Key Idea
Notes: By
doing so, the performance of the underlying PUD architecture
can improve by 1.6×, in case the application utilizes linearlyscaling PUD operations (such as addition), or 2.6×, in case the
application utilizes quadratically-scaling PUD operations (such
as multiplication).

## Slide 74: Proteus: Design Overview (I)
1
Parallelism-Aware uProgram Library
hand-optimized implementations of different PUD operations with different performance vs. bit-precision trade-offs
2
Dynamic Bit-Precision Engine aims to identify the dynamic range of memory objects associated with a PUD operation
3
uProgram Select Unit aims to identify the appropriate bit-precision based on the input operations of the target PUD operation
  Proteus is composed of three main components:
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 75: Proteus: Design Overview (II)
1
Parallelism-Aware uProgram Library
hand-optimized implementations of different PUD operations with different performance vs. bit-precision trade-offs
2
Dynamic Bit-Precision Engine aims to identify the dynamic range of memory objects associated with a PUD operation
3
uProgram Select Unit aims to identify the appropriate bit-precision based on the input operations of the target PUD operation
  Proteus is composed of three main components:
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 76: Proteus: Design Overview (III)
1
Parallelism-Aware uProgram Library
hand-optimized implementations of different PUD operations with different performance vs. bit-precision trade-offs
2
Dynamic Bit-Precision Engine aims to identify the dynamic range of memory objects associated with a PUD operation
3
uProgram Select Unit aims to identify the appropriate bit-precision based on the input operations of the target PUD operation
  Proteus is composed of three main components:
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 77: Proteus: Design Overview (IV)
1
Parallelism-Aware uProgram Library
hand-optimized implementations of different PUD operations with different performance vs. bit-precision trade-offs
2
Dynamic Bit-Precision Engine aims to identify the dynamic range of memory objects associated with a PUD operation
3
uProgram Select Unit aims to identify the appropriate bit-precision based on the input operations of the target PUD operation
  Proteus is composed of three main components:
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 78: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU (with and without Tensor Cores)
  PUD: SIMDRAM [Oliveira+, 2021]
Workloads:
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  495 multi-programmed application mixes
Notes: We compared MIMDRAM to a high-end CPU and GPU, two state-of-the-art PUD systems that use large DRAM access for computation, and a processing-near-DRAM architecture.
[CLICK] In our analyses, we use 12 workloads from four benchmark suites and 495 application mixes from such workloads
[CLICK] We perform a two-level analysis. For single applications, MIMDRAM can leverage its intra-application data parallelism and for multiple applications, MIMDRAM leverages inter-application data parallelism
[NEXT]

## Slide 79: Evaluation: Performance Analysis
Proteus significantly improves performance/mm2 compared to CPU (17x), GPU (7.3x), and SIMDRAM (10.2x)
Takeaway
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 80: Evaluation: Energy Analysis
Proteus significantly improves energy-efficiency compared to CPU (90.3x), GPU (21x), and SIMDRAM (8.1x)
Takeaway
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 81: More on Proteus
Geraldo F. Oliveira, Mayank Kabra, Yuxin Guo, Kangqi Chen, A. Giray Yağlıkçı, Melina Soysal, Mohammad Sadrosadati, Joaquin Olivares Bueno, Saugata Ghose, Juan Gómez-Luna, Onur Mutlu “Proteus: Achieving High-Performance Processing-Using-DRAM via Dynamic Precision Bit-Serial Arithmetic” arXiv, 2025.
https://arxiv.org/pdf/2501.17466

## Slide 82: In-DRAM Lookup-Table Based Execution
João Dinis Ferreira, Gabriel Falcao, Juan Gómez-Luna, Mohammed Alser, Lois Orosa, Mohammad Sadrosadati, Jeremie S. Kim, Geraldo F. Oliveira, Taha Shahroodi, Anant Nori, and Onur Mutlu, "pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (26 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2104.07699.pdf

## Slide 83: The Goal of pLUTo
Extend Processing-using-DRAM to support the execution of arbitrarily complex operations
Notes: STATED PLAINLY, THE GOAL OF PLUTO IS THUS, PRECISELY, TO **EXTEND**…

## Slide 84
x
pLUTo: Key Idea
?
output
x
input
x
ALU
f(x)
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 85
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 86
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 87
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
0
1
2
3
row buffer
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 88
row buffer
row decoder
0
1
2
3
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
2
3
5
7
2
3
5
7
2
3
5
7
Multiple copies of the lookup table
→ exploit DRAM parallelism
2
3
5
7
2
3
5
7
DRAM array
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 89
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
pLUTo
row sweep
DRAM array
row buffer
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 90
0
0
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 91
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
match logic
Accessing
the 2nd (1) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 92
match logic
Accessing
the 2nd (1) prime number?
input
vector
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
input
vector
row buffer
pLUTo
row sweep
0 = 1 ?
1
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 93
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
?
𝘅
input
vector
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 94
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
𝘅
input
vector
input
vector
row buffer
Accessing
the 1st (0) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 95
input
vector
Accessing
the 1st (0) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
row buffer
𝘅
0
pLUTo
row sweep
0 = 0 ?
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 96
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 97
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 98
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
input
vector
?
✓
𝘅
input
vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 99
Accessing
the 4th (3) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
?
✓
𝘅
𝘅
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 100
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
3 | 3 | 3 | 3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 101
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 102
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 103
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 104
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 105
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
3
𝘅
𝘅
1
2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
𝘅
𝘅
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 106
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
7 | 7 | 7 | 7
3 | 2 | 3 | -
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 107
0
1
2
3
output
vector
3 | 2 | 3 | -
- | - | - | -
7 | 7 | 7 | 7
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
𝘅
✓
𝘅
7
𝘅
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 108
0
1
2
3
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
7 | 7 | 7 | 7
𝘅
✓
𝘅
𝘅
3 | 2 | 3 | -
7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 109
System Integration
C-Like Code with
pLUTo API calls
Assembly Code with pLUTo ISA Extensions
Execution in the DRAM Substrate
pLUTo Compiler
pLUTo Controller
api_pluto_mul
pluto_subarray_alloc
pluto_bit_shift_l
pluto_or
pluto_op
ACT
PRE
ACT
ACT
PRE
...

## Slide 110
Average speedup normalized to area across 7 real-world workloads
Performance (normalized to area)
Chart: Average Speedup per Unit Area
| CPU | GPU | PnM
pLUTo-GSA | 426 | 441
pLUTo-BSA | 801 | 830
pLUTo-GMC | 1504 | 1558
pLUTo provides substantially higher performance per unit area than both the CPU and the GPU

## Slide 111
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 112: More Results in the Paper
Comparison with FPGA
Area Overhead Analysis
Circuit-Level Reliability & Correctness
Subarray-Level Parallelism
LUT Loading Overhead
Range of Supported Operations
https://arxiv.org/pdf/2104.07699.pdf

## Slide 113: SRC TECHCON Presentation
Geraldo F. Oliveira
  pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables
  https://arxiv.org/pdf/2104.07699.pdf
https://youtu.be/9t1FJQ6nNw4?si=bhylWCLZde2DC7os

## Slide 114: Bulk Bitwise Operations in Real DRAM Chips
Ismail Emir Yüksel, Yahya Can Tugrul Ataberk Olgun, F. Nisa Bostancı, A. Giray Yaglıkçı, Geraldo F. Oliveira, Haocong Luo, Juan Gómez-Luna, Mohammad Sadrosadati, Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis," Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.18736

## Slide 115: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 116: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 117: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 118: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 119: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 120: 1st Workshop on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025