## Slide 1: 1st Workshop on Memory-Centric Computing: Research Challenges & Closing Remarks
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025

## Slide 2: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 3: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 4: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 5: Adoption: How to Keep It Simple?
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 6: Adoption: How to Ease Programmability? (I)
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu, “DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” in PACT SRC Student Competition, Vienna, Austria, October 2023.

## Slide 7: Adoption: How to Ease Programmability? (II)
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, YuXin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 8: Adoption: How to Maintain Coherence? (I)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 9: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 10: Adoption: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 11: Adoption: How to Support Synchronization?
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 12: Adoption: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 13: Adoption: Code and Data Mapping
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 14: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 15: Identifying Memory Bottlenecks
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
9
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]

## Slide 16: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Compute Roof
y = Peak System Throughput
Memory Roof
y = BW x AI
Compute Bound →
Not suitable for NDP
Memory Bound →
Suitable for NDP
10
Notes: A roofline model is a simple model used to identify if an application is memory-bound or compute-bound. The x-axis of the plot defines the Arithmetic Intensity of an application, calculated as the number of Operations the application executes per byte it accesses. The y-axis defines the performance of the application in GOPS/s
[CLICK] it has two main lines that characterizes the application and system. The first line is called Compute Roof, and it is defined as the maximum peak system throughput. Applications below this curve are called compute-bound. Prior works show that a compute bound application does not benefit from NDP
[CLICK] The second line is called memory roof. It is defined as the maximum DRAM bandwidth times the arithmetic intensity of the application. Prior works show that an application below this curve are memory-bound, and are suitable for NDP offloading.
[NEXT]

## Slide 17: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
11
Notes: We use this model with more than 40 applications that we will analyze later. We compare when such applications benefits from a general purpose NDP architecture.
In the plot, we classify the applications as:
[CLICK] Runs faster on the CPU, compared to running on the NDP system
[CLICK] Runs faster on the NDP, compared to running on the CPU system
[CLICK] Similar on CPU and NDP, when running an application on the NDP and host system achieves similar performance.
[CLICK] And depends, when application benefits from NDP depending on system configuration (e.g., core count) compared to a regular host system.
[CLICK] Based on that, we make the following observations.
[NEXT]

## Slide 18: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Memory Bound applications are
faster on NDP
Compute Bound applications
are faster on CPU
Memory Bound applications
are faster on CPU,
or performance depends ❌
Compute Bound applications
have similar performance on CPU/NDP or performance depends ❌
12
✓
✓
Notes: First, memory bound applications benefit from NDP, as prior works indicated
[CLICK] Second, compute bound applications do not benefit from NDP, also as indicated by prior works
[CLICL] However, we observe that some memory bound applications can also not benefit from NDP, or benefit from it in particular configurations (at different core counts for example)
[CLICK] This behavior also happens for compute bound applications [NEXT]

## Slide 19: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Memory Bound applications are
faster on NDP
Compute Bound applications
are faster on CPU
Memory Bound applications
are faster on CPU,
or performance depends ❌
Compute Bound applications
have similar performance on CPU/NDP or performance depends ❌
13
✓
✓
  Roofline model does not accurately account
  for the NDP suitability of memory-bound applications
Notes: [CLICK] Therefore, we conclude that the roofline model cannot accurately account for NDP suitability of memory-bound applications
[NEXT]

## Slide 20: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
14
LLC MPKI
NDP Speedup over CPU
Notes: Next, we analyze another metric utilized to indicate NDP suitability. Prior works say that an application with high LLC MPKI (usually a value higher than 10) benefits from NDP. We checked this observation by evaluating the speedup provided by NDP for of a large number of application (in the y-axis), and the applications MPKI (in the x-axis). We make the following observations
[NEXT]

## Slide 21: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
Applications with
high MPKI are
faster on NDP
Applications with
low MPKI are
faster on CPU
Applications with low MPKI can be
faster on NDP;
have similar performance on
CPU/NDP or;
performance can depends ❌
15
✓
✓
LLC MPKI
NDP Speedup over CPU
Notes: First, as expected, applications with high last-level misses per-kilo instructions always benefit from NDP.
[CLICK] Likewise, applications with low MPKI never benefit from NDP
[CLICK] However, we observe that applications with low MPKI can either benefit from NDP depending on the system configuration or they can have similar performance as the NDP system
[NEXT]

## Slide 22: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
Applications with
high MPKI are
faster on NDP
Applications with
low MPKI are
faster on CPU
Applications with low MPKI can be
faster on NDP;
have similar performance on
CPU/NDP or;
performance can depends ❌
16
✓
✓
LLC MPKI
NDP Speedup over CPU
  LLC MPKI does not accurately account
  for the NDP suitability of memory-bound applications
Notes: [CLICK] Therefore, we conclude that the MPKI alone cannot accurately account for NDP suitability of memory-bound applications
[NEXT]

## Slide 23: Identifying Memory Bottlenecks
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
17
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
Notes: [NEXT]

## Slide 24: The Problem
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
18
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
  No available methodology can comprehensively:
  − identify data movement bottlenecks
  − correlate them with the most suitable data movement mitigation mechanism
Notes: To summarize, different approaches used by prior works to identify memory bottlenecks and NDP suitability are not comprehensive enough in
[CLICK] identifying data movement bottlenecks
[CLICK] correlating different data movement mitigation mechanisms, as NDP, with the different types of data movement bottlenecks.
[NEXT]

## Slide 25: Our Goal
Our Goal: develop a methodology to:
    methodically identify sources of data movement bottlenecks
    comprehensively compare compute- and memory-centric data movement mitigation techniques
19
Notes: THEREFORE, our goal is to develop a methodology to
[CLICK] methodically identify the major sources of inefficiency that lead to data movement bottlenecks by observing and identifying relevant metrics and
[CLICK] comprehensively compare traditional compute-centric data movement mitigation techniques to more memory-centric techniques, thereby developing a rigorous understanding of the best techniques to mitigate each source of data movement.
[NEXT]

## Slide 26: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
264
Notes: Our methodology has three steps.
[CLICK] It takes as input an application’s source code and its input datasets.
[CLICK] In Step 1, we use a hardware profiling tool to identify memory-bound functions across many applications. This step allows for a quick first-level identification of many applications that suffer from memory bottlenecks and functions that cause these bottlenecks.
[CLICK] We utilize a new simulator, called DAMOV-SIM to collect key metrics and execute performance analysis of the functions identified in Step 1.
[CLICK] In Step 2, we use the architecture-independent profiling tool to collect metrics that provide insights about the memory access behavior of the memory-bottlenecked functions.
[CLICK] In Step 3, we collect architecture-dependent metrics and analyze the performance and energy of each function in an application when each of our three candidate data movement mitigation mechanisms is applied to the system.
[CLICK] By combining the data obtained from all three steps, we can systematically classify the leading causes of data movement bottlenecks in an application or function into different bottleneck classes
[NEXT]

## Slide 27: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
265
Notes: So let’s check the first step
[NEXT]

## Slide 28: Step 1: Application Profiling
Goal: Identify application functions that suffer from data movement bottlenecks
266
Physics
Security
Machine learning
Database
Graph processing
Data analytics
Data reorganization
Genomics
Deep Neural Networks
Image processing
Linear algebra
Signal processing
Data mining
Hardware Profiling Tool:
Intel VTune
MemoryBound:
CPU is stalled due to load/store
Notes: [CLICK] The goal of the first step is to identify functions in an application that suffers from memory bottlenecks
[CLICK] To profile the applications and identify functions that suffer from data movement bottlenecks
[CLICK] we use a hardware profiling tool. In this work, we decided to use Intel Vtune
[CLICK] Intel Vtune provides a metric called Memory bound, which is defined as the percentage of CPU pipeline slots that are not utilized because of memory stalls.
[NEXT]

## Slide 29: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
267
Notes: Let's give a look to the second step.
[NEXT]

## Slide 30: Step 2: Locality-Based Clustering
Low spatial locality
Goal: analyze application’s memory characteristics
Stride Profile (bin)
…
1
2
4
8
16
32
2N
Frequency (count)
Stride Profile Histogram
High spatial locality
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
stride profile(1)+= 1
0
1
2
3
4
5
Memory Trace
Spatial Locality7
[7] Weinberg+, “Quantifying Locality in the Memory Access Patterns of HPC Applications,” SC, 2005
268
Notes: In Step 2, we aim to analyze application’s memory characteristics, as locality, thus we could understand how it affects the components of the memory system, as cache behavior or prefetching. To this end, we evaluate two key metrics.
[CLICK] We first evaluate spatial locality from an application.
[CLICK] For this, we collect the memory trace of an application
[CLICK] To build a histogram called the stride profile, where each bin stores how many times each stride appear in the memory trace.
[CLICK] In this example, the stride between the first accessed address and the next accessed address is equal to 1. We increment a stride profile histogram in bin 1 to indicate such stride has been observed.
[CLICK] We use the stride profile histogram to calculate the cumulative distribution of stride profiles, which represents the final spatial locality value.
[CLICK] A spatial locality value close to 0 is caused by large stride values or random accesses, as shown in this example. In such case, we say the application has low spatial locality
[CLICK] A spatial locality value close to 1 is caused by a completely sequential access pattern. . In such case, we say the application has high spatial locality
[NEXT]

## Slide 31: Step 2: Locality-Based Clustering
Low spatial locality
Goal: analyze application’s memory characteristics
…
1
2
4
8
16
32
2N
Reuse Profile (bin)
Frequency (count)
Reuse Profile Histogram
High temporal locality
…
1
2
4
8
16
32
2N
Reuse Profile (bin)
Frequency (count)
Reuse Profile Histogram
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
High spatial locality
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
stride profile(1)+= 1
0
1
2
3
4
5
Memory Trace
reuse profile(4)+= 1
A
A
A
A
Memory Trace
Spatial Locality7
Temporal Locality7
[7] Weinberg+, “Quantifying Locality in the Memory Access Patterns of HPC Applications,” SC, 2005
269
Low temporal locality
Notes: [CLICK] Similarly, we evaluate how much temporal locality an application has.
[CLICK] For this, we collect the memory trace of an application
[CLICK] to create a histogram called reuse profile, where each bin represents the number of times a memory address is reused. For each memory address, we increment the bin that represents the corresponding number of repetitions.
[CLICK] In this example, memory address A is reused 4 times. Thus, we increment the reuse profile histogram in bin 4 to indicate such reuse has been observed.
[CLICK] We use the reuse profile histogram to calculate the cumulative distribution of rese profiles, which represents the final temporal locality value.
[CLICK] A temporal locality value close to 0 is caused by low data reuse. In such case, we say the application has low temporal locality
[CLICK] A temporal locality value close to 1 is caused by high data reuse/ In such case, we say the application has high temporal locality
[NEXT]

## Slide 32: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
270
Notes: Finally, let's look deeper into Step 3 of our methodology
[NEXT]

## Slide 33: Step 3: Memory Bottleneck Classification (1/2)
Arithmetic Intensity (AI)
- floating-point/arithmetic operations per L1 cache lines accessed
→ shows computational intensity per memory request
LLC Misses-per-Kilo-Instructions (MPKI)
- LLC misses per one thousand instructions
→ shows memory intensity
Last-to-First Miss Ratio (LFMR)
- LLC misses per L1 misses
→ shows if an application benefits from L2/L3 caches
271
Notes: While Step 2 allows us to understand inherent application sources for memory boundedness, it is important to understand how hardware architectural features can also result in memory bottlenecks. As a result, in our third step we perform a scalability analysis of the functions selected in Step 1, where we evaluate performance and energy scaling for three different system configurations. The scalability analysis makes use of three architecture-dependent metrics:
[CLICK] First, Arithmetic Intensity (AI), defined as the number of arithmetic and logic operations performed per L1 cache line accessed.
[CLICK] This metric indicates how much computation there is per memory request. Intuitively, applications with high AI are likely to be computationally intensive, while applications with low AI tend to be memory intensive
[CLICK] Second, Misses per Kilo-Instruction (MPKI), defined as the number of LLC misses per one thousand instructions.
[CLICK] This metric is considered to be a good indicator of NDP suitability by several prior works since it indicates memory intensity of an application.
[CLICK] and third, a new metric called Last-to-First Miss-Ratio (LFMR) define as the ratio between the number of LLC misses and the total number of L1 cache misses.
[CLICK] We find that this metric accurately identifies how much an application benefits from the deep cache hierarchy. An LFMR value close to 0 means that the number of LLC misses is very small compared to the number of L1 misses. However, an LFMR value close to 1 means that very few L1 misses hit in L2 or L3 caches, and the application does not benefit much from the deep cache hierarchy, and most L1 misses need to be serviced by main memory
[NEXT]
[NEXT]

## Slide 34: Step 3: Memory Bottleneck Classification (2/2)
Goal: identify the specific sources of data movement bottlenecks
DAMOV-SIM Simulator
# Cores
Scalability Analysis
Integrated ZSim and Ramulator
Scalability Analysis:
  1, 4, 16, 64, and 256 out-of-order/in-order host and NDP CPU cores
  3D-stacked memory as main memory
Configuration 2: NDP System
Off-chip link
DRAM
CPU
CPU
CPU
L2
L1
L3
L2
L1
L2
L1
L2
L1
CPU
Configuration 1: Host CPU System
Off-chip link
272
DAMOV-SIM: https://github.com/CMU-SAFARI/DAMOV
…
Logic Layer
CPU
CPU
CPU
L1
L1
L1
L1
CPU
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Notes: [CLICK] The goal of the scalability analysis we perform is to nail down the specific sources of data movement bottlenecks in the application.
In this analysis, we evaluate the performance and energy scaling of an application in three different system configurations; and collect the key metrics for our bottleneck classification
[CLICK] During scalability analysis, we simulate three system configurations of a general-purpose multicore processor. To this end, we build a framework that integrates the ZSim CPU simulator with the Ramulator memory simulator to produce a fast, scalable, and cycle-accurate open-source simulator called DAMOV-SIM. We use ZSim to simulate the core microarchitecture, cache hierarchy, coherence protocol, and prefetchers. We use Ramulator to simulate the DRAM architecture, memory controllers, and memory accesses.
[CLICK] The first configuration we evaluate is of a host CPU with a deep cache hierarchy, with a 32 KB, private L1 cache, a 256 KB private L2 cache, and a shared 8MB L3 cache.
[CLICK] The second configuration is of an NDP CPU with only a private read-only L1 cache of 32 KB.
In our paper we evaluate an third configuration that includes hardware prefetcher on top of configuration 1. However, we omit such configuration in this talk.
The remaining components of the processor configuration are kept the same to isolate the impact of only the caches, prefetchers, and NDP.
This way, we expect that the performance and energy differences between the three configurations to come exclusively from the different data movement requirements.
[CLICK] For all configurations, we sweep the number of CPU cores in our analysis from 1 to 256, as previous works show that large core counts are necessary to saturate the bandwidth provided by modern high-bandwidth memories, and because modern CPUs and NDP proposals can have varying core counts.
[CLICK] We simulate a memory architecture similar to the Hybrid Memory Cube device where the host CPU accesses memory through a high-speed off-chip link,
[CLICK] and the NDP logic resides in the logic layer of the memory chip and has direct access to the DRAM banks, thus taking advantage of higher memory bandwidth and lower memory latency.
[NEXT]

## Slide 35: Step 3: Memory Bottleneck Analysis
Temporal Locality
Low
High
LFMR
Decreasing
High
MPKI
High
AI
AI
MPKI
AI
LFMR
MPKI
MPKI
Low
Increasing
AI
AI
Low
Low
Low
Low
High
Low
Low
Low
Low
Low
1a: DRAM Bandwidth
1b: DRAM Latency
1c: L1/L2
Cache Capacity
2a: L3 Cache Contention
2c: Compute-Bound
2b: L1 Cache Capacity
Memory Bottleneck Class
  Six classes of
  data movement bottlenecks:
  each class ↔ data movement
  mitigation mechanism
Notes: [CLICK] With such classification, we analyze how the functions in each class correlates with different data movement mitigation mechanisms in terms of performance and energy using our scalability analysis.
[NEXT]

## Slide 36: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 37: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 38: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 39: More on DAMOV Methods & Benchmarks
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 40: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 41: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 42: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 43: Concluding Remarks
We must design systems to be balanced, high-performance, energy-efficient (all at the same time)  intelligent systems
  Data-centric, data-driven, data-aware
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Future of truly memory-centric computing is bright
  We need to do research & design across the computing stack
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 44: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 45: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 46: We Need to Exploit Good Principles
Data-centric system design
All components intelligent
Better (cross-layer) communication, better interfaces
Better-than-worst-case design
Heterogeneity
Flexibility, adaptability
Open minds

## Slide 47: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 48: Special Research Sessions & Courses (I)
Special Session at ISVLSI 2022: 9 cutting-edge talks
https://www.youtube.com/watch?v=qeukNs5XI3g

## Slide 49: Special Research Sessions & Courses (II)
Special Session at ISVLSI 2022: 9 cutting-edge talks
https://www.youtube.com/playlist?list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy

## Slide 50: Processing-in-Memory Course (Fall 2024)
Short weekly lectures
Hands-on projects
https://safari.ethz.ch/projects_and_seminars/fall2024/doku.php?id=processing_in_memory
https://www.youtube.com/playlist?list=PL5Q2soXY2Zi9DSQg7OAlsNO8dOQKxF9sl

## Slide 51: Processing-in-Memory Course (Spring 2023)
https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=processing_in_memory
https://www.youtube.com/playlist?list=PL5Q2soXY2Zi_EObuoAZVSq_o6UySWQHvZ
Short weekly lectures
Hands-on projects

## Slide 52: PIM Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=processing_in_memory
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=QLL0wQ9I4Dw&list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures
52

## Slide 53: Real PIM Tutorials [ISCA’23, ASPLOS’23, HPCA’23]
June, March, Feb : Lectures + Hands-on labs + Invited talks
https://events.safari.ethz.ch/isca-pim-tutorial/

## Slide 54: Real PIM Tutorial [ISCA 2023]
June 18: Lectures + Hands-on labs + Invited talks
https://events.safari.ethz.ch/isca-pim-tutorial/
https://www.youtube.com/live/GIb5EgSrWk0

## Slide 55: Real PIM Tutorial [ASPLOS 2023]
https://events.safari.ethz.ch/asplos-pim-tutorial/
March 26: Lectures + Hands-on labs + Invited talks
https://www.youtube.com/watch?v=oYCaLcT0Kmo

## Slide 56: Real PIM Tutorial [HPCA 2023]
February 26: Lectures + Hands-on labs + Invited Talks
https://www.youtube.com/watch?v=f5-nT1tbz5w
https://events.safari.ethz.ch/real-pim-tutorial/

## Slide 57
October 29: Lectures + Hands-on labs + Invited talks
https://events.safari.ethz.ch/micro-pim-tutorial
https://www.youtube.com/ live/ohU00NSIxOI
Real PIM Tutorial [MICRO 2023]

## Slide 58: PIM Tutorial at HEART 2024
  https://events.safari.ethz.ch/heart24-memorycentric-tutorial

## Slide 59: PIM Tutorial at ISCA 2024
https://events.safari.ethz.ch/isca24-memorycentric-tutorial

## Slide 60: PIM Tutorial at MICRO 2024
https://events.safari.ethz.ch/micro24-memorycentric-tutorial

## Slide 61: PIM Tutorial at PPoPP 2025

## Slide 62: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 63: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 64: 1st Workshop on Memory-Centric Computing: Research Challenges & Closing Remarks
Geraldo F. Oliveira
https://geraldofojunior.github.io
ASPLOS 2025
30 March 2025