## Slide 1: 1st Workshop on Memory-Centric Computing: Storage-Centric Computing
Mohammad Sadrosadati
m.sadr89@gmail.com
ASPLOS 2025
30 March 2025

## Slide 2: Goal: Processing Inside Memory/Storage
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory/Storage
Database
Graphs
Media
ML Model
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 3: Processing in Memory: Two Types
1. Processing near Memory
2. Processing using Memory

## Slide 4: Storage-Centric Computing: Two Types
1. Processing near Storage
2. Processing using Storage

## Slide 5: Flash-Cosmos: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 6: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 7: Bulk Bitwise Operations
Bulk Bitwise Operations
Web Search
Cryptography
Set Operations
Genome Analysis
Databases
Graph Processing
Hyper-dimensional
Computing
...

## Slide 8: Bulk Bitwise Operations
Bulk Bitwise Operations
Web Search
Cryptography
Set Operations
Genome Analysis
Databases
(database queries and indexing)
Graph Processing
Hyper-dimensional
Computing
...
Data movement between compute units and the memory hierarchy significantly affects the performance of bulk bitwise operations

## Slide 9: Data-Movement Bottleneck
Conventional systems perform outside-storage processing (OSP) after moving the data to host CPU through the memory hierarchy
Host Processor
(CPU, GPU)
Main
Memory
Write
Read
Storage
Write
Read
Memory Bandwidth tens to hundreds of GB/s
Storage I/O Bandwidth ~ 8 GB/s
Data Movement Bottleneck
The external I/O bandwidth of storage is the main bottleneck for data movement in OSP
Computation

## Slide 10: NDP for Bulk Bitwise Operations
Near-Data
Processing
Cache
(e.g., Compute Cache1)
DRAM-based
main memory
(e.g., Ambit2)
In-Storage
(e.g., Biscuit4)
NVM-based
main memory
(e.g., Pinatubo3)
[1] Aga+, “Compute Caches," HPCA, 2017
[2] Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO, 2017
[3] Li+, “Pinatubo: A Processing-in-Memory Architecture for Bulk Bitwise Operations in Emerging Non-Volatile Memories,” DAC, 2016
[4] Gu+, “Biscuit: A Framework for Near-Data Processing of Big Data Workloads,” ISCA, 2016
[5] Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021
In-Flash
(e.g., ParaBit5)
...
Our focus
Large data sets
that do not fit
in main memory

## Slide 11: In-Storage Processing (ISP)
ISP performs computation using an in-storage computation unit
ISP reduces external data movement by transferring only the computation results to the host
Host Processor
(CPU, GPU)
Main
Memory
Read
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Write
Read
Write
Write
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Movement Bottleneck
Computation

## Slide 12: In-Storage Processing (ISP)
ISP performs computation using the in-storage computation unit
ISP reduces external data movement by transferring only the computation results to the host
Processor
(CPU, GPU)
Main
Memory
Read
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Write
Read
Write
Write
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Movement Bottleneck
Storage internal I/O bandwidth is the main bottleneck for data movement in ISP

## Slide 13: In-Flash Processing (IFP)
IFP performs computation within the flash chips as the data operands are being read serially
IFP reduces the internal data movement bottleneck in storage by transferring only the computation results to the in-storage computation unit
Host Processor
(CPU, GPU)
Main
Memory
Read
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Write
Read
Write
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Sensing Bottleneck
Computation
Write

## Slide 14: In-Flash Processing (IFP)
IFP performs computation within the flash chips as the data operands are being read serially
IFP reduces the internal data movement bottleneck in storage by transferring only the computation results to the in-storage computation unit
Host Processor
(CPU, GPU)
Main
Memory
Read
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Write
Read
Write
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Sensing Bottleneck
Computation
Write
IFP fundamentally mitigates the data movement

## Slide 15: Data Sensing Bottleneck in IFP
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
Page Buffer
Operand A
Operand B
Operand C
Operand D
…
[1] Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021

## Slide 16: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
A
B
…
C
D
Page Buffer
Data Sensing
A
A

## Slide 17: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
A
B
…
C
D
Page Buffer
A
B
Data Sensing
A AND B

## Slide 18: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
NAND Flash Chip
A
B
…
C
D
Page Buffer
A AND B
Data Sensing
C
A AND B AND C

## Slide 19: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
NAND Flash Chip
A
B
…
C
D
Page Buffer
A AND B
Data Sensing
C
A AND B AND C
Serial data sensing is the bottleneck in prior in-flash processing techniques

## Slide 20: Reliability Issues in IFP
Prior IFP approaches cannot leverage ECC and data-randomization techniques as computation is performed within the flash chips during data sensing
A
NAND Flash Chip
A
B
…
C
D
Page Buffer

## Slide 21: Reliability Issues in IFP
Prior IFP approaches cannot leverage ECC and data-randomization techniques as computation is performed within the flash chips during data sensing
NAND Flash Chip
B
…
C
D
Page Buffer
A
Data Sensing
B
A

## Slide 22: Reliability Issues in IFP
Prior IFP approaches cannot leverage ECC and data-randomization techniques as computation is performed within the flash chips during data sensing
NAND Flash Chip
B
…
C
D
Page Buffer
A
A
Data Sensing
B
B
A AND B

## Slide 23: Reliability Issues in IFP
Prior IFP approaches cannot leverage ECC and data-randomization techniques as computation is performed within the flash chips during data sensing
NAND Flash Chip
B
…
C
D
Page Buffer
A
A
Data Sensing
B
B
A AND B
Prior IFP techniques requires the application to be highly error-tolerant

## Slide 24: Our Goal
Address the bottleneck of state-of-the-art IFP techniques
(serial sensing of operands)
Make IFP reliable
(provide accurate computation results)

## Slide 25: Our Proposal
Flash-Cosmos enables
  Computation on multiple operands using a single sensing operation
  Provide high reliability during in-flash computation
NAND Flash Chip
B
…
D
Page Buffer
C
A
Data Sensing
B
A
C
A AND B AND C

## Slide 26: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 27: NAND Flash Basics: A Flash Cell
A flash cell stores data by adjusting the amount of charge in the cell
Erased Cell
(Low Charge Level)
1
Programmed Cell
(High Charge Level)
0
Activation
Operates as a resistor
Operates as an open switch

## Slide 28: NAND Flash Basics: A NAND String
A set of flash cells are serially connected to form a NAND String
1
0
0
1
0
Bitline (BL)
…
NAND String

## Slide 29: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String

## Slide 30: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)

## Slide 31: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
BLi
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
0
1
1
0
1
BLj
…
Reads as ‘1’
if BL current
flows
Reads as ‘0’
if BL current
cannot flow

## Slide 32: NAND Flash Basics: A NAND Flash Block
NAND strings connected to different bitlines comprise a NAND block
BL1
BL2
BL3
BL4
BL5
1
0
0
1
0
BLN
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
…
…
…
…
…
WL1
WL2
WL3
WL4
WLM
Block
A single wordline (WL) controls a large number of flash cells: High bit-level parallelism

## Slide 33: NAND Flash Basics: Block Organization
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…

## Slide 34: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital NAND
A
B
(A•B)’
2-input NAND
Notes: Our key observation is that NAND flash memory has similar organization to digital AND logic, as multiple cells are serially connected to the bitline, [Click] and

## Slide 35: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines.
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital NAND
A
B
(A•B)’
2-input NAND
Cells in different blocks
are connected in parallel: Similar to digital NOR
2-input NOR
A
B
(A+B)’
Notes: It also similar to digital OR logic, in that multiple NAND strings are connected to the bitline in parallel. [Click]

## Slide 36: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 37: Flash-Cosmos: Overview
Enables in-flash bulk bitwise operations on multiple operands with a single sensing operation using Multi-Wordline Sensing (MWS)

## Slide 38: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki

## Slide 39: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Non-Target Cells:
Operate
as resistors

## Slide 40: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:

## Slide 41: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells

## Slide 42: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:

## Slide 43: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells

## Slide 44: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
1
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Flash-Cosmos (Intra-Block MWS) enables
bitwise AND of multiple pages in the same block
via a single sensing operation

## Slide 45: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
1
1
0
0
…
WLy in Blocki
…
…
…
…

## Slide 46: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:

## Slide 47: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells

## Slide 48: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLy in Blocki
Notes: Like intra-block MWS, [Click] this property holds when we activate more than two wordlines in different blocks at the same time, [Click], as we can see …

## Slide 49: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLy in Blocki
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells

## Slide 50: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLy in Blocki
Flash-Cosmos (Inter-Block MWS) enables
bitwise OR of multiple pages in different blocks
via a single sensing operation

## Slide 51: Supporting Other Bitwise Operations
Exploit Inverse Read[1] which is supported in modern NAND flash memory
Bitwise NOT
Exploit MWS + Inverse Read
Bitwise NAND/ NOR
Use XOR between sensing and cache latches [2] which is also supported in NAND flash memory
Bitwise XOR/XNOR
[1] Lee+, “High-Performance 1-Gb-NAND Flash Memory with 0.12-µm Technology,” JSSC, 2002
[2] Kim+, “A 512-Gb 3-b/Cell 64-Stacked WL 3-D-NAND Flash Memory,” JSSC, 2018

## Slide 52: Flash-Cosmos: Overview
Increases the reliability of in-flash bulk bitwise operations by using Enhanced SLC-mode Programming (ESP)
Enables in-flash bulk bitwise operations on multiple operands with a single sensing operation using Multi-Wordline Sensing (MWS)

## Slide 53: Enhanced SLC-Mode Programming (ESP)
SLC-mode programming provides a large voltage margin between the erased and programmed states
Based on our real device characterization, we observe that SLC-mode programming is still highly error-prone without the use of ECC and data-randomization
# of cells
Erased
0
Prog.
1
Threshold voltage
Voltage margin in SLC-mode

## Slide 54: Enhanced SLC-Mode Programming (ESP)
ESP further increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability by making the cells less vulnerable to errors
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage

## Slide 55: Enhanced SLC-Mode Programming (ESP)
ESP increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability during data sensing by making the cells less vulnerable to errors
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage
ESP improves the reliability of in-flash computation without the use of ECC or data-randomization techniques

## Slide 56: Enhanced SLC-Mode Programming (ESP)
ESP increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability during data sensing by making the cells less vulnerable to errors
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage
ESP can improve the reliability of prior in-flash processing techniques as well

## Slide 57: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 58: Evaluation Methodology
We evaluate Flash-Cosmos using
160 real state-of-the-art 3D NAND flash chips

## Slide 59: Real Device Characterization
We validate the feasibility, performance, and reliability of Flash-Cosmos
160 48-layer 3D TLC NAND flash chips
  3,686,400 tested wordlines
Under worst-case operating conditions
  1-year retention time at 10K P/E cycles
  Worst-case data patterns

## Slide 60: Results: Real-Device Characterization
Both intra- and inter-block MWS operations
require no changes to the cell array
of commodity NAND flash chips
Both MWS operations can activate multiple WLs
(intra: up to 48, inter: up to 4) at the same time
with small increase in sensing latency (< 10%)
ESP significantly improves
the reliability of computation results
(no observed bit error in the tested flash cells)
Notes: Through our real-device characterization, we demnostrated that both MWS operations are possible without requiring any change ot the cell array of commodity NAND flash chips, [Click] and they can reliably activate multiple wordlines at the same time without significant increase in sensing latency. [Click]
We also observed no errors in the tested cells when we program data using ESP, which shows that Flash-Cosmos enables reliable in-flash bulk bitwise operations. [Click]

## Slide 61: Evaluation Methodology
We evaluate Flash-Cosmos using
160 real state-of-the-art 3D NAND flash chips
Three real-world applications that perform bulk bitwise operations

## Slide 62: Evaluation with real-world workloads
Simulation
  MQSim [Tavakkol+, FAST’18] to model the performance of Flash-Cosmos and the baselines
Workloads
  Three real-world applications that heavily rely on bulk bitwise operations
  Bitmap Indices (BMI): Bitwise AND of up to ~1,000 operands
  Image Segmentation (IMS): Bitwise AND of 3 operands
  k-clique star listing (KCS): Bitwise OR of up to 32 operands
Baselines
  Outside-Storage Processing (OSP): a multi-core CPU (Intel i7 11700K)
  In-Storage Processing (ISP): an in-storage hardware accelerator
  ParaBit [Gao+, MICRO’21]: the state-of-the-art in-flash processing (IFP) mechanism

## Slide 63: Results: Performance & Energy
Speedup over OSP
Chart: 
| BMI | IMS | KCS | AVG
 | 1.3181 | 1.1935 | 1.3007 | 1.2794
 | 14.1649 | 2.9997 | 12.8867 | 9.2742
 | 198.4035 | 2.9998 | 25.8962 | 32.4204
ISP
ParaBit
Flash-Cosmos
Flash-Cosmos provides significant performance & energy benefits over all the baselines
The larger the number of operands,
the higher the performance & energy benefits
Chart: 
| BMI | IMS | KCS | AVG
ISP | 8.2558 | 5.4514 | 7.4777 | 7.1709
ParaBit | 49.449 | 8.7761 | 38.1762 | 29.1277
Flash-Cosmos | 582.8533 | 8.9811 | 76.5954 | 95.9386
Energy benefit over OSP
150×
14×
2.5×
20×
2×
70×
12×
1.6×
10×
2×
25×
3.5×
3.3×
13.4×
Notes: Add average

## Slide 64: More in the Paper
https://arxiv.org/abs/2209.05566.pdf
Notes: Direct to the PDF

## Slide 65: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation of Flash-Cosmos and Key Results
Summary

## Slide 66: Flash-Cosmos: Summary
First work to enable multi-operand bulk bitwise operations with a single sensing operation and high reliability
Improves performance by 3.5x/25x/32x on average over ParaBit/ISP/OSP across the workloads
Improves energy efficiency by 3.3x/13.4x/95x on average over ParaBit/ISP/OSP across the workloads
Low-cost & requires no changes to flash cell arrays

## Slide 67: More on Flash-Cosmos
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 68: CIPHERMATCH: Accelerating Secure String Matching
Mayank Kabra, Rakesh Nadig, Harshita Gupta, Rahul Bera, Manos Frouzakis, Vamanan Arulchelvan, Yu Liang, Haiyu Mao, Mohammad Sadrosadati and Onur Mutlu, ”CIPHERMATCH: Accelerating Homomorphic Encryption-Based String Matching via Memory-Efficient Data Packing and In-Flash Processing" Proceedings of the 30th International Conference on Architectural Support for Programming Languages and Operating System (ASPLOS), Rotterdam, Netherlands April 2025. [arXiv version]
https://arxiv.org/pdf/2503.08968.pdf

## Slide 69: Upcoming Presentation at ASPLOS 2025
To be presented at ASPLOS 2025
Presenter - Mayank Kabra
Visit us in Session 1D: Homomorphic Encryption
Location: Van Oldenbarneveld
https://arxiv.org/pdf/2503.08968.pdf

## Slide 70: Storage-Centric Computing: Two Types
1. Processing near Storage
2. Processing using Storage

## Slide 71: In-Storage Genomic Data Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]
https://github.com/CMU-SAFARI/GenStore
https://arxiv.org/pdf/2202.10400

## Slide 72: GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 73: Genome Sequence Analysis
Genome sequence analysis is critical for many applications
  Personalized medicine
  Outbreak tracing
  Evolutionary studies
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: Genome sequence analysis (GSA) is critical for many applications [CLICK]
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads. [CLICK]

## Slide 74: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 75: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 76: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 77: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 78: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 79: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 80: More on GenStore
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]
https://github.com/CMU-SAFARI/GenStore
https://arxiv.org/pdf/2202.10400

## Slide 81: In-Storage Metagenomics [ISCA 2024]
Nika Mansouri Ghiasi, Mohammad Sadrosadati, Harun Mustafa, Arvid Gollwitzer, Can Firtina, Julien Eudine, Haiyu Mao, Joel Lindegger, Meryem Banu Cavlak, Mohammed Alser, Jisung Park, and Onur Mutlu, "MegIS: High-Performance and Low-Cost Metagenomic Analysis with In-Storage Processing" Proceedings of the 51st Annual International Symposium on Computer Architecture (ISCA), Buenos Aires, Argentina, July 2024. [Slides (pptx) (pdf)] [arXiv version]
https://github.com/CMU-SAFARI/MegIS
https://arxiv.org/pdf/2406.19113

## Slide 82: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 83: MegIS’s Steps
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 1
Step 2
Step 3

## Slide 84: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 85: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 86: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 87: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 88: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 89: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 90: Evaluation: Methodology Overview
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1-TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 91: Evaluation: Speedup over the Software Baselines
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 92: Evaluation: Speedup over the Software Baselines
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs

## Slide 93: Evaluation: Speedup over the PIM Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 94: Evaluation: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 95: Evaluation: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 scores
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2 (Only 1.7% of the area of three ARM Cortex R4 cores in an SSD controller)
Power: 7.658 mW
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 96: Evaluation: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 97: Evaluation: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
MegIS improves system cost-efficiency
and makes metagenomics more accessible
for wider adoption
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 98: More in the Paper
MegIS’s performance when running in-storage processing operations on the cores existing in the SSD controller
MegIS’s performance when using the same accelerators outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 99: More in the Paper
MegIS’s performance with the cores in the SSD controller
MegIS’s performance outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
https://arxiv.org/abs/2406.19113

## Slide 100: MegIS: Summary
Metagenomic analysis suffers from
significant storage I/O data movement overhead
The first in-storage processing system for end-to-end metagenomic analysis
Leverages and orchestrates processing inside and outside the storage system
MegIS
Improves performance
2.7×–37.2× over performance-optimized software
6.9×–100.2× over accuracy-optimized software
1.5×–5.1× over hardware-accelerated PIM baseline
Low area overhead
1.7% of the three cores
in an SSD controller
Reduces energy consumption
5.4× over performance-optimized software
15.2× over accuracy-optimized software
1.9× over hardware-accelerated PIM baseline
High accuracy
Same as accuracy-optimized
4.8× higher F1 scores
over performance-optimized/PIM

## Slide 101: More on MegIS
Nika Mansouri Ghiasi, Mohammad Sadrosadati, Harun Mustafa, Arvid Gollwitzer, Can Firtina, Julien Eudine, Haiyu Mao, Joel Lindegger, Meryem Banu Cavlak, Mohammed Alser, Jisung Park, and Onur Mutlu, "MegIS: High-Performance and Low-Cost Metagenomic Analysis with In-Storage Processing" Proceedings of the 51st Annual International Symposium on Computer Architecture (ISCA), Buenos Aires, Argentina, July 2024. [Slides (pptx) (pdf)] [arXiv version]
https://github.com/CMU-SAFARI/MegIS
https://arxiv.org/pdf/2406.19113

## Slide 102: Storage-Centric Computing: Two Types
1. Processing near Storage
2. Processing using Storage

## Slide 103: Summary and Future Outlook

## Slide 104: Our Vision on Storage-Centric Computing
Entire storage system as a specialized-enough accelerator
  Special-purpose accelerators
  General-purpose computation
  Multiple different memory technologies
    Processing-using-Flash/DRAM
    Processing-near-Flash/DRAM
Storage system becomes a first-class citizen where computation takes place when it makes
  greatly improving performance, energy efficiency, system cost, sustainability, …

## Slide 105: Storage-Centric Computing: Some Challenges
Reliability of computation
Limited endurance
Higher latencies of flash memories
Small internal DRAMs
Limited power and area budgets
Programming framework
Security guarantees
…
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 106: 1st Workshop on Memory-Centric Computing: Storage-Centric Computing
Mohammad Sadrosadati
m.sadr89@gmail.com
ASPLOS 2025
30 March 2025