## Slide 1: Pitfalls of UPMEM kernel development
Heterogeneous Memory Software Lab, Poland
Krystian Chmielewski, Tadeusz Kobus, Paweł Piotrowicz, Jarosław Ławnicki, Uladzislau Lukyanau, Maciej Maciejewski, Zhang Hongjun
krystian.chmielewski@huawei.com

## Slide 2: What is UPMEM?
x8
BANK
High Bandwidth (1GB/s) Internal Data Bus
DRAM Processing Unit (DPU)
DRAM Array
(MRAM) 64MB
Instruction Memory (IRAM) <= 3968 instr
Working Memory (WRAM)
<= 63488 B
RISC Multi-threaded Pipeline
400MHz
UPMEM PIM Rank
ule
dule
UPMEM PIM Module
HOST
CPU
CPU
MC
CPU
CPU
CPU
MC
CPU
DRAM
NUMA 0
NUMA 1
ule
dule
UPMEM PIM Module
DRAM
DDR4 channels
DDR4 channels

## Slide 3: ADD and MUL performance analysis

## Slide 4: Basic operations on UPMEM
Chart: MOPS
| INT8 ADD | INT8 MUL | INT32 ADD | INT32 MUL
 | 79.9332 | 28.5414 | 66.7875 | 11.7515
-82%
No native support for INT32 MUL
-64%
But why?

## Slide 5: Basic operations on UPMEM
Chart: MOPS
| INT8 ADD | INT8 MUL | INT32 ADD | INT32 MUL
 | 79.9332 | 28.5414 | 66.7875 | 11.7515
-82%
No native support for INT32 MUL
-64%
But why?

## Slide 6: Issues with INT8 MUL
Compiler sometimes uses INT32 MUL __mulsi3 function (SHIFT&ADD, ~9 cycles) instead of INT8 MUL mul_sl_sl (1 cycle) instruction
Often loops are not being unrolled at all
Unrolling through #pragma unroll is often not possible – not enough IRAM

## Slide 7
__mulsi3 – SHIFT & ADD

## Slide 8: Changing instructions on function inline
Compilation with –O2 or –O3 will result in inlining based on N (if it’s compile time constant)
Loop unrolling also depends on N
Inside the main function, INT32 MUL (SHIFT&ADD) is used
Function is inlined
Loop is fully unrolled
INT8 MUL is used (1 cycle)
Function is not inlined
Loop is fully unrolled,
INT8 MUL is used (1 cycle)
Function is inlined
Loop is not unrolled
INT32 MUL (SHIFT&ADD) is used (~9 cycles)
0
28
39
N:

## Slide 9: INT8/INT32 MUL Optimization

## Slide 10: Optimized INT8 MUL
Chart: MOPS
| INT8 (x1, __mulsi3) | INT8 (x1) | INT8 (x4) | INT8 (x8) | INT8 (full_unroll) | INT8x4 (x1) | INT8x4 (full_unroll) | INT8x8 (x1) | INT8x8 (full unroll)
 | 28.5414 | 79.9651 | 114.2215 | 123.1091 | 133.1288 | 123.0405 | 159.8646 | 145.5249 | 168.2959
baseline
  Ensuring the use of the correct instruction for INT8
  Unrolling:
    Full (compiler decides) #pragma unroll
    Manual, e.g., x4 #pragma unroll 4
  Loading data by 4 or 8 bytes (INT8x4, INT8x8)
> 5x speedup
vs baseline

## Slide 11: Optimized INT32 MUL
Chart: MOPS
| INT32 | INT32 (full unroll) | INT32_FAST | INT32_FAST (x64)
 | 11.7515 | 12.8883 | 19.0367 | 22.156
Replacing _mulsi3 (SHIFT&ADD, ~30 cycles) with a custom implementation that uses INT8 MUL
Unrolling also helps
baseline
2x speedup vs baseline
X = (x3, x2, x1, x0)
Y = (y3, y2, y1, y0)
X * Y = 2^0 (x0 * y0)
+ 2^8 (x0 * y1 + x1 * y0)
+ 2^16 (x0 * y2 + x1 * y1 + x2 * y0)
+ 2^24 (x0 * y3 + x1 * y2 + x2 * y1 + x3 * y0)

## Slide 12: Unrolling helps a lot
Loops are pretty costly, when we are not spending a lot of cycles on single iteration
Use #pragma unroll to force compiler to unroll loops
Chart: Speedup
| FLOAT ADD | DOUBLE ADD | INT8 ADD | INT32 ADD | INT64 ADD | FLOAT MUL | DOUBLE MUL | INT8 MUL - 64 | INT8_ASM MUL | INT8x4 MUL | INT8x8 MUL | INT32 MUL | INT32_FAST MUL - 64 | INT64 MUL
 | 0.04416 | 0.029429 | 0.6678 | 1.0078 | 0.75565 | 0 | 0 | 0.16366 | 0.66574 | 0.29858 | 0.15647 | 0.096735 | 0.16385 | 0.02259

## Slide 13: Basic operations on UPMEM revisited
Chart: MOPS
| INT32 ADD | INT32 ADD full unroll | INT32 MUL | INT32_FAST MUL x64
 | 66.7875 | 134.0971 | 11.7515 | 22.156
Chart: MOPS
| INT8 ADD | INT8 ADD full unroll | INT8 MUL | INT8x8 full unroll
 | 79.9332 | 133.3125 | 28.5414 | 168.2959
+26%
MUL is now faster than optmized ADD for INT8
-82%
MUL is still slower than ADD for INT32
Still, 2x speedup for MUL in raw numbers
baseline
baseline
baseline
baseline

## Slide 14: UPMEM vs CPU
Chart: GOPS
| INT8 ADD | INT8 MUL | INT32 ADD | INT32 MUL
Upmem (2560 DPUs) | 204.629 | 73.066 | 170.9761 | 30.084
Upmem optimized (2560 DPUs) | 341.28 | 430.8375 | 343.2887 | 56.7193
Kunpeng 920 (2*64 cores) | 133 | 66 | 33 | 16
1.5x → 2.6x
1.1x → 6.5x
5.2x → 10.4x
1.9x → 3.5x
Speedup vs Kunpeng

## Slide 15: Memory transfer optimizations

## Slide 16: Memory transfers
Host  PIM (dpu_prepare_xfer, dpu_push_xfer):
Transfer size and symbol offset need to be a multiple of 8B  error otherwise
Extra care is needed to handle the remainder, if any
Host buffers need to be aligned up to 8B
MRAM  WRAM (mram_read, mram_write):
Transfer size needs to be a multiple of 8B (max 2048B)
Read/write operations silently align down the address to 8B  no error is raised
mram_read_unaligned and mram_write_unaligned functions require ~300 more instructions  GEMV where the matrix is stored contiguously and row size is odd

## Slide 17: Reading unaligned memory MRAM
Address we read from/write to must be aligned to 8B
Number of bytes read/written must be a multiple of 8B

## Slide 18: Optimized data transfers
UPMEM server:
DRAM can be the bottleneck (only 2 DDR4-3200 channels)
Transposing data heavily engages the CPU
DPU allocation is not NUMA-aware:
No way to allocate DPUs assigned to specific CPU
A significant variance (~12%) in memory transfer speeds with default DPU allocation
Simple API extension to allow DPU allocation on specific NUMA node:
Changes only in the user-space library
Simple filtering of available ranks during DPU allocations
CPU
DRAM
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS
CPU
DRAM
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS
UPMEM DIMMS

## Slide 19: Optimized data transfers (parallel copy)
Chart: Ranks
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
PIM to host (baseline) | 1.9282 | 3.8672 | 3.0637 | 4.0615 | 5.0071 | 5.876 | 6.8382 | 7.5707 | 8.388 | 9.0389 | 9.2602 | 9.75 | 9.9912 | 10.3241 | 10.0738 | 10.1072 | 10.0443 | 10.6115 | 10.8627 | 11.2163
PIM to host (NUMA aware) | 4.1998 | 4.2919 | 6.2748 | 7.9949 | 6.7943 | 6.1728 | 7.039 | 7.7777 | 8.6053 | 9.4241 | 10.0255 | 10.4475 | 10.4882 | 10.5515 | 11.0772 | 11.6036 | 11.9961 | 12.355 | 12.2899 | 12.4199
Host to PIM (baseline) | 3.4381 | 6.4132 | 5.0211 | 6.6846 | 7.8863 | 9.4089 | 10.7731 | 11.8495 | 13.1717 | 14.3238 | 14.7334 | 15.8324 | 16.8005 | 17.0505 | 17.7263 | 18.2774 | 19.0264 | 19.6434 | 18.5562 | 20.5239
Host to PIM (NUMA aware) | 8.2607 | 8.3413 | 11.4169 | 14.0312 | 12.3596 | 11.4153 | 12.8091 | 13.9376 | 14.9706 | 16.1081 | 17.2156 | 18.3225 | 18.9188 | 19.6031 | 20.1496 | 20.8149 | 21.673 | 22.4295 | 22.6471 | 23.1247

## Slide 20: Summary
UPMEM Compiler:
Generates inefficient INT8 MUL (__mulsi3 SHIFT&ADD)
Rarely performs unrolling
DPU Optimizations:
A little extra care with INT8 MUL provides huge gains
INT32 MUL performance is also improved
The achieved performance of INT8/INT32 ADD/MUL makes UPMEM viable for testing AI workloads (albeit with quantization, FP remains unpractical on UPMEM)
Optimized data transfers:
NUMA-awareness can go a long way
Contact me at: krystian.chmielewski@huawei.com

## Slide 21: Thank you!