## Slide 1
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula
https://cgiannoula.github.io/
Peiming Yang, Ivan Fernandez, Jiacheng Yang, Sankeerth Durvasula, Yu Xin Li, Mohammad Sadrosadati, Juan Gomez Luna, Onur Mutlu, Gennady Pekhimenko
1st Workshop on Memory-Centric Computing Systems (MCCSys)
March 2025

## Slide 2
Key Results: PyGim improves (i) performance and energy efficiency by 3.7× and 2.3× over state-of-the-art schemes, and (ii) resource utilization on PIM system by 11.6× over PyTorch on GPUs
Executive Summary
Motivation: Graph Neural Networks (GNNs) analyze graph-structure data in important real-world applications such as drug discovery, social network analysis, recommendation systems…
Problem: The memory-intensive kernels of GNNs, which dominate execution time (~91%), are significantly bottlenecked by memory bandwidth in procesor-centric systems (CPUs/GPUs)
PyGim: An efficient and easy-to-use GNN library for real PIM systems
Key Ideas & Benefits:
Cost Effectiveness: Heteregenous GNN kernels are executed in the best-fit hardware
High Performance: (i) Enabling three levels of parallelism with various strategies in the PIM side and (ii) adapting best-performing parallelization strategy to the graph’s unique characteristics
High Programming Ease: (i) Providing a handy Python API and (ii) automatically tuning the best-fit parallelization strategy without programmer intervention
github.com/CMU-SAFARI/PyGim

## Slide 3
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 4
GNNs Are Widely Used in Real-World Applications
GNNs are state-of-the-art ML models for analyzing graph-structure data
Applications of GNNs are:
Drug Discovery
Recommendation Systems
Fraud Detection

## Slide 5
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
Adjacency (Sparse) Matrix
(= input graph data)
Input Feature Matrix
Output Feature Matrix
Aggregation
Combination
Output Result
Small Neural
Network
Aggregation corresponds to Sparse Matrix Matrix Multiplication (SpMM)
Combination typically comprises computational kernels (e.g., GEMMs)

## Slide 6
GNN Aggregation Is Memory-Bandwidth-Bound In GPUs
Using a RTX 3090 GPU with ~900 GB/s bandwidth, we find that GNN Aggregation
takes ~91% of the inference time
achieves less than 2% core utilization
Roofline Analysis
Bandwidth-Bound

## Slide 7
PIM Provides A Promising Solution for GNN Aggregation
Near-bank PIM: each PIM core is tightly coupled with one (or a few) DRAM banks
Near-bank PIM cores have significantly higher memory bandwidth than that available on Host cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus

## Slide 8
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 9
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
  Cooperative Acceleration (CoA)
  Parallelism Fusion (PaF)
  Lightweight Tuning
  Handy Programming Interface
PyGim is open source:
PyGim: github.com/CMU-SAFARI/PyGim
Deploy your GNNs effortless and enjoy the PIM benefits!

## Slide 10
1. Cooperative Acceleration (CoA)
Heterogeneous kernels are running in the best-fit underlying hardware
Combination runs on Host cores
Aggregation runs on PIM cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination

## Slide 11
Challenge 1: Data Transfer Costs
Minimize the overheads of passing the output data of the one step as input data to the next step
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination
data

## Slide 12
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
  Within PIM Core: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core
Reduces data transfer costs
Reduce computation costs

## Slide 13
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters

## Slide 14
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster

## Slide 15
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
  Within PIM Core: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core

## Slide 16
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
  Within PIM Core: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core
Reduces data transfer costs
Reduce computation costs

## Slide 17
Across PIM Clusters: Edge- + Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 sparse partitions and 2 dense partitions
Adjacency (Sparse) Matrix
Clusters 1,2
Clusters 3,4
Input Feature Matrix
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Partial Results for Output
(merged by Host cores)
Cluster 1
Cluster 3
Cluster 2
Cluster 4
sparse partitions (e.g., 2)
dense partitions (e.g., 2)
1
2
3
4
5
8
6
7
1
2
3
4
5
8
6
7
edge-level parallelism
1
2
3
4
5
8
6
7
1
2
3
4
5
8
6
7
Cluster 1
Cluster 2
Cluster 3
Cluster 4
feature-level parallelism

## Slide 18
Within a PIM Cluster: Vertex-/Edge-Level Parallelism
E.g., balancing vertices or balancing edges across PIM cores within the cluster
Adjacency (Sparse) Matrix
Core 1
Balance Vertices Across PIM Cores
Balance Edges Across PIM Cores
Adjacency (Sparse) Matrix
Core 2
Core 1
Core 2
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1 has 2 PIM Cores
Cluster 2
Each core undertakes 4 vertices
Each core undertakes 10 non-zeross

## Slide 19
Within a PIM Core: Vertex-/Edge-Level Parallelism
E.g., balancing vertices or balancing edges across threads within a PIM core
Adjacency (Sparse) Matrix
Thread 1
Balance Vertices Across Threads
Balance Edges Across Threads
Adjacency (Sparse) Matrix
PIM Core
Threads
PIM Core supports 4 threads
Thread 2
Thread 3
Thread 4
Thread 1
Thread 2
Thread 3
Thread 4
Synchronization is implement with coarse-grained and fine-grained locking schemes
Each thread undertakes 2 vertices
Each thread undertakes 5 non-zeros

## Slide 20
Real-world graphs exhibit diverse (non-zero point) characteristics:
  Min, max or average vertex neighboring degree, graph’s diameter…
Typically there is no one-size-fits-all solution:
  PaF supports a wide variety of parallelization strategies for diverse real-world graphs
Key challenge = manually tuning the best-performing parallelization strategy for each unique graph's characteristics poses significant challenges for developers
Challenge 2: Programmability in Real-World Graphs
real-world graphs with diverse characteristics
regular graph
power-law graph
diagonal graph
Notes: - Real-world graphs exhibit diverse characteristics, e.g., the average, min or max vertex neighboring degrees vary across different graphs. Therefore, as discussed in prior works [39, 62, 77, 122, 138], the execution behavior of sparse kernels, such as the SpMV/SpMM, depends on the particular characteristics of the input given, and there is no typically one-size-fits-all parallelization solution that performs best across various inputs
- Programming a real near-bank PIM system is hard task.

## Slide 21
PyGim Tuner predicts and automatically tunes the best-performing PaF strategy without the need for manual programmer intervention based on the:
  Graph’s characteristics (i.e., non-zero patterns)
  PIM system’s characteristics (i.e., compute capabilities, available memory bandwidth…)
3. Lightweight Tuning
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Real PIM System
Real-world Graph
PyGim Tuner
PyGim PaF Strategy
tunes

## Slide 22
PyGim integrates a handy Python interface (currently integrated with PyTorch)
4. Handy Programming Interface
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy

## Slide 23
PyGim integrates a handy Python interface (currently integrated with PyTorch)
4. Handy Programming Interface
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy
UPMEM PIM
fast-forwarded
Memory
small cores
PyGim: github.com/CMU-SAFARI/PyGim
Deploy your GNNs effortless and enjoy the PIM benefits!
Computation is performed inside real PIM devices!

## Slide 24
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 25
Evaluation Methodology
UPMEM PIM server: 16 PIM DIMMs with 1992 PIM Cores (24 threads per core) in total
Graph models: GCN, GIN SAGE
Datasets: obn-proteins, reddit, amazonProducts
Comparison points:
  PyTorch running on host CPU
  SparseP [Sigmetrics’22] (2×) running SpMM as multiple SpMV kernels on PIM cores
  GraNDe [IEEE Trans. Comput.’23]: optimizes GNN aggregation on near-rank PIM systems
UPMEM PIM System
PIM-Enabled Memory
PIM-Enabled Memory
124 GB PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU (2-socket Intel Xeon)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
128 GB Main Memory
Bus

## Slide 26
Performance Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts
PyGim significantly outperforms PyTorch (CPU) and prior PIM-based schemes by 3.1× and 4.4× respectively

## Slide 27
Energy Efficiency Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 2564.2726 | 2587.1552 | 2442.4522 | 4433.7424 | 4279.762 | 4359.3713 | 5852.4966 | 5620.9367 | 5704.5425
SparseP1 | 4946.4061 | 4897.4054 | 4944.507 | 7214.2204 | 7086.3536 | 7154.5176 | 10135.5761 | 9977.7677 | 10039.4813
SparseP2 | 4487.6501 | 4451.2338 | 4496.3087 | 6478.7246 | 6381.0069 | 6422.2122 | 9143.2736 | 9046.1845 | 9065.546
GraNDe | 6149.8183 | 5918.9864 | 6105.7194 | 8200.6406 | 7889.4481 | 7882.9551 | 13149.1481 | 13064.0146 | 13328.4552
PyGim_CSR | 1856.5666 | 1765.8154 | 1798.3173 | 2555.2897 | 2450.003 | 2473.5083 | 3737.752 | 3570.6333 | 3628.2915
PyGim_COO | 1912.043 | 1882.2876 | 1899.8371 | 2572.9546 | 2496.2467 | 2576.2211 | 3735.719 | 3580.2291 | 3671.5764
ogbn-proteins
reddit
amazonProducts
PyGim improves energy efficiency by 2.7× and 3.3× compared to PyTorch (CPU) and prior PIM-based schemes respectively

## Slide 28
Characteristics of CPU, PIM and GPU Systems
System | Total Cores | Freq. | INT32 Peak Performance | FP32 Peak Performance | Memory Capacity | Total Bandwidth | Technology Node
CPU Intel Xeon 4215 | 2×8 x86 cores | 2.5 GHz | 0.64 TOPS | 1.28 TFLOPS | 128 GB | 23.1 GB/s | 14nm
UPMEM PIM | 1992 PIM cores | 350 MHz | 115.93 GOPS | 24.85 GFLOPS | 124.5 GB | 1.39 TB/s | at least 20nm
GPU GTX 1080 Ti | 3584 CUDA cores | 1.48 GHz | 13.25 TOPS | 13.25 TFLOPS | 11 GB | 359.9 GB/s | 16nm
GPU RTX 2080 Ti | 4352 CUDA cores | 1.35 GHz | 16.94 TOPS | 16.94 TFLOPS | 11 GB | 558.1 GB/s | 12nm
GPU RTX 3090 | 10496 CUDA cores | 1.40 GHz | 17.79 TOPS | 35.58 TFLOPS | 24 GB | 936.2 GB/s | 8nm
Across last GPU generations:
memory bandwidth has tripled (~3×)
(last two generations) compute throughput has been doubled (~2×)
Comparing latest GPU vs PIM:
GPU RTX 3090 provides ~150× greater compute throughput
PIMs provide only ~1.5× larger memory bandwidth

## Slide 29
Resource Utilization in GNN Aggregation
Dataset & data type/ Software library | OGBN INT32 | RDT INT32 | AMZ INT32 | OGBN FP32 | RDT FP32 | AMZ FP32
pytorch_sparse – Intel MKL (CPU Intel Xeon 4215) | 0.74% | 0.63% | 0.67% | 0.26% | 0.22% | 0.20%
pytorch_sparse – CUDA (GPU GTX 1080 Ti) | 2.15% | 0.62% | 0.71% | 2.02% | 0.62% | 0.71%
pytorch_sparse – CUDA (GPU RTX 2080 Ti) | 1.45% | 0.68% | 0.71% | 1.45% | 0.67% | 0.71%
pytorch_sparse – CUDA (GPU RTX 3090) | 3.03% | 1.56% | 1.32% | 1.58% | 0.78% | 0.67%
PyGim (UPMEM PIM) | 14.09% | 13.86% | 12.32% | 8.21% | 9.13% | 8.84%
Although memory bandwidth and compute throughput have improved across GPU generations, resource utilization in GNN aggregation remains similarly low (less than ~3%)
PyGim running on a real PIM system achieves significantly higher resource utilization than the state-of-the-art PyTorch library running on high-end GPUs (at least a 9× increase)

## Slide 30
More in the Paper
Analysis within a PIM core
Analysis within a PIM cluster
Analysis across PIM clusters
PyGim tuning efficiency
Scalability analysis
Analysis on different data types
Analysis on different compression formats
Performance evaluation in GNN training
Recommendations
https://arxiv.org/pdf/2402.16731

## Slide 31
PyGim is Open Source
github.com/CMU-SAFARI/PyGim
PyGim

## Slide 32
Conclusion
We present PyGim, a handy ML library that significantly improves performance, energy efficiency and cost effectiveness in GNNs through real PIM devices
Key Ideas & Benefits: PyGim runs heterogeneous kernels in the best-fit underlying hardware and balances computation and data transfer costs via configurable parallelization strategies for diverse real-world graphs. PyGim automatically tunes the best-fit strategy, enhancing both efficiency and ease of use without programmer intervention
Key Results: PyGim improves (i) performance and energy efficiency by 3.7× and 2.3× over state-of-the-art schemes, and (ii) resource utilization on PIM system by 11.6× over PyTorch on GPUs
github.com/CMU-SAFARI/PyGim
PyGim
Notes: - PyGim balances computation and data transfer costs through adaptable parallelization strategies for diverse graphs. It automatically tunes optimal strategies, enhancing efficiency and ease of use without programmmer intervention
- PyGim balances computation and data transfer costs using configurable parallelization strategies for diverse real-world graphs. It automatically tunes the best-fit strategy, enhancing both efficiency and ease of use without programmer intervention

## Slide 33
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula
https://cgiannoula.github.io/
Thank you!