## Slide 1: Harnessing CIM techniques for accelerating sum operations in FPGA-DRAM architectures
Theocharis Diamantidis
NATIONAL TECHNICAL UNIVERSITY OF ATHENS
School of Electrical and Computer Engineering
Microprocessors and Digital Systems Lab
Supervisor: D. Soudris
Co-Supervisor: G. Lentaris

## Slide 2: Context
Introduction
Background & Related Work
Proposed Solution & Methodology
Experiments & Results
Conclusions & Future Work

## Slide 3: Introduction
Modern Systems are Processor-Centric
  Repeated Data Movement between CPU & Memory
  High Energy Consumption
  Reduced Speed
"Memory Wall”
  Multicore Architectures
  Memory Latency Bottleneck
Near Memory Computing
Computation is moved near memory
Compute In Memory
Computation is executed directly in memory

## Slide 4: Introduction
Computations in Commercial DRAM chips
Compute In Memory
Computation is executed directly in memory
Previous work already show simple logical operations (AND/OR/NOT/ROW COPY)
e.g Group Safari / O. Mutlu [1] [2] [3]
Current Thesis / Motivation: It is possible to develop extensions towards more complex logic/arithmetic functions
                in already available chips, in the field
[1] Safari, Yuksel, I E PULSAR: Simultaneous Many-Row Activation for Reliable and High-Performance Computing in Off-the-Shelf DRAM Chips
[2] Safari, Yuksel, I E Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis
[3] Safari Nastanar Hajinazar SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM

## Slide 5
Contributions
Simulation Level approximation of the timing Constraints
Developing a Full-Adder with 1, 2, 4, 8, 16 bits on actual commercial DRAM HW
Proof of Concept Function (Sum) with proposed FPGA-DRAM co-processing approach
Evaluation of Success Rate and Acceleration factors for multiple scenarios of logical operations

## Slide 6: Background
DRAM Organization
DRAM Module
DRAM
Chip
…
…
Chip I/O
Bank
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Row
Safari, Yuksel, I E Pulsar: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis

## Slide 7: Background
DRAM Subarray
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
Row Buffer
I/O Circuitry
DRAM Cell
Wordline
Capacitor
Access transistor
Bitline
charge
leakage
paths
Safari, Yuksel, I E Pulsar: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis

## Slide 8: Related Work
ROW-COPY
ACT src
Fetch src’s content into the sense amplifiers
d
s
t
r
c
s
d
s
t
s
r
c
Enabe the src’s wordline
Safari, Yuksel, I E Pulsar: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis

## Slide 9: Related Work
ROW-COPY
d
s
t
r
c
s
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
ACT src
ACT dst
Bitlines are still at src voltage
PRE
No time violation
Time Violation
Safari, Yuksel, I E Pulsar: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis

## Slide 10: Related Work
FRAC Operation
Safari, Yuksel, I E Pulsar: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis

## Slide 11: Related Work
LOGICAL AND/OR
d
s
t
a
a
a
b
b
b
ACT R1
ACT R2
PRE
Frac Op.
c
c
c
Time violation
Time violation
R1
R2

## Slide 12: Related Work
LOGICAL AND/OR
d
s
t
a
a
a
b
b
b
ACT R1
ACT R2
PRE
Frac Op.
c
c
c
Time violation
Time violation
R1
R2
MAJ3 (a,b,c)

## Slide 13: Related Work
LOGICAL AND/OR
d
s
t
a
a
a
b
b
b
ACT R1
ACT R2
PRE
Frac Op.
c
c
c
Time violation
Time violation
R1
R2
MAJ (A, B, 0) = AND (A, B)
MAJ (A, B, 1) = OR (A, B)
MAJ (A, B, C)

## Slide 14: Proposed Solutions
Limitation
Corresponding Solution
Bit transfer (i.e. shifting, propagation of carry out) between columns is prohibited.
Column-major architectures, where all numbers and their bits are stored in the same bit-line.
NOT operation cannot be executed in the same sub-array.
Store the operand and the complementary one and (if necessary) calculate the complementary result in each step
Logical operations for the same full-adder cannot be conducted in parallel.
Use bit-serial arithmetic and exploit the group of rows as much as possible.
The number of operands is restricted by the number of rows in the sub-array.
Utilize co-processing in memory and in the FPGA.
The results of each operation overwrites all the rows in the group.
Execute each operation in different groups of rows.

## Slide 15: Methodology & Design Space Exploration for improving Accuracy and Speed
  Estimate the timing parameters to violate on a simulation level.
  Identifying the boundaries of the sub-array on actual hardware level
  Exploring Simultaneously Opening-Rows
  Activate different groups of rows to achieve more accurate results.
  Testing timing parameters between commands.
  Evaluate the in-Memory Full-Adder
DSE parameters: Banks, sub-arrays, group of rows, bit-lines, bit width, numbers per column, total numbers per sum, DRAM command timing, operands for logical operations.

## Slide 16: Setup
Experiment Setup
  Xilinx Alveo U200 FPGA Board (200MHz).
  Evaluation was conducted on DDR4 memories.
  DRAM Bender HW → infrastructure with fine-grained control over DRAM.
  DRAM Bender SW →Framework facilitating memory access flexibility.
  Add commands into a list (Control flow, Arithmetic, Memory) with high-level programming languages (C++) and then schedule the DDR commands into the DRAM.
A. Olgun"DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips

## Slide 17: Experiments & Results
  Estimate the timing parameters to violate on a simulation level.
Capacitors equal to the parasitic capacitance of bit-line.
The inverters have a positive feedback. With small deviations the output is driven to Vdd or ground.
Precharge Circuit. The Voltage that is precharged must be without noise.

## Slide 18: Experiments & Results
Estimation of the Timing Parameters
Monte Carlo Analysis

## Slide 19: Experiments & Results
Identifying the boundaries of the sub-array
…
…
…
Sense Amplifiers
…
…
…
We implement the Row-Copy
Zeroing the whole memory
Write all ones in a random row R1
Issue a row-copy command Act(R1)-Pre-Act(R2)
Read the data in row R2
Loop for rows R2

## Slide 20: Experiments & Results
…
…
Results
512 rows in each sub-array
32 sub-arrays in each bank
Success Rate in Row Copy depends:
Data Stored in Cells
The Row Index

## Slide 21: Experiments & Results
Exploring Simultaneously Opening-Rows
Activating two rows in quick succession
can simultaneously activate
many rows in a subarray
ACT Row A
PRE
ACT Row B
WR
Row A
Row B
…
ACT
ACT
If rows are activated, WR command overwrites all of the activated rows’ content
Results: 2, 4, 8, 16 rows can be activated simultaneously

## Slide 22: Experiments & Results
The results are almost the same for AND/OR
Next: study single AND/OR operations for the given DRAM chip
    DSE for optimal timing
    Evaluation of Success Rate
    A subset of columns (~6000) have higher success rate without redundancy.
    Idle cycles between ACT-PRE-ACT equal 0
    Randomness of bit values lead to worse results

## Slide 23: Experiments & Results
Next: 1-bit Full Adder
Step 1: Store operands in the same Bit-Line
Step 2: Store the complementary values
Step 3: Choose how many groups of rows will be used
Step 4: Execute the logical operations in these groups
Step 5: Store the result in another row

## Slide 24: Experiments & Results
1-bit Full Adder
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
A
A’
B
B’
Cin
Cin’
Sum
Cout
R251
R261
. . .

## Slide 25: Experiments & Results
1-bit Full Adder
Cout will be used as input in the next bits
We need 15 groups of 4 rows in total

## Slide 26: Experiments & Results
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
A
A’
B
B’
Cin
Cin’
R12
R15

## Slide 27: Experiments & Results
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
A
A’
B
B’
Cin
Cin’
R12
R15
1
1
1
1
1
1
1
1
1
1
We issue the commands ACT(R12)-PRE-ACT(R13) and produce the logical OR

## Slide 28: Experiments & Results
R12
R15
To the next group
If we have more than 1 bit in each operand, we add the Cout of the previous stage in the same way we add Cin

## Slide 29: Experiments & Results
Next: Addition of more than 1 bit-length operands

## Slide 30: Experiments & Results
Next: Sum of more than two operands
We need 45000 cycles to add 32 8-bit operands!
Do we exploit all the 65000 bit-lines?

## Slide 31: Comments
The presented full-adder was designed in a general way using AND/OR logical gates based on Boolean algebra.
We can achieve better results by using Majority logic which must be specific for every function which is ~ 4x times faster
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout

## Slide 32: DRAM-FPGA Co-Processing
DRAM
Interleaver with Ping-Pong buffers
8 bits
8 bits
8 bits
MUX
8 bits
8 bits
Ping Pong Pipelined Buffers / Interleaver
Accumulator
SUM
Interleaver: Write per row Read per column

## Slide 33: DRAM-FPGA Co-Design
Accelaration of the sum-operation
8 bits

## Slide 34: Conclusions & Future Work
8 bits
For small number of operands, we have no acceleration
For larger number of operands, we have speed-up but with errors

## Slide 35: Conclusions & Future Work
8 bits
Explore the multiplication operator
Estimation of the Power Efficiency
DSP applications (thousands of Convolution Kernel multiplications via thousands of columns operating in parallel, such as Sobel, approximate Gauss)
ML applications where there is bit error tolerance