## Slide 1
Geraldo F. Oliveira
Dr. Juan Gómez Luna
Professor Onur Mutlu
Processing-Near-Memory
Programming General-purpose PIM
HEART 2024 Tutorial
Memory-Centric Computing Systems
Friday, June 21, 2024

## Slide 2: UPMEM PIM

## Slide 3: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/
CPU
(x86, ARM, RV…)
DDR
Data bus

## Slide 4: UPMEM DIMMs
E19: 8 chips/DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips/DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 5: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 6: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 7: UPMEM Patent
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 8: UPMEM PIM System Organization (I)
FIG. 1 schematically illustrates a computing system comprising DRAM circuits having integrated processors according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 9: UPMEM PIM System Organization (II)
In a UPMEM-based PIM system UPMEM DIMMs coexist with regular DDR4 DIMMs
Notes: P21 DIMMs.
DPUs cannot be shared. There is a large number of DPUs.
No need for OS.
This simplifies security implications. No side channels.

## Slide 10: UPMEM PIM System Organization (III)
A UPMEM DIMM contains 8 or 16 chips
  Thus, 1 or 2 ranks of 8 chips each
Inside each PIM chip there are:
  8 64MB banks per chip: Main RAM (MRAM) banks
  8 DRAM Processing Units (DPUs) in each chip, 64 DPUs per rank

## Slide 11: DRAM Processing Unit (I)
FIG. 4 schematically illustrates part of the computing system of FIG. 1 in more detail according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 12: DRAM Processing Unit (II)

## Slide 13: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 14: Fine-grained Multithreading

## Slide 15: Fine-Grained Multithreading (I)
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 16: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependence latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964
Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978

## Slide 17: Lecture on Fine-Grained Multithreading
https://www.youtube.com/watch?v=6e5KZcCGBYw&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN&index=16

## Slide 18: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 19: DPU Instruction Set Architecture
Specific 32-bit ISA
  Aiming at scalar, in-order, and multithreaded implementation
  Allowing compilation of 64-bit C code
  LLVM/Clang compiler
https://sdk.upmem.com/2021.2.0/201_IS.html#

## Slide 20: More on the UPMEM PIM Architecture
https://youtu.be/p_sLhKeo6ys
https://youtu.be/7c6x5GJG6dw

## Slide 21: Programming a General-purpose PIM System

## Slide 22: Accelerator Model (I)
Integration of UPMEM DIMMs in a system follows an accelerator model
UPMEM DIMMs coexist with conventional DIMMs
UPMEM DIMMs can be seen as a loosely coupled accelerator
  Explicit data movement between the main processor (host CPU) and the accelerator (UPMEM)
  Explicit kernel launch onto the UPMEM processors
This resembles GPU computing

## Slide 23: GPU Computing
Computation is offloaded to the GPU
Three steps
  CPU-GPU data transfer (1)
  GPU kernel execution (2)
  GPU-CPU data transfer (3)
https://www.youtube.com/watch?v=y40-tY5WJ8A
https://safari.ethz.ch/digitaltechnik/spring2018/lib/exe/fetch.php?media=digitaldesign-2018-lecture22-gpuprogramming-afterlecture.pdf

## Slide 24: Accelerator Model (II)
FIG. 6 is a flow diagram representing operations in a method of delegating a processing task to a DRAM processor according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 25: System Organization
FIG. 1 schematically illustrates a computing system comprising DRAM circuits having integrated processors according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 26: First Programming Example: Vector Addition

## Slide 27: Observations, Recommendations, Takeaways
GENERAL PROGRAMMING RECOMMENDATIONS
Execute on the DRAM Processing Units (DPUs) portions of parallel code that are as long as possible.
Split the workload into independent data blocks, which the DPUs operate on independently.
Use as many working DPUs in the system as possible.
Launch at least 11 tasklets (i.e., software threads) per DPU.
PROGRAMMING RECOMMENDATION 1
For data movement between the DPU’s MRAM bank and the WRAM, use large DMA transfer sizes when all the accessed data is going to be used.
KEY OBSERVATION 7
Larger CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks result in higher sustained bandwidth.
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound. As a result, the most suitable work- loads are memory-bound.

## Slide 28: Vector Addition (VA)
Our first programming example
We partition the input arrays across:
  DPUs
  Tasklets, i.e., software threads running on a DPU
DPU 0
DPU 1
DPU 2
DPU 3
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1

## Slide 29: UPMEM SDK Documentation
https://sdk.upmem.com/2023.1.0/

## Slide 30: General Programming Recommendations
From UPMEM programming guide✻, presentations★, and white papers☆
✻ https://sdk.upmem.com/2021.1.1/index.html
★ F. Devaux, "The true Processing In Memory accelerator," HotChips 2019. doi: 10.1109/HOTCHIPS.2019.8875680
☆ UPMEM, “Introduction to UPMEM PIM. Processing-in-memory (PIM) on DRAM Accelerator,” White paper
GENERAL PROGRAMMING RECOMMENDATIONS
Execute on the DRAM Processing Units (DPUs) portions of parallel code that are as long as possible.
Split the workload into independent data blocks, which the DPUs operate on independently.
Use as many working DPUs in the system as possible.
Launch at least 11 tasklets (i.e., software threads) per DPU.

## Slide 31: DPU Allocation
dpu_alloc() allocates a number of DPUs
  Creates a dpu_set
Can we allocate different DPU sets
over the course of a program?
Yes, we can. We show an example next
We deallocate a DPU set with dpu_free()

## Slide 32: DPU Allocation: Needleman-Wunsch (NW)
In NW we change the number of DPUs in the DPU set as computation progresses

## Slide 33: Load DPU Binary
dpu_load() loads a program in all DPUs of a dpu_set
Is it possible to launch different kernels onto different DPUs?
Yes, it is possible. This enables:
Workloads with task-level parallelism
Different programs using different DPU sets

## Slide 34: CPU-DPU/DPU-CPU Data Transfers
CPU-DPU and DPU-CPU transfers
  Between host CPU’s main memory and DPUs’ MRAM banks
Serial CPU-DPU/DPU-CPU transfers:
  A single DPU (i.e., 1 MRAM bank)
Parallel CPU-DPU/DPU-CPU transfers:
  Multiple DPUs (i.e., many MRAM banks)
Broadcast CPU-DPU transfers:
  Multiple DPUs with a single buffer

## Slide 35: Serial Transfers
dpu_copy_to();
dpu_copy_from();
We transfer (part of) a buffer to/from each DPU in the dpu_set
DPU_MRAM_HEAP_POINTER_NAME: Start of the MRAM range that can be freely accessed by applications
  We do not allocate MRAM explicitly
Offset within MRAM
Pointer to main memory
Transfer size

## Slide 36: Parallel Transfers
We push different buffers to/from a DPU set in one transfer
  All buffers need to be of the same size
First, prepare (dpu_prepare_xfer);
then, push (dpu_push_xfer)
Direction:
  DPU_XFER_TO_DPU
  DPU_XFER_FROM_DPU
Pointer to main memory
Offset within MRAM
Transfer size
Direction

## Slide 37: Broadcast Transfers
dpu_broadcast_to();
  Only CPU to DPU
We transfer the same buffer to all DPUs in the dpu_set
Pointer to main memory
Transfer size

## Slide 38: Different Types of Transfers in a Program
An example benchmark that uses both parallel and serial transfers
Select (SEL)
  Remove even values
DPU 0
DPU 1
DPU 2
DPU 0
DPU 1
DPU 2
Parallel transfers
Serial transfers

## Slide 39: Inter-DPU Communication
There is no direct communication channel between DPUs
Inter-DPU communication takes place via the host CPU using CPU-DPU and DPU-CPU transfers
Example communication patterns:
  Merging of partial results to obtain the final result
    Only DPU-CPU transfers
  Redistribution of intermediate results for further computation
    DPU-CPU transfers and CPU-DPU transfers

## Slide 40: How Fast are these Data Transfers?
With a microbenchmark, we obtain the sustained bandwidth of all types of CPU-DPU and DPU-CPU transfers
Two experiments:
  1 DPU: variable CPU-DPU and DPU-CPU transfer size (8 bytes to 32 MB)
  1 rank: 32 MB CPU-DPU and DPU-CPU transfers to/from a set of 1 to 64 MRAM banks within the same rank
Preliminary experiments with more than one rank
  Channel-level parallelism
DDR4 bandwidth bounds the maximum transfer bandwidth
The cost of the transfers can be amortized,
if enough computation is run on the DPUs

## Slide 41: CPU-DPU/DPU-CPU Transfers: 1 DPU
Data transfer size varies between 8 bytes and 32 MB
Chart: Data transfer size (bytes)
| 8 | 32 | 128 | 512 | 2K | 8K | 32K | 128K | 512K | 2M | 8M | 32M
CPU-DPU | 0.000155 | 0.000652 | 0.002771 | 0.010059 | 0.036637 | 0.10489 | 0.20328 | 0.29402 | 0.60928 | 0.66017 | 0.38165 | 0.33248
DPU-CPU | 0.000155 | 0.000668 | 0.002795 | 0.009094 | 0.027453 | 0.052312 | 0.072383 | 0.08808 | 0.11749 | 0.12198 | 0.12252 | 0.12209
KEY OBSERVATION 7
Larger CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks result in higher sustained bandwidth.

## Slide 42: CPU-DPU/DPU-CPU Transfers: 1 Rank (I)
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)
The number of DPUs varies between 1 and 64
Chart: #DPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64
CPU-DPU (serial) | 0.33248 | 0.33347 | 0.33201 | 0.33127 | 0.30251 | 0.30048 | 0.27371
DPU-CPU (serial) | 0.12209 | 0.12213 | 0.12212 | 0.12211 | 0.11496 | 0.11515 | 0.11561
CPU-DPU (parallel) | 0.33204 | 0.54059 | 0.73245 | 0.87673 | 1.8109 | 4.2349 | 6.6828
DPU-CPU (parallel) | 0.12227 | 0.22521 | 0.42437 | 0.63153 | 1.4964 | 3.1702 | 4.7395
CPU-DPU (broadcast) | 0.33281 | 0.66768 | 1.3535 | 2.5643 | 5.0996 | 10.1432 | 16.8846
KEY OBSERVATION 8
The sustained bandwidth of parallel CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks increases with the number of DRAM Processing Units inside a rank.

## Slide 43: CPU-DPU/DPU-CPU Transfers: 1 Rank (II)
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)
The number of DPUs varies between 1 and 64
Chart: #DPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64
CPU-DPU (serial) | 0.33248 | 0.33347 | 0.33201 | 0.33127 | 0.30251 | 0.30048 | 0.27371
DPU-CPU (serial) | 0.12209 | 0.12213 | 0.12212 | 0.12211 | 0.11496 | 0.11515 | 0.11561
CPU-DPU (parallel) | 0.33204 | 0.54059 | 0.73245 | 0.87673 | 1.8109 | 4.2349 | 6.6828
DPU-CPU (parallel) | 0.12227 | 0.22521 | 0.42437 | 0.63153 | 1.4964 | 3.1702 | 4.7395
CPU-DPU (broadcast) | 0.33281 | 0.66768 | 1.3535 | 2.5643 | 5.0996 | 10.1432 | 16.8846
KEY OBSERVATION 9
The sustained bandwidth of parallel CPU-DPU transfers is higher than the sustained bandwidth of parallel DPU-CPU transfers due to different implementations of CPU-DPU and DPU-CPU transfers in the UPMEM runtime library.
The sustained bandwidth of broadcast CPU-DPU transfers (i.e., the same buffer is copied to multiple MRAM banks) is higher than that of parallel CPU-DPU transfers (i.e., different buffers are copied to different MRAM banks) due to higher temporal locality in the CPU cache hierarchy.
Notes: Load uses AVX write instructions, which are asynchronous.
However, AVX read instructions are synchronous

## Slide 44: “Transposing” Library
F. Devaux, "The true Processing In Memory accelerator," HotChips 2019. doi: 10.1109/HOTCHIPS.2019.8875680

## Slide 45: Microbenchmark: CPU-DPU
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)

## Slide 46: DPU Kernel Launch
dpu_launch() launches a kernel on a dpu_set
  DPU_SYNCHRONOUS suspends the application until the kernel finishes
  DPU_ASYNCHRONOUS returns the control to the application
    dpu_sync or dpu_status to check kernel completion
What does the asynchronous execution enable?
Some ideas:
Task-level parallelism: concurrent execution of different kernels on different DPU sets
Concurrent heterogeneous computation on CPU and DPUs

## Slide 47: How to Pass Parameters to the Kernel?
We can use serial and parallel transfers
We pass them directly to the scratchpad memory of the DPU
  Working RAM (WRAM): 64KB per DPU
This is useful for input parameters and some results

## Slide 48: Recall: Vector Addition (VA)
Our first programming example
We partition the input arrays across:
  DPUs
  Tasklets, i.e., software threads running on a DPU
DPU 0
DPU 1
DPU 2
DPU 3
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1

## Slide 49: Programming a DPU Kernel (I)
Vector addition
Tasklet ID
Size of vector tile processed by a DPU
MRAM addresses of arrays A and B
WRAM allocation
MRAM-WRAM DMA transfers
Vector addition (see next slide)
WRAM-MRAM DMA transfer

## Slide 50: Programming a DPU Kernel (II)
Vector addition

## Slide 51: Intra-DPU Synchronization

## Slide 52: Synchronization Primitives
A tasklet is the software abstraction of a hardware thread
Each tasklet can have its own memory space in WRAM
  Tasklets can also share data in WRAM by sharing pointers
Tasklets within the same DPU can synchronize
  Mutual exclusion
    mutex_lock(); mutex_unlock();
  Handshakes
    handshake_wait_for(); handshake_notify();
  Barriers
    barrier_wait();
  Semaphores
    sem_give(); sem_take();

## Slide 53: Parallel Reduction (I)
Tasklets in a DPU can work together on a parallel reduction
Tasklet 0
Tasklet 1
Tasklet 2
Tasklet 3

## Slide 54: Parallel Reduction (II)
Each tasklet computes a local sum
Tasklet 0
Tasklet 1
Tasklet 2
Tasklet 3

## Slide 55: Parallel Reduction (III)
Each tasklet computes a local sum
Accumulate in a local sum
Copy local sum into WRAM

## Slide 56: Final Reduction
A single tasklet can perform the final reduction
Accumulate in a local sum
Copy local sum into WRAM
Sequential accumulation
Barrier synchronization

## Slide 57: Vector Reduction: Naïve Mapping
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
Slide credit: Hwu & Kirk
…

## Slide 58: Using Barriers: Tree-Based Reduction
Multiple tasklets can perform a tree-based reduction
  After every iteration tasklets synchronize with a barrier
  Half of the tasklets retire at the end of an iteration
“offset” tasklets working
Barrier synchronization
A handshake-based tree-based reduction is also possible.
We can compare single-tasklet, barrier-based,
and handshake-based versions*
*Gómez-Luna et al., “Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture,”
https://arxiv.org/pdf/2105.03814.pdf

## Slide 59: Tree-Based Reduction on UPMEM PIM (I)
Single-thread vs. Barrier-based vs. Handshake-based on 1 DPU
Gómez-Luna et al. "Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture." arXiv preprint arXiv:2105.03814 (2021). https://arxiv.org/pdf/2105.03814.pdf
High cost of intra-DPU synchronization
(especially, barrier synchronization)
when there is small amount of computation

## Slide 60: Tree-Based Reduction on UPMEM PIM (II)
Single-thread vs. Barrier-based vs. Handshake-based on 1 DPU
Gómez-Luna et al. "Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture." arXiv preprint arXiv:2105.03814 (2021). https://arxiv.org/pdf/2105.03814.pdf
Cost of intra-DPU synchronization
gets amortized when there is large amount of computation
2K elements
2M elements

## Slide 61: Parallel Reduction on GPU
https://youtu.be/tJmcV9AMfp4

## Slide 62: Prefix-Sum (Scan)
Output (Exclusive Scan)
1
3
6
10
11
12
13
14
14
15
17
20
22
24
0
26
Output (Inclusive Scan)
3
6
10
11
12
13
14
14
15
17
20
22
24
26
1
28
2
3
4
1
1
1
1
0
1
2
3
2
2
2
1
2
Input
out[0] = 0; // Identity value
for(int i=1; i<n; i++)
out[i] = out[i-1] + in[i-1];
out[0] = in[0];
for(int i=1; i<n; i++)
out[i] = out[i-1] + in[i];

## Slide 63: Hierarchical (Inclusive) Scan: 1 DPU
Per-tasklet (Inclusive) Scan
3
6
10
1
2
3
4
0
1
3
6
2
4
6
1
8
3
6
10
11
12
13
14
14
15
17
20
22
24
26
1
28
14
20
2
3
4
1
1
1
1
0
1
2
3
2
2
2
1
2
Input
Tasklet 0
Tasklet 1
Tasklet 2
Tasklet 3
Output (Inclusive Scan)

## Slide 64: Per-DPU (Inclusive) Scan (I)
Each tasklet computes scan locally
Per-tasklet scan

## Slide 65: Per-DPU (Inclusive) Scan (II)
Each tasklet communicates with adjacent tasklets
Per-tasklet scan
Handshake-based synchronization

## Slide 66: Per-DPU (Inclusive) Scan (III)
Each tasklet adds an offset to each own element
Per-tasklet scan
Handshake-based synchronization
Per-tasklet add

## Slide 67: Scan-Scan-Add (SSA)
Per-DPU (Inclusive) Scan
3
6
10
1
2
3
4
0
1
3
6
2
4
6
1
8
2
3
4
1
1
1
1
0
1
2
3
2
2
2
1
2
10
4
6
8
10
4
6
8
10
14
20
28
Scan Partial Sums
Output (Inclusive Scan)
3
6
10
11
12
13
14
14
15
17
20
22
24
26
1
28
Add
+10
+14
+20
11
12
13
14
14
15
17
20
22
24
26
28
3
6
10
1
2
3
4
0
1
3
6
2
4
6
1
8
Input
DPU 0
DPU 1
DPU 2
DPU 3
DPU kernel termination

## Slide 68: SSA: Memory Accesses
Scan
  First kernel reads input array (N elements) and writes array with per-DPU prefix sums (N elements)
Scan
  Second kernel reads and writes N / PER_DPU_SIZE elements
Add
  Third kernel reads array with per-DPU prefix sums (N elements) and writes output (N elements)
4N elements are read/written

## Slide 69: Reduce-Scan-Scan (RSS)
2
3
4
1
1
1
1
0
1
2
3
2
2
2
1
2
Input
Per-DPU Reduction
10
4
6
8
10
4
6
8
10
14
20
28
10
4
6
8
Scan Partial Sums
Output (Inclusive Scan)
3
6
10
11
12
13
14
14
15
17
20
22
24
26
1
28
2
3
4
1
1
1
1
0
1
2
3
2
2
2
1
2
+10
+14
+20
11
12
13
14
14
15
17
20
22
24
26
28
DPU kernel termination
Add
3
6
10
1
2
3
4
0
1
3
6
2
4
6
1
8
Per-DPU Scan
DPU 0
DPU 1
DPU 2
DPU 3

## Slide 70: RSS: Memory Accesses
Reduce
  First kernel reads input array (N elements) and writes per-DPU reduction (N / PER_DPU_SIZE elements)
Scan
  Second kernel reads and writes N / PER_DPU_SIZE elements
Scan
  Third kernel reads input array (N elements) and scan partial sums (N / PER_DPU_SIZE elements), and writes output (N elements)
3N elements are read/written

## Slide 71: SCAN-SSA vs. SCAN-RSS on UPMEM PIM
SCAN-SSA vs. SCAN-RSS on 1 DPU
Gómez-Luna et al. "Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture." arXiv preprint arXiv:2105.03814 (2021). https://arxiv.org/pdf/2105.03814.pdf
The cost of intra-DPU synchronization in RSS (in Reduce step)
may be noticeable for small arrays.
For large arrays, RSS is faster than SSA,
since it saves memory accesses

## Slide 72: Parallel Prefix-Sum (Scan) on GPU
https://youtu.be/SG0gvcbf2eo

## Slide 73: UPMEM SDK Documentation
https://sdk.upmem.com/2023.1.0/

## Slide 74: Programming UPMEM PIM (I)
https://youtu.be/zF70xuhesME

## Slide 75: Programming UPMEM PIM (II)
https://youtu.be/pHEHdLsnNdk

## Slide 76: Real PIM Tutorial: Hands-on Lab

## Slide 77: Template Files
Contain templates for task 1 and task 2
Task 2’s template can be used for the remaining tasks

## Slide 78: Task 1: CPU-DPU and DPU-CPU Transfers
Use serial, parallel, and broadcast transfers

## Slide 79: Task 2: AXPY
VA is a good reference code for this task

## Slide 80: Task 3: Operations and Datatypes
You will observe significant variations in arithmetic throughput for different operations and datatypes

## Slide 81: Task 4: Vector Reduction
Performance differences due to the final reduction step

## Slide 82: Real PIM Tutorial: Hands-on Lab

## Slide 83
Geraldo F. Oliveira
Dr. Juan Gómez Luna
Professor Onur Mutlu
Processing-Near-Memory
Programming General-purpose PIM
HEART 2024 Tutorial
Memory-Centric Computing Systems
Friday, June 21, 2024