## Slide 1: 2nd Workshop on Memory-Centric Computing: Processing-Using-Memory - Part I
Dr. Geraldo F. Oliveira
https://geraldofojunior.github.io
ICS 2025
08 June 2025

## Slide 2: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 3: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 4: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array
of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
Row Buffer
Notes: A DRAM module
[CLICK] is composed of many DRAM chips
[CLICK] Each DRAM chip is composed of several banks.
[CLICK] Each bank has many subarrays, which are a 2D array of DRAM cells
[CLICK] The 2D array of DRAM cells are horizontally connected via a wordline
[CLICK] And vertically connected via a bitline
[CLICK] The bitlines are connected to an array of sense amplifiers
[CLICK] called row buffer .
[CLICK] A DRAM cell is composed of
[CLICK] A storage capacitor, which holds the data stored in DRAM as charge and
[CLICK] An access transistor, which enables and disables the charge flow from the storage capacitor to the bitline
[NEXT]

## Slide 5: DRAM Cell Operation
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
Notes: The DRAM cells operates using three main commands: ACTIVATE, READ/WRITE, and PRECHARGE.
[NEXT]

## Slide 6: DRAM Cell Operation (1/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. raise wordline
2. capacitor loses charge to bitline
4. amplify deviation
in the bitline
+ δ
3. enable
sense amplifier
VDD
5. capacitor charge is restored
Notes: To read the charge level stored in the storage capacitor, the memory controller issues an ACTIVATE command. Prior to receiving the ACTIVATE command, the bitline is held under a reference voltage, usually 1/2 VDD.
[CLICK] First, once the DRAM array receives the ACTIVE command, the wordline of the target row is asserted, which connects all cells along the row to their respective bitlines.
[CLICK] Second, the storage capacitor shares charge with its corresponding bitline
[CLICK] Third, the sense amplifier is enabled and
[CLICK] Fourth, the resulting bitline voltage shift is sensed and amplified by the bitline’s sense amplifier. Once the sense amplifiers finish amplification
[CLICK] the row buffer will contain the values originally stored within the cells along the asserted wordline. Also, the charge in the storage capacitor is fully restored. At the end of the ACTIVATE operation, the DRAM array is ready to receive read and write requests from the memory controller.
[NEXT]]

## Slide 7: DRAM Cell Operation (2/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
read/write charge
latched in sense amplifier
Notes: The memory controller then issues read or write commands to columns within the activated row.
[NEXT]

## Slide 8: DRAM Cell Operation (3/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
½ VDD
2. precharge bitline for next access
1. lower
wordline
3. disable
sense amplifier
Notes: To prepare the DRAM array for future access to other DRAM rows, the memory controller issues a precharge command. It works as follows
[CLICK] First, the capacitor is disconnected from the bitline by disabling the wordline
[CLICK] Second, the bitline voltage is restored to its quiescent state. Now, the DRAM array is ready for next accesses.
[CLICK] Third, the sense amplifier is disabled.
[NEXT]

## Slide 9: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
11.6X latency reduction, 74X energy reduction
Notes: copy

## Slide 10: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst

## Slide 11: RowClone: Inter-Bank
Memory Channel
Chip I/O
Bank
Shared internal bus
Overlap the latency of the read and the write
1.9X latency reduction, 3.2X energy reduction

## Slide 12: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)
0.01% area cost

## Slide 13: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 14: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 15: Lecture on RowClone & Processing using DRAM
https://www.youtube.com/watch?v=n6Pwg1qax_E&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4&index=4

## Slide 16: RowClone Extensions and Follow-Up Work
Can we do faster inter-subarray copy?
  Yes, see LISA [Chang et al., HPCA 2016]
Can we enable data movement at smaller granularities within a bank?
  Yes, see FIGARO [Wang et al., MICRO 2020]
Can we do better inter-bank copy?
  Yes, see Network-on-Memory [CAL 2020]
Can similar ideas and DRAM properties be used to perform computation on data?
  Yes, see Ambit [Seshadri et al., CAL 2015, MICRO 2017]
  Yes, see SIMDRAM [Hajinazar & Oliveira, ASPLOS 2021]

## Slide 17: Network-On-Memory: Fast Inter-Bank Copy
Seyyed Hossein SeyyedAghaei Rezaei, Mehdi Modarressi, Rachata Ausavarungnirun, Mohammad Sadrosadati, Onur Mutlu, and Masoud Daneshtalab, "NoM: Network-on-Memory for Inter-Bank Data Transfer in Highly-Banked Memories" IEEE Computer Architecture Letters (CAL), 2020.

## Slide 18: LISA: Increasing Connectivity in DRAM
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 19: Moving Data Inside DRAM?
DRAM cell
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 20: Key Idea and Applications
Low-cost Inter-linked subarrays (LISA)
  Fast bulk data movement between subarrays
  Wide datapath via isolation transistors: 0.8% DRAM chip area
LISA is a versatile substrate → new applications
Subarray 1
Subarray 2
…
  Fast bulk data copy: Copy latency 1.363ms→0.148ms (9.2x) → 66% speedup, -55% DRAM energy
  In-DRAM caching: Hot data access latency 48.7ns→21.5ns (2.2x) → 5% speedup
  Fast precharge: Precharge latency 13.1ns→5.0ns (2.6x) → 8% speedup

## Slide 21: More on LISA
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 22: FIGARO: Fine-Grained In-DRAM Copy
Yaohua Wang, Lois Orosa, Xiangjun Peng, Yang Guo, Saugata Ghose, Minesh Patel, Jeremie S. Kim, Juan Gómez Luna, Mohammad Sadrosadati, Nika Mansouri Ghiasi, and Onur Mutlu, "FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020.

## Slide 23: In-Memory Bulk Bitwise Operations
We can support in-DRAM COPY, ZERO, AND, OR, NOT, MAJ
At low cost
Using inherent analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 24: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 25: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 26: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 27: In-DRAM NOT Operation
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 28: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 29: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 30: Example Data Structure: Bitmap Index
Alternative to B-tree and its variants
Efficient for performing range queries and joins
Many bitwise operations to perform a query
Bitmap 1
Bitmap 2
Bitmap 4
Bitmap 3
age < 18
18 < age < 25
25 < age < 60
age > 60

## Slide 31: Performance: Bitmap Index on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>5.4-6.6X Performance Improvement

## Slide 32: Performance: BitWeaving on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 33: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 34: More on In-DRAM Bitwise Operations
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 35: More on In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 36: Outline
Processing-Using-Memory (PUM) Solutions
  Review of DRAM Background, RowClone, and Ambit
  SIMDRAM & MIMDRAM: Generalizing PUM Computing
  pLUTo: Extending Operation Support with LUTs
  PUM in Off-the-Shelf DRAM Chips
  PUM Beyond Boolean/Arithmetic and DRAM
Processing-Near-Memory (PNM) Solutions
  Overview
  Accelerating Neural Networks & Databases
  Real PNM Systems
Barriers for Adoption (and Current Solutions)
Conclusion

## Slide 37: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]
https://arxiv.org/abs/2105.12839

## Slide 38: SIMDRAM Key Idea
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
38

## Slide 39: SIMDRAM: PuM Substrate
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Higher throughput
Lower energy consumption
39

## Slide 40: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
40

## Slide 41: SIMDRAM Framework: Step 1
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
41

## Slide 42
Step 1: Naïve MAJ/NOT Implementation
A
B
Cin
Cout
Part 1
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
A
B
C
A
B
C
output is “1” only when A = B = “1”
  output is “0” only when A = B = “0”
Naïvely converting AND/OR/NOT-implementation to MAJ/NOT-implementation leads to an unoptimized circuit
MAJ
A
B
C
0
MAJ
A
B
C
1
42

## Slide 43
Step 1: Efficient MAJ/NOT Implementation
Part 2
Step 1 generates an optimized
MAJ/NOT-implementation of the desired operation
A
B
Cout
Cin
MAJ
Greedy
optimization
algorithm4
4 L. Amarù et al, “Majority-Inverter Graph: A Novel Data-Structure and Algorithms for Efficient Logic Optimization”, DAC, 2014.
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
43

## Slide 44: SIMDRAM Framework: Step 2
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
44

## Slide 45: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
45

## Slide 46: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
46

## Slide 47: Task 1: Allocating DRAM Rows to Operands
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
regular
row decoder
Compute
Row decoder
subarray organization
Constraint 1:
Limited number of rows reserved for computation
Allocation algorithm considers two constraints specific to processing-using-DRAM
Compute
rows
47

## Slide 48: Task 1: Allocating DRAM Rows to Operands
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
regular
row decoder
Compute
Row decoder
subarray organization
Constraint 2:
Destructive behavior
of triple-row activation
Overwritten with MAJ output
Allocation algorithm considers two constraints specific to processing-using-DRAM
48

## Slide 49: Task 1: Allocating DRAM Rows to Operands
A
B
Cout
Cin
MAJ
Allocation
algorithm
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
Allocation algorithm:
Triple-row activation
Cout
Cout
Cout
Assigns as many inputs as the number of free compute rows
All three input rows contain the MAJ output and can be reused
49

## Slide 50: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
50

## Slide 51: Task 2: Generate an Initial µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
Initial µProgram
51

## Slide 52: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
Initial µProgram
2. Optimize
52

## Slide 53: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
Coalesce
row copies
Initial µProgram
2. Optimize
53

## Slide 54: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
Merge
MAJ + row copy
Initial µProgram
2. Optimize
54

## Slide 55: Task 2: Optimize the µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Initial µProgram
Coalesce
row copies
Merge
MAJ + row copy
Optimized µProgram
2. Optimize
55

## Slide 56: Task 2: Generate N-bit Computation
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
3. Generate N-bit
computation
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Final µProgram
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Final µProgram is optimized and computes the desired operation for operands of N-bit size in a bit-serial fashion
2. Optimize
Optimized µProgram
56

## Slide 57: Task 2: Generate µProgram
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Stored in a reserved DRAM region
for future use
A new SIMDRAM instruction (called bbop_new)
added to CPU ISA
Final µProgram
Final µProgram is optimized and computes the desired operation for operands of N-bit size in a bit-serial fashion
57

## Slide 58: SIMDRAM Framework: Step 3
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
58

## Slide 59: Step 3: µProgram Execution
SIMDRAM control unit: handles the execution of the µProgram at runtime
Upon receiving a bbop instruction, the control unit:
  Loads the µProgram corresponding to SIMDRAM operation
  Issues the sequence of DRAM commands (ACT/PRE) stored in the µProgram to SIMDRAM subarrays to perform the in-DRAM operation
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
59

## Slide 60: System Integration
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
60

## Slide 61: Transposing Data
SIMDRAM operates on vertically-laid-out data
Other system components expect data to be laid out horizontally
Challenging to share data between SIMDRAM and CPU
61

## Slide 62: Transposition Unit
Last–Level Cache
Transposition Unit
Memory Controller
Object Tracker (OT)
Fetch Unit
Vertical → Horizontal
Transpose
Transpose Buffer
Store Unit
Horizontal → Vertical
Transpose
Transpose Buffer
Transforms the data layout from horizontal to vertical, and vice versa
62

## Slide 63: Efficiently Transposing Data
Last–Level Cache
Transposition Unit
Memory Controller
Object Tracker (OT)
Fetch Unit
Vertical → Horizontal
Transpose
Transpose Buffer
Store Unit
Horizontal → Vertical
Transpose
Transpose Buffer
Low impact on the throughput of
SIMDRAM operations
Low area cost (0.06 mm2 in 22nm tech. node)
63

## Slide 64: Throughput Analysis
Chart: Average Normalized Throughput (GOPS/s) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 5.5 | 0.36 | 1.98
SIMDRAM - 4 Banks | 22 | 1.5 | 7.9
SIMDRAM - 16 Banks | 88.01 | 5.82 | 31.61
SIMDRAM significantly outperforms
all state-of-the-art baselines for a wide range of operations
Average normalized throughput across all 16 SIMDRAM operations
64

## Slide 65: Energy Analysis
Average normalized energy efficiency across all 16 SIMDRAM operations
Chart: Average Energy Efficiency (GOPS/s/Watt) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 257 | 31 | 2.6
SIMDRAM - 4 Banks | 257 | 31 | 2.6
SIMDRAM - 16 Banks | 257 | 31 | 2.6
SIMDRAM is more energy-efficient than
all state-of-the-art baselines for a wide range of operations
65

## Slide 66: Real-World Applications
Chart: Average Speedup -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 3 | 0.30612 | 2.5
SIMDRAM - 4 Banks | 8.7 | 0.88776 | 7.25
SIMDRAM - 16 Banks | 21 | 2.1429 | 17.5
SIMDRAM effectively and efficiently accelerates
many commonly-used real-world applications
Average speedup across 7 real-world applications
66

## Slide 67: SIMDRAM Conclusion
SIMDRAM:
  Enables efficient computation of a flexible set and wide range of operations in a PuM massively parallel SIMD substrate
  Provides the hardware, programming, and ISA support, to:
    Address key system integration challenges
    Allow programmers to define and employ new operations without hardware changes
More in the paper:
  Efficiently transposing data
  Programming interface
  Handling page faults, address translation, coherence, and interrupts
  Security implications
  Reliability evaluation
  Comparison to in-cache computing
  And more …
  SIMDRAM is a promising PuM framework
  Can ease the adoption of processing-using-DRAM architectures
  Improves the performance and efficiency of processing-using-memory architectures
67

## Slide 68: Lecture on SIMDRAM
https://youtu.be/pmZoAAhvkRQ

## Slide 69: SIMDRAM: Follow-Ups
Limitations of current substrate?
  Computing granularity
  Data layout conversion
  High-latency bit-serial operations
  Assembly-like programming model
  Application scope
  …
We are working on even better processing-using-memory substrates
  One step at a time!

## Slide 70: 2nd Workshop on Memory-Centric Computing: Processing-Using-Memory - Part I
Dr. Geraldo F. Oliveira
https://geraldofojunior.github.io
ICS 2025
08 June 2025