## Slide 1: 2nd Workshop on Memory-Centric Computing: Processing-Using-Memory - Part II
Dr. Geraldo F. Oliveira
https://geraldofojunior.github.io
ICS 2025
08 June 2025

## Slide 2: SIMDRAM Follow-Up: MIMDRAM
Geraldo F. Oliveira, Ataberk Olgun, Abdullah Giray Yağlıkçı, F. Nisa Bostancı, Juan Gómez-Luna, Saugata Ghose, and Onur Mutlu "MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.19080.pdf

## Slide 3: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 4: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Starting with the SIMD underutilization
[NEXT]

## Slide 5: Limitations of PUD Systems: Underutilization of SIMD Lanes (I)
Ideal maximum vectorization factor = # DRAM columns (e.g., 65,536)
Application Analysis: quantify the fraction of SIMD parallelism in real applications
Maximum Vectorization Factor:
maximum number of scalar operands that fit into a SIMD register
row decoder
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: In order to understand the amount of data parallelism a processing-using-DRAM architecture can leverage, we quantify the SIMD parallelism in real applications
[CLICK] To do so, we use the maximum vectorization factor metric, which is the maximum number of scalar operands that fit into a SIMD register a given loop
[CLICK] To achieve high SIMD utilization, the ideal maximum vectorization factor of a loop should match the number of DRAM columns in a DRAM subarray
[NEXT]

## Slide 6: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: In our application analysis, we collect the maximum vectorization of all vectorizable loops in twelve applications, and report their distribution using box plots, where whiskers extend to the maximum and minimum values, and a bubble depicts averages
[CLICK] As a reference, any value above the green line represents high SIMD utilization for a PUD system.
We draw two key observations.
[NEXT]

## Slide 7: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
SIMD parallelism significantly varies within a single application and across different applications
Takeaway
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: [CLICK] First, SIMD parallelism significantly varies within and across applications
[NEXT]

## Slide 8: Limitations of PUD Systems: Underutilization of SIMD Lanes (III)
A small fraction of vectorized loops have a large enough maximum vectorization factor to fully exploit the SIMD parallelism of PUD systems
Takeaway
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: Second, only very few loops have enough data parallelism to achieve high SIMD utilization of the processing-using-DRAM architecture.
[NEXT]

## Slide 9: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Let’s now look at the second issue.
[NEXT]

## Slide 10: Limitations of PUD Systems: Limited Computation Support
row decoder
PUD systems do not support vector reduction at low area cost since data movement is bounded to within a DRAM column
Directly connecting all DRAM columns
using a custom all-to-all interconnect
leads to large (i.e., 21%) area cost
Takeaway
no direct communication path across columns
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Processing-using-DRAM can only support parallel map operations. Unfortunally, this limits processing-using-DRAM applicability, since commonly used reduction operations cannot be implemented natively.
The limiting factor to implement in-DRAM vector reduction is the lack of direct communication path across the many DRAM columns in a subarray
[CLICK] directly connecting all DRAM columns using custom fabric leads to large area costs
[NEXT]

## Slide 11: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Third, processing-using-DRAM suffers from a challenging programming model

## Slide 12: Limitations of PUD Systems: Challenging Programming Model
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
 |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Currently, processing-using-DRAM pototypes use assembly-like programming models, which leaves several key tasks for the programmer to manually handle. I will illustrate such tasks with a simple predicated addition/subtraction operation
[NEXT]

## Slide 13: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: A programmer needs to map and align the data structures involved in the computation respecting DRAM’s organization.

## Slide 14: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Identify the array boundaries of the target loops

## Slide 15: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Manually vectorize the target loop, while worrying to feed as many data operands to the DRAM array as possible, for high utilization
[NEXT]

## Slide 16: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: and manually orchestrate data movement across dependent operands.
[NEXT]

## Slide 17: Limitations of PUD Systems: Challenging Programming Model
bbop_trsp_init(A , size , elm_size);
bbop_trsp_init(B , size , elm_size);
bbop_trsp_init(C , size , elm_size);
bbop_add(D , A , B , size , elm_size);
bbop_sub(E , A , B , size , elm_size);
bbop_greater(F , A , pred , size , elm_size);
bbop_if_else(C , D , E , F , size , elm_size);
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD’s assembly-like code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: As a result, the produced processing-using-DRAM code is often complicated and potentially inefficient
[NEXT]

## Slide 18: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 19: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 20: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 21: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 22: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 23: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 24: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 rows
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 25: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 26: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 27: MIMDRAM: Modifications to DRAM Chip
inter-mat
interconnect
row decoder
global wordline
mat range
mat selector
isolation transistors
row decoder latch
IO interface
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 28: MIMDRAM: Control Unit Design
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 29: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 30: MIMDRAM: Compiler Support (I)
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 31: MIMDRAM: Compiler Support (II)
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The first pass is responsible for identifying SIMD parallelism in a code, using LLVM’s auto-vectorization engine, generate PUD instructions and set the best vectorization factor for such PUD instruction
[NEXT]

## Slide 32: MIMDRAM: Compiler Support (II)
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The second pass is responsible for scheduling and mapping computation. Our pass uses metadata to mark independent PUD instructions that should be executed concurrently across mats
[NEXT]

## Slide 33: MIMDRAM: Compiler Support (III)
Generate the appropriate binary for data allocation and PUD instructions
Goal
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: Finally, the third pass is responsible for code generation and data allocation for PUD instructions
[NEXT]

## Slide 34: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Notes: Such system support includes ISA extensions, execution and data transposition, data coherence, address translation, data allocation and alignment, and metadata translation
[NEXT]

## Slide 35: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 36: Evaluation: Multi-Programmed Workload Analysis
Chart: Normalized Weighted Speedup (Higher is Better)
| SIMDRAM:1 | SIMDRAM:2 | SIMDRAM:4 | SIMDRAM:8 | MIMDRAM
ws_average | 1 | 1.2006 | 1.3094 | 1.3253 | 2.0209
MIMDRAM significantly improves system throughput (1.68x) compared to SIMDRAM
Takeaway
Notes: [CLICK] Next, we evaluate the system throughput of MIMDRAM and SIMDRAM using the weighted speedup metric. For fairness, we enable concurrent executions of PUD operations in SIMDRAM using bank-level parallelism of
[CLICK] One
[CLICK] Two
[CLICK] Fourth,
[CLICK] Eight simultaneous PUD operations
[CLICK]
[CLICK] We observe that MIMDRAM improves system throughput using a single DRAM bank for computation compared to SIMDRAM.
[NEXT]

## Slide 37: Evaluation: More in the Paper
MIMDRAM with subarray and bank-level parallelism
  MIMDRAM provides significant performance gains compared to the baseline CPU (13.2x) and GPU (2x)
Comparison to DRISA and Fulcrum for multi-programmed workloads
  MIMDRAM achieves system throughput on par with DRISA and Fulcrum
MIMDRAM’s SIMD utilization versus SIMDRAM
  MIMDRAM provides 15.6x the utilization of SIMDRAM
Area analysis
  MIMDRAM adds small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
Notes: We have many more results in our paper, including.
[CLICK] Comparison to DRISA and Fulcrum for multi-applications
[CLICK] SIMDRAM utilization versus SIMDRAM
[CLICK] MIMDRAM’s performance with subarray and bank-level parallelism
[CLICK] and area analysis
[NEXT]

## Slide 38: Outline
Processing-Using-Memory (PUM) Solutions
  Review of DRAM Background, RowClone, and Ambit
  SIMDRAM & MIMDRAM: Generalizing PUM Computing
  pLUTo: Extending Operation Support with LUTs
  PUM in Off-the-Shelf DRAM Chips
  PUM Beyond Boolean/Arithmetic and DRAM
Processing-Near-Memory (PNM) Solutions
  Overview
  Accelerating Neural Networks & Databases
  Real PNM Systems
Barriers for Adoption (and Current Solutions)
Conclusion

## Slide 39: In-DRAM Lookup-Table Based Execution
João Dinis Ferreira, Gabriel Falcao, Juan Gómez-Luna, Mohammed Alser, Lois Orosa, Mohammad Sadrosadati, Jeremie S. Kim, Geraldo F. Oliveira, Taha Shahroodi, Anant Nori, and Onur Mutlu, "pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (26 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2104.07699.pdf

## Slide 40: Limitations of Processing-using-DRAM
Data Movement | RowClone, Seshadri+ 2013 LISA, Chang+ 2013
Bitwise Operations | Ambit, Seshadri+ 2017
Bit Shifting | DRISA, Li+ 2017
Arithmetic Operations | SIMDRAM, Hajinazar & Oliveira+ 2021
Existing Processing-using-DRAM architectures only support a limited range of operations
Notes: THE RANGE OF OPERATIONS SUPPORTED BY PRIOR PROCESSING-USING-MEMORY PROPOSALS IS LIMITED TO DATA MOVEMENT, BITWISE OPERATIONS, BUT SHIFTING, AND ARITHMETIC OPERATIONS.
THIS LIMITS THE POTENTIAL OF PROCESSING-USING-MEMORY TO TARGET MANY REAL-WORLD APPLICATIONS THAT REQUIRE MORE COMPLEX OPERATIONS.

## Slide 41: The Goal of pLUTo
Extend Processing-using-DRAM to support the execution of arbitrarily complex operations
Notes: STATED PLAINLY, THE GOAL OF PLUTO IS THUS, PRECISELY, TO **EXTEND**…

## Slide 42
x
pLUTo: Key Idea
?
output
x
input
x
ALU
f(x)
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 43
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 44
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 45
row buffer
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 46
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
0
1
2
3
row buffer
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 47
row buffer
row decoder
0
1
2
3
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
2
3
5
7
2
3
5
7
2
3
5
7
Multiple copies of the lookup table
→ exploit DRAM parallelism
2
3
5
7
2
3
5
7
DRAM array
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 48
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
pLUTo
row sweep
DRAM array
row buffer
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 49
0
0
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 50
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
match logic
Accessing
the 2nd (1) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 51
match logic
Accessing
the 2nd (1) prime number?
input
vector
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
input
vector
row buffer
pLUTo
row sweep
0 = 1 ?
1
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 52
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
?
𝘅
input
vector
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 53
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
𝘅
input
vector
input
vector
row buffer
Accessing
the 1st (0) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 54
input
vector
Accessing
the 1st (0) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
row buffer
𝘅
0
pLUTo
row sweep
0 = 0 ?
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 55
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 56
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 57
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
input
vector
?
✓
𝘅
input
vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 58
Accessing
the 4th (3) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
?
✓
𝘅
𝘅
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 59
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
3 | 3 | 3 | 3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 60
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 61
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 62
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 63
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 64
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
3
𝘅
𝘅
1
2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
𝘅
𝘅
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 65
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
7 | 7 | 7 | 7
3 | 2 | 3 | -
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 66
0
1
2
3
output
vector
3 | 2 | 3 | -
- | - | - | -
7 | 7 | 7 | 7
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
𝘅
✓
𝘅
7
𝘅
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 67
0
1
2
3
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
7 | 7 | 7 | 7
𝘅
✓
𝘅
𝘅
3 | 2 | 3 | -
7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 68
pLUTo Designs: Tradeoff Space
Chart: 
| Performance | Energy Efficiency | Area Efficiency
BSA | 8 | 8 | 5
GSA | 4 | 4 | 10
GMC | 10 | 10 | 3
v
Performance
Area Efficiency
Energy Efficiency
Gated Sense Amplifier
Buffered Sense Amplifier
Gated Memory Cell
pLUTo designs cover a broad design space and provide different performance, energy, and area efficiency

## Slide 69
System Integration
C-Like Code with
pLUTo API calls
Assembly Code with pLUTo ISA Extensions
Execution in the DRAM Substrate
pLUTo Compiler
pLUTo Controller
api_pluto_mul
pluto_subarray_alloc
pluto_bit_shift_l
pluto_or
pluto_op
ACT
PRE
ACT
ACT
PRE
...

## Slide 70: More in the Paper
https://arxiv.org/pdf/2104.07699.pdf
Notes: YOU CAN FIND MORE DETAILS ABOUT OUR PROPOSED SYSTEM INTEGRATION STACK IN OUR PAPER,
INCLUDING A STEP-BY-STEP EXAMPLE OF HOW AN APPLICATION CHANGES FROM HIGH-LEVEL C CODE TO THE LOW-LEVEL PLUTO INSTRUCTIONS THAT MAP TO DRAM COMMANDS.

## Slide 71
Average speedup across 7 real-world workloads
Performance
Chart: Average Speedup
| CPU | GPU | PnM
pLUTo-GSA | 357 | 0.6 | 9.2
pLUTo-BSA | 713 | 1.2 | 18.3
pLUTo-GMC | 1413 | 2.3 | 36.2
pLUTo significantly outperforms CPU, GPU and PnM baselines

## Slide 72
Average speedup normalized to area across 7 real-world workloads
Performance (normalized to area)
Chart: Average Speedup per Unit Area
| CPU | GPU | PnM
pLUTo-GSA | 426 | 441
pLUTo-BSA | 801 | 830
pLUTo-GMC | 1504 | 1558
pLUTo provides substantially higher performance per unit area than both the CPU and the GPU

## Slide 73
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 74: SRC TECHCON Presentation
Geraldo F. Oliveira
  pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables
  https://arxiv.org/pdf/2104.07699.pdf
https://youtu.be/9t1FJQ6nNw4?si=bhylWCLZde2DC7os

## Slide 75: Outline
Processing-Using-Memory (PUM) Solutions
  Review of DRAM Background, RowClone, and Ambit
  SIMDRAM & MIMDRAM: Generalizing PUM Computing
  pLUTo: Extending Operation Support with LUTs
  PUM in Off-the-Shelf DRAM Chips
  PUM Beyond Boolean/Arithmetic and DRAM
Processing-Near-Memory (PNM) Solutions
  Overview
  Accelerating Neural Networks & Databases
  Real PNM Systems
Barriers for Adoption (and Current Solutions)
Conclusion

## Slide 76: Bulk Bitwise Operations in Real DRAM Chips
Ismail Emir Yüksel, Yahya Can Tugrul Ataberk Olgun, F. Nisa Bostancı, A. Giray Yaglıkçı, Geraldo F. Oliveira, Haocong Luo, Juan Gómez-Luna, Mohammad Sadrosadati, Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis," Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.18736

## Slide 77: The Capability of COTS DRAM Chips
77
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 78: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
78
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 79: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
79
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 80: The Capability of COTS DRAM Chips
80
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: In this analysis,
[CLICK] we will demonstrate that how off-the-shelf DRAM chips are capable of simultaneously activating up to 48 rows in two neighboring subarrays

## Slide 81: Characterization Methodology
81
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
All rows in Subarray X
To understand which and how many rows are simultaneously activated
  Sweep Row A and Row B addresses
All rows in Subarray Y
Notes: [CLICK] To rigorously characterize and to understand which and how many rows are activated
[CLICK] We sweep two key parameters: Row A address: we sweep it to test all rows in Subarray X and Row B address: we test all rows in Subarray Y, again to remind you Subarray X and Subarray Y are neighbors

## Slide 82: Key Results
82
Exactly the same number of rows
in each subarray
are activated
Twice as many rows in one subarray
compared to its neighbor subarray are activated
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
when two rows are activated with violated timings
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
A total of 32 rows
A total of 48 rows
Notes: We observe when Row A and B in neighboring subarrays are activated with violated timing parameters
[CLICK] Off-the-shelf DRAM chips have two distinct sets of simultaneous activation patterns in two neighboring subarrays
[CLICK] First pattern is exactly the same number rows in each subarray are activated.
[CLICK] We observe that we can activate up to 16 rows in neighboring subarrays, in other words a total of 32 rows
[CLICK] Second pattern is twice as many rows in one subarray compared to its neighbor subarray are activated
[CLICK] We observe that we can activate up to 16 rows in one subarray while activating up to 32 rows in its neighbor subarray, a total of 48 rows

## Slide 83: The Capability of COTS DRAM Chips
83
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays
[CLICK] By leveraging our first observation, now let’s see how we can perform NOT operation in off-the-shelf DRAM chips

## Slide 84: Characterization Methodology
84
ACT Row A
PRE
ACT Row B
<3ns
All rows in Subarray X
All rows in Subarray Y
Nominal
Sweep Row A and Row B addresses
Sweep DRAM chip temperature
50◦C
95◦C
Notes: To answer these questions,
[CLICK] similar to our previous analysis, we sweep Row addresses where Row A and Row B in neighboring subarrays
[CLICK] We sweep DRAM chip temperature from 50 degree Celsius to 95 degree celcius

## Slide 85: Key Takeaways from In-DRAM NOT Operation
85
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Key Takeaway 1
Temperature has a small effect on
the reliability of NOT operations
Key Takeaway 2
Notes: This analysis provides two key takeaway lessons: [CLICK]
[CLICK] First, off-the-shelf DRAM chips can perform NOT operations with up to 32 destination rows
[CLICK] Second, temperature has a small effect on the reliability of NOT operations

## Slide 86: The Capability of COTS DRAM Chips
86
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] Until now, We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays and performing NOT operation
[CLICK] Now we will see how these two demonstrations enables us to perform up to 16-input AND, NAND, OR, and NOR operations

## Slide 87: Key Idea
87
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in A and B and the bitline at the top subarray becomes the function of voltages in X and Y
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 88: Two-Input AND and NAND Operations
88
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
VDD
VDD/2*
Notes: Now let me show you the basic intuition to perform two-input AND and NAND operations.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2
[CLICK] and in the compute subarray we have X and Y.
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half.
With this setup, if we activate all these four cells
[CLICK] using ACT-PRE-ACT sequence, we will get AND of X and Y in the compute subarray and NAND of X and Y in the reference subarray. Now let me prove that that is the case. I am going to cover all combinations of X and Y values.

## Slide 89: Two-Input AND and NAND Operations
VDD=1 & GND = 0
89
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1
Notes: Now let’s see an example of how we can perform two-input AND and NAND operations in off-the-shelf DRAM chips.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2 as a side note we store VDD/2,using FracDRAM’s technique.
[CLICK] and in the compute subarray we have X and Y.
[CLICK] Again we use our key command sequence ACT-PRE-ACT which simultaneously activates all four cells in our example
[CLICK] We will see how this operation enables us to store the result AND operation of X and Y in Compute cells
[CLICK] And the result of NAND of X and Y in Reference cells
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half. Let’s iterate the rows in the truth table one by one

## Slide 90: Characterization Methodology
90
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
All rows in Subarray X
Sweep Row A and Row B addresses
All rows in Subarray Y

## Slide 91: Key Takeaways from In-DRAM Operations
91
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
Key Takeaway 1
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
Key Takeaway 3
COTS DRAM chips can perform
AND, NAND, OR, and NOR operations
with very high reliability
Key Takeaway 2

## Slide 92: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 93: PiDRAM
Goal: Develop a flexible platform to explore end-to-end implementations of PuM techniques
Enable rapid integration via key components
Hardware
Software
Easy-to-extend Memory Controller
ISA-transparent PuM Controller
1
2
1
2
Extensible Software Library
Custom Supervisor Software

## Slide 94: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 95: PiDRAM Workflow
1- User application interfaces with the OS via system calls
2- OS uses PuM Operations Library (pumolib) to convey operation related information to the hardware using
3- STORE instructions that target the memory mapped registers of the PuM Operations Controller (POC)
4- POC oversees the execution of a PuM operation (e.g., RowClone, bulk bitwise operations)
5- Scheduler arbitrates between regular (load, store) and PuM operations and issues DRAM commands with custom timings

## Slide 96: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 97: Microbenchmark Copy/Initialization Throughput
In-DRAM Copy and Initialization improve throughput by 119x and 89x
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 98: PiDRAM is Open Source
https://github.com/CMU-SAFARI/PiDRAM
Notes: PiDRAM is openly and freely available on Github. If you are interested in PiDRAM, please use it and feel free to contribute to it.

## Slide 99: Extended Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 100: Long Talk + Tutorial on Youtube
https://youtu.be/s_z_S6FYpC8
Notes: I also describe PiDRAM in more detail and give a tutorial on how to use our framework in this SAFARI live seminar talk.

## Slide 101: Outline
Processing-Using-Memory (PUM) Solutions
  Review of DRAM Background, RowClone, and Ambit
  SIMDRAM & MIMDRAM: Generalizing PUM Computing
  pLUTo: Extending Operation Support with LUTs
  PUM in Off-the-Shelf DRAM Chips
  PUM Beyond Boolean/Arithmetic and DRAM
Processing-Near-Memory (PNM) Solutions
  Overview
  Accelerating Neural Networks & Databases
  Real PNM Systems
Barriers for Adoption (and Current Solutions)
Conclusion

## Slide 102: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 103: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 104: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 105: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 106: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 107: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 108: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 109: Aside: In-Memory Crossbar Computation
Shafiee+, “ISAAC: A Convolutional Neural Network Accelerator
with In-Situ Analog Arithmetic in Crossbars”, ISCA 2016.

## Slide 110: Aside: In-Memory Crossbar Computation
Notes: This is a core part of ReRAM-based PIM. We use resistance of each cell to represent the value of weight, and add voltages representing values of inputs on each row.
According to the Kirchhoff‘s law, we finally obtain a current, representing the value of output. Thus, by modifying the peripheral circuit of ReRAM array, it can support a Matrix-Multiply-Vector operation in almost one read cycle. Let’s see how to do it.
We have an input vector, multiply it with a matrix, and get an output vector.
First, we write the matrix into a ReRAM array.
Then we feed inputs into the ReRAM array, through performing an analog sum, finally we obtain outputs.

## Slide 111: 2nd Workshop on Memory-Centric Computing: Processing-Using-Memory - Part II
Dr. Geraldo F. Oliveira
https://geraldofojunior.github.io
ICS 2025
08 June 2025