## Slide 1
Proteus Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic
Geraldo F. Oliveira |  |  | 
Mayank Kabra | Yuxin Guo | Kangqi Chen | Giray Yağlıkçı
Melina Soysal | Mohammad Sadr | Joaquin O. Bueno | Saugata Ghose
Juan Gómez-Luna |  | Onur Mutlu | 
2025 International Conference on Supercomputing (ICS)
Notes: Hi, I am Geraldo, a PhD student at the SAFARI Research Group.
Today, I will talk about our work MIMDRAM: An End-to-End Processing-using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple Data Computing.
So, let’s get started.
[NEXT]

## Slide 2: Executive Summary
Key Mechanism: Proteus, a data-aware runtime PUD framework that
dynamically adjust the bit-precision, and based on that,
chooses and uses the most appropriate data representation and arithmetic algorithm implementation
for a given PUD operation
Goal: Design a PUD system that overcomes the three limitations caused by naively employing a bit-serial execution model
Key Results: Proteus achieves
17x (90.3x), 7.3x (21x), and 10.2x (8.1x) the performance per mm2 (energy reduction) of a high-end CPU, GPU, and state-of-the-art PUD system
Small area cost to a DRAM chip (1.6%) and CPU die (0.03%)
Problem: Processing-Using-DRAM (PUD) suffers from three limitations caused naive employing a bit-serial execution model
Rigid and static data representation leading to unnecessary computation
Throughput-oriented execution leading to limited latency tolerance
Scalability challenges for high-precision operations
https://github.com/CMU-SAFARI/Proteus
Notes: Before we start, I will give a summary of OUR work.
Processing-in-memory architectures are emerging solutions to mitigate data movement bottlenecks by moving computation where the data resides. In particular, processing using DRAM is a PIM architecture that utilizes DRAM’s analog operating principles to implement bulk operations.
[CLICK] Even though processing-using-DRAM can often accelerate many application domains, they suffer from three issues caused by DRAM’s large and rigid access granularity
[CLICK] First, they suffer from under-utilization due to a mismatch in the data parallelism in applications and DRAM’s data parallelism
[CLICK] Second, they suffer from limited computation support, in particular for reduction operations, due to a lack of native interconnects for data movement within a DRAM array
[CLICK] Third, programming processing using-DRAM architectures is a challenging task due to a lack of automation tools
[CLICK] Therefore, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[CLICK] To this end, we propose MIMDRAM, a hardware/software co-designed PUD system
[CLICK] The key idea of MIMDRAM is to leverage fine-grained DRAM for PUD operation, which is, the ability to access only segments of a DRAM row. We leverage such key idea in both hardware and software
[CLICK] On the hardware-side, we implement simple modifications to the DRAM array to enable the allocation of only the resources required for a PUD operation. This also allows MIMDRAM to concurrently execute independent PUD operations in a single DRAM array.
We also implement low-cost interconnects at the DRAM peripheral logic, enabling native in-DRAM vector reduction.
[CLICK] On the software side, we implement compiler and operating system support to generate and map PUD operations to the underlying hardware substrate.
[CLICK[ We extensively evaluation MIMDRAM, and we observe that it achieves
[CLICK] significant performance and energy efficiency gains compared to state-of-the-art PUD systems, a high-end CPU and GPU
[CLICK] while incuring low area cost to a DRAM chip and CPU die.
[NEXT]

## Slide 3: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 4: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 5: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 6: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 7: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
…
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
Notes: In this work, we focus on processing-using-memory architectures. In particular, its implementation using DRAM.
Before I introduce processing-using-DRAM architectures, I will provide a short background on DRAM organization and operation.
[NEXT]

## Slide 8: Background: DRAM Hierarchical Organization
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows/columns)
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 9: Background: DRAM Hierarchical Organization
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 10: Background: DRAM Operation – Row Access (ACTIVATE)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: To access data, the memory controller executes two main operations.
[CLICK] To access a DRAM row, the memory controller issues an ACTIVATE command to DRAM. On receiving an ACT, the global and local row decoder assess the wordline of the target row, connecting the DRAM cells to the bitlines
[CLICK] Then, the sense amplifier senses the perturbation caused in the bitline, amplifying and latching the data from the DRAM cells
[NEXT]

## Slide 11: Background: DRAM Operation – Column Access (READ)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
column
to memory channel
global wordline
Notes: Then, the memory controller issues a read command to read a column of data from the previously latched DRAM row.
[CLICK] The read command moves the target DRAM column from the local sense amplifiers to the global sense amplifier and finally to the memory channel via the I/O interface
[NEXT]

## Slide 12: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 13: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B0
← A0
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 14: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B0
← A0
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 15: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B0
← A0
← tmp
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
A
Sum
MAJ
Cout
MAJ
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 16: Background: Bulk Bitwise Arithmetic Operations
← A0
← tmp
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 17: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B0
← A0
← Sum0
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 18: Background: Bulk Bitwise Arithmetic Operations
← Cin
← BN
← AN
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 19: Background: Bulk Bitwise Arithmetic Operations
← Cin
← BN
← AN
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 20: Background: PUD in Commodity Off-the-Shelf DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 21: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 22: Limitations of Bit-Serial PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 23: Limitations of Bit-Serial PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 24: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → increased latency and energy
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6

## Slide 25: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → increased latency and energy
← Cin
← B0
← A0
row decoder
← Sum0
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 26: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → increased latency and energy
← Cin
← B1
← A1
row decoder
← Sum1
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 27: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → increased latency and energy
← Cin
← B2
← A2
row decoder
← Sum2
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 28: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → wasted latency and energy
← Cin
← B3
← A3
row decoder
← Sum3
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 29: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → wasted latency and energy
← Cin
← B4
← A4
row decoder
← Sum4
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 30: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → wasted latency and energy
← Cin
← B5
← A5
row decoder
← Sum5
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 31: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → wasted latency and energy
← Cin
← B6
← A6
row decoder
← Sum6
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 32: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → wasted latency and energy
← Cin
← B7
← A7
row decoder
← Sum7
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy

## Slide 33: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
minimum number of bits required to represent input operands
largest bit-precision
smallest bit-precision
bit-precision distribution

## Slide 34: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
Applications display a significant amount of narrow values → bit-precision can be reduced from 32 bits to 20 bits, on average
narrow values

## Slide 35: Limitations of Bit-Serial PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 36: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (I)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
PUD operations are inherently slow → need to operate on each bit serially to perform an operation with a data width > 1
Problem
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 37: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
2 (2’b10)
2 (2’b10)
+
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
inter-bit
dependency
tmp
tmp
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 38: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
tmp
tmp
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 39: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
tmp
tmp
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 40: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 41: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 42: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 43: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 44: Limitations of Bit-Serial PUD Systems: Throughput Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
ACT
ACT
Inter-bit dependency forces the serialization of PUD primitives
when bits of a data word are placed within the same DRAM subarray
Problem
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 45: Limitations of Bit-Serial PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 46: Limitations of Bit-Serial PUD Systems: Scalability Challenges (I)
8
16
32
64
Bit-Precision
Latency
8
16
32
64
Bit-Precision
Energy
8
16
32
N
Bit-Precision
Latency
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
8
16
32
N
Bit-Precision
Energy
bit 0
MAJ
bit 1
MAJ
bit N
MAJ
…
…
Linearly-Scaling PUD Operations (e.g., addition)
Quadratically-Scaling PUD Operations (e.g., multiplication)

## Slide 47: Problem & Goal
Naively employing a bit-serial execution model for Processing-Using-DRAM architectures limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by naively employing a bit-serial execution model
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 48: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
5
Conclusion
6
Notes: So let’s get started.
[NEXT]

## Slide 49: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 50: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 51: Opportunities for Bit-Serial PUD: Narrow Values for PUD Operations
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → dynamically identify and skip
← Cin
← B2
← A2
row decoder
← Sum2
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy
x
x
saved latency
saved energy

## Slide 52: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 53: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
Leverage bit-level parallelism to execute independent PUD primitives concurrently across different DRAM subarrays
Key Idea
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
inter-bit
independency
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 54: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
Proteus’ one-bit per-subarray data mapping → scatter bits of a data word across DRAM subarrays to expose bit-level parallelism
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
subarray0
all-bits per-subarray → forces serialization across bits
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
one-bit per-subarray → exposes bit-level parallelism
inter-subarray interconnect
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 55: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 56: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
inter-subarray interconnect
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 57: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 58: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
x
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 59: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
ACT
ACT
ACT
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 60: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
ACT
ACT
ACT
ACT
saved cycles
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 61: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
[NEXT].

## Slide 62: Opportunities for Bit-Serial PUD: Alternative Data Representation for High-Precision
Use a positional number system representation, i.e., the redundant binary representation (RBR) for high-precision PUD operations:
the operation no longer needs to propagate carry bits
the operation latency is independent of the data precision
Key Idea
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 63: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
5
Conclusion
6
Notes: So let’s get started.
[NEXT]

## Slide 64: Proteus: Design Overview (I)
3
Program Select Unit
2
Dynamic Bit-Precision Engine
1
Parallelism-Aware Program Library
Proteus, a data-aware runtime mechanism that dynamically and transparently adapts the in-DRAM implementation, bit-precision, and data format based on the input data for efficient PUD execution
  Proteus is composed of three main components:
Notes: To this end, we propose Proteus, a data-aware runtime mechanism for efficient PUD execution. Proteus adapts the bit-precision, in-DRAM implementation, and data format based on the target input data transparently from the user.
[CLICK[ Proteus is composed of three main components:
[CLICK] A parallelism-aware uProgram library
[CLICK] a Dynamic bit-precision engine
[CLICK] and a uprogram select unit
I briefly elaborate on each component next
[NEXT]

## Slide 65: Proteus: Design Overview (II)
data transposition unit
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
precision:
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine
3
Program Select Unit
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
parallelism-aware Programs
impl. #2
latency
#bits
impl. n
latency
#bits
AP
AAP
AAP
done
…
AP
AAP
AAP
done
Notes: First, the parallelism-aware uProgram is a collection of hand-optimized implementations of different PUD operations (called uPrograms). Each implementation has different trade-offs in terms of performance based on the target bit-precision
[NEXT]

## Slide 66: Proteus: Design Overview (III)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
object tracker
…
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
7
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
9
9
evicted cache line
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit
precision:
Notes: Second, the dynamic bit-precision engine aims to identify the dynamic range of evicted cache lines belonging to the target PUD operation by scanning the data within evicted cache lines to identify the largest value within a PUD memory object
[NEXT]

## Slide 67: Proteus: Design Overview (IV)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
…
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
precision:
4 bits
Notes: Third, the uProgram select unit aims to identify the appropriate bit-precision based on the previously identified largest values belonging to the memory addresses involved in the PUD operation

## Slide 68: Proteus: Design Overview (IV)
data transposition unit
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
Progs.
AAP
AP
AAP
done
AP
AAP
AAP
done
latency
#bits
impl. #2
AP
AAP
AAP
done
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
bit-precision cal.
log2
ALU
target
precision
AP
AAP
AAP
done
parallelism-aware Programs
Program
select unit
cost model
…
impl. #1
impl. n
latency
#bits
latency
#bits
precision:
4 bits
Notes: Based on this calculated target bit-precision, the uProgram select unit probes the parallelism-aware uProgram library to identify what is the best in-DRAM realization of the target operation based on the target bit-precision
[NEXT]

## Slide 69: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 70: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU (with and without Tensor Cores)
  PUD: SIMDRAM [Oliveira+, 2021]
  https://github.com/CMU-SAFARI/Proteus
Workloads
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  Linear algebra, data mining, video processing, machine learning
Metrics
  CPU-Normalized performance per area
  Energy reduction (compared to baseline CPU)
Notes: We compared Proteus to a high-end CPU and GPU, and a SIMDRAM
In our analyses, we use 12 workloads from four benchmark suites
And we evaluated CPU-normalized performance per area and energy savings
[NEXT[

## Slide 71: Evaluation: Performance Analysis
Chart: CPU-Normalized Performance/mm2
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | GMean
GPU | 211.61 | 123.42 | 0.0024 | 82.55 | 96.77 | 2.27 | 3.67 | 2.32
SIMDRAM | 2.22 | 1.69 | 6955.88 | 283.58 | 0.2 | 0.04 | 0.84 | 5.69 | 0.05 | 0.77 | 0.06 | 0.62 | 1.66
Proteus (Only w/ Dynamic Bit-Precision) | 7.72 | 18.86 | 35014.76 | 335.85 | 2.25 | 4.46 | 2.84 | 46.64 | 0.16 | 2.49 | 0.94 | 1.99 | 10.43
Proteus | 14.61 | 26.43 | 54891.64 | 1360.9 | 2.83 | 5.05 | 5.37 | 64.61 | 0.28 | 11.75 | 1.07 | 3.06 | 16.98
Proteus significantly improves performance/mm2 compared to CPU (17x), GPU (7.3x), and SIMDRAM (10.2x)
Takeaway
Notes: First, in terms of
[CLICK] performance per area, compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant performance improvements.
[CLICK] We observe that a significant portion of such improvements comes from our dynamic bit-precision engine.
[NEXT]

## Slide 72: Evaluation: Energy Analysis
Proteus significantly improves energy-efficiency compared to CPU (90.3x), GPU (21x), and SIMDRAM (8.1x)
Takeaway
Chart: CPU-Normalized Energy Reduction
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | Gmean
GPU | 133.666 | 137.751 | 0.004 | 62.848 | 163.015 | 0.001 | 9.166 | 14.832 | 4.279
SIMDRAM | 13.85 | 20.286 | 548.649 | 2941.47 | 2.992 | 0.566 | 10.539 | 13.359 | 0.713 | 9.869 | 1.279 | 3.633 | 11.108
Proteus (Only w/ Dynamic Bit-Precision) | 59.764 | 284.603 | 3426.534 | 4224.656 | 42.203 | 100.775 | 43.966 | 136.038 | 2.915 | 39.355 | 23.889 | 13.486 | 88.52
Proteus | 59.764 | 284.603 | 3426.534 | 11653.015 | 42.203 | 109.32 | 43.966 | 136.038 | 2.915 | 142.796 | 24.424 | 14.939 | 90.307
Notes: Second, in terms of
[CLICK] energy savings, we compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant energy-efficient improvements.
[NEXT]

## Slide 73: Outline
Introduction
1
Background
2
Limitations of PUD Systems
3
Proteus: Key Ideas
4
Proteus: Overview
5
Evaluation
6
Conclusion
7
Notes: So let’s get started.
[NEXT]

## Slide 74: Conclusion
https://github.com/CMU-SAFARI/Proteus
We introduce Proteus, a data-aware hardware runtime PUD framework that
that dynamically adjusts the bit-precision and, based on that, chooses and uses the most appropriate data representation and arithmetic algorithm implementation for a given PUD operation
Our extensive evaluation shows that Proteus achieves
17x (90.3x), 7.3x (21x), and 10.2x (8.1x) the performance per mm2 (energy reduction) of a CPU, GPU, and state-of-the-art PUD system, small area cost to a DRAM chip (1.6%) and CPU die (0.03%)
Notes: [CLICK] In this paper, we proposed MIMDRAM, a hardware and software co-designed PUD system that leverages fine-grained DRAM access for energy efficiency and ease to program computation
[CLICK] We extensively evaluate MIMDRAM and observe that it significantly improves performance, energy efficiency and system throughput compared to processor-centric and memory-centric architectures while incurring small area overheads
We hope and believe that MIMDRAM’s ideas and results will help to enable more efficient and easy-to-program PUD systems. To aid with this effort, we open source all our infrastructure and programs at our GitHub.
[NEXT]

## Slide 75
Proteus Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic
Geraldo F. Oliveira |  |  | 
Mayank Kabra | Yuxin Guo | Kangqi Chen | Giray Yağlıkçı
Melina Soysal | Mohammad Sadr | Joaquin O. Bueno | Saugata Ghose
Juan Gómez-Luna |  | Onur Mutlu | 
2025 International Conference on Supercomputing (ICS)
Notes: Hi, I am Geraldo, a PhD student at the SAFARI Research Group.
Today, I will talk about our work MIMDRAM: An End-to-End Processing-using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple Data Computing.
So, let’s get started.
[NEXT]