## Slide 1: Tutorial on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
Prof. Onur Mutlu
ISCA 2024
29 June 2024

## Slide 2: Agenda
Introduction to Memory-Centric Computing Systems
Invited Talk by Prof. Minsoo Rhu: “Memory-Centric Computing Systems – For AI and Beyond”
Coffee Break
Real-World Processing-Near-Memory Systems
Processing-Using-Memory Architectures for Bulk Bitwise Op.
Invited Talk by Prof. Saugata Ghose: “RACER and ReRAM PUM”
PIM Programming & Infrastructure for PIM Research
Closing Remarks

## Slide 3: Processing in Memory: Two Approaches
1. Processing near Memory
2. Processing using Memory

## Slide 4: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 5: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 6: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 7: Brief Review: Inside A DRAM Chip

## Slide 8: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array
of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
Row Buffer
Notes: A DRAM module
[CLICK] is composed of many DRAM chips
[CLICK] Each DRAM chip is composed of several banks.
[CLICK] Each bank has many subarrays, which are a 2D array of DRAM cells
[CLICK] The 2D array of DRAM cells are horizontally connected via a wordline
[CLICK] And vertically connected via a bitline
[CLICK] The bitlines are connected to an array of sense amplifiers
[CLICK] called row buffer .
[CLICK] A DRAM cell is composed of
[CLICK] A storage capacitor, which holds the data stored in DRAM as charge and
[CLICK] An access transistor, which enables and disables the charge flow from the storage capacitor to the bitline
[NEXT]

## Slide 9: Inside a DRAM Chip: Another View
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Row Buffer
Row of DRAM Cells

## Slide 10: DRAM Cell Operation
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
Notes: The DRAM cells operates using three main commands: ACTIVATE, READ/WRITE, and PRECHARGE.
[NEXT]

## Slide 11: DRAM Cell Operation (1/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. raise wordline
2. capacitor loses charge to bitline
4. amplify deviation
in the bitline
+ δ
3. enable
sense amplifier
VDD
5. capacitor charge is restored
Notes: To read the charge level stored in the storage capacitor, the memory controller issues an ACTIVATE command. Prior to receiving the ACTIVATE command, the bitline is held under a reference voltage, usually 1/2 VDD.
[CLICK] First, once the DRAM array receives the ACTIVE command, the wordline of the target row is asserted, which connects all cells along the row to their respective bitlines.
[CLICK] Second, the storage capacitor shares charge with its corresponding bitline
[CLICK] Third, the sense amplifier is enabled and
[CLICK] Fourth, the resulting bitline voltage shift is sensed and amplified by the bitline’s sense amplifier. Once the sense amplifiers finish amplification
[CLICK] the row buffer will contain the values originally stored within the cells along the asserted wordline. Also, the charge in the storage capacitor is fully restored. At the end of the ACTIVATE operation, the DRAM array is ready to receive read and write requests from the memory controller.
[NEXT]]

## Slide 12: DRAM Cell Operation (2/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
read/write charge
latched in sense amplifier
Notes: The memory controller then issues read or write commands to columns within the activated row.
[NEXT]

## Slide 13: DRAM Cell Operation (3/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
½ VDD
2. precharge bitline for next access
1. lower
wordline
3. disable
sense amplifier
Notes: To prepare the DRAM array for future access to other DRAM rows, the memory controller issues a precharge command. It works as follows
[CLICK] First, the capacitor is disconnected from the bitline by disabling the wordline
[CLICK] Second, the bitline voltage is restored to its quiescent state. Now, the DRAM array is ready for next accesses.
[CLICK] Third, the sense amplifier is disabled.
[NEXT]

## Slide 14: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 15: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
15
Notes: copy

## Slide 16: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst
16

## Slide 17: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 18: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]
18

## Slide 19: RowClone Extensions and Follow-Up Work
Can we do faster inter-subarray copy?
  Yes, see LISA [Chang et al., HPCA 2016]
Can we enable data movement at smaller granularities within a bank?
  Yes, see FIGARO [Wang et al., MICRO 2020]
Can we do better inter-bank copy?
  Yes, see Network-on-Memory [CAL 2020]
Can similar ideas and DRAM properties be used to perform computation on data?
  Yes, see Ambit [Seshadri et al., CAL 2015, MICRO 2017]

## Slide 20: LISA: Increasing Connectivity in DRAM
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 21: Moving Data Inside DRAM?
DRAM cell
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 22: Key Idea and Applications
Low-cost Inter-linked subarrays (LISA)
  Fast bulk data movement between subarrays
  Wide datapath via isolation transistors: 0.8% DRAM chip area
LISA is a versatile substrate → new applications
Subarray 1
Subarray 2
…
  Fast bulk data copy: Copy latency 1.363ms→0.148ms (9.2x) → 66% speedup, -55% DRAM energy
  In-DRAM caching: Hot data access latency 48.7ns→21.5ns (2.2x) → 5% speedup
  Fast precharge: Precharge latency 13.1ns→5.0ns (2.6x) → 8% speedup

## Slide 23: More on LISA
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 24: FIGARO: Fine-Grained In-DRAM Copy
Yaohua Wang, Lois Orosa, Xiangjun Peng, Yang Guo, Saugata Ghose, Minesh Patel, Jeremie S. Kim, Juan Gómez Luna, Mohammad Sadrosadati, Nika Mansouri Ghiasi, and Onur Mutlu, "FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020.

## Slide 25: Network-On-Memory: Fast Inter-Bank Copy
Seyyed Hossein SeyyedAghaei Rezaei, Mehdi Modarressi, Rachata Ausavarungnirun, Mohammad Sadrosadati, Onur Mutlu, and Masoud Daneshtalab, "NoM: Network-on-Memory for Inter-Bank Data Transfer in Highly-Banked Memories" IEEE Computer Architecture Letters (CAL), to appear in 2020.

## Slide 26: (Truly) In-Memory Computation
We can support in-DRAM AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 27: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 28: In-DRAM Bulk Bitwise AND/OR Operation
BULKAND A, B  C
Semantics: Perform a bitwise AND of two rows A and B and store the result in row C
R0 – reserved zero row, R1 – reserved one row
D1, D2, D3 – Designated rows for triple activation
1. RowClone A into D1
2. RowClone B into D2
3. RowClone R0 into D3
4. ACTIVATE D1,D2,D3
5. RowClone Result into C

## Slide 29: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 30: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 31: In-DRAM NOT Operation
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 32: Performance: In-DRAM Bitwise Operations

## Slide 33: Energy of In-DRAM Bitwise Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 34: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 35: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 36: More on Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 37: In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 38: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 39: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
39

## Slide 40: SIMDRAM Framework: Step 1
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
40

## Slide 41
Step 1: Naïve MAJ/NOT Implementation
A
B
Cin
Cout
Part 1
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
A
B
C
A
B
C
output is “1” only when A = B = “1”
  output is “0” only when A = B = “0”
Naïvely converting AND/OR/NOT-implementation to MAJ/NOT-implementation leads to an unoptimized circuit
MAJ
A
B
C
0
MAJ
A
B
C
1
41

## Slide 42
Step 1: Efficient MAJ/NOT Implementation
Part 2
Step 1 generates an optimized
MAJ/NOT-implementation of the desired operation
A
B
Cout
Cin
MAJ
Greedy
optimization
algorithm4
4 L. Amarù et al, “Majority-Inverter Graph: A Novel Data-Structure and Algorithms for Efficient Logic Optimization”, DAC, 2014.
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
42

## Slide 43: SIMDRAM Framework: Step 2
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
43

## Slide 44: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
44

## Slide 45: SIMDRAM Framework: Step 3
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
45

## Slide 46: Step 3: µProgram Execution
SIMDRAM control unit: handles the execution of the µProgram at runtime
Upon receiving a bbop instruction, the control unit:
  Loads the µProgram corresponding to SIMDRAM operation
  Issues the sequence of DRAM commands (ACT/PRE) stored in the µProgram to SIMDRAM subarrays to perform the in-DRAM operation
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
46

## Slide 47: More in the Paper
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
47
https://people.inf.ethz.ch/omutlu/pub/SIMDRAM_asplos21.pdf

## Slide 48: SIMDRAM Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications
48

## Slide 49: More on SIMDRAM
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 50: SIMDRAM: Follow-Ups
Limitations of current substrate?
  Computing granularity
  Data layout conversion
  High-latency bit-serial operations
  Assembly-like programming model
  Application scope
  …
We are working on even better processing-using-memory substrates
  One step at a time!

## Slide 51: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 52: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 53: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 54: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 55: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 56: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 57: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 58: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 rows
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 59: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 60: MIMDRAM: Modifications to DRAM Chip
inter-mat
interconnect
row decoder
global wordline
mat range
mat selector
isolation transistors
row decoder latch
IO interface
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 61: MIMDRAM: Control Unit Design
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 62: MIMDRAM: Compiler Support
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 63: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 64: More on MIMDRAM
Geraldo F. Oliveira, Ataberk Olgun, Abdullah Giray Yağlıkçı, F. Nisa Bostancı, Juan Gómez-Luna, Saugata Ghose, and Onur Mutlu " MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.19080.pdf

## Slide 65: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 66: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 67: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 68: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 69: In-DRAM Lookup-Table Based Execution
João Dinis Ferreira, Gabriel Falcao, Juan Gómez-Luna, Mohammed Alser, Lois Orosa, Mohammad Sadrosadati, Jeremie S. Kim, Geraldo F. Oliveira, Taha Shahroodi, Anant Nori, and Onur Mutlu, "pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (26 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2104.07699.pdf

## Slide 70: Limitations of Processing-using-DRAM
Data Movement | RowClone, Seshadri+ 2013 LISA, Chang+ 2013
Bitwise Operations | Ambit, Seshadri+ 2017
Bit Shifting | DRISA, Li+ 2017
Arithmetic Operations | SIMDRAM, Hajinazar & Oliveira+ 2021
Existing Processing-using-DRAM architectures only support a limited range of operations
Notes: THE RANGE OF OPERATIONS SUPPORTED BY PRIOR PROCESSING-USING-MEMORY PROPOSALS IS LIMITED TO DATA MOVEMENT, BITWISE OPERATIONS, BUT SHIFTING, AND ARITHMETIC OPERATIONS.
THIS LIMITS THE POTENTIAL OF PROCESSING-USING-MEMORY TO TARGET MANY REAL-WORLD APPLICATIONS THAT REQUIRE MORE COMPLEX OPERATIONS.

## Slide 71: The Goal of pLUTo
Extend Processing-using-DRAM to support the execution of arbitrarily complex operations
Notes: STATED PLAINLY, THE GOAL OF PLUTO IS THUS, PRECISELY, TO **EXTEND**…

## Slide 72
x
pLUTo: Key Idea
?
output
x
input
x
ALU
f(x)
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 73
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 74
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 75
System Integration
C-Like Code with
pLUTo API calls
Assembly Code with pLUTo ISA Extensions
Execution in the DRAM Substrate
pLUTo Compiler
pLUTo Controller
api_pluto_mul
pluto_subarray_alloc
pluto_bit_shift_l
pluto_or
pluto_op
ACT
PRE
ACT
ACT
PRE
...

## Slide 76
Average speedup normalized to area across 7 real-world workloads
Performance (normalized to area)
Chart: Average Speedup per Unit Area
| CPU | GPU | PnM
pLUTo-GSA | 426 | 441
pLUTo-BSA | 801 | 830
pLUTo-GMC | 1504 | 1558
pLUTo provides substantially higher performance per unit area than both the CPU and the GPU

## Slide 77
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 78: More Results in the Paper
Comparison with FPGA
Area Overhead Analysis
Circuit-Level Reliability & Correctness
Subarray-Level Parallelism
LUT Loading Overhead
Range of Supported Operations
https://arxiv.org/pdf/2104.07699.pdf

## Slide 79: SRC TECHCON Presentation
Geraldo F. Oliveira
  pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables
  https://arxiv.org/pdf/2104.07699.pdf
https://youtu.be/9t1FJQ6nNw4?si=bhylWCLZde2DC7os

## Slide 80: Bulk Bitwise Operations in Real DRAM Chips
Ismail Emir Yüksel, Yahya Can Tugrul Ataberk Olgun, F. Nisa Bostancı, A. Giray Yaglıkçı, Geraldo F. Oliveira, Haocong Luo, Juan Gómez-Luna, Mohammad Sadrosadati, Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis," Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.18736

## Slide 81: The Capability of COTS DRAM Chips
81
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 82: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
82
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 83: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
83
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 84: The Capability of COTS DRAM Chips
84
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: In this analysis,
[CLICK] we will demonstrate that how off-the-shelf DRAM chips are capable of simultaneously activating up to 48 rows in two neighboring subarrays

## Slide 85: Characterization Methodology
85
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
All rows in Subarray X
To understand which and how many rows are simultaneously activated
  Sweep Row A and Row B addresses
All rows in Subarray Y
Notes: [CLICK] To rigorously characterize and to understand which and how many rows are activated
[CLICK] We sweep two key parameters: Row A address: we sweep it to test all rows in Subarray X and Row B address: we test all rows in Subarray Y, again to remind you Subarray X and Subarray Y are neighbors

## Slide 86: Key Results
86
Exactly the same number of rows
in each subarray
are activated
Twice as many rows in one subarray
compared to its neighbor subarray are activated
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
when two rows are activated with violated timings
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
A total of 32 rows
A total of 48 rows
Notes: We observe when Row A and B in neighboring subarrays are activated with violated timing parameters
[CLICK] Off-the-shelf DRAM chips have two distinct sets of simultaneous activation patterns in two neighboring subarrays
[CLICK] First pattern is exactly the same number rows in each subarray are activated.
[CLICK] We observe that we can activate up to 16 rows in neighboring subarrays, in other words a total of 32 rows
[CLICK] Second pattern is twice as many rows in one subarray compared to its neighbor subarray are activated
[CLICK] We observe that we can activate up to 16 rows in one subarray while activating up to 32 rows in its neighbor subarray, a total of 48 rows

## Slide 87: The Capability of COTS DRAM Chips
87
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays
[CLICK] By leveraging our first observation, now let’s see how we can perform NOT operation in off-the-shelf DRAM chips

## Slide 88: Characterization Methodology
88
ACT Row A
PRE
ACT Row B
<3ns
All rows in Subarray X
All rows in Subarray Y
Nominal
Sweep Row A and Row B addresses
Sweep DRAM chip temperature
50◦C
95◦C
Notes: To answer these questions,
[CLICK] similar to our previous analysis, we sweep Row addresses where Row A and Row B in neighboring subarrays
[CLICK] We sweep DRAM chip temperature from 50 degree Celsius to 95 degree celcius

## Slide 89: Key Takeaways from In-DRAM NOT Operation
89
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Key Takeaway 1
Temperature has a small effect on
the reliability of NOT operations
Key Takeaway 2
Notes: This analysis provides two key takeaway lessons: [CLICK]
[CLICK] First, off-the-shelf DRAM chips can perform NOT operations with up to 32 destination rows
[CLICK] Second, temperature has a small effect on the reliability of NOT operations

## Slide 90: The Capability of COTS DRAM Chips
90
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] Until now, We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays and performing NOT operation
[CLICK] Now we will see how these two demonstrations enables us to perform up to 16-input AND, NAND, OR, and NOR operations

## Slide 91: Key Idea
91
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in A and B and the bitline at the top subarray becomes the function of voltages in X and Y
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 92: Two-Input AND and NAND Operations
VDD=1 & GND = 0
92
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1
Notes: Now let’s see an example of how we can perform two-input AND and NAND operations in off-the-shelf DRAM chips.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2 as a side note we store VDD/2,using FracDRAM’s technique.
[CLICK] and in the compute subarray we have X and Y.
[CLICK] Again we use our key command sequence ACT-PRE-ACT which simultaneously activates all four cells in our example
[CLICK] We will see how this operation enables us to store the result AND operation of X and Y in Compute cells
[CLICK] And the result of NAND of X and Y in Reference cells
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half. Let’s iterate the rows in the truth table one by one

## Slide 93: Key Takeaways from In-DRAM Operations
93
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
Key Takeaway 1
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
Key Takeaway 3
COTS DRAM chips can perform
AND, NAND, OR, and NOR operations
with very high reliability
Key Takeaway 2

## Slide 94: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 95: PiDRAM
Goal: Develop a flexible platform to explore end-to-end implementations of PuM techniques
Enable rapid integration via key components
Hardware
Software
Easy-to-extend Memory Controller
ISA-transparent PuM Controller
1
2
1
2
Extensible Software Library
Custom Supervisor Software

## Slide 96: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 97: PiDRAM Workflow
1- User application interfaces with the OS via system calls
2- OS uses PuM Operations Library (pumolib) to convey operation related information to the hardware using
3- STORE instructions that target the memory mapped registers of the PuM Operations Controller (POC)
4- POC oversees the execution of a PuM operation (e.g., RowClone, bulk bitwise operations)
5- Scheduler arbitrates between regular (load, store) and PuM operations and issues DRAM commands with custom timings

## Slide 98: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 99: Microbenchmark Copy/Initialization Throughput
In-DRAM Copy and Initialization improve throughput by 119x and 89x
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 100: PiDRAM is Open Source
https://github.com/CMU-SAFARI/PiDRAM
Notes: PiDRAM is openly and freely available on Github. If you are interested in PiDRAM, please use it and feel free to contribute to it.

## Slide 101: Extended Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 102: Long Talk + Tutorial on Youtube
https://youtu.be/s_z_S6FYpC8
Notes: I also describe PiDRAM in more detail and give a tutorial on how to use our framework in this SAFARI live seminar talk.

## Slide 103: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 104: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 105: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 106: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 107: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 108: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 109: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 110: Aside: In-Memory Crossbar Computation
Shafiee+, “ISAAC: A Convolutional Neural Network Accelerator
with In-Situ Analog Arithmetic in Crossbars”, ISCA 2016.

## Slide 111: Aside: In-Memory Crossbar Computation
Notes: This is a core part of ReRAM-based PIM. We use resistance of each cell to represent the value of weight, and add voltages representing values of inputs on each row.
According to the Kirchhoff‘s law, we finally obtain a current, representing the value of output. Thus, by modifying the peripheral circuit of ReRAM array, it can support a Matrix-Multiply-Vector operation in almost one read cycle. Let’s see how to do it.
We have an input vector, multiply it with a matrix, and get an output vector.
First, we write the matrix into a ReRAM array.
Then we feed inputs into the ReRAM array, through performing an analog sum, finally we obtain outputs.

## Slide 112: Tutorial on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
Prof. Onur Mutlu
ISCA 2024
29 June 2024

## Slide 113: Agenda
Introduction to Memory-Centric Computing Systems
Invited Talk by Prof. Minsoo Rhu: “Memory-Centric Computing Systems – For AI and Beyond”
Coffee Break
Real-World Processing-Near-Memory Systems
Processing-Using-Memory Architectures for Bulk Bitwise Op.
Invited Talk by Prof. Saugata Ghose: “RACER and ReRAM PUM”
PIM Programming & Infrastructure for PIM Research
Closing Remarks