## Slide 1: Tutorial on Memory-Centric Computing: PIM Adoption & Programmability
Geraldo F. Oliveira
Prof. Onur Mutlu
ISCA 2024
29 June 2024

## Slide 2: Agenda
Introduction to Memory-Centric Computing Systems
Invited Talk by Prof. Minsoo Rhu: “Memory-Centric Computing Systems – For AI and Beyond”
Coffee Break
Real-World Processing-Near-Memory Systems
Processing-Using-Memory Architectures for Bulk Bitwise Op.
Invited Talk by Prof. Saugata Ghose: “RACER and ReRAM PUM”
PIM Programming & Infrastructure for PIM Research
Closing Remarks

## Slide 3: Processing in Memory: Adoption Challenges
1. Processing near Memory
2. Processing using Memory

## Slide 4: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 5: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 6: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 7: Adoption: How to Keep It Simple?
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 8: Adoption: How to Ease Programmability? (I)
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu, “DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” in PACT SRC Student Competition, Vienna, Austria, October 2023.

## Slide 9: Adoption: How to Ease Programmability? (II)
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, YuXin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 10
Jinfan Chen, Juan Gómez Luna, Izzat El Hajj, Yuxin Guo, Onur Mutlu
SimplePIM:
A Software Framework for Productive and Efficient Processing-in-Memory
https://arxiv.org/pdf/2310.01893.pdf
https://github.com/CMU-SAFARI/SimplePIM

## Slide 11: Executive Summary
Processing-in-Memory (PIM) promises to alleviate the data movement bottleneck
Real PIM hardware is now available, e.g., UPMEM PIM
However, programming real PIM hardware is challenging, e.g.:
  Distribute data across PIM memory banks,
  Manage data transfers between host cores and PIM cores, and between PIM cores,
  Launch PIM kernels on the PIM cores, etc.
SimplePIM is a high-level programming framework for real PIM hardware
  Iterators such as map, reduce, and zip
  Collective communication with broadcast, scatter, and gather
Implementation on UPMEM and evaluation with six different workloads
  Reduction, vector add, histogram, linear/logistic regression, K-means
  4.4x fewer lines of code compared to hand-optimized code
  Between 15% and 43% faster than hand-optimized code for three workloads
Source code: https://github.com/CMU-SAFARI/SimplePIM

## Slide 12: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 13: Processing-in-Memory (PIM)
PIM is a computing paradigm that advocates for memory-centric computing systems, where processing elements are placed near or inside the memory arrays
Real-world PIM architectures are becoming a reality
  UPMEM PIM, Samsung HBM-PIM, Samsung AxDIMM, SK Hynix AiM, Alibaba HB-PNM
These PIM systems have some common characteristics:
  There is a host processor (CPU or GPU) with access to (1) standard main memory, and (2) PIM-enabled memory
  PIM-enabled memory contains multiple PIM processing elements (PEs) with high bandwidth and low latency memory access
  PIM PEs run only at a few hundred MHz and have a small number of registers and small (or no) cache/scratchpad
  PIM PEs may need to communicate via the host processor

## Slide 14: A State-of-the-Art PIM System
In our work, we use the UPMEM PIM architecture
  General-purpose processing cores called DRAM Processing Units (DPUs)
    Up to 24 PIM threads, called tasklets
    32-bit integer arithmetic, but multiplication/division are emulated*, as well as floating-point operations
  64-MB DRAM bank (MRAM), 64-KB scratchpad (WRAM)
* 8-bit integer multiplication is natively supported

## Slide 15: Programming a PIM System (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 16: Programming a PIM System (II)
PIM programming is challenging
  Manage data movement between host DRAM and PIM DRAM
    Parallel, serial, broadcast, and gather/scatter transfers
  Manage data movement between PIM DRAM bank and scratchpad
    8-byte aligned and maximum of 2,048 bytes
  Multithreaded programming model
  Inter-thread synchronization
    Barriers, handshakes, mutexes, and semaphores
Our Goal
Design a high-level programming framework that abstracts these hardware-specific complexities and provides a clean yet powerful interface for ease of use and high program performance

## Slide 17: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 18: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads
Notes: [CLICK] Our software framework, SimplePIM, leverages the massive memory bandwidth and parallelism offered by PIM hardware to operate on arrays of arbitrary size and dimensions. SimplePIM offers three key interfaces to support PIM systems like UPMEM.
[CLICK] The management interface stores metadata for the PIM-resident arrays, which can be accessed by the programmer and other parts of SimplePIM as needed.
[CLICK] The communication interface provides abstractions for both Host-PIM and PIM-PIM communication patterns.
These patterns are similar to communication patterns in other distributed frameworks such as MPI [71], which makes it easier for SimplePIM to be adopted.
[CLICK] The processing interface leverages PIM’s high memory bandwidth and parallelism to execute map, reduce, and zip iterators on PIM arrays.
Programmers can combine these iterators to implement many widely-used workloads ranging from simple vector addition to complex machine learning model training.
[CLICK] Let’s check each one of these interfaces next
[NEXT]

## Slide 19: Management Interface
Metadata for PIM-resident arrays
  array_meta_data_t describes a PIM-resident array
  simple_pim_management_t for managing PIM-resident arrays
lookup: Retrieves all relevant information of an array
register: Registers the metadata of an array
free: Removes the metadata of an array
void simple_pim_array_free(const char* id, simple_pim_management_t* management);
array_meta_data_t* simple_pim_array_lookup(const char* id,
simple_pim_management_t* management);
void simple_pim_array_register(array_meta_data_t* meta_data,
simple_pim_management_t* management);

## Slide 20: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads

## Slide 21: Host-to-PIM Communication: Broadcast
SimplePIM Broadcast
  Transfers a host array to all PIM cores in the system
void simple_pim_array_broadcast(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 22: Host-to-PIM Communication: Scatter/Gather
SimplePIM Scatter
  Distributes an array to PIM DRAM banks
SimplePIM Gather
  Collects portions of an array from PIM DRAM banks
void* simple_pim_array_gather(char* const id, simple_pim_management_t* management);
void simple_pim_array_scatter(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 23: PIM-PIM Communication: AllReduce
SimplePIM AllReduce
  Used for algorithm synchronization
  The programmer specifies an accumulative function
void simple_pim_array_allreduce(char* const id, handle_t* handle,
simple_pim_management_t* management);

## Slide 24: PIM-PIM Communication: AllGather
SimplePIM AllGather
  Combines array pieces and distributes the complete array to all PIM cores
void simple_pim_array_allgather(char* const id, char* new_id,
simple_pim_management_t* management);

## Slide 25: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads

## Slide 26: Processing Interface: Map
Array Map
  Applies map_func to every element of the data array
void simple_pim_array_map(const char* src_id, const char* dest_id,
uint32_t output_type, handle_t* handle, simple_pim_management_t* management);

## Slide 27: Processing Interface: Reduction
Array Reduction
  The map_to_val_func function transforms an input element to an output value and an output index
  The acc_func function accumulates the output values onto the output array
void simple_pim_array_red(const char* src_id, const char* dest_id,
uint32_t output_type, uint32_t output_len, handle_t* handle,
simple_pim_management_t* management);

## Slide 28: Processing Interface: Zip
Array Zip
  Takes two input arrays and combines their elements into an output array
void simple_pim_array_zip(const char* src1_id, const char* src2_id,
const char* dest_id, simple_pim_management_t* management);

## Slide 29: General Code Optimizations
Strength reduction
Loop unrolling
Avoiding boundary checks
Function inlining
Adjustment of data transfer sizes

## Slide 30: More in the Paper
Strength reduction
Loop unrolling
Avoiding boundary checks
Function inlining
Adjustment of data transfer sizes
https://arxiv.org/pdf/2310.01893.pdf

## Slide 31: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 32: Evaluation Methodology
Evaluated system
  UPMEM PIM system with 2,432 PIM cores with 159 GB of PIM DRAM
Real-world Benchmarks
  Vector addition
  Reduction
  Histogram
  K-Means
  Linear regression
  Logistic regression
Comparison to hand-optimized codes in terms of programming productivity and performance

## Slide 33: Productivity Improvement (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 34: Productivity Improvement (II)
Example: SimplePIM histogram
// Programmer-defined functions in the file "histo_filepath"
void init_func (uint32_t size, void* ptr) {
char* casted_value_ptr = (char*) ptr;
for (int i = 0; i < size; i++)
casted_value_ptr[i] = 0;
}
void acc_func (void* dest, void* src) {
*(uint32_t*)dest += *(uint32_t*)src;
}
void map_to_val_func (void* input, void* output, uint32_t* key) {
uint32_t d = *((uint32_t*)input);
*(uint32_t*)output = 1;
*key = d * bins >> 12;
}
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);

## Slide 35: Productivity Improvement (III)
Lines of code (LoC) reduction
 | SimplePIM | Hand-optimized | LoC Reduction
Reduction | 14 | 83 | 5.93×
Vector Addition | 14 | 82 | 5.86×
Histogram | 21 | 114 | 5.43×
Linear Regression | 48 | 157 | 3.27×
Logistic Regression | 59 | 176 | 2.98×
K-Means | 68 | 206 | 3.03×
SimplePIM reduces the number of lines of effective code
by a factor of 2.98× to 5.93×

## Slide 36: Performance Evaluation (I)
Weak scaling analysis
SimplePIM achieves comparable performance for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 10%-37%

## Slide 37: Performance Evaluation (II)
Strong scaling analysis
SimplePIM scales better than hand-optimized implementations for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 15%-43%

## Slide 38: Discussion
SimplePIM is devised for PIM architectures with
  A host processor with access to standard main memory and PIM-enabled memory
  PIM processing elements (PEs) that communicate via the host processor
  The number of PIM PEs scales with memory capacity
SimplePIM emulates the communication between PIM cores via the host processor
Other parallel patterns can be incorporated in future work
  Prefix sum and filter can be easily added
  Stencil and convolution would require fine-grained scatter-gather for halo cells
  Random access patterns would be hard to support

## Slide 39: SimplePIM: arXiv Version
https://arxiv.org/pdf/2310.01893.pdf

## Slide 40: Source Code
https://github.com/CMU-SAFARI/SimplePIM

## Slide 41: Conclusion
Processing-in-Memory (PIM) promises to alleviate the data movement bottleneck
Real PIM hardware is now available, e.g., UPMEM PIM
However, programming real PIM hardware is challenging, e.g.:
  Distribute data across PIM memory banks,
  Manage data transfers between host cores and PIM cores, and between PIM cores,
  Launch PIM kernels on the PIM cores, etc.
SimplePIM is a high-level programming framework for real PIM hardware
  Iterators such as map, reduce, and zip
  Collective communication with broadcast, scatter, and gather
Implementation on UPMEM and evaluation with six different workloads
  Reduction, vector add, histogram, linear/logistic regression, K-means
  4.4x fewer lines of code compared to hand-optimized code
  Between 15% and 43% faster than hand-optimized code for three workloads
Source code: https://github.com/CMU-SAFARI/SimplePIM

## Slide 42: Adoption: How to Maintain Coherence? (I)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 43: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 44: Adoption: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 45: Adoption: How to Support Synchronization?
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 46: Adoption: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 47: Adoption: Code and Data Mapping
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 48: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 49: Identifying Memory Bottlenecks
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
9
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]

## Slide 50: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Compute Roof
y = Peak System Throughput
Memory Roof
y = BW x AI
Compute Bound →
Not suitable for NDP
Memory Bound →
Suitable for NDP
10
Notes: A roofline model is a simple model used to identify if an application is memory-bound or compute-bound. The x-axis of the plot defines the Arithmetic Intensity of an application, calculated as the number of Operations the application executes per byte it accesses. The y-axis defines the performance of the application in GOPS/s
[CLICK] it has two main lines that characterizes the application and system. The first line is called Compute Roof, and it is defined as the maximum peak system throughput. Applications below this curve are called compute-bound. Prior works show that a compute bound application does not benefit from NDP
[CLICK] The second line is called memory roof. It is defined as the maximum DRAM bandwidth times the arithmetic intensity of the application. Prior works show that an application below this curve are memory-bound, and are suitable for NDP offloading.
[NEXT]

## Slide 51: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
11
Notes: We use this model with more than 40 applications that we will analyze later. We compare when such applications benefits from a general purpose NDP architecture.
In the plot, we classify the applications as:
[CLICK] Runs faster on the CPU, compared to running on the NDP system
[CLICK] Runs faster on the NDP, compared to running on the CPU system
[CLICK] Similar on CPU and NDP, when running an application on the NDP and host system achieves similar performance.
[CLICK] And depends, when application benefits from NDP depending on system configuration (e.g., core count) compared to a regular host system.
[CLICK] Based on that, we make the following observations.
[NEXT]

## Slide 52: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Memory Bound applications are
faster on NDP
Compute Bound applications
are faster on CPU
Memory Bound applications
are faster on CPU,
or performance depends ❌
Compute Bound applications
have similar performance on CPU/NDP or performance depends ❌
12
✓
✓
Notes: First, memory bound applications benefit from NDP, as prior works indicated
[CLICK] Second, compute bound applications do not benefit from NDP, also as indicated by prior works
[CLICL] However, we observe that some memory bound applications can also not benefit from NDP, or benefit from it in particular configurations (at different core counts for example)
[CLICK] This behavior also happens for compute bound applications [NEXT]

## Slide 53: Limitations of Prior Approaches (1/2)
Roofline model → identifies when an application is bounded by compute or memory units
Memory Bound applications are
faster on NDP
Compute Bound applications
are faster on CPU
Memory Bound applications
are faster on CPU,
or performance depends ❌
Compute Bound applications
have similar performance on CPU/NDP or performance depends ❌
13
✓
✓
  Roofline model does not accurately account
  for the NDP suitability of memory-bound applications
Notes: [CLICK] Therefore, we conclude that the roofline model cannot accurately account for NDP suitability of memory-bound applications
[NEXT]

## Slide 54: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
14
LLC MPKI
NDP Speedup over CPU
Notes: Next, we analyze another metric utilized to indicate NDP suitability. Prior works say that an application with high LLC MPKI (usually a value higher than 10) benefits from NDP. We checked this observation by evaluating the speedup provided by NDP for of a large number of application (in the y-axis), and the applications MPKI (in the x-axis). We make the following observations
[NEXT]

## Slide 55: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
Applications with
high MPKI are
faster on NDP
Applications with
low MPKI are
faster on CPU
Applications with low MPKI can be
faster on NDP;
have similar performance on
CPU/NDP or;
performance can depends ❌
15
✓
✓
LLC MPKI
NDP Speedup over CPU
Notes: First, as expected, applications with high last-level misses per-kilo instructions always benefit from NDP.
[CLICK] Likewise, applications with low MPKI never benefit from NDP
[CLICK] However, we observe that applications with low MPKI can either benefit from NDP depending on the system configuration or they can have similar performance as the NDP system
[NEXT]

## Slide 56: Limitations of Prior Approaches (2/2)
Application with a last-level cache MPKI > 10 → memory intensive and benefits from NDP
Applications with
high MPKI are
faster on NDP
Applications with
low MPKI are
faster on CPU
Applications with low MPKI can be
faster on NDP;
have similar performance on
CPU/NDP or;
performance can depends ❌
16
✓
✓
LLC MPKI
NDP Speedup over CPU
  LLC MPKI does not accurately account
  for the NDP suitability of memory-bound applications
Notes: [CLICK] Therefore, we conclude that the MPKI alone cannot accurately account for NDP suitability of memory-bound applications
[NEXT]

## Slide 57: Identifying Memory Bottlenecks
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
17
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
Notes: [NEXT]

## Slide 58: The Problem
Multiple approaches to identify applications that:
  suffer from data movement bottlenecks
  take advantage of NDP
Existing approaches are not comprehensive enough
18
Arithmetic Intensity (OPS/byte)
Performance (GOPS/s)
Roofline model
Last-Level Cache MPKI
NDP Speedup over CPU
High LLC MPKI
  No available methodology can comprehensively:
  − identify data movement bottlenecks
  − correlate them with the most suitable data movement mitigation mechanism
Notes: To summarize, different approaches used by prior works to identify memory bottlenecks and NDP suitability are not comprehensive enough in
[CLICK] identifying data movement bottlenecks
[CLICK] correlating different data movement mitigation mechanisms, as NDP, with the different types of data movement bottlenecks.
[NEXT]

## Slide 59: Our Goal
Our Goal: develop a methodology to:
    methodically identify sources of data movement bottlenecks
    comprehensively compare compute- and memory-centric data movement mitigation techniques
19
Notes: THEREFORE, our goal is to develop a methodology to
[CLICK] methodically identify the major sources of inefficiency that lead to data movement bottlenecks by observing and identifying relevant metrics and
[CLICK] comprehensively compare traditional compute-centric data movement mitigation techniques to more memory-centric techniques, thereby developing a rigorous understanding of the best techniques to mitigate each source of data movement.
[NEXT]

## Slide 60: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
264
Notes: Our methodology has three steps.
[CLICK] It takes as input an application’s source code and its input datasets.
[CLICK] In Step 1, we use a hardware profiling tool to identify memory-bound functions across many applications. This step allows for a quick first-level identification of many applications that suffer from memory bottlenecks and functions that cause these bottlenecks.
[CLICK] We utilize a new simulator, called DAMOV-SIM to collect key metrics and execute performance analysis of the functions identified in Step 1.
[CLICK] In Step 2, we use the architecture-independent profiling tool to collect metrics that provide insights about the memory access behavior of the memory-bottlenecked functions.
[CLICK] In Step 3, we collect architecture-dependent metrics and analyze the performance and energy of each function in an application when each of our three candidate data movement mitigation mechanisms is applied to the system.
[CLICK] By combining the data obtained from all three steps, we can systematically classify the leading causes of data movement bottlenecks in an application or function into different bottleneck classes
[NEXT]

## Slide 61: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
265
Notes: So let’s check the first step
[NEXT]

## Slide 62: Step 1: Application Profiling
Goal: Identify application functions that suffer from data movement bottlenecks
266
Physics
Security
Machine learning
Database
Graph processing
Data analytics
Data reorganization
Genomics
Deep Neural Networks
Image processing
Linear algebra
Signal processing
Data mining
Hardware Profiling Tool:
Intel VTune
MemoryBound:
CPU is stalled due to load/store
Notes: [CLICK] The goal of the first step is to identify functions in an application that suffers from memory bottlenecks
[CLICK] To profile the applications and identify functions that suffer from data movement bottlenecks
[CLICK] we use a hardware profiling tool. In this work, we decided to use Intel Vtune
[CLICK] Intel Vtune provides a metric called Memory bound, which is defined as the percentage of CPU pipeline slots that are not utilized because of memory stalls.
[NEXT]

## Slide 63: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
267
Notes: Let's give a look to the second step.
[NEXT]

## Slide 64: Step 2: Locality-Based Clustering
Low spatial locality
Goal: analyze application’s memory characteristics
Stride Profile (bin)
…
1
2
4
8
16
32
2N
Frequency (count)
Stride Profile Histogram
High spatial locality
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
stride profile(1)+= 1
0
1
2
3
4
5
Memory Trace
Spatial Locality7
[7] Weinberg+, “Quantifying Locality in the Memory Access Patterns of HPC Applications,” SC, 2005
268
Notes: In Step 2, we aim to analyze application’s memory characteristics, as locality, thus we could understand how it affects the components of the memory system, as cache behavior or prefetching. To this end, we evaluate two key metrics.
[CLICK] We first evaluate spatial locality from an application.
[CLICK] For this, we collect the memory trace of an application
[CLICK] To build a histogram called the stride profile, where each bin stores how many times each stride appear in the memory trace.
[CLICK] In this example, the stride between the first accessed address and the next accessed address is equal to 1. We increment a stride profile histogram in bin 1 to indicate such stride has been observed.
[CLICK] We use the stride profile histogram to calculate the cumulative distribution of stride profiles, which represents the final spatial locality value.
[CLICK] A spatial locality value close to 0 is caused by large stride values or random accesses, as shown in this example. In such case, we say the application has low spatial locality
[CLICK] A spatial locality value close to 1 is caused by a completely sequential access pattern. . In such case, we say the application has high spatial locality
[NEXT]

## Slide 65: Step 2: Locality-Based Clustering
Low spatial locality
Goal: analyze application’s memory characteristics
…
1
2
4
8
16
32
2N
Reuse Profile (bin)
Frequency (count)
Reuse Profile Histogram
High temporal locality
…
1
2
4
8
16
32
2N
Reuse Profile (bin)
Frequency (count)
Reuse Profile Histogram
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
High spatial locality
…
1
2
4
8
16
32
2N
Stride Profile (bin)
Frequency (count)
Stride Profile Histogram
stride profile(1)+= 1
0
1
2
3
4
5
Memory Trace
reuse profile(4)+= 1
A
A
A
A
Memory Trace
Spatial Locality7
Temporal Locality7
[7] Weinberg+, “Quantifying Locality in the Memory Access Patterns of HPC Applications,” SC, 2005
269
Low temporal locality
Notes: [CLICK] Similarly, we evaluate how much temporal locality an application has.
[CLICK] For this, we collect the memory trace of an application
[CLICK] to create a histogram called reuse profile, where each bin represents the number of times a memory address is reused. For each memory address, we increment the bin that represents the corresponding number of repetitions.
[CLICK] In this example, memory address A is reused 4 times. Thus, we increment the reuse profile histogram in bin 4 to indicate such reuse has been observed.
[CLICK] We use the reuse profile histogram to calculate the cumulative distribution of rese profiles, which represents the final temporal locality value.
[CLICK] A temporal locality value close to 0 is caused by low data reuse. In such case, we say the application has low temporal locality
[CLICK] A temporal locality value close to 1 is caused by high data reuse/ In such case, we say the application has high temporal locality
[NEXT]

## Slide 66: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
270
Notes: Finally, let's look deeper into Step 3 of our methodology
[NEXT]

## Slide 67: Step 3: Memory Bottleneck Classification (1/2)
Arithmetic Intensity (AI)
- floating-point/arithmetic operations per L1 cache lines accessed
→ shows computational intensity per memory request
LLC Misses-per-Kilo-Instructions (MPKI)
- LLC misses per one thousand instructions
→ shows memory intensity
Last-to-First Miss Ratio (LFMR)
- LLC misses per L1 misses
→ shows if an application benefits from L2/L3 caches
271
Notes: While Step 2 allows us to understand inherent application sources for memory boundedness, it is important to understand how hardware architectural features can also result in memory bottlenecks. As a result, in our third step we perform a scalability analysis of the functions selected in Step 1, where we evaluate performance and energy scaling for three different system configurations. The scalability analysis makes use of three architecture-dependent metrics:
[CLICK] First, Arithmetic Intensity (AI), defined as the number of arithmetic and logic operations performed per L1 cache line accessed.
[CLICK] This metric indicates how much computation there is per memory request. Intuitively, applications with high AI are likely to be computationally intensive, while applications with low AI tend to be memory intensive
[CLICK] Second, Misses per Kilo-Instruction (MPKI), defined as the number of LLC misses per one thousand instructions.
[CLICK] This metric is considered to be a good indicator of NDP suitability by several prior works since it indicates memory intensity of an application.
[CLICK] and third, a new metric called Last-to-First Miss-Ratio (LFMR) define as the ratio between the number of LLC misses and the total number of L1 cache misses.
[CLICK] We find that this metric accurately identifies how much an application benefits from the deep cache hierarchy. An LFMR value close to 0 means that the number of LLC misses is very small compared to the number of L1 misses. However, an LFMR value close to 1 means that very few L1 misses hit in L2 or L3 caches, and the application does not benefit much from the deep cache hierarchy, and most L1 misses need to be serviced by main memory
[NEXT]
[NEXT]

## Slide 68: Step 3: Memory Bottleneck Classification (2/2)
Goal: identify the specific sources of data movement bottlenecks
DAMOV-SIM Simulator
# Cores
Scalability Analysis
Integrated ZSim and Ramulator
Scalability Analysis:
  1, 4, 16, 64, and 256 out-of-order/in-order host and NDP CPU cores
  3D-stacked memory as main memory
Configuration 2: NDP System
Off-chip link
DRAM
CPU
CPU
CPU
L2
L1
L3
L2
L1
L2
L1
L2
L1
CPU
Configuration 1: Host CPU System
Off-chip link
272
DAMOV-SIM: https://github.com/CMU-SAFARI/DAMOV
…
Logic Layer
CPU
CPU
CPU
L1
L1
L1
L1
CPU
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Notes: [CLICK] The goal of the scalability analysis we perform is to nail down the specific sources of data movement bottlenecks in the application.
In this analysis, we evaluate the performance and energy scaling of an application in three different system configurations; and collect the key metrics for our bottleneck classification
[CLICK] During scalability analysis, we simulate three system configurations of a general-purpose multicore processor. To this end, we build a framework that integrates the ZSim CPU simulator with the Ramulator memory simulator to produce a fast, scalable, and cycle-accurate open-source simulator called DAMOV-SIM. We use ZSim to simulate the core microarchitecture, cache hierarchy, coherence protocol, and prefetchers. We use Ramulator to simulate the DRAM architecture, memory controllers, and memory accesses.
[CLICK] The first configuration we evaluate is of a host CPU with a deep cache hierarchy, with a 32 KB, private L1 cache, a 256 KB private L2 cache, and a shared 8MB L3 cache.
[CLICK] The second configuration is of an NDP CPU with only a private read-only L1 cache of 32 KB.
In our paper we evaluate an third configuration that includes hardware prefetcher on top of configuration 1. However, we omit such configuration in this talk.
The remaining components of the processor configuration are kept the same to isolate the impact of only the caches, prefetchers, and NDP.
This way, we expect that the performance and energy differences between the three configurations to come exclusively from the different data movement requirements.
[CLICK] For all configurations, we sweep the number of CPU cores in our analysis from 1 to 256, as previous works show that large core counts are necessary to saturate the bandwidth provided by modern high-bandwidth memories, and because modern CPUs and NDP proposals can have varying core counts.
[CLICK] We simulate a memory architecture similar to the Hybrid Memory Cube device where the host CPU accesses memory through a high-speed off-chip link,
[CLICK] and the NDP logic resides in the logic layer of the memory chip and has direct access to the DRAM banks, thus taking advantage of higher memory bandwidth and lower memory latency.
[NEXT]

## Slide 69: Step 3: Memory Bottleneck Analysis
Temporal Locality
Low
High
LFMR
Decreasing
High
MPKI
High
AI
AI
MPKI
AI
LFMR
MPKI
MPKI
Low
Increasing
AI
AI
Low
Low
Low
Low
High
Low
Low
Low
Low
Low
1a: DRAM Bandwidth
1b: DRAM Latency
1c: L1/L2
Cache Capacity
2a: L3 Cache Contention
2c: Compute-Bound
2b: L1 Cache Capacity
Memory Bottleneck Class
  Six classes of
  data movement bottlenecks:
  each class ↔ data movement
  mitigation mechanism
Notes: [CLICK] With such classification, we analyze how the functions in each class correlates with different data movement mitigation mechanisms in terms of performance and energy using our scalability analysis.
[NEXT]

## Slide 70: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 71: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 72: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 73: More on DAMOV Methods & Benchmarks
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 74: Tutorial on Memory-Centric Computing: PIM Adoption & Programmability
Geraldo F. Oliveira
Prof. Onur Mutlu
ISCA 2024
29 June 2024