## Slide 1: Processing-Using-Memory Systems for Bulk Bitwise Operations
Geraldo F. Oliveira geraldofojunior@gmail.com
https://geraldofojunior.github.io
3rd Workshop on Memory-Centric Computing Systems @ ISCA’25
June 21st 2025
Notes: Hi, I’m Geraldo, a PhD Student under the supervision of professor Multu at ETH Zurich and I’ll be talking about our work DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks.
[NEXT]

## Slide 2: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
…
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
Notes: In this work, we focus on processing-using-memory architectures. In particular, its implementation using DRAM.
Before I introduce processing-using-DRAM architectures, I will provide a short background on DRAM organization and operation.
[NEXT]

## Slide 3: Background: DRAM Hierarchical Organization
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows/columns)
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 4: Background: DRAM Hierarchical Organization
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 5: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
← src
← dst
Notes: The operating principles of DRAM can be used to implement bulk-bitwise operations inside DRAM. For example, RowClone implements in-DRAM row copy operation by issuing back-to-back ACTIVATE commands to DRAM
[CLICK] The first activate copies the source row into the local sense amplifier
[NEXT]

## Slide 6: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 7: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy improves performance & energy: 1046 ns, 3.6 uJ → 90 ns, 0.04 nJ
← src
← dst
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 8: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst

## Slide 9: RowClone: Inter-Bank
Memory Channel
Chip I/O
Bank
Shared internal bus
Overlap the latency of the read and the write
1.9X latency reduction, 3.2X energy reduction

## Slide 10: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)
0.01% area cost

## Slide 11: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 12
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Background: In-DRAM Majority Operations
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 13: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority reduces energy: 137.9 nJ/KB → 3.2 nJ/KB
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 14: In-DRAM NOT: Dual Contact Cell
Idea:
Feed the
negated value
in the sense amplifier
into a special row
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017

## Slide 15: NOT in PUD: Alternative I
Sudarshan, Chirag, et al. "A Critical Assessment of DRAM Architectures-Trends, Challenges and Solutions,” in SAMOS, 2022.

## Slide 16: NOT in PUD: Alternative II
Shin, Hoon, Rihae Park, and Jae W. Lee. "A Processing-using-Memory Architecture for Commodity DRAM Devices with Enhanced Compatibility and Reliability," in ICCAD, 2024.

## Slide 17: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: In order to implement bulk bitwise arithmetic operations, the authors of SIMDRAM implements a three-step framework that maps a designed operation into a series of in-DRAM row copy and majority operations. I will illustrate such process using a ripple carry adder.
In order to add two arrays A and B with data values of 1-bit, SIMDRAM converts
[CLICK] an AND/OR/NOT-based rippled carry adder into
[CLICK] its equivalent MAJ/NOT-based circuit.
[NEXT]

## Slide 18: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Notes: Then it issues in-DRAM triple-row activations in order to realize the required MAJ/NOT operations, one majority gate at a gate.
[NEXT]

## Slide 19: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
← Sum0
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Notes: In the end, one DRAM row will hold the generated Sum and carry out bits for the 1-bit addition operation.

## Slide 20: Background: Bulk Bitwise Arithmetic Operations (II)
← Cin
← BN
← AN
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Notes: This processes is repeated for all individual N bits in the input data word
[NEXT]

## Slide 21: Background: Bulk Bitwise Arithmetic Operations (II)
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
← Cin
← BN
← AN
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Notes: Thus, SIMDRAM transforms a DRAM chip into a very-wide bit-serial SIMD engine.
[NEXT]

## Slide 22: Background: PUD in Commodity Off-the-Shelf (COTS) DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 23: PUD in COTS DRAM: Summary of Results
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 24: Processing-in-Memory: Challenges
Adopting PIM as a mainstream architecture holistically and efficiently is still very challenging due to a lack of:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
2
Execution paradigms that can map applications effectively onto PIM hardware resources
3
Compiler support and programming frameworks targeting PIM architectures
4
Adaptive data-aware runtime mechanisms that use the intrinsic properties of data for efficient PIM execution
  The lack of tools, programming, and system support for PIM architectures limit the adoption of PIM system

## Slide 25: Processing-in-Memory: Challenges
Adopting PIM as a mainstream architecture holistically and efficiently is still very challenging due to a lack of:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
2
Execution paradigms that can map applications effectively onto PIM hardware resources
3
Compiler support and programming frameworks targeting PIM architectures
4
Adaptive data-aware runtime mechanisms that use the intrinsic properties of data for efficient PIM execution
  The lack of tools, programming, and system support for PIM architectures limit the adoption of PIM system

## Slide 26: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 27: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 28: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 29: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 30: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 31: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 32: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 33: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 34: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 35: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting from its DRAM array modifications for fine-grained PUD computation
[NEXT]

## Slide 36: MIMDRAM: DRAM Array Modifications
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
mat selector
mat range
isolation transistors
row decoder latch
Notes: We modify a DRAM array circuitry with four main components
[CLICK] First, the isolation transistors segment the global wordline, allowing a single mat to be activated
[CLICK] The row decoder latch stores the address of the currently activated row for a mat, allowing the row decoder to issue an request to a different row
[CLICK] The mat selector asserts the isolation transistors
[CLICK] based on a mat range specified by the PUD operation. The mat range addresses a physically contiguous set of DRAM mats
[NEXT]

## Slide 37: MIMDRAM: Moving Data Across Mats
row decoder
global wordline
mat selector
mat range
isolation transistors
row decoder latch
IO interface
inter-mat
interconnect
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 38: MIMDRAM: Control Unit
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 39: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 40: MIMDRAM: Compiler Support (I)
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 41: MIMDRAM: Compiler Support (II)
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The first pass is responsible for identifying SIMD parallelism in a code, using LLVM’s auto-vectorization engine, generate PUD instructions and set the best vectorization factor for such PUD instruction
[NEXT]

## Slide 42: MIMDRAM: Compiler Support (II)
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: The second pass is responsible for scheduling and mapping computation. Our pass uses metadata to mark independent PUD instructions that should be executed concurrently across mats
[NEXT]

## Slide 43: MIMDRAM: Compiler Support (III)
Generate the appropriate binary for data allocation and PUD instructions
Goal
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Notes: Finally, the third pass is responsible for code generation and data allocation for PUD instructions
[NEXT]

## Slide 44: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Notes: Such system support includes ISA extensions, execution and data transposition, data coherence, address translation, data allocation and alignment, and metadata translation
[NEXT]

## Slide 45: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU
  PUD: SIMDRAM [Oliveira+, 2021] and DRISA [Li+, 2017]
  PND: Fulcrum [Lenjani+, 2020]
  https://github.com/CMU-SAFARI/MIMDRAM
Workloads:
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  495 multi-programmed application mixes
Two-Level Analysis
  Single application → leverages intra-application data parallelism
  Multi-programmed workload → leverages inter-application data parallelism
Notes: We compared MIMDRAM to a high-end CPU and GPU, two state-of-the-art PUD systems that use large DRAM access for computation, and a processing-near-DRAM architecture.
[CLICK] In our analyses, we use 12 workloads from four benchmark suites and 495 application mixes from such workloads
[CLICK] We perform a two-level analysis. For single applications, MIMDRAM can leverage its intra-application data parallelism and for multiple applications, MIMDRAM leverages inter-application data parallelism
[NEXT]

## Slide 46: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 47: Evaluation: Comparison to Other PIM Architectures
MIMDRAM significantly improves performance/area compared to DRISA (1.18x) and Fulcrum (1.92x)
Takeaway
Chart: MIMDRAM-Normalized Performance/Area
| pca | hw | fdtd | doitgen | gemm | kmeans | 2mm | gs | 3mm | bp | cov | x264 | GMean
DRISA | 0.9 | 1.5 | 0.7 | 3.5 | 1 | 1.4 | 1 | 0.9 | 0.6 | 0.1 | 0.3 | 2.7 | 0.9
Fulcrum | 0.4 | 1.6 | 0.7 | 3.1 | 1 | 0.8 | 0.9 | 0.9 | 0.5 | 0.1 | 0.1 | 0.1 | 0.5
MIMDRAM | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: [CLICK] Finally, we compared MIMDRAM to other processing-in-memory architectures for our twelve workloads
For fairness, we report performance normalized area results, since such PIM architectures incur significant area costs to DRAM for computation
[CLICK] We evaluate the performance of DRISA
[CLICK] Fulcrum,
[CLICK] and MIMDRAM
Values are normalized to MIMDRAM
[CLICK] We observe that on average across all applications, MIMDRAM improves performance per area compared to both DRISA and Fulcrum
[NEXT]

## Slide 48: Processing-in-Memory: Challenges
Adopting PIM as a mainstream architecture holistically and efficiently is still very challenging due to a lack of:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
2
Execution paradigms that can map applications effectively onto PIM hardware resources
3
Compiler support and programming frameworks targeting PIM architectures
4
Adaptive data-aware runtime mechanisms that use the intrinsic properties of data for efficient PIM execution
  The lack of tools, programming, and system support for PIM architectures limit the adoption of PIM system

## Slide 49: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
I will briefly expand on each issue next.
[NEXT].

## Slide 50: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Staring with the rigid and static data representation of bit-serial PUD architectures
[NEXT]

## Slide 51: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
B
Sum
1
0
0
A
bit0
bit1
bit2
0
0
0
0
0
bit7
bit3
bit4
bit5
bit6
Notes: [CLICK] It’ is well known that many applications display what is called narrow values, which are data with small dynamic range stored in large data formats. For example, let’s assume you have a data element A storing ’4` in its three least-significant bits. However, the minimum standard data format available in high-level programming languages as C is eight bits. Thus, the remaining 5 most significant bits of such data element will be leading 0s.
[CLICK] When adding two values that display narrow values using a bit-serial execution model
[NEXT]

## Slide 52: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
Narrow Values:
data with small dynamic range stored in large data formats
inconsequential bits → do not contribute to the output’s dynamic range
← Cin
← B7
← A7
row decoder
← Sum7
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
B
Sum
1
0
0
A
bit0
bit1
bit2
0
0
0
0
0
bit7
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy
Notes: The leading zero values will not contribute to the dynamic range of the produced output.
[CLICK] Yet, such inconsequential bits will still be processed by the bit-serial engine, wasting memory cycles and energy.
[NEXT]

## Slide 53: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
minimum number of bits required to represent input operands
largest bit-precision
smallest bit-precision
bit-precision distribution
Notes: In our work, we quantized the amount of narrow values present in real applications.
To do so, we profiled the required bit-precision of data arrays of loops in twelve real-world applications.
[CLICK] We define the required-bit precision such as the minimum number of bits required to represent input operands.
[CLICK] In our box plots, whiskers extend to the largest and smallest bit-precision
[NEXT]

## Slide 54: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
Applications display a significant amount of narrow values → bit-precision can be reduced from 32 bits to 20 bits, on average
narrow values
Notes: [CLICK] We make the key observation that applications display a significant amount of narrow values, where the bit-precision can be reduced from 32 bits to 20 bits on average.
[NEXT]

## Slide 55: Opportunities for Bit-Serial PUD: Narrow Values for PUD Operations
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → dynamically identify and skip during computation
← Cin
← B2
← A2
row decoder
← Sum2
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy
x
x
saved latency
saved energy
Notes: In order to solve this issue, we propose to dynamically identify and skip inconsequential bits in narrow values during bit-serial operation.
[CLICK] Doing so allows our PUD substrate to save DRAM cycles and energy during PUD operation
[NEXT]

## Slide 56: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Next, we discuss issue caused by PUD’s throughput-oriented execution with low latency tolerance
[NEXT]

## Slide 57: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (I)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
PUD operations are inherently slow → need to operate on each bit serially to perform an operation with a data width > 1
Problem
Notes: We observe that PUD operations are inherently slow due to the need to operate on each bit of a data world serially.
[CLICK] This issue is further exacerbated by the inter-bit dependency present in bit-serial arithmetic operations
[NEXT]

## Slide 58: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
2 (2’b10)
2 (2’b10)
+
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
tmp
tmp
Notes: I will illustrate this issue by showcasing a two-bit PUD addition operation of two plus two.
PUD substrates store all data bits of the input data world vertically within a single DRAM subarray
[NEXT]

## Slide 59: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
Notes: During operation, the MAJ/NOT operations required to implement the PUD addition will be first performed over bits 0 of the data world
[NEXT]

## Slide 60: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
inter-bit
dependency
ACT
Notes: During this process, a carry from bit 0 will be generate and propagate to the input carry that will be used for bit 1
Note that Inter-bit dependency forces the serialization of PUD primitives when bits of a data word are placed within the same DRAM subarray
[NEXT]

## Slide 61: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
ACT
ACT
Notes: Only after the inter-bit dependency is satisfied, the MAJ/NOT operations over bit 1 can be executed, one MAJ/NOT operation per-time in a serial manner.
[NEXT]

## Slide 62: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (I)
Leverage bit-level parallelism to execute independent PUD primitives concurrently across different DRAM subarrays
Key Idea
MAJ
B1
Cin
A1
Sum1
MAJ
Cout
MAJ
MAJ
B0
Cin
A0
Sum0
MAJ
Cout
MAJ
bit 0
bit 1
inter-bit
dependency
inter-bit
independency
Notes: To reduce the latency of PUD operations, we aim to leverage bit-level parallelism to execute independent PUD primitives concurrently across different DRAM subarrays.
In the bit-serial addition example, after the carry from bit 0 is propagate to bit 1, the yellow and red MAJ gates become bit-independent and can be executed concurrently.
[NEXT]

## Slide 63: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (II)
Proteus’ one-bit per-subarray data mapping → scatter bits across subarrays to expose bit-level parallelism
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
subarray0
all-bits per-subarray → forces serialization across bits
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
one-bit per-subarray → exposes bit-level parallelism
inter-subarray interconnect*
Chang, Kevin K. et al. ”Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM," in HPCA, 2016
Notes: In order to exploit such key idea, Proteus implements a specialized data mapping called one-bit per-subarray, where bits of a data world are scattered across DRAM subarrays for parallel execution.
[CLICK] In this example, instead of storing all-bits of the input arrays in a single DRAM subarray,
[CLICK] Proteus stores in subarray 0 bits 0 and subarray 1 bits 1 of the input arrays A and B. Thus allowing both subarrays to operate concurrently over bit-independent values
[CLICK] Besides that, Proteus leverages a high-bandwidth inter-subarray interconnect that allows for data movement (required during carry propagation) between neighboring DRAM subarrays.
[NEXT]

## Slide 64: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
Notes: Let’s see how proteus exploit bit-level parallelism in our two-digit bit-serial addition
[NEXT]

## Slide 65: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
inter-subarray interconnect
ACT
Notes: First, Proteus executes the carry generation MAJ gate for bit 0 in subarray 0
[NEXT]

## Slide 66: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
ACT
Notes: Next, Proteus uses the inter-subarray interconnect to copy the generated carry from subarray 0 to subarray 1.
[NEXT]

## Slide 67: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
ACT
ACT
ACT
ACT
saved cycles
Notes: Afterward, bit-independency is achieved, and the remaining MAJ operations across bits 0 and 1 can be concurrently executed in subarrays 0 and 1, respectively, hence reducing overall latency
[NEXT]

## Slide 68: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Notes: Finally, let’s look at the third issue caused by bit-serial execution, which is the scalability challenge for high-precision operations
[NEXT]

## Slide 69: Limitations of Bit-Serial PUD Systems: Scalability Challenges for High-Precision
8
16
32
N
Bit-Precision
Latency
…
8
16
32
N
Bit-Precision
Energy
bit 0
MAJ
bit 1
MAJ
bit N
MAJ
…
…
Linearly-Scaling PUD Operations (e.g., addition)
8
16
32
64
Bit-Precision
Latency
8
16
32
64
Bit-Precision
Energy
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
Quadratically-Scaling PUD Operations (e.g., multiplication)
Notes: Due to inter-bit dependency, bit-serial operations scales linearly for addition and subtraction operations
[CLICK] And quadratically for multiplication operation,
Resulting in high latencies as the bit-precision increases
[NEXT]

## Slide 70: Opportunities for Bit-Serial PUD: Alternative Data Representation for High-Precision
Use the redundant binary representation (RBR) for high-precision PUD operations
Key Idea
each bit position is represented by two bits that can take on a value ∈ {−1, 0, 1} <0, 1, 0, -1> = 0 x 23 + 1 x 22 + 0 x 21 + (-1) x 20 = 4 - 1 = 3
+
A0
B0
+
+
A1
B1
+
C0
C1
B2
+
A2
+
C2
BN
+
AN
+
CN
…
RBR-Based Arithmetic
limits carry propagation to at most two places
latency is independent bit-precision
Notes: To solve such an issue, we propose to use alternative data representation formats for high-precision PUD operations. In particular, we use the redundant binary representation format.
[CLICK] In such data format, each bit position is represented by two bits that can take a value of -1, 0, or 1. For example, the number 3 can be represented using for bits such as 0, 1, 0, and -1
[CLICK] Because of its redundancy nature, when implementing RBR-based arithmetic, the carry propagation is limited by at most two places, making the latency of PUD operations using such data format independent of the bit-precision
[NEXT]

## Slide 71: Proteus: Design Overview (I)
3
Program Select Unit
2
Dynamic Bit-Precision Engine
1
Parallelism-Aware Program Library
Proteus, a data-aware hardware runtime framework that dynamically and transparently adapts the in-DRAM implementation, bit-precision, and data format based on the input data for efficient PUD execution
  Proteus is composed of three main components:
Notes: Proteus IS a data-aware runtime mechanism for efficient PUD execution. Proteus adapts the bit-precision, in-DRAM implementation, and data format based on the target input data transparently from the user.
[CLICK[ Proteus is composed of three main components implemented at the memory controller:
[CLICK] A parallelism-aware uProgram library
[CLICK] a Dynamic bit-precision engine
[CLICK] and a uprogram select unit
I briefly elaborate on each component next
[NEXT]

## Slide 72: Proteus: Design Overview (II)
data transposition unit
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
precision:
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine
3
Program Select Unit
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
parallelism-aware Programs
impl. #2
latency
#bits
impl. n
latency
#bits
AP
AAP
AAP
done
…
AP
AAP
AAP
done
Notes: First, the parallelism-aware uProgram is a collection of hand-optimized implementations of different PUD operations (called uPrograms). Each implementation has different trade-offs in terms of performance based on the target bit-precision
[NEXT]

## Slide 73: Proteus: Design Overview (III)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
object tracker
…
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
7
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
9
9
evicted cache line
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit
precision:
Notes: Second, the dynamic bit-precision engine aims to identify the dynamic range of evicted cache lines belonging to the target PUD operation by scanning the data within evicted cache lines to identify the largest value within a PUD memory object
[NEXT]

## Slide 74: Proteus: Design Overview (IV)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
…
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
precision:
4 bits
Notes: Third, the uProgram select unit aims to identify the appropriate bit-precision based on the previously identified largest values belonging to the memory addresses involved in the PUD operation

## Slide 75: Proteus: Design Overview (IV)
data transposition unit
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
Progs.
AAP
AP
AAP
done
AP
AAP
AAP
done
latency
#bits
impl. #2
AP
AAP
AAP
done
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
bit-precision cal.
log2
ALU
target
precision
AP
AAP
AAP
done
parallelism-aware Programs
Program
select unit
cost model
…
impl. #1
impl. n
latency
#bits
latency
#bits
precision:
4 bits
Notes: Based on this calculated target bit-precision, the uProgram select unit probes the parallelism-aware uProgram library to identify what is the best in-DRAM realization of the target operation based on the target bit-precision
[NEXT]

## Slide 76: Proteus: More in the Paper & GitHub
Detailed hardware description
Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations
Notes: Due to time constraints, I refer you to the paper for more details on proteus implementation, including Detailed hardware description, Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations

## Slide 77: Proteus: More in the Paper & GitHub
Detailed hardware description
Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations
https://arxiv.org/abs/2501.17466
https://github.com/CMU-SAFARI/Proteus
Notes: For more details, please, check our paper
[NEXT]

## Slide 78: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU (with and without Tensor Cores)
  PUD: SIMDRAM [Oliveira+, 2021]
  https://github.com/CMU-SAFARI/Proteus
Workloads
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  Linear algebra, data mining, video processing, machine learning
Metrics
  CPU-normalized performance per area
  Energy reduction (compared to baseline CPU)
Notes: We compared Proteus to a high-end CPU and GPU, and a SIMDRAM
In our analyses, we use 12 workloads from four benchmark suites
And we evaluated CPU-normalized performance per area and energy savings
[NEXT[

## Slide 79: Evaluation: Performance Analysis
Chart: CPU-Normalized Performance/mm2
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | GMean
GPU | 211.61 | 123.42 | 0.0024 | 82.55 | 96.77 | 2.27 | 3.67 | 2.32
SIMDRAM | 2.22 | 1.69 | 6955.88 | 283.58 | 0.2 | 0.04 | 0.84 | 5.69 | 0.05 | 0.77 | 0.06 | 0.62 | 1.66
Proteus (Only w/ Dynamic Bit-Precision) | 7.72 | 18.86 | 35014.76 | 335.85 | 2.25 | 4.46 | 2.84 | 46.64 | 0.16 | 2.49 | 0.94 | 1.99 | 10.43
Proteus | 14.61 | 26.43 | 54891.64 | 1360.9 | 2.83 | 5.05 | 5.37 | 64.61 | 0.28 | 11.75 | 1.07 | 3.06 | 16.98
Proteus significantly improves performance/mm2 compared to CPU (17x), GPU (7.3x), and SIMDRAM (10.2x)
Takeaway
Notes: First, in terms of
[CLICK] performance per area, compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant performance improvements.
[CLICK] We observe that a significant portion of such improvements comes from our dynamic bit-precision engine.
[NEXT]

## Slide 80: Evaluation: Energy Analysis
Proteus significantly improves energy-efficiency compared to CPU (90.3x), GPU (21x), and SIMDRAM (8.1x)
Takeaway
Chart: CPU-Normalized Energy Reduction
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | Gmean
GPU | 133.666 | 137.751 | 0.004 | 62.848 | 163.015 | 0.001 | 9.166 | 14.832 | 4.279
SIMDRAM | 13.85 | 20.286 | 548.649 | 2941.47 | 2.992 | 0.566 | 10.539 | 13.359 | 0.713 | 9.869 | 1.279 | 3.633 | 11.108
Proteus (Only w/ Dynamic Bit-Precision) | 59.764 | 284.603 | 3426.534 | 4224.656 | 42.203 | 100.775 | 43.966 | 136.038 | 2.915 | 39.355 | 23.889 | 13.486 | 88.52
Proteus | 59.764 | 284.603 | 3426.534 | 11653.015 | 42.203 | 109.32 | 43.966 | 136.038 | 2.915 | 142.796 | 24.424 | 14.939 | 90.307
Notes: Second, in terms of
[CLICK] energy savings, we compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant energy-efficient improvements.
[NEXT]

## Slide 81: Evaluation: More in the Paper
Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis
Notes: In our paper, we have further analysis including Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis

## Slide 82: Evaluation: More in the Paper
Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis
https://arxiv.org/abs/2501.17466
https://github.com/CMU-SAFARI/Proteus
Notes: For all that, please check our paper
[NEXT]

## Slide 83: Processing-Using-Memory Systems for Bulk Bitwise Operations
Geraldo F. Oliveira geraldofojunior@gmail.com
https://geraldofojunior.github.io
3rd Workshop on Memory-Centric Computing Systems @ ISCA’25
June 21st 2025
Notes: Hi, I’m Geraldo, a PhD Student under the supervision of professor Multu at ETH Zurich and I’ll be talking about our work DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks.
[NEXT]

## Slide 84
MIMDRAM An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing
Geraldo F. Oliveira |  | 
Ataberk Olgun | A. Giray Yağlıkçı | F. Nisa Bostancı
Saugata Ghose | Juan Gómez-Luna | Onur Mutlu
2024 International Symposium on High-Performance Computer Architecture
Backup Slides
Notes: Thanks for your attention.

## Slide 85: Bit-Serial PUD Addition

## Slide 86: Intra-Mat Interconnect

## Slide 87: Performance for Single Applications

## Slide 88: SIMD Utilization: MIMDRAM vs. SIMDRAM

## Slide 89: Weighted Speedup vs. CPU

## Slide 90: Multi-Applications: Full Data

## Slide 91: Multi-Applications: DRISA & Fulcrum

## Slide 92: BLP and SALP

## Slide 93: System Configuration

## Slide 94: Workload Characteristics

## Slide 95: MIMDRAM: In-DRAM Vector Reduction (I)
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We leverage the inter-and intra-mat interconnects to implement in-DRAM vector reduction in three steps that implement a reduction three.
Let’s assume that we want to sum all elements of two vectors into a single element. We use two DRAM mats in this example.
[NEXT]

## Slide 96: MIMDRAM: In-DRAM Vector Reduction (II)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 1: C = A + B
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: To do so, we first compute the target PUD operation using both data elements

## Slide 97: MIMDRAM: In-DRAM Vector Reduction (III)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 2: inter-mat data movement
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: Then, we move the result of the first computation in the first DRAM mat to the second DRAM mat via the inter-mat network

## Slide 98: MIMDRAM: In-DRAM Vector Reduction (IV)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 3: out = C[1] + tmp
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: Once the data from the first mat is in the second mat, we can once again compute the reduction step using only the second mat
[NEXT]

## Slide 99: PUD in COTS DRAM: Experimental Setup
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 100: PUD in COTS DRAM: Tested DRAM Chips
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 101: PUD in COTS DRAM: Testing Methodology
Carefully sweep:
  Row addresses: Row A and Row B
  Timing parameters: Between ACT → PRE and PRE → ACT
ACT row A
PRE
ACT row B
neighboring subarrays
subarray X
subarray Y
row A
row B
ACT
DRAM bank
ACT
shared sense amplifiers
Notes: In this study, we focus on two neighboring subarrays, here denoted as Subarray X and Subarray Y, which share a common component, sense amplifiers
[CLICK] We perform our experiment using the following command sequence: Activate Row A, which is in the subarray X, Precharge, and Activate Row B
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 102: PUD in COTS DRAM: Conclusion
We experimentally demonstrate that commercial off-the-shelf (COTS) DRAM chips can perform:
  Functionally-complete Boolean NOT, NAND, and NOR
  Up to 16-input AND, NAND, OR, and NOR operations
We characterize the success rate of these operations on 256 COTS DDR4 chips from two major manufacturers
We highlight two key results:
  We can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations on COTS DRAM chips with very high success rates (>94%)
  Data pattern and temperature only slightly affect the reliability of these operations
We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate

## Slide 103: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Notes: The key observation is that, if we simultaneously activate multiple wordlines within a block, which we call intra-block MWS, it results in the bitwise AND of stored data in the wordlines. [Click]

## Slide 104: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Non-Target Cells:
Operate
as resistors
Notes: As explained all the non-target cell would operate as a resistance, [Click] while …

## Slide 105: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:
Notes: Target cells operate as either a resistance or an open switch depending the stored data. [Click]
In this example, only Bitline 4 can conduct flow, as the other bitlines have at least one cell that operates as an open switch. [Click]

## Slide 106: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: So, the sensing result would be ‘1’ only when all the target cells store bit data ‘1’, which is equivalent to the bitwise AND of all the target cells. [Click]

## Slide 107: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
Notes: This property also holds [Click] when we activate more than two wordlines at the same time, [Click], for example, …

## Slide 108: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: The bitline current cannot flow through Bitline 4 any longer, as it has a cell that stores ‘0’ and blocks the bitline current. [Click]

## Slide 109: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
1
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Flash-Cosmos (Intra-Block MWS) enables
bitwise AND of multiple pages in the same block
via a single sensing operation
Notes: This way, intra-block MWS enables bitwise AND operation on any pages in the same block via a single sensing operation. [Click]

## Slide 110: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
1
1
0
0
…
WLy in Blocki
…
…
…
…
Notes: Flash-Cosmos also enables bitwise OR operations by simultaneously activating multiple wordlines in different blocks, which we call inter-block MWS. [Click]

## Slide 111: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
Notes: In this example, only Bitline 4 cannot conduct current, as both the target NAND string have a cell that operates as an open switch. [Click]

## Slide 112: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: It means that the sensing result would read as ‘0’ only when all the target cells store bit data ‘0’, which is equivalent to the bitwise OR of all the target cells. [Click]

## Slide 113: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Notes: Like intra-block MWS, [Click] this property holds when we activate more than two wordlines in different blocks at the same time, [Click], as we can see …

## Slide 114: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: As we can see the current can flow through Bitline 4 as well, since there is a cell that operates as a resistance. [Click]

## Slide 115: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Flash-Cosmos (Inter-Block MWS) enables
bitwise OR of multiple pages in different blocks
via a single sensing operation
Notes: This way, inter-block MWS enables bitwise OR operations on any pages in different blocks via only a single sensing operation. [Click]

## Slide 116: Other Types of Bitwise Operations
Flash-Cosmos also enables other types of bitwise operations (NOT/NAND/NOR/XOR/XNOR)
leveraging existing features of NAND flash memory
https://arxiv.org/abs/2209.05566.pdf