## Slide 1: Functionally-Complete Boolean Logic in Real DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
Ismail Emir Yüksel
Yahya C. Tugrul Ataberk Olgun F. Nisa Bostancı
A. Giray Yaglıkçı Geraldo F. Oliveira Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Functionally-Complete Boolean Logic in Real DRAM Chips

## Slide 2: Executive Summary
Motivation: Processing-using-DRAM can alleviate the performance and energy bottlenecks caused by data movement
  Prior works show that existing DRAM chips can perform three-input majority and two-input AND and OR operations
Problem: Proof-of-concept demonstrations on commercial off-the-shelf (COTS) DRAM chips do not provide
  functionally-complete operations (e.g., NAND or NOR)
  NOT operation
  AND and OR operations with more than two inputs
Experimental Study: 256 DDR4 chips from two major manufacturers
Key Results:
  COTS DRAM chips can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations with very high reliability (>94% success rate)
  Data pattern and temperature only slightly affect the reliability of these operations (<1.98% decrease in success rate)
2
Notes: Let’s start with an executive summary.
[CLICK] Processing-Using-DRAM is a promising paradigm that can alleviate the performance and energy bottlenecks caused by frequent data movement between main memory and processing units.
[CLICK] Proof-of-concept demonstrations on commercial-off-the-shelf DRAM chips do not provide
[CLICK]Functionally-complete operations, such as NAND or NOR
[CLICK] NOT operation
[CLICK] More than two-input AND and OR operations
[CLICK]In this study, we test 256 off-the-shelf DDR4 DRAM chips from two major manufacturers
[CLICK] Based on our analyses, we highlight that
[CLICK] We can perform NOT and up to 16-input AND, NAND, OR, and NOR operations with very high reliability
[CLICK] The impact of data patterns and the temperature on the reliability of these operations are small.
our work demonstrates the capability of performing functionally-complete Boolean logic in COTS DRAM chips. We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate. Now let’s delve in ..

## Slide 3: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
3
Goal & Overview
Notes: Here is the outline of my talk [CLICK]

## Slide 4: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
4
Goal & Overview
Notes: Let’s start with a background and the overview of our study

## Slide 5: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018

## Slide 6: Processing-In-Memory (PIM)
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-In-Memory:
1
Processing-Near-Memory: PIM logic is added
near the memory arrays or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the analog operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory

## Slide 7: DRAM Organization
DRAM Module
DRAM
Chip
DRAM Chip
…
…
Chip I/O
Bank
DRAM Bank
Subarray
Sense Amplifiers
DRAM Cell
DRAM Row
Wordline
Bitline
Sense Amps.
7
Notes: DRAM is used as the main memory in many computing systems. [CLICK]
a DRAM module consists of multiple DRAM chips [CLICK]
Each chip contains multiple banks [CLICK]
Each bank is composed of multiple subarrays and sense amplifiers [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row of sense amplifiers via bitlines [CLICK]

## Slide 8: DRAM Open Bitline Architecture
SA
SA
SA
SA
SA
SA
DRAM Bank
Subarray
8
SA
bitline
bitline
Sense
Amplifier
Notes: To achieve high-density DRAM chips, open-bitline architecture is widely adopted in modern DRAM modules.
[CLICK]
In this architecture each subarray’s bitlines are connected to two rows of sense amplifiers one above and one below the subarray,
This results in neighboring subarrays share common sense amplifiers.

## Slide 9: DRAM Open Bitline Architecture
Sense
Amplifier
SA
SA
SA
SA
SA
SA
DRAM Bank
Subarray
bitline
bitline
Serves as the reference for the SA
Activated
Not
Activated
NOT
Gate
9
Notes: [Click] During an activation, another bitline in a neighboring subarray is also involved to serve as the reference of the sense amplifier, which is bitline-bar in this example.
After a successful activation, the bitline and bitline-bar have a complementary voltage
[CLICK] as the sense amplifier consists of two back-to-back inverters.

## Slide 10
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the subarray for a new ACTIVATE
1
1
1
1
1
2
3
I/O Circuitry
Sense
Amps.
DRAM Subarray
DRAM Operation
Notes: Data is internally accessed in a row granularity. To access data, [CLICK]
the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers [CLICK]
Then, column accesses are serviced from the sense amplifiers [CLICK]
Finally, the subarray needs to be precharged to get ready for the next row activation [CLICK]

## Slide 11: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
11
Goal & Overview
Notes: Let’s start with a background and the overview of our study

## Slide 12
Understand the capability of COTS DRAM chips beyond just storing data
Our Goal
COTS: Commercial Off-The-Shelf
Rigorously characterize
the reliability of this capability
Notes: Our goal is to
[CLICK] understand the capability of off-the-shelf DRAM chips other than just storing data and
[CLICK] Rigorously characterize the reliability of this capability

## Slide 13: The Capability of COTS DRAM Chips
13
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 14: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
14
Goal & Overview
Notes: <Script>

## Slide 15: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
15
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 16: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
16
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 17: Testing Methodology
Carefully sweep:
  Row addresses: Row A and Row B
  Timing parameters: Between ACT → PRE and PRE → ACT
17
ACT Row A
PRE
ACT Row B
Neighboring Subarrays
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
Notes: In this study, we focus on two neighboring subarrays, here denoted as Subarray X and Subarray Y, which share a common component, sense amplifiers
[CLICK] We perform our experiment using the following command sequence: Activate Row A, which is in the subarray X, Precharge, and Activate Row B
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 18: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
18
Goal & Overview
Notes: Let’s move to our first analysis

## Slide 19: The Capability of COTS DRAM Chips
19
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: In this analysis,
[CLICK] we will demonstrate that how off-the-shelf DRAM chips are capable of simultaneously activating up to 48 rows in two neighboring subarrays

## Slide 20: Key Observation
36ns
20
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Activating two rows in quick succession
can simultaneously activate
multiple rows in neighboring subarrays
Neighboring Subarrays
Subarray X
Subarray Y
Row A
Row B
DRAM Bank
Shared Sense Amplifiers
14ns
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate multiple rows in neighboring subarrays
[CLICK] You may remember this pictorial example where Subarray X and Subarray Y are neighbor subarrays and Row A is in Subarray X and Row B is in Subarray Y.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT, we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate multiple rows at once in neighboring subarrays

## Slide 21: Characterization Methodology
21
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
All rows in Subarray X
To understand which and how many rows are simultaneously activated
  Sweep Row A and Row B addresses
All rows in Subarray Y
Notes: [CLICK] To rigorously characterize and to understand which and how many rows are activated
[CLICK] We sweep two key parameters: Row A address: we sweep it to test all rows in Subarray X and Row B address: we test all rows in Subarray Y, again to remind you Subarray X and Subarray Y are neighbors

## Slide 22: Key Results
22
Exactly the same number of rows
in each subarray
are activated
Twice as many rows in one subarray
compared to its neighbor subarray are activated
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
when two rows are activated with violated timings
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
A total of 32 rows
A total of 48 rows
Notes: We observe when Row A and B in neighboring subarrays are activated with violated timing parameters
[CLICK] Off-the-shelf DRAM chips have two distinct sets of simultaneous activation patterns in two neighboring subarrays
[CLICK] First pattern is exactly the same number rows in each subarray are activated.
[CLICK] We observe that we can activate up to 16 rows in neighboring subarrays, in other words a total of 32 rows
[CLICK] Second pattern is twice as many rows in one subarray compared to its neighbor subarray are activated
[CLICK] We observe that we can activate up to 16 rows in one subarray while activating up to 32 rows in its neighbor subarray, a total of 48 rows

## Slide 23: Key Takeaway
23
Exactly the same number of rows
in each subarray
Twice as many rows in one subarray
compared to its neighbor subarray
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
COTS DRAM chips can simultaneously activate
up to 48 rows in two neighboring subarrays
(More results in the paper)
https://arxiv.org/pdf/2402.18736.pdf
Notes: Our takeaway is
[CLICK] off-the-shelf DRAM chips can indeed simultaneously activate multiple rows in two neighboring subarrays and they can activate up to 48 rows.
[CLICK] As our time limited, I would like to refer you to our paper for more results and detailed analysis

## Slide 24: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
24
Goal & Overview
Notes: Now our second analysis: NOT operation

## Slide 25: The Capability of COTS DRAM Chips
25
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays
[CLICK] By leveraging our first observation, now let’s see how we can perform NOT operation in off-the-shelf DRAM chips

## Slide 26: Key Idea
26
Connect rows in neighboring subarrays
through a NOT gate by simultaneously activating rows
SA
A
src
dst
ACT src
ACT dst
SA
A
src
dst
SA
A
src
dst
~A
NOT gate
Notes: Our key idea is to leverage the connection between neighboring subarrays,
[CLICK] the NOT gate in the sense amplifier.
[CLICK] By simultaneously activating rows in neighboring subarrays, we can connect these rows through a NOT gate
[CLICK] As an example, source and destination in neighboring subarrays and if we first activate src
[CLICK] and then activate destination, this result in sense amplifier to drive the negated src value to the dst

## Slide 27: NOT Operation: A Walkthrough
½ VDD
src
dst
½ VDD
GND
GND
27
ACT src
connects src to bitline
Notes: Let’s see how we can perform NOT operation in real DRAM chips at a lower abstraction-level
[CLICK] As an example, we have source and destination cells, both store GROUND (low voltage) and bitlines are precharged to vdd over two
[CLICK] We first issue an activation to the source, which asserts the source wordline and starts charge sharing process between source and its bitline

## Slide 28: NOT Operation: A Walkthrough
GND
src
dst
GND
GND
VDD
28
ACT src
Nominal
drives bitline to GND
drives bitline to VDD
Notes: We wait for nominal timing parameters, which assures sense amplifier amplifies the difference and
[CLICK] drives ground to the source’s bitline and VDD to the destination’s bitline

## Slide 29: NOT Operation: A Walkthrough
src
dst
connects dst to bitline
29
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
sense amplifier is still enabled
dst’s bitline is still VDD
Notes: We then issue back-to-back precharge and activation commands with violated timing parameters. This operation leads to
[CLICK] connecting destination cell to its bitline
[CLICK] keeping the sense amplifier enabled
[CLICK] keeping the destination’s bitline to VDD

## Slide 30: NOT Operation: A Walkthrough
src
dst
negated value of src (VDD) is written to dst
30
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
Notes: Eventually, as sense amplifier is enabled and bitline is still VDD, the negated value of the source, which is VDD, is written to dst

## Slide 31: Characterization Methodology
31
ACT Row A
PRE
ACT Row B
<3ns
All rows in Subarray X
All rows in Subarray Y
Nominal
Sweep Row A and Row B addresses
Sweep DRAM chip temperature
50◦C
95◦C
Notes: To answer these questions,
[CLICK] similar to our previous analysis, we sweep Row addresses where Row A and Row B in neighboring subarrays
[CLICK] We sweep DRAM chip temperature from 50 degree Celsius to 95 degree celcius

## Slide 32: Reliability Metric
Success Rate (for a DRAM cell)
Percentage of trials where the correct output of
a tested operation is stored in the cell
Total of 10000 trials
GND
src
dst
GND
32
…
Success rate for this cell: 50%
Notes: To evaluate the reliability of NOT Operation,
[CLICK]we define a metric called success rate
[CLICK] Success rate for a DRAM cell refers to percentage of correct trials
[CLICK] We test total of 10000 trials and record the success rate for each tested cell

## Slide 33: Key Takeaways from In-DRAM NOT Operation
33
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Key Takeaway 1
Temperature has a small effect on
the reliability of NOT operations
Key Takeaway 2
Notes: This analysis provides two key takeaway lessons: [CLICK]
[CLICK] First, off-the-shelf DRAM chips can perform NOT operations with up to 32 destination rows
[CLICK] Second, temperature has a small effect on the reliability of NOT operations

## Slide 34: Performing NOT in COTS DRAM Chips
34
There is at least one DRAM cell that can
perform the NOT operation
with a 100% success rate
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Notes: Let’s take a look at our first results
[CLICK] In the x-axis you see the number of destination rows and y-axis shows the success rate distributions across tested DRAM cells
[CLICK] We observe that there is at least one DRAM cell that can perform the NOT operation with a 100% success rate in every tested number of destination rows
[CLICK] Our takeaway from this experiment is off-the-shelf DRAM chips are capable of performing NOT operations with up to 32 destination rows

## Slide 35: Impact of Temperature
Used destination cells that can perform NOT operation with >90% success rate at 50◦C
Temperature has a small effect on
the reliability of NOT operations
35
from 50◦C to 95◦C
only 0.2% variation in average success rate
Notes: Our next experiment is the impact of temperature on the reliability of the NOT operation
[CLICK] To maintain a reasonable experiment time we use destination cells that can perform NOT operation with more than 90% success rate at 50 degree Celsius
[CLICK] In this plot again x-axis is the number of destination rows and the y-axis shows the success rate distribution across DRAM cells and hue shows the tested temperature levels in each cluster of boxes temperature increases from left to right
[CLICK] We observe that when we increase the temperature from 50 degree Celsius to 95 degree Celsius, there is only 0.2% variation in average success rate in 32 destination rows
[CLICK] Our takeaway from this experiment is temperature has a small effect on the reliability of NOT operations

## Slide 36: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
36
Goal & Overview
Notes: Now, let’s move to our last analysis

## Slide 37: The Capability of COTS DRAM Chips
37
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK] Until now, We demonstrated that off-the-shelf DRAM chips are capable of activating multiple rows in neighboring subarrays and performing NOT operation
[CLICK] Now we will see how these two demonstrations enables us to perform up to 16-input AND, NAND, OR, and NOR operations

## Slide 38: Key Idea
38
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in X and Y and the bitline at the top subarray becomes the function of voltages in A and B
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 39: Two-Input AND and NAND Operations
39
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
VDD
VDD/2*
Notes: Now let me show you the basic intuition to perform two-input AND and NAND operations.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2 as a side note we store VDD/2,using FracDRAM’s technique.
[CLICK] and in the compute subarray we have X and Y.
With this setup, if we activate all these four cells
[CLICK] using ACT-PRE-ACT sequence, we will get AND of X and Y in the compute subarray and NAND of X and Y in the reference subarray.
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half.
Now let me prove that that is the case. I am going to cover all combinations of X and Y values.

## Slide 40: Two-Input AND and NAND Operations
VDD=1 & GND = 0
X
Y
COM
0
0
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
40
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
GND
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
Notes: In the first row of truth table, X and Y are GND.
[CLICK] This results in bitline in the compute subarray to be GND and the reference bitline is 3 vdd over 4.
[CLICK] Sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than GND, reference cells store VDD and compute cells store GND

## Slide 41: Two-Input AND and NAND Operations
VDD=1 & GND = 0
41
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
0
1
0
0
0
1
Notes: In the second row of truth table, X is GND and Y is VDD
[CLICK] As the bitline voltage in compute subarray is lower than reference subarray’s bitline voltage
[CLICK] reference cells store VDD and compute cells store GND

## Slide 42: Two-Input AND and NAND Operations
VDD=1 & GND = 0
42
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
sense amp.
compares
the voltages on the bitlines
VDD
GND
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
1
0
0
1
0
0
0
1
0
1
0
1
Notes: In the third row of truth table, X is VDD and Y is GND
[CLICK] This results in bitline in the compute subarray to be VDD half and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than vdd half, reference cells store VDD and compute cells store GND

## Slide 43: Two-Input AND and NAND Operations
VDD=1 & GND = 0
43
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
GND
VDD
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1
Notes: In the last row of truth table, X and Y are both VDD
[CLICK] This results in bitline in the compute subarray to be VDD and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference. However, this time compute subarray’s bitline is greater than. As a results reference cells store GND and compute cells store VDD
Consequently, this example shows compute subarray stores the result of the and operation of X and Y. and reference subarray cells store the result of the nand of operation of X and Y.

## Slide 44: Two-Input AND and NAND Operations
VDD=1 & GND = 0
44
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1

## Slide 45: Many-Input AND, NAND, OR, and NOR Operations
VDD=1 & GND = 0
X
Y
AND
0
0
0
0
1
0
1
0
0
1
1
1
NAND
1
1
1
0
45
Reference Subarray (REF)
Compute Subarray (COM)
VDD/2
VDD
X
Y
ACT REF
PRE
ACT COM
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
We can express AND, NAND, OR, and NOR operations
by carefully manipulating the reference voltage
(More details in the paper)
https://arxiv.org/pdf/2402.18736.pdf
Notes: By carefully choosing the voltage levels of the cells in the reference subarray, we can express many-input AND, NAND, OR, and NOR operations
[CLICK] As our time is limited, please check our paper for more details.

## Slide 46: Characterization Methodology
46
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Subarray X
Subarray Y
Row A
Row B
ACT
DRAM Bank
ACT
Shared Sense Amplifiers
All rows in Subarray X
Sweep Row A and Row B addresses
All rows in Subarray Y

## Slide 47: Key Takeaways from In-DRAM Operations
47
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
Key Takeaway 1
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
Key Takeaway 3
COTS DRAM chips can perform
AND, NAND, OR, and NOR operations
with very high reliability
Key Takeaway 2

## Slide 48: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
48
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 49: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
16-input AND, NAND, OR, and NOR operations
with very high success rate (>94%)
49
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 50: Impact of Data Pattern
50
1.98% variation in average success rate
across all number of input operands
Notes: Our second analysis the impact of data pattern
[CLICK] This plot depicts the effect of data pattern on the NOR operation’s success rate: x-axis shows the number of input operands and y-axis shows the success rate distribution and hue shows the tested data patterns: either all 1s/0s in a row and random data pattern.
[CLICK] We observe a 1.97% variation in average success rate across all tested number of input operands

## Slide 51: Impact of Data Pattern
51
Impact of data pattern is consistent
across all tested operations
Notes: Here we show AND, NAND, OR, and NOR operations and
[CLICK] We observe that the impact of data pattern is consistent across all tested operations

## Slide 52: Impact of Data Pattern
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
52
Notes: Our takeaway from this experiment is data pattern slightly affects the reliability of AND, NAND, OR, and NOR operations.

## Slide 53: More in the Paper
Detailed hypotheses & key ideas to perform
  NOT operation
  Many-input AND, NAND, OR, and NOR operations
How the reliability of bitwise operations are affected by
  The location of activated rows
  Temperature (for AND, NAND, OR, and NOR)
  DRAM speed rate
  Chip density and die revision
Discussion on the limitations of COTS DRAM chips
53
Notes: You can find the following in the paper
[CLICK] The key ideas and hypotheses on how a COTS DRAM chip is capable of performing these operations
[CLICK] How the reliability of tested operations are affected by: Spatial Variation, more temperature results, DRAM Speed Rate and Chip density and Die revision
[CLICK] And what are the limitations that we face in off-the-shelf DRAM chips and a broad discussion on this topic

## Slide 54: Available on arXiv
https://arxiv.org/pdf/2402.18736.pdf
54
Notes: The extended version of our study is available on arxiv

## Slide 55: Outline
Background
Experimental Methodology
AND, NAND, OR, and NOR Operations
Multiple-Row Activation in Neighboring Subarrays
Conclusion
NOT Operation
55
Goal & Overview
Notes: Let me conclude my talk

## Slide 56: Conclusion
We experimentally demonstrate that commercial off-the-shelf (COTS) DRAM chips can perform:
  Functionally-complete Boolean operations: NOT, NAND, and NOR
  Up to 16-input AND, NAND, OR, and NOR operations
We characterize the success rate of these operations on 256 COTS DDR4 chips from two major manufacturers
We highlight two key results:
  We can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations on COTS DRAM chips with very high success rates (>94%)
  Data pattern and temperature only slightly affect the reliability of these operations
56
We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate

## Slide 57: Functionally-Complete Boolean Logic in Real DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
Ismail Emir Yüksel
Yahya C. Tugrul Ataberk Olgun F. Nisa Bostancı
A. Giray Yaglıkçı Geraldo F. Oliveira Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Functionally-Complete Boolean Logic in Real DRAM Chips

## Slide 58: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 59: Executive Summary
Experimental Study: 120 DDR4 chips from two major manufacturers
COTS DRAM chips can perform MAJ5, MAJ7, and MAJ9 operations and copy one DRAM row to up to 31 different rows at once
Storing multiple redundant copies of MAJ’s input operands (i.e., input replication) drastically increases robustness (>30% higher success rate)
Operating conditions (temperature, voltage, and data pattern) affect the robustness of in-DRAM operations (by up to 11.52% success rate)
Goal: To experimentally analyze and understand
The computational capability of COTS DRAM chips beyond that of prior works
The robustness of such capability under various operating conditions
Motivation:
Processing-Using-DRAM (PUD) alleviates data movement bottlenecks
Commercial off-the-shelf (COTS) DRAM chips can perform three-input majority (MAJ3) and in-DRAM copy operations
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: Let’s start with an executive summary
[CLICK] Processing-Using-DRAM is a promising paradigm to alleviate performance and energy overheads caused by frequent data movement between main memory and processing unit
[CLICK] Prior works show that off-the-shelf DRAM chips are capable of performing three-input majority and in-DRAM copy operations
[CLICK] In this study, our goal is to experimentally analyze and understand the computational capability of off-the-shelf DRAM chips beyond what prior works have demonstrated
[CLICK] and the robustness of such capability under various operating conditions
[CLICK] To this end, we conduct our experimental study on 120 DDR4 DRAM chips from two major manufacturers and
[CLICK] We show that off-the-shelf DRAM chips can perform MAJ5, MAJ7, and MAJ7 operations and copy one row’s content to up to 31 different rows simultaneously
[CLICK] We show that storing multiple redundant copies of majority operations’ input operands drastically increases robustness, more than 30% increase in success rate, which is our robustness metric
[CLICK] Finally, we observe that operating conditions (such as temperature, voltage, and data pattern) can affect the robustness of in-DRAM operations by up to 11.52% on average
[CLICK] Our work is artifact evaluated and fully open sourced, you can access our repository from this link here
-----
Whitespace is broken

## Slide 60: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: By leveraging simultaneous many-row activation, we can
[CLICK] Perform majority operations with more than three inputs
[CLICK] We can increase the robustness of majority operations
[CLICK] And we can copy one row’s content to multiple rows

## Slide 61: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Next, I will show how we can copy one row’s content to multiple rows

## Slide 62: In-DRAM Multiple Row Copy (Multi-RowCopy)
d
s
t
r
c
s
Simultaneously activate many rows to copy one row’s content to multiple destination rows
d
s
t
s
r
c
RowClone
s
r
c
r
c
s
s
r
c
d
s
t
d
s
t
d
s
t
Multi-RowCopy
s
r
c
s
r
c
s
r
c
[Seshadri+ MICRO’13]
Notes: [CLICK] Our key idea is since we can activate many rows simultaneously, we can copy one row’s content to other simultaneously activated rows
[CLICK] Let’s recall the RowClone example where we copy source to destination
[CLICK] In RowClone, we first activate the source row which will copy its content to sense amplifiers
[CLICK] And then, we activate destination row to drive the sense amplifier’s content to destination row
[CLICK] In our mechanism, which we call Multi-RowCopy, we have several destination rows
[CLICK] Here we activate many destination rows simultaneously
[CLICK] and thus sense amplifier drives its content to these destination rows.

## Slide 63: Robustness of Multi-RowCopy
COTS DRAM chips can copy one row’s content to up to 31 rows with a very high success rate
Average: >99.98%
Notes: Now let me show you the first result
[CLICK] In this plot, y-axis shows the success rate
[CLICK] x-axis shows the number of destination rows from 1 to 31
[CLICK] And we plot the success rate distribution as a box-and-whiskers plot
[CLICK] We observe that the average success rate is higher than 99.98% across all tested number of destination rows
[CLICK] Hence, we conclude that off-the-shelf DRAM chips can copy one row’s content to up to 31 rows with a very high success rate

## Slide 64: Available on arXiv
https://arxiv.org/pdf/2405.06081
Notes: The extended version of our study is available on arxiv

## Slide 65: Our Work is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: And our work is artifact evaluated and got every badges
[CLICK] You can download our code from github and start testing right away!

## Slide 66: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Paper
GitHub
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 67: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, PuDHammer [..]

## Slide 68: Executive Summary
Experimental Study: 316 COTS DDR4 chips from four major manufacturers to study read disturbance effects of multiple-row activation, which we call PuDHammer
PuDHammer significantly exacerbates DRAM read disturbance, causing up to 158.58x reduction in min. hammer count to induce first bitflip (HCfirst)
PuDHammer bypasses in-DRAM RowHammer mitigation in DDR4 and induces 11340x more bitflips than RowHammer
Motivation: Processing-using-DRAM (PuD) alleviates data movement bottlenecks
DRAM can perform many PuD operations by activating multiple DRAM rows in quick succession or simultaneously (i.e., multiple-row activation)
Modern DRAM is subject to read disturbance (e.g., RowHammer)
    Repeatedly activating even a single row induces bitflips in unaccessed rows
Problem: No prior work study the read disturbance effects of multiple-row activation
Goal: Understand and analyze read disturbance effects of multiple-row activation
Mitigation: We adapt Per Row Activation Counting (PRAC) for PuDHammer
Adapted PRAC solution incurs an average system performance overhead of 48.26%

## Slide 69: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 70: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 71: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018

## Slide 72: DRAM Organization
Row Decoder
DRAM Subarray
DRAM Module
DRAM
Chip
Bitline
DRAM Row
DRAM Cell
Wordline
Sense Amps.
DRAM Chip
…
…
Bank
Chip I/O
DRAM Bank
Subarray
Notes: DRAM is used as the main memory in many computing systems.
[CLICK] a DRAM module consists of multiple DRAM chips
[CLICK]Each chip contains multiple banks
[CLICK] Each bank is composed of multiple subarrays and sense amplifiers
[CLICK] And within each subarray, there is a two dimensional array of DRAM cells.
[CLICK] These cells are organized into rows that are selected using wordlines
[CLICK] And the cells are connected to a row of sense amplifiers via bitlines

## Slide 73: DRAM Operation
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 74: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-using-DRAM uses the analog operational principles of DRAM cells to perform computation
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
Many PuD operations involves a key technique called multiple-row activation

## Slide 75: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-
Using-DRAM
…
…
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
1. Consecutive Multiple-Row Activation (CoMRA)
2. Simultaneous Multiple-Row Activation (SiMRA)
Multiple-row activation is a key technique to realize many PuD operations
Notes: We categorize multiple-row activation into two categories
First, consecutive multiple-row activation, CoMRA
Second, simultaneous multiple-row activatio,, SiMRA
Now, let me dive deeper into these two and give their key ideas

## Slide 76: Consecutive Multiple-Row Activation
Violating timing of PRE command greatly
can activate two rows consecutively
Notes: First, Consecutive Multiple-Row Activation.
[CLICK] The key observation is that violating timing of PRE command greatly can activate two rows consecutively

## Slide 77: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
s
t
d
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively
Notes: Let’s see how CoMRA works with an example: Here we have two rows source, src, and destination, dst.
[CLICK] If we obey the DRAM timing parameters while issuing this command sequence
[CLICK] We will only activate a single DRAM row at once, firstly source and then destination
[CLICK] However, if we violate the timing between PRE and ACT dst
[CLICK] We can activate destination row without deactivating sense amplifier and keeping the bitlines at source voltage level
[CLICK] As a result of this, we can perform in-dram row copy operation: source row can be copied to destination row

## Slide 78: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively
src’s content is copied to dst
s
r
c

## Slide 79: Simultaneous Multiple-Row Activation
Activating two rows in quick succession
can simultaneously activate
multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Now let’s see how SiMRA works
[CLICK] The key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] In this pictorial example Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we can activate many rows at once in the same subarray

## Slide 80: Example: In-DRAM Majority-of-Three (MAJ3)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
[Seshadri+ MICRO’17, Gao+ MICRO’19]
Assert three rows’ wordlines
Three rows perturb bitlines simultaneously
Sense amplifiers sample the output of majority
ACT
PRE
ACT
<3ns
<3ns
Notes: One example of SiMRA is In-DRAM MAJ3 operation
[CLICK] Assume ACT-PRE-ACT with violated timnigs will activate three rows simultaneously that contain a,b, and b values, respectively.
[CLICK] By activating three rows simultaneously, DRAM will assert these rows’ wordlines
[CLICK] After that these activated rows perturb bitlines simultaneously
[CLICK] After some time, sense amplifier amplifies the perturbation on the bitline and sample the output of majority of the values stored in activated rows, which is b in this example

## Slide 81: Read Disturbance in DRAM
Unfortunately, even activating a single DRAM row disturbs the data-integrity of other unaccessed DRAM rows
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
Notes: Read disturbance bitflips have significant system-level implications because they break memory isolation.
[CLICK] Even activating a single DRAM row disturbs the data integrity of ther unaccessed DRAM rows.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICKx9] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows.

## Slide 82: Outline
Background
Testing Infrastructure
Combined Effect of CoMRA, SiMRA, and RowHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: This phenomenon brings us to the problem and the goal of this paper

## Slide 83: Problem & Goal
Problem
No prior work investigates the read disturbance effects of multiple-row activation
Goal
Understand how multiple-row activation affect read disturbance vulnerability in DRAM

## Slide 84: Outline
Background
Real DRAM Chip Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 85: DRAM Bender: DRAM Testing Infrastructure
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Fine-grained control over DRAM commands, timings, temperature, and voltage
Notes: This infrastucture
[CLICK] enables fine-grained control over DRAM commands, timings, temperature and voltage

## Slide 86: DRAM Chips Tested
316 DDR4 chips from four major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK] We test 120 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 87: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 88: Recall: CoMRA
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively
src’s content is copied to dst
s
r
c
Notes: Let’s recall that CoMRA violates PRE to ACT to activate two rows consecutively, which allows to perform in-DRAM row copy operation

## Slide 89: Hammering with CoMRA
DRAM Subarray
.
.
.
.
.
.
Double-Sided
Single-Sided
.
.
.
DRAM Subarray
src
dst
dst
src
ACT src
ACT dst
PRE
7.5ns
36ns
victim
victim
victim
victim
victim
aggressor
aggressor
aggressor
aggressor
Notes: To hammer using CoMRA access pattern, we use two versions of hammering:
[CLICK] First, double-sided where we sandwich a victim row
[CLICK] We adapt CoMRA to perform copy operation to sandwich a victim row for double-sided
[CLICK] Second, single-sided
[CLICK] where a single aggressor row disturbs its neighboring victim rows
[CLICK] To perform single-sided CoMRA, we perform the copy operation between two rows that are far away from each other

## Slide 90: Characterization Methodology
Carefully sweep
    Row addresses: src and dst
    Timing parameters: Between PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
ACT
ACT
ACT src
PRE
ACT dst
.
.
.
src
victim
dst
aggressor
aggressor
.
.
.
DRAM Subarray
DRAM Bank
Temperature
50 ◦C
80 ◦C
Notes: To characterize the read disturbance effects of CoMRA
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between prechrage to activate command
[CLICK] Data pattern
[CLICK] And temperature

## Slide 91: Read Disturbance Vulnerability Metric: HCfirst
The minimum hammer count required to induce the first bitflip
Lower is worse
Record bitflips in victim
Victim Row
Aggressor Row (src)
Aggressor Row (dst)
1 Hammer
ACT src
ACT dst
PRE
Notes: To evaluate the read disturbance vulnerability of DRAM chips, we use widely-adopted metric called Hcfirst
[CLICK] which is the minimum hammer count required to induce the first bitflip and lower the Hcfirst worse the read disturbance is
[CLICK] Here we have a double sided scenario where we sandwich a victim row
[CLICK] We count one CoMRa operation, ACT-PRE-ACT as 1 Hammer and we record bitflips in victim

## Slide 92: Double-Sided CoMRA vs. RowHammer (I)
13.98x
Double-sided CoMRA decreases lowest HCfirst by 13.98x compared to double-sided RowHammer
Lowest HCfirst reduction trend consistent across all four manufacturer
1.18x
3.28x
1.58x

## Slide 93: Double-Sided CoMRA vs. RowHammer (II)
Represents 99% of tested victim rows
Represents 50% of tested victim rows
HCfirst reduction of 50%
RowHammer HCfirst = 100
CoMRA HCfirst = 50

## Slide 94: Double-Sided CoMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
Double-sided CoMRA decreases HCfirst for a large fraction of rows compared to double-sided RowHammer

## Slide 95: Double-Sided CoMRA vs. RowHammer
CoMRA exacerbates DRAM’s vulnerability to read disturbance in all four major manufacturers
Key Takeaway

## Slide 96: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 97: Recall: SiMRA
Activating two rows in quick succession
can simultaneously activate
multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 98: Characterization Methodology
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
Temperature
50 ◦C
80 ◦C
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
Row A
Row B
Notes: [CLICK] In this study, we focus on individual subarrays, here denoted as Subarray X
[CLICK] We perform our experiment using the following command sequence: Activate Row A, Precharge, and Activate Row B, where Row A and Row B in the same subarray
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 99: Double-Sided SiMRA vs. RowHammer (I)
159x
Double-sided SiMRA decreases lowest HCfirst by 159x compared to double-sided RowHammer
51x
86x
125x
Lowest HCfirst reduction trend consistent across all tested number of simultaneously activated rows

## Slide 100: Double-Sided SiMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
at least 25.19% of tested victim rows experience >99% HCfirst reduction

## Slide 101: Double-Sided SiMRA vs. RowHammer (II)
Double-sided SiMRA significantly decreases HCfirst for a majority of rows compared to double-sided RowHammer

## Slide 102: Double-sided SiMRA vs. RowHammer
SiMRA drastically exacerbates DRAM’s vulnerability to read disturbance
Key Takeaway

## Slide 103: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 104: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 105: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 106: Target Row Refresh (TRR)
Row 0
Row 1
Row 2
Row 3
Row 4
TRR-equipped DRAM Chip
TRR
Memory Controller
DRAM vendors equip their DRAM chips with a proprietary mitigation mechanisms known as Target Row Refresh (TRR)
Aggressor detected: Row 2
Refresh neighbor rows
TRR-induced refreshes
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
REF
aggressor
Notes: To protect their DRAM chips against RowHammer, DRAM vendors currently implement proprietary RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row
[CLICK] We demonstrate how TRR operates at a high-level.
[CLICK] The TRR mechanism detects [CLICK] an aggressor row as a result of [CLICK] repeatedly activating and precharging the same row. [CLICK]
[CLICK] To protect the neighbor victim rows from experiencing RowHammer bit flips, [CLICK] TRR refreshes the victim rows by performing TRR-induced refresh operations. TRR refreshes victim rows by piggybacking TRR-induced refreshes to the REFRESH commands that the memory controller periodically issues.

## Slide 107: Reverse Engineering TRR
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by on-die mitigation
[Hassan+, MICRO’21, source code available at https://github.com/CMU-SAFARI/U-TRR]
Hassan et al., "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” in MICRO, 2021.
Notes: We use the methodology presented in this paper
[CLICK] Where the key idea is to use data retention failures as a side channel to detect when a row is refreshed by the on-die mitigation mechanism
[CLICK] We re-use the source code that is publicly available on this Github page.

## Slide 108: PuDHammer in the presence of TRR
>10K bitflips
<60 bitflips
>10K bitflips
~60 bitflips
CoMRA induces 1.10x more bitflips than RowHammer on average in the presence of TRR

## Slide 109: PuDHammer in the presence of TRR
>10K bitflips
<60 bitflips
~240K bitflips
~180K bitflips
SiMRA induces 11340x more bitflips than RowHammer on average in the presence of TRR

## Slide 110: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 111: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 112: Adapting RowHammer Mitigations for PuDHammer
A Naïve Approach (PRAC-Naïve)
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting (PRAC-WC)
Count each operation differently depending on their lowest observed HCfirst

## Slide 113: Methodology
Environment: Cycle-level DRAM simulator Ramulator2 [Kim+ CAL'15, Luo+ CAL'23]
System Configuration:
  Processor 4-core, out-of-order, 4.2GHz clock frequency
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4
  PRAC 4 RFMs per Back-off
  PIM Unit 1-core, issues CoMRA & SiMRA operations with a fixed invertal
Workloads:
    60 five-core five-core multiprogrammed workload mixes.
    Each mix is composed of
      four workloads from five major benchmark suites and
      one synthetic workload that periodically performs back-to-back one SiMRA with 32-row activation and one CoMRA operation

## Slide 114: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-Naïve
PRAC-WC
DRAM performs PuD operations in every 125ns
Normalized to no RH mitigation

## Slide 115: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-WC greatly outperforms PRAC-Naïve until 2us.
PRAC-WC incurs an average (maximum) performance overhead of 48.26% (98.83%).

## Slide 116: More in the Paper
More characterization results
    Temperature, spatial variation, timing parameters, access pattern, data pattern, aggressor row on time analyses for CoMRA and SiMRA
    Combined Read Disturbance Effect of RowHammer with PuD
      Combined pattern is more effective than RowHammer alone (e.g., 1.66x reduction in HCfirst on average)
Details and analyses on mitigating PuDHammer
    Discussion on how modifying DRAM chips could help mitigating PuDHammer
    More details on PRAC adaptation
      Challenges on adapting for PuDHammer
      An area-efficient PRAC solution
      ..
Notes: We have more content in the paper, including
…

## Slide 117: Available on arXiv
https://arxiv.org/pdf/2506.12947
Notes: The extended version of our study is available on arxiv

## Slide 118: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 119: Conclusion
We extensively study the interaction between read disturbance and multiple-row activation-based Processing-using-DRAM operations
We characterize 316 DDR4 chips from four major manufacturers
PuDHammer significantly exacerbates the DRAM read vulnerability (e.g., HCfirst reduces from 4K to 26)
PuDHammer bypasses in-DRAM RowHammer mitigation (TRR) and induces 11340x more bitflips than RowHammer
We hope our findings guide system-level and architectural solutions to enable read-disturbance-resilient future PuD systems.
We adapt Per Row Activation Counting (PRAC) for PuDHammer
Incurs 48.26% performance overhead on average across 60 multiprogrammed workload mixes
Notes: In this study,
[CLICK] We experimentally demonstrate that off-the-shelf DRAM chips can simultaneously activate up to 32 DRAM rows
[CLICK] perform MAJ3, MAJ5, MAJ7, and MAJ9 operations
[CLICK] and copy one row’s content into up to 31 different rows simultaneously
[CLICK] We characterize the success rate of in-DRAM operations on 120 DDR4 chips from two major manufacturers And we highlight three key results
[CLICK] By storing multiple copies of majority’s input operands, we can increase the success rate of majority operations
[CLICK] and operating conditions can significantly affect the robustness of in-DRAM operations
[CLICK] We conclude that these empirical results demonstrate the promising potential of using DRAM as a computation substrate

## Slide 120: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 121: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Backup Slides
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 122: Per Row Activation Counting in DDR5 (April 2024)
DRAM Rows
0xA
PRAC Counters
DRAM Command Timeline
ACT A
ACT A
1
ACT A
ACT A
2
...
ACT A
ACT A
NBO
accurately tracks activation counts of each row
requires
preventive
action
Back-off
RFM
RFM
allocates a fixed time for preventive refresh
ACT
Back-off
continue to send commands
back-off threshold

## Slide 123: Adapting PRAC for PuDHammer
A Naïve Approach
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting
Count each operation differently depending on their lowest observed HCfirst

## Slide 124: A Naïve Approach (PRAC-Naïve)
DRAM Rows
0xA
PRAC Counters
1
2
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=20
Lowest HCfirst for tested DRAM chips
RH: ~4K
CoMRA: ~400
SiMRA: ~20

## Slide 125: Weighted Counting (PRAC-WC)
DRAM Rows
0xA
PRAC Counters
1
201
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=4K
Threshold is set to 4K (RH Threshold) Each operation increases counters by
RH (ACT): 1
CoMRA: 10
SiMRA: 200

## Slide 126: Limitations of Tested COTS DRAM Chips (I)
Some COTS DRAM chips do not support all in-DRAM operations
    We do not observe simultaneous multiple-row activation in all tested Samsung chips
    Hypothesis
      Internal DRAM circuitry ignores the PRE command or the second ACT command when the timing parameters are greatly violated
    If such a limitation were not imposed, we believe these DRAM chips are also fundamentally capable of performing the operations we examine in this work

## Slide 127: Limitations of Tested COTS DRAM Chips (II)
Tested COTS DRAM chips support only consecutive two row activation and simultaneous activation of 2, 4, 8, 16, and 32 rows
    Hypothesis
      This is due to our current infrastructure limitations, where we can issue DRAM commands at intervals of only 1.5ns.
      Having fine-grained control on timing would allow us to deassert/assert desired intermediate signals in the row decoder circuitry

## Slide 128: In-DRAM Row-Copy (RowClone)
Fetch src’s content into the sense amplifiers
d
s
t
r
c
s
d
s
t
s
r
c
ACT src
Assert the src’s wordline
36ns
Notes: [CLICK] To perform RowClone, we first activate the source row by issuing ACT src command. This will assert the src’s wordline
[CLICK] and then fetch src’s content into the sense amplifiers

## Slide 129: In-DRAM Row-Copy (RowClone)
sense amplifier is still enabled
d
s
t
r
c
s
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
ACT src
ACT dst
Bitlines are still at src voltage
PRE
7.5ns
36ns
Activates dst row
Notes: After that, we activate
[CLICK] the destination row without performing precharge operation in between two activate commands
[CLICK] By doing that DRAM will keep the bitlines at src voltage
[CLICK] and keep the sense amplifier enabled
[CLICK] As a result, after some time, the source row’s content is copied to the destination row

## Slide 130: Aggressor Row On Time & RowPress
Instead of using a high hammer count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
[Luo+, ISCA’23]
hammer count = 2
Aggressor row on time (tAggON)
Minimum allowed row on time
(tRASmin)
Notes: In contrast, RowPress, instead of a high activation count, [CLICK] increases the time the that aggressor stays open.
Doing so disturbs adjacent rows enough to cause bitflips without having very high activation count.

## Slide 131: CoMRA (w/ increased tAggOn)
ACT src
ACT dst
PRE
7.5ns
36ns
36ns
Hammering with CoMRA
ACT src
ACT dst
PRE
7.5ns
36ns
tAggOn
(more than 36ns)
Pressing with CoMRA
PRE
PRE

## Slide 132: CoMRA (w/ Aggressor Row On Time) vs RowPress
For CoMRA
From 36ns to 70.2us
79x reduction
For RH/RP
From 36ns to 70.2us
31x reduction

## Slide 133: CoMRA (w/ Aggressor Row On Time) vs RowPress
Trend consistent across all four manufacturer:
Increasing tAggOn significantly reduces HCfirst for both CoMRA and RH/RP

## Slide 134: CoMRA (w/ Aggressor Row On Time) vs RowPress
Pressing with CoMRA is more effective than hammering with CoMRA
Key Takeaway 2

## Slide 135: Impact of the Data Pattern
(Victim has negated data pattern)
Aggressor Rows = 0xFF..FF
Victim Rows = 0x00..00

## Slide 136: Impact of the Data Pattern
(Victim has negated data pattern)
58x
Initializing victim rows with 0x00
increases avg. HCfirst by 58x
Dominant bitflip direction for SiMRA
1->0
Dominant bitflip direction for RH*
0->1
*not shown in the figure

## Slide 137: Impact of the Data Pattern
Trend consistent across all tested number of simultaneously activated rows
SiMRA is significantly affected by data pattern and directionality of SiMRA and RowHammer bitflips are opposite
Key Takeaway 2

## Slide 138: PuDHammer in the presence of TRR

## Slide 139: PuDHammer in the presence of TRR

## Slide 140: Functionally-Complete Boolean Logic in Real DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
Ismail Emir Yüksel
Yahya C. Tugrul Ataberk Olgun F. Nisa Bostancı
A. Giray Yaglıkçı Geraldo F. Oliveira Haocong Luo
Backup Slides
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Functionally-Complete Boolean Logic in Real DRAM Chips

## Slide 141: Experimental Methodology
DRAM Chip
…
…
Chip I/O
Bank
We test all banks in each DRAM chip
We test three neighboring subarray pairs in each bank
DRAM Bank
We test all possible combinations of activated rows
141
Notes: We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that enables fine-grained control over DRAM commands, timings, and temperature to characterize RowPress

## Slide 142: Experimental Methodology
We test all possible combinations of Row A and Row B
DRAM Bank
Sense Amps.
…
…
…
…
…
…
…
…
Subarray X
Subarray Y
RA
RA
RB
RB
RB
RA
142
Notes: We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that enables fine-grained control over DRAM commands, timings, and temperature to characterize RowPress

## Slide 143: Performing NOT in COTS DRAM Chips
As the number of destination rows increases,
more DRAM cells produce incorrect results.
The average success of the NOT operation with
four destination row: 98.37%
thirty-two destination rows: 7.95%
143

## Slide 144: The Coverage of Multiple-Row Activation
144
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 145: NOT vs. Activation Trend
145
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 146: Impact of Location in NOT Op.
The distance between activated rows and the sense amplifiers significantly affects the reliability
Categorize the distance between activated rows (source and destination rows) and the sense amplifiers into three regions: Far, Middle, and Close
Sense Amp.
Far
Middle
Close
Close
Middle
Far
Source Subarray
Destination Subarray
146

## Slide 147: The effect of DRAM Speed Rate on NOT
147
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 148: Chip Density & Die Revision (NOT)
148
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 149: Performing AND, NAND, OR, and NOR
The reliability distributions are very similar between 1) AND-NAND and 2) OR – NOR operations.
149

## Slide 150: Impact of Temperature
Temperature has a small effect on
the reliability of AND, NAND, OR, and NOR operations
150

## Slide 151: Boolean Operations vs. Number of 1s
151
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 152: The Effect of the Location
152
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 153: DRAM Speed Rate vs. Bitwise Ops.
153
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 154: Chip Density&Die Revision vs. Bitwise Ops.
154
Notes: COTS DRAM chips can perform 1:1, 1:2, 2:2, 2:4, 4:4, 4:8, 8:8, 8:16, 16:16, and 16:32 activation with an average coverage across all tested DRAM chips of 0.23%, 0.15%, 2.60%, 1.53%, 11.58%, 5.42%, 24.52%, 7.95%, 24.35%, and 3.82%, respectively.

## Slide 155: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline
NOT Gate
1. ACTIVATE (ACT)
2. PRECHARGE (PRE)
155
Notes: Here we take a closer look into DRAM cell.
A DRAM cell consists of two main components: capacitor and access transistor.
Capacitor holds the data as a form of electrical charge.
Access transistor connects cell to the subarray through wordline and bitline.
As we discussed, bitline is connected to the sense amplifier which consists of two back-to-back NOT gates.
In this study, we focus on two major DRAM commands: ACT and PRE, let’s see how they work.

## Slide 156: DRAM Cell Operation - ACTIVATE
raise wordline
enable
bitline
wordline
capacitor
access transistor
bitline
½ VDD
½ VDD
0
0
1
connects cell to bitline
cell loses
charge to bitline
+ δ
deviation in bitline voltage
1
enable sense amp
VDD
0
cell regains charge
156
Notes: First, ACT

## Slide 157: DRAM Cell Operation - PRECHARGE
enable
bitline
wordline
capacitor
access transistor
bitline
0
0
1
VDD
0
lower wordline
1
Precharge bitline
for next access
½ VDD
½ VDD
Disable
Sense Amp
157
Notes: PRE

## Slide 158: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 159: Executive Summary
Experimental Study: 120 DDR4 chips from two major manufacturers
COTS DRAM chips can perform MAJ5, MAJ7, and MAJ9 operations and copy one DRAM row to up to 31 different rows at once
Storing multiple redundant copies of MAJ’s input operands (i.e., input replication) drastically increases robustness (>30% higher success rate)
Operating conditions (temperature, voltage, and data pattern) affect the robustness of in-DRAM operations (by up to 11.52% success rate)
Goal: To experimentally analyze and understand
The computational capability of COTS DRAM chips beyond that of prior works
The robustness of such capability under various operating conditions
Motivation:
Processing-Using-DRAM (PUD) alleviates data movement bottlenecks
Commercial off-the-shelf (COTS) DRAM chips can perform three-input majority (MAJ3) and in-DRAM copy operations
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: Let’s start with an executive summary
[CLICK] Processing-Using-DRAM is a promising paradigm to alleviate performance and energy overheads caused by frequent data movement between main memory and processing unit
[CLICK] Prior works show that off-the-shelf DRAM chips are capable of performing three-input majority and in-DRAM copy operations
[CLICK] In this study, our goal is to experimentally analyze and understand the computational capability of off-the-shelf DRAM chips beyond what prior works have demonstrated
[CLICK] and the robustness of such capability under various operating conditions
[CLICK] To this end, we conduct our experimental study on 120 DDR4 DRAM chips from two major manufacturers and
[CLICK] We show that off-the-shelf DRAM chips can perform MAJ5, MAJ7, and MAJ7 operations and copy one row’s content to up to 31 different rows simultaneously
[CLICK] We show that storing multiple redundant copies of majority operations’ input operands drastically increases robustness, more than 30% increase in success rate, which is our robustness metric
[CLICK] Finally, we observe that operating conditions (such as temperature, voltage, and data pattern) can affect the robustness of in-DRAM operations by up to 11.52% on average
[CLICK] Our work is artifact evaluated and fully open sourced, you can access our repository from this link here
-----
Whitespace is broken

## Slide 160: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Here is the outline of my talk

## Slide 161: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Let’s start with a background

## Slide 162: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018

## Slide 163: Processing-In-Memory (PIM)
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-In-Memory:
1
Processing-Near-Memory: PIM logic is added near the memory arrays or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the analog operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory

## Slide 164: Processing-In-Memory (PIM)
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
1
Processing-Near-Memory: PIM logic is added near the memory arrays or to the logic layer of 3D-stacked memory
  Two main approaches for Processing-In-Memory:
2
Processing-Using-Memory: uses the analog operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: In this work, we focus on processing-using-memory architectures. In particular, its implementation using DRAM.
Before I introduce processing-using-DRAM architectures, I will provide a short background on DRAM organization and operation.

## Slide 165: DRAM Organization
Row Decoder
DRAM Subarray
DRAM Module
DRAM
Chip
Bitline
DRAM Row
DRAM Cell
Wordline
Sense Amps.
DRAM Chip
…
…
Bank
Chip I/O
DRAM Bank
Subarray
Notes: DRAM is used as the main memory in many computing systems.
[CLICK] a DRAM module consists of multiple DRAM chips
[CLICK]Each chip contains multiple banks
[CLICK] Each bank is composed of multiple subarrays and sense amplifiers
[CLICK] And within each subarray, there is a two dimensional array of DRAM cells.
[CLICK] These cells are organized into rows that are selected using wordlines
[CLICK] And the cells are connected to a row of sense amplifiers via bitlines

## Slide 166: DRAM Operation
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 167: In-DRAM Row-Copy (RowClone)
[Seshadri+ MICRO’13]
d
s
t
r
c
s
d
s
t
s
r
c
Copying the source (src) row’s content to the destination (dst) row
s
r
c
Notes: In this study, we focus on two prior in-DRAM operations. First one is in-DRAM Row-Copy, which is also called RowClone
[CLICK] The RowClone operation copies the source row’s content to the destination row. Now let’s see how we perform RowClone

## Slide 168: In-DRAM Row-Copy (RowClone)
Fetch src’s content into the sense amplifiers
[Seshadri+ MICRO’13]
d
s
t
r
c
s
d
s
t
s
r
c
ACT src
Assert the src’s wordline
Notes: [CLICK] To perform RowClone, we first activate the source row by issuing ACT src command. This will assert the src’s wordline
[CLICK] and then fetch src’s content into the sense amplifiers

## Slide 169: In-DRAM Row-Copy (RowClone)
sense amplifier is still enabled
[Seshadri+ MICRO’13]
d
s
t
r
c
s
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
ACT src
ACT dst
Bitlines are still at src voltage
Notes: After that, we activate
[CLICK] the destination row without performing precharge operation in between two activate commands
[CLICK] By doing that DRAM will keep the bitlines at src voltage
[CLICK] and keep the sense amplifier enabled
[CLICK] As a result, after some time, the source row’s content is copied to the destination row

## Slide 170: In-DRAM Majority-of-Three (MAJ3)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
MAJ3(a, b, b) = b
[Seshadri+ MICRO’17]
Performing a MAJ3 operation using three rows as input operands
Notes: Similarly,
[CLICK] prior works show that DRAM can perform MAJ3 operation using three rows as input operands

## Slide 171: In-DRAM Majority-of-Three (MAJ3)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
[Seshadri+ MICRO’17, Gao+ MICRO’19]
Activate three rows simultaneously
Assert three rows’ wordlines
Three rows perturb bitlines simultaneously
Sense amplifiers sample the output of majority
Notes: These works first
[CLICK] activate three rows simultaneously by either modifying the row decoder circuitry or violating standard DRAM timing parameters in off-the-shelf DRAM chips, we will see how this works in real DRAM chips later in this talk
[CLICK] By activating three rows simultaneously, DRAM will assert these rows’ wordlines
[CLICK] After that these activated rows perturb bitlines simultaneously
[CLICK] After some time, sense amplifier amplifies the perturbation on the bitline and sample the output of majority of the values stored in activated rows

## Slide 172: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Now let’s move to our goal in this study

## Slide 173: Our Goal
Experimentally understand
the computational capability of COTS DRAM chips
Experimentally analyze
the robustness of such capability under various operating conditions
Notes: Our goal is to
[CLICK] Experimentally understand the computational capability of off-the-shelf DRAM chips beyond what prior works have demonstrated
[CLICK] And experimentally analyze the robustness of such capability under various operating conditions

## Slide 174: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Now, let’s move to our methodology

## Slide 175: DRAM Testing Infrastructure (I)
DRAM Bender DDR3/4 Testing Infrastructure
https://github.com/CMU-SAFARI/DRAM-Bender
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure called DRAM bender which is fully open-sourced

## Slide 176: DRAM Testing Infrastructure (II)
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Fine-grained control over DRAM commands, timings, temperature, and voltage
Notes: This infrastucture
[CLICK] enables fine-grained control over DRAM commands, timings, temperature and voltage

## Slide 177: DRAM Chips Tested
120 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK] We test 120 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 178: Testing Methodology (I)
Carefully sweep
    Row addresses: Row A and Row B (>3M row pairs)
    Timing parameters: Between ACT → PRE and PRE → ACT
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
All rows in Subarray X
Row A
Row B
Notes: [CLICK] In this study, we focus on individual subarrays, here denoted as Subarray X
[CLICK] We perform our experiment using the following command sequence: Activate Row A, Precharge, and Activate Row B, where Row A and Row B in the same subarray
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 179: Testing Methodology (II)
Temperature
50◦C
90◦C
Wordline Voltage
2.5V
2.1V
Notes: We also test two major operating parameters
[CLICK] First, temperature. We sweep temperature from 50C to 90C Celsius
[CLICK] Second, wordline voltage. We reduce the wordline voltage from its nominal value, 2.5V to 2.1V

## Slide 180: Robustness Metric: Success Rate
Percentage of DRAM cells that produce correct output of a tested operation in all test trials
Total of 10,000 trials
Success rate for this example: 66.67% (2/3)
Notes: To evaluate the robustness of in-DRAM operations, we define a metric called success rate
[CLICK] as the percentage of DRAM cells that produce correct output of a tested operation in all test trials. We test total of 10000 trials and record the success rate for each tested cell
[CLICK] Let’s see the success rate in a in-DRAM copy example where we try to copy src to dst.
[CLICK] Assume we have three trials and in the first trial, first cell produce incorrect result. Meaning we couldn’t copy s value to that cell.
[CLICK] As a result, two out of three cells for this source and destination row pair produce correct output in all test trials.
[CLICK]Hence the success rate for this experiment is 66.67%

## Slide 181: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Now, let’s see how we perform simultaneous many-row activation in off-the-shelf DRAM chips

## Slide 182: Key Observation
Activating two rows in quick succession
can simultaneously activate
many rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 183: Hypothesis: Row Decoder Circuitry
Simultaneous many-row activation is possible due to the hierarchical DRAM row decoder design
Row Decoder
Row Address
Wordline
DRAM Subarray
Row Address (RA)
2x4
Stage 1 Decoder
Stage 2 Decoder
Stage 3 Decoder
Stage 4 Decoder
Stage 5 Decoder
Notes: We hypothesize that simultaneous many-row activation is possible due to the hierarchical DRAM row decoder design
[CLICK] Let’s recall a DRAM subarray where we have rows, sense amplifiers and row decoder circuitry
[CLICK] Row decoder circuitry decodes the row address that is sent with activate command and assert the corresponding wordline
[CLICK] As we mentioned, row decoder circuitry is hierarchical and has multiple stages of decoders
[CLICK] Each decoder stage takes some parts of the row address and asserts intermediate signals that are essentially drives the wordline using such intermediate signals

## Slide 184: Row Decoder: A Tree Example
We can visualize the hierarchical row decoder circuitry as a tree
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline B
...
...
Stage 1
Decoder
Stage 5
Decoder
Decoder Output
2x4
Notes: To explain it in a higher abstraction level,
[CLICK] We can visualize the row decoder as a tree which
[CLICK] Each level of the tree represents a decoder stage
[CLICK] each node represents a decoder output

## Slide 185: Activating a Single Row
Wordline B
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline A
ACT Row A
PRE
36ns
1. Decode Row A address
2. Assert corresponding signals
3. Follow asserted nodes path from root to leaf
4. Assert wordline
Notes: Let’s see an example when we activate a single row
[CLICK] Assume that we issue ACT Row A command, which will essentially assert the Wordline A signal
[CLICK] After issuing the activation command, the row decoder circuitry decodes Row A address
[CLICK] And assert corresponding signals in the tree
[CLICK] After the decoding completed, row decoder follows the asserted nodes path from root to leaf
[CLICK] As a result, it asserts wordline, in this it is Wordline A
[CLICK] After a successful activation we can issue PRE command which deasserts every asserted signals in the row decoder circuitry including the wordline

## Slide 186: Activating Many Rows: A Walkthrough
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline B
...
...
Wordline B
Wordline A
Back-to-back ACT commands with violated timings asserts many more signals in the row decoder
ACT Row A
PRE
36ns
ACT Row B
14ns
<3ns
<3ns
1. Keep the previously asserted signals active
2. Decode Row B & assert corresponding signals
3. Follow newly asserted nodes’ path
4. Simultaneously activate many rows
Notes: So that was an activation of a single row, now let’s see a simultaneous activation of many rows.
[CLICK] Our hypothesis is back-to-back ACT commands with violated timings asserts many more signals in the circuitry

## Slide 187: Hypothesis: Row Decoder Circuitry
(More discussions & hypotheses in the paper)
https://arxiv.org/pdf/2405.06081
Notes: As our time limited, I would like to refer you to our paper for more detailed circuitry and discussions about row decoder circuitry

## Slide 188: Characterization Methodology (I)
Subarray X
DRAM Bank
…
ACT
ACT
Row A
Row B
If rows are activated, WR command overwrites all of the activated rows’ content
ACT Row A
PRE
ACT Row B
WR

## Slide 189: Characterization Methodology (II)
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Temperature (◦C): 50, 60, 70, 80, and 90
    Wordline Voltage (V): 2.5, 2.4, 2.3, 2.2, and 2.1
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
All rows in Subarray X
Row A
Row B
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V
Notes: As we mentioned previously; we carefully sweep
[CLICK] Row Addresses and timing parameters
[CLICK] Temperature and wordline voltage

## Slide 190: Key Takeaways from Simultaneous Many-Row ACT
COTS DRAM chips are capable of simultaneously activating 2, 4, 8, 16, and 32 rows
Key Takeaway 1
Simultaneous many-row activation is highly resilient to temperature and wordline voltage changes
Key Takeaway 2
Notes: Our analysis provides two key takeaway lessons:
[CLICK] First, off-the-shelf DRAM chips can are capable of simultaneously activating 2, 4, 8, 16, and 32 rows
[CLICK] Second, temperature and wordline voltage has a small effect on the robustness of simultaneous many-row activation

## Slide 191: Robustness of Simultaneous Many-Row Activation
COTS DRAM chips can simultaneously activate
2, 4, 8, 16, and 32 rows in the same subarray
Average: 99.85%
Average: 99.99%
Percentage of cells overwritten with WR command
Notes: Let’s take a look at our first results
[CLICK] Y-axis shows the success rate [CLICK] In the x-axis you see the number of simultaneously activated rows from 2 to 32
[CLICK] This plots shows a distributions across tested DRAM cells as a box-and-whiskers plot.
[CLICK] We observe that up to 16 row activation we can achieve 99.99 percent success rate while in 32 row activation we have 99.85 percent
[CLICK] Our takeaway from this experiment is off-the-shelf DRAM chips can activate 2, 4, 8, 16, and 32 rows in the same subarray

## Slide 192: Also in the Paper: Impact of Temperature & Voltage
Increasing temperature up to 90◦C has a small effect on the success rate of simultaneous many-row activation
Reducing the wordline voltage only slightly affects the success rate of simultaneous many-row activation
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V

## Slide 193: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: By leveraging simultaneous many-row activation, we can
[CLICK] Perform majority operations with more than three inputs
[CLICK] We can increase the robustness of majority operations
[CLICK] And we can copy one row’s content to multiple rows

## Slide 194: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Next, let’s see how we leverage many-row activation to perform majority operations

## Slide 195: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Let’s start with the first one

## Slide 196: In-DRAM Majority-of-X (MAJX)
b
b
b
d
s
t
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
a
a
a
MAJ5(a, b, b, b, a) = b
MAJ7(a, b, b, a, a, b, b) = b
Simultaneously activate many rows to perform MAJX (where X>3) operations
b
b
b
b
b
b
b
b
b
a
a
a
a
a
a
a
a
a
b
b
b
b
b
b
Notes: Our key idea is to simultaneously activate many rows to perform MAJX operations where X is greater than 3
[CLICK] For example, if we can activate 5 rows at once
[CLICK] we can perform MAJ5 operations
[CLICK] Or if we simultaneously activate seven rows,
[CLICK] we can perform MAJ7

## Slide 197: MAJX in Real DRAM Chips
For MAJX, we need to activate X rows simultaneously
We can only simultaneously activate 2, 4, 8, 16, and 32 rows
Question
  How do we perform MAJX while simultaneously activating more than X rows?
Answer
  Making some rows neutral during the MAJX operation using the Frac operation*
b
b
a
b
b
a
b
b
a
b
b
a
N
N
N
3x Neutral Rows
=
MAJ5
w/ 5-row activation
MAJ5
w/ 8-row activation
*[Gao+MICRO’22]
Notes: So, let’s see how we can perform majority operations in real chips
[CLICK] For MAJX, we need to activate X rows simultaneously
[CLICK] However, we can simultaneously activate 2, 4, 8, 16, and 32 rows
[CLICK] The question is straightforward: How do we perform MAJX by simultaneously activating more than X rows? For example MAJ5 with 8-row activation
[CLICK] The answer is we prevent some rows from contributing to charge using the Frac operation, which is demonstrated in the prior work. Basically, these rows will be neutral rows, as if they are not activated
[CLICK] For example, MAJ5 with 5-row activation will be the same as MAJ5 with 8-row activation where three of these rows are neutral rows

## Slide 198: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Now we are done with performing MAJX operations, let’s see how we can increase the robustness of these operations

## Slide 199: Improving the Robustness (Input Replication)
b
b
b
d
s
t
MAJ6(a, b, b, a, b, b) = b
MAJ3(a, b, b) = b
Storing multiple copies of MAJX input operands can increase the robustness of MAJX operations
a
b
b
d
s
t
d
s
t
d
s
t
d
s
t
b
a
a
a
b
b
b
b
b
b
b
b
a
a
a
b
b
b
Incorrect result
b
b
b
a
a
a
b
b
b
b
b
b
a
a
a
b
b
b
b
b
b
a
a
a
b
b
b
Correct result
Notes: Our key idea is to store multiple copies of majority operations’ input operands, which we call Input Replication
[CLICK] For example, we can increase the success rate of MAJ3 operation by activating 6 rows and replicating input operands two times

## Slide 200: Characterization Methodology
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Temperature (◦C): 50, 60, 70, 80, and 90
    Wordline Voltage (V): 2.5, 2.4, 2.3, 2.2, and 2.1
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
All rows in Subarray X
Row A
Row B
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V
Notes: As we mentioned previously; we carefully sweep
[CLICK] Row Addresses and timing parameters
[CLICK] Temperature and wordline voltage

## Slide 201: Key Takeaways from MAJX Operation
COTS DRAM chips are capable of performing MAJ5, MAJ7, and MAJ9 operations
Key Takeaway 1
Storing multiple copies of MAJX’s input operands significantly increases the MAJX’s success rate
Key Takeaway 2
Voltage and temperature slightly affect the success rate, whereas data pattern affects significantly
Key Takeaway 3
Notes: Our analysis provides three key takeaway lessons:
[CLICK] First, off-the-shelf DRAM chips are capable of performing MAJ5, MAJ7, MAJ9 operations
[CLICK] Second, storing multiple copies of MAJX’s input operands significantly increases the MAJX’s success rate
[CLICK] Voltage and temperature slightly affects the success rate whereas data pattern affects significantly

## Slide 202: Robustness of MAJX Operations
COTS DRAM chips are capable of performing MAJ5, MAJ7, and MAJ9 operations
Notes: Now let me show you the first result the robustness of tested majority operations. In this figure, each subplot shows a different majority operation, from left to right the number of input operand in majority operation increases.
[CLICK] x-axis shows the number simultaneously activated rows
[CLICK] For this analysis, we will first focus on one data pattern: all ones or zeros
[CLICK] Let’s take look at the MAJ3 results where we use boxplot to show the success rate distributions
[CLICK] To simplify things, we focus on one distribution point that achieves highest success rate
[CLICK] From this figure we conclude that off-the-shelf DRAM chips are capable of performing up to nine-input majority operations

## Slide 203: Impact of Input Replication
Storing multiple copies of MAJ’s input operands increases the success rate of MAJ3, MAJ5, MAJ7, and MAJ9 operations
30.81% increase
Similar trend in success rate increase in all tested MAJX operations
56.27% increase
35.15% increase
13.11% increase
Final average success rate MAJ3 (MAJ5): 99.68% (93.49%)
Notes: Now let’s see how input replication affects the success rate
[CLICK] Again, here, let’s first focus on MAJ3 operation
[CLICK] We observe that when we increase the number of input operand copies in majority-of-three operation, we observe a drastic 30.81% increase in average success rate
[CLICK] And this increasing trend in success rate is consistent across all tested majority operations
[CLICK] Hence, we conclude that storing multiple copies of input operands increases the success rate of MAJ3, 5, 7, and 9 operations

## Slide 204: Impact of Data Pattern
Data pattern significantly affects the success rate of the MAJX operation
11.52% decrease in success rate on average (up to 32.56%) across all tested MAJX operations
Notes: Here, we see the full results for MAJ3 operations where each colored boxplot represent a different data pattern in every tested data points in x-axis
[CLICK] We observe that when we use random data pattern to perform MAJ3 operation success rate decreases in every number of simultaneously activated rows
[CLICK] And this observation is consistent across all tested majority operations. We observe that on average across all tested majority operations there is a 11.52% decrease in success rate and the maximum decrease is 32.56%
[CLICK] We conclude that data pattern significantly affects the success rate of majority operations

## Slide 205: Also in the Paper: Impact of Temperature & Voltage
Temperature slightly affects
the success rate of the MAJX operation
Wordline voltage has a small effect on the success rate of the MAJX operation
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V

## Slide 206: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Now let’s move to our last but not least in-DRAM operation

## Slide 207: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Next, I will show how we can copy one row’s content to multiple rows

## Slide 208: In-DRAM Multiple Row Copy (Multi-RowCopy)
d
s
t
r
c
s
Simultaneously activate many rows to copy one row’s content to multiple destination rows
d
s
t
s
r
c
RowClone
s
r
c
r
c
s
s
r
c
d
s
t
d
s
t
d
s
t
Multi-RowCopy
s
r
c
s
r
c
s
r
c
[Seshadri+ MICRO’13]
Notes: [CLICK] Our key idea is since we can activate many rows simultaneously, we can copy one row’s content to other simultaneously activated rows
[CLICK] Let’s recall the RowClone example where we copy source to destination
[CLICK] In RowClone, we first activate the source row which will copy its content to sense amplifiers
[CLICK] And then, we activate destination row to drive the sense amplifier’s content to destination row
[CLICK] In our mechanism, which we call Multi-RowCopy, we have several destination rows
[CLICK] Here we activate many destination rows simultaneously
[CLICK] and thus sense amplifier drives its content to these destination rows.

## Slide 209: Characterization Methodology (II)
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Temperature (◦C): 50, 60, 70, 80, and 90
    Wordline Voltage (V): 2.5, 2.4, 2.3, 2.2, and 2.1
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
All rows in Subarray X
Row A
Row B
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V
Notes: As we mentioned previously; we carefully sweep
[CLICK] Row Addresses and timing parameters
[CLICK] Temperature and wordline voltage

## Slide 210: Key Takeaways from Multi-RowCopy
COTS DRAM chips are capable of copying one row’s data to 1, 3, 7, 15, and 31 other rows at very high success rates
Key Takeaway 1
Multi-RowCopy in COTS DRAM chips is highly resilient to changes in data pattern, temperature, and wordline voltage
Key Takeaway 2
Notes: Our analysis provides two key takeaway lessons:
[CLICK] First, off-the-shelf DRAM chips are capable of copying one row’s data to 1, 3, 7, 15, and 31 other rows at very high success rates
[CLICK] Multi-RowCopy in COTS DRAM chips is highly resilient to changes in data pattern, temperature, and wordline voltage

## Slide 211: Robustness of Multi-RowCopy
COTS DRAM chips can copy one row’s content to up to 31 rows with a very high success rate
Average: >99.98%
Notes: Now let me show you the first result
[CLICK] In this plot, y-axis shows the success rate
[CLICK] x-axis shows the number of destination rows from 1 to 31
[CLICK] And we plot the success rate distribution as a box-and-whiskers plot
[CLICK] We observe that the average success rate is higher than 99.98% across all tested number of destination rows
[CLICK] Hence, we conclude that off-the-shelf DRAM chips can copy one row’s content to up to 31 rows with a very high success rate

## Slide 212: Impact of Data Pattern
Data pattern has a small effect on the success rate of the Multi-RowCopy operation
At most 0.79% decrease in average success rate
Notes: Now let’s analyze the impact of data pattern
[CLICK] We plot the average success rate for each number of destination rows and show the trend using a lineplot. Each colered line represent a different data pattern
[CLICK] We observe that data pattern decreases the average success rate at most by 0.79%
[CLICK] We conclude that data pattern has a small effect on the success rate

## Slide 213: Also in the Paper: Impact of Temperature & Voltage
Increasing temperature up to 90◦C has a very small effect on the success rate of the Multi-RowCopy operation
Reducing the wordline voltage
only slightly affects the success rate of the Multi-RowCopy operation
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V

## Slide 214: More in the Paper
Detailed hypotheses and key ideas on
    Hypothetical row decoder circuitry
    Input Replication
More characterization results
    Power consumption of simultaneous many-row activation
    Effect of timing delays between ACT-PRE and PRE-ACT commands
    Effect of temperature and wordline voltage
Circuit-level (SPICE) experiments for input replication
Potential performance benefits of enabling new in-DRAM operations
    Majority-based computation
    Content destruction-based cold-boot attack prevention
Discussions on the limitations of tested COTS DRAM chips
Notes: We have more content in the paper, including
…

## Slide 215: Available on arXiv
https://arxiv.org/pdf/2405.06081
Notes: The extended version of our study is available on arxiv

## Slide 216: Our Work is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: And our work is artifact evaluated and got every badges
[CLICK] You can download our code from github and start testing right away!

## Slide 217: Outline
Motivation & Background
Experimental Methodology
Multi-RowCopy Operation
Simultaneous Many-Row Activation
Conclusion
MAJX Operation
Goal
Notes: Let me conclude my talk

## Slide 218: Conclusion
We experimentally demonstrate that COTS DRAM chips can
simultaneously activate up to 32 DRAM rows
perform MAJ3, MAJ5, MAJ7, and MAJ9 operations
copy one row’s content to up to 31 rows
We characterize 120 DDR4 chips and highlight three key results
Storing multiple copies of MAJX’s input operands (i.e., input replication) drastically increases the success rate of MAJX operations
Voltage and temperature slightly affect the success rate of MAJX operation, whereas data pattern affects significantly
Multi-RowCopy is highly resilient to changes in data pattern, temperature, and wordline voltage
We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: In this study,
[CLICK] We experimentally demonstrate that off-the-shelf DRAM chips can simultaneously activate up to 32 DRAM rows
[CLICK] perform MAJ3, MAJ5, MAJ7, and MAJ9 operations
[CLICK] and copy one row’s content into up to 31 different rows simultaneously
[CLICK] We characterize the success rate of in-DRAM operations on 120 DDR4 chips from two major manufacturers And we highlight three key results
[CLICK] By storing multiple copies of majority’s input operands, we can increase the success rate of majority operations
[CLICK] and operating conditions can significantly affect the robustness of in-DRAM operations
[CLICK] We conclude that these empirical results demonstrate the promising potential of using DRAM as a computation substrate

## Slide 219: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Paper
GitHub
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 220: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Backup Slides
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 221: Power Consumption of Many-Row ACT
Simultaneous many-row activation power draw likely meets the power budget of DDR4 chips
32-row activation consumes 21.19% less power than the most power-consuming single DRAM operation (i.e., REF)

## Slide 222: Impact of Temperature in Many-Row ACT
Increasing temperature up to 90◦C has a small effect on the success rate
Max. decrease: 0.16%
Notes: Next, we analyze the impact of temperature, again y-axis shows the success rate and x-axis shows the number of simultaneously activated rows
[CLICK] We plot the average success rate for each temperature as lineplot
[CLICK] Colors indicate different temperature levels
[CLICK] We observe that the maximum decrease in average success rate is 0.16% in 32-row activation
[CLICK] We conclude that increasing temperature up to 90C has a small effect on the success rate

## Slide 223: Impact of Voltage in Many-Row ACT
Reducing the wordline voltage only slightly affects the success rate
Max. decrease: 0.64%
Notes: Lastly, let’s see how voltage scaling affects the success rate.
[CLICK] Again we plot the average success rate as a lineplot
[CLICK] And each color indicate different voltage level
[CLICK] We observe that when we reduce the voltage from 2.5V to 2.1V average success rate decreases by 0.64% at most, which is in 32-row activation
[CLICK] We conclude that reducing the wordline voltage only slightly affects the success rate

## Slide 224: Impact of Temperature in MAJX
Temperature slightly affects
the success rate of the MAJX operation
15.20% increase
from 50 ◦C to 90 ◦C , the success rate varies by 4.25% on average across all the tested operations
Notes: Next, let’s see the effect of temperature
[CLICK] In this plot each coloered box represents a different temperature level and temperature increases from left to right
[CLICK] In some cases, we observe a significant increase in success rate when we increase the temperature from 50C to 90C
[CLICK] On average, the success varies by 4.25% across all tested majority operations when we increase the temperature from 50 to 90
[CLICK] We conclude that temperature slightly affects the success rate of majority operations

## Slide 225: Impact of Voltage in MAJX Operations
Wordline voltage slightly affects the success rate of the MAJX operation

## Slide 226: Impact of Timing Delays in Many-Row ACT

## Slide 227: Impact of Timing Delays in MAJX

## Slide 228: Impact of Timing Delays in Multi-RowCopy

## Slide 229: Impact of Temperature in Multi-RowCopy
Increasing temperature up to 90◦C has a very small effect on the success rate
Only 0.04% decrease in average success rate
Notes: Lastly, let’s see how temperature affects the success rate of the Multi-RowCopy operation
[CLICK] Here again we plot the average success rate as a lineplot and each colored line represent a different temperature level
[CLICK] We observe that there is only 0.04% percent decrease in average success rate when we increase the temperature to 90C
[CLICK] We conclude that increasing temperature up to 90C has a very small effect on the success rate

## Slide 230: Impact of Voltage in Multi-RowCopy
Reducing the wordline voltage
only slightly affects the success rate

## Slide 231: Majority-based Computation
New MAJX operations provide 121.61% (46.54%) higher performance over using only MAJ3 in Mfr. M (Mfr. H) on average.

## Slide 232: Cold Boot Attack Prevention
Multi-RowCopy-based content destruction outperforms both RowClone-based and Frac-based content destruction by up to 20.87× and 7.55×, respectively.

## Slide 233: Frac Operation

## Slide 234: Input Replication in Real Chips
F
MAJ6(a, b, c, a, b, c) = F
MAJ3(a, b, c) = F
VPRE
VPRE+ Δa + Δb + Δc
VPRE
VPRE + 2x(Δa + Δb + Δc)
X
b
a
c
b
a
c
N
N
b
a
c
N
Neutral Rows
Low perturbation
Incorrect Result
2x higher perturbation
Correct Result
Notes: Let’s see how we can perform input replication in real DRAM chips at a lower abstraction-level
[CLICK] Assume we want to perform MAJ3(a,b,c) operation and the correct output for this operation is F
[CLICK] Without any replication, we would use 4-row activation map the inputs into three cells and make the remaining row neutral. Initially the bitlines that these four rows are connected to has precharge voltage value
[CLICK] To perform MAJ3 we activate these four rows simultaneously
[CLICK] Then they perturb the bitline
[CLICK] However, these perturbation is sometimes lower than the safe margin that sense amplifier operates due to connecting multiple cells to the bitline concurrently. As a result, sense amplifier cannot correctly amplify the perturbation and produce incorrect result
[CLICK] Now let’s see what happens when we use input replication
[CLICK] For this example, we will perform MAJ3 operation with 8-row activation where we replicate each input two times and make the remaining two rows neutral
[CLICK] To perform this operation we activate these eight rows simultaneously
[CLICK] Then they perturb the bitline, note that since we have two copies from each we have 2x higher perturbation
[CLICK] As a result of the higher perturbation, sense amplifier amplifies the perturbation safely and produce correct result

## Slide 235: DRAM Chips Tested: Extended Table

## Slide 236: Row Decoder Circuitry

## Slide 237: Effect of Input Replication on the Bitline Deviation

## Slide 238: Limitations of Tested COTS DRAM Chips (I)
Some COTS DRAM chips do not support all in-DRAM operations
    We do not observe simultaneous many-row activation in tested 64 Samsung chips
    Hypothesis
      Internal DRAM circuitry ignores the PRE command or the second ACT command when the timing parameters are greatly violated
    If such a limitation were not imposed, we believe these DRAM chips are also fundamentally capable of performing the operations we examine in this work

## Slide 239: Limitations of Tested COTS DRAM Chips (II)
Tested COTS DRAM chips support only consecutive two row activation and simultaneous activation of 2, 4, 8, 16, and 32 rows
    Hypothesis
      This is due to our current infrastructure limitations, where we can issue DRAM commands at intervals of only 1.5ns.
      Having fine-grained control on timing would allow us to deassert/assert desired intermediate signals in the row decoder circuitry

## Slide 240: Limitations of Tested COTS DRAM Chips (III)
Performing in-DRAM operations potentially have an effect on transient errors in DRAM chips
    We perform each test (a single data point in the distribution) 10K times
    We do not observe any errors in rows outside of the simultaneously activated row group
    We believe that investigating all potential effects (e.g., on transient errors) requires a much more extensive exploration of various aspects

## Slide 241: Open Research Questions
What other PUD operations can be realized in COTS DRAM chips?
2
How robustly can PUD operations be performed in COTS DRAM chips?
3
Can the robustness of PUD operations be improved?
4
Is it possible to robustly activate more than four DRAM rows simultaneously?
1
What are the effects of operating conditions on the robustness of PUD operations?
5

## Slide 242: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline
NOT Gate
1. ACTIVATE (ACT)
2. PRECHARGE (PRE)
242
Notes: Here we take a closer look into DRAM cell.
A DRAM cell consists of two main components: capacitor and access transistor.
Capacitor holds the data as a form of electrical charge.
Access transistor connects cell to the subarray through wordline and bitline.
As we discussed, bitline is connected to the sense amplifier which consists of two back-to-back NOT gates.
In this study, we focus on two major DRAM commands: ACT and PRE, let’s see how they work.

## Slide 243: DRAM Cell Operation - ACTIVATE
raise wordline
enable
bitline
wordline
capacitor
access transistor
bitline
½ VDD
½ VDD
0
0
1
connects cell to bitline
cell loses
charge to bitline
+ δ
deviation in bitline voltage
1
enable sense amp
VDD
0
cell regains charge
243
Notes: First, ACT

## Slide 244: DRAM Cell Operation - PRECHARGE
enable
bitline
wordline
capacitor
access transistor
bitline
0
0
1
VDD
0
lower wordline
1
Precharge bitline
for next access
½ VDD
½ VDD
Disable
Sense Amp
244
Notes: PRE