## Slide 1: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 2: Executive Summary
Experimental Study: 316 COTS DDR4 chips from four major manufacturers to study read disturbance effects of multiple-row activation, which we call PuDHammer
PuDHammer significantly exacerbates DRAM read disturbance, causing up to 158.58x reduction in min. hammer count to induce first bitflip (HCfirst)
PuDHammer bypasses in-DRAM RowHammer mitigation in DDR4 and induces 11340x more bitflips than RowHammer
Motivation: Processing-using-DRAM (PuD) alleviates data movement bottlenecks
DRAM can perform many PuD operations by activating multiple DRAM rows in quick succession or simultaneously (i.e., multiple-row activation)
Modern DRAM is subject to read disturbance (e.g., RowHammer)
    Repeatedly activating even a single row induces bitflips in unaccessed rows
Problem: No prior work study the read disturbance effects of multiple-row activation
Goal: Understand and analyze read disturbance effects of multiple-row activation
Mitigation: We adapt Per Row Activation Counting (PRAC) for PuDHammer
Adapted PRAC solution incurs an average system performance overhead of 48.26%

## Slide 3: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 4: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 5: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018

## Slide 6: DRAM Organization
Row Decoder
DRAM Subarray
DRAM Module
DRAM
Chip
Bitline
DRAM Row
DRAM Cell
Wordline
Sense Amps.
DRAM Chip
…
…
Bank
Chip I/O
DRAM Bank
Subarray
Notes: DRAM is used as the main memory in many computing systems.
[CLICK] a DRAM module consists of multiple DRAM chips
[CLICK]Each chip contains multiple banks
[CLICK] Each bank is composed of multiple subarrays and sense amplifiers
[CLICK] And within each subarray, there is a two dimensional array of DRAM cells.
[CLICK] These cells are organized into rows that are selected using wordlines
[CLICK] And the cells are connected to a row of sense amplifiers via bitlines

## Slide 7: DRAM Operation
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 8: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-using-DRAM uses the analog operational principles of DRAM cells to perform computation
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory

## Slide 9: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-
Using-DRAM
…
…
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
1. Consecutive Multiple-Row Activation (CoMRA)
2. Simultaneous Multiple-Row Activation (SiMRA)
Multiple-row activation is a key technique to realize many PuD operations
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory

## Slide 10: Consecutive Multiple-Row Activation
Violating timing of PRE command greatly
can activate two rows consecutively

## Slide 11: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
s
t
d
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively

## Slide 12: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively
src’s content is copied to dst
s
r
c

## Slide 13: Simultaneous Multiple-Row Activation
Activating two rows in quick succession
can simultaneously activate
multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 14: Example: In-DRAM Majority-of-Three (MAJ3)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
[Seshadri+ MICRO’17, Gao+ MICRO’19]
Assert three rows’ wordlines
Three rows perturb bitlines simultaneously
Sense amplifiers sample the output of majority
ACT
PRE
ACT
<3ns
<3ns
Notes: These works first
[CLICK] activate three rows simultaneously by either modifying the row decoder circuitry or violating standard DRAM timing parameters in off-the-shelf DRAM chips, we will see how this works in real DRAM chips later in this talk
[CLICK] By activating three rows simultaneously, DRAM will assert these rows’ wordlines
[CLICK] After that these activated rows perturb bitlines simultaneously
[CLICK] After some time, sense amplifier amplifies the perturbation on the bitline and sample the output of majority of the values stored in activated rows

## Slide 15: Read Disturbance in DRAM
Unfortunately, even activating a single DRAM row disturbs the data-integrity of other unaccessed DRAM rows
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows

## Slide 16: Outline
Background
Testing Infrastructure
Combined Effect of CoMRA, SiMRA, and RowHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 17: Problem & Goal
Problem
No prior work investigates the read disturbance effects of multiple-row activation
Goal
Understand how multiple-row activation affect read disturbance vulnerability in DRAM

## Slide 18: Outline
Background
Real DRAM Chip Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 19: DRAM Bender: DRAM Testing Infrastructure
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Fine-grained control over DRAM commands, timings, temperature, and voltage
Notes: This infrastucture
[CLICK] enables fine-grained control over DRAM commands, timings, temperature and voltage

## Slide 20: DRAM Chips Tested
316 DDR4 chips from four major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK] We test 120 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 21: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 22: Recall: CoMRA
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
Violating timing of PRE command greatly
can activate two rows consecutively
src’s content is copied to dst
s
r
c

## Slide 23: Hammering with CoMRA
DRAM Subarray
.
.
.
.
.
.
Double-Sided
Single-Sided
.
.
.
DRAM Subarray
src
dst
dst
src
ACT src
ACT dst
PRE
7.5ns
36ns
victim
victim
victim
victim
victim
aggressor
aggressor
aggressor
aggressor

## Slide 24: Characterization Methodology
Carefully sweep
    Row addresses: src and dst
    Timing parameters: Between ACT → PRE and PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
ACT
ACT
ACT src
PRE
ACT dst
.
.
.
src
victim
dst
aggressor
aggressor
.
.
.
DRAM Subarray
DRAM Bank
Temperature
50 ◦C
80 ◦C
Notes: [CLICK] In this study, we focus on individual subarrays, here denoted as Subarray X
[CLICK] We perform our experiment using the following command sequence: Activate Row A, Precharge, and Activate Row B, where Row A and Row B in the same subarray
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 25: Read Disturbance Vulnerability Metric: HCfirst
The minimum hammer count required to induce the first bitflip
Lower is worse
Record bitflips in victim
Victim Row
Aggressor Row (src)
Aggressor Row (dst)
1 Hammer
ACT src
ACT dst
PRE
Notes: To evaluate the robustness of in-DRAM operations, we define a metric called success rate
[CLICK] as the percentage of DRAM cells that produce correct output of a tested operation in all test trials. We test total of 10000 trials and record the success rate for each tested cell
[CLICK] Let’s see the success rate in a in-DRAM copy example where we try to copy src to dst.
[CLICK] Assume we have three trials and in the first trial, first cell produce incorrect result. Meaning we couldn’t copy s value to that cell.
[CLICK] As a result, two out of three cells for this source and destination row pair produce correct output in all test trials.
[CLICK]Hence the success rate for this experiment is 66.67%

## Slide 26: Double-Sided CoMRA vs. RowHammer (I)
13.98x
Double-sided CoMRA decreases lowest HCfirst by 13.98x compared to double-sided RowHammer
Lowest HCfirst reduction trend consistent across all four manufacturer
1.18x
3.28x
1.58x

## Slide 27: Double-Sided CoMRA vs. RowHammer (II)
Represents 99% of tested victim rows
Represents 50% of tested victim rows
HCfirst reduction of 50%
RowHammer HCfirst = 100
CoMRA HCfirst = 50

## Slide 28: Double-Sided CoMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
Double-sided CoMRA decreases HCfirst for a large fraction of rows compared to double-sided RowHammer

## Slide 29: Double-Sided CoMRA vs. RowHammer
CoMRA exacerbates DRAM’s vulnerability to read disturbance in all four major manufacturers
Key Takeaway

## Slide 30: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 31: Recall: SiMRA
Activating two rows in quick succession
can simultaneously activate
multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 32: Characterization Methodology
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
Temperature
50 ◦C
80 ◦C
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
Row A
Row B
Notes: [CLICK] In this study, we focus on individual subarrays, here denoted as Subarray X
[CLICK] We perform our experiment using the following command sequence: Activate Row A, Precharge, and Activate Row B, where Row A and Row B in the same subarray
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 33: Double-Sided SiMRA vs. RowHammer (I)
159x
Double-sided SiMRA decreases lowest HCfirst by 159x compared to double-sided RowHammer
51x
86x
125x
Lowest HCfirst reduction trend consistent across all tested number of simultaneously activated rows

## Slide 34: Double-Sided SiMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
at least 25.19% of tested victim rows experience >99% HCfirst reduction

## Slide 35: Double-Sided SiMRA vs. RowHammer (II)
Double-sided SiMRA significantly decreases HCfirst for a majority of rows compared to double-sided RowHammer

## Slide 36: Double-sided SiMRA vs. RowHammer
SiMRA drastically exacerbates DRAM’s vulnerability to read disturbance
Key Takeaway

## Slide 37: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 38: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 39: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 40: Target Row Refresh (TRR)
Row 0
Row 1
Row 2
Row 3
Row 4
TRR-equipped DRAM Chip
TRR
Memory Controller
DRAM vendors equip their DRAM chips with a proprietary mitigation mechanisms known as Target Row Refresh (TRR)
Aggressor detected: Row 2
Refresh neighbor rows
TRR-induced refreshes
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
REF
aggressor
Notes: To protect their DRAM chips against RowHammer, DRAM vendors currently implement proprietary RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row
[CLICK] We demonstrate how TRR operates at a high-level.
[CLICK] The TRR mechanism detects [CLICK] an aggressor row as a result of [CLICK] repeatedly activating and precharging the same row. [CLICK]
[CLICK] To protect the neighbor victim rows from experiencing RowHammer bit flips, [CLICK] TRR refreshes the victim rows by performing TRR-induced refresh operations. TRR refreshes victim rows by piggybacking TRR-induced refreshes to the REFRESH commands that the memory controller periodically issues.

## Slide 41: Reverse Engineering TRR
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by on-die mitigation
[Hassan+, MICRO’21, source code available at https://github.com/CMU-SAFARI/U-TRR]
Hassan et al., "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” in MICRO, 2021.
Notes: We use the methodology presented in this paper
[CLICK] Where the key idea is to use data retention failures as a side channel to detect when a row is refreshed by the on-die mitigation mechanism
[CLICK] We re-use the source code that is publicly available on this Github page.

## Slide 42: PuDHammer in the presence of TRR
>10K bitflips
<60 bitflips
>10K bitflips
~60 bitflips
CoMRA induces 1.10x more bitflips than RowHammer on average in the presence of TRR

## Slide 43: PuDHammer in the presence of TRR
>10K bitflips
<60 bitflips
~240K bitflips
~180K bitflips
SiMRA induces 11340x more bitflips than RowHammer on average in the presence of TRR

## Slide 44: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 45: Mitigating PuDHammer
Adapt RowHammer mitigations to account for against PuDHammer
2
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 46: Adapting RowHammer Mitigations for PuDHammer
A Naïve Approach (PRAC-Naïve)
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting (PRAC-WC)
Count each operation differently depending on their lowest observed HCfirst

## Slide 47: Methodology
Environment: Cycle-level DRAM simulator Ramulator2 [Kim+ CAL'15, Luo+ CAL'23]
System Configuration:
  Processor 4-core, out-of-order, 4.2GHz clock frequency
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4
  PRAC 4 RFMs per Back-off
  PIM Unit 1-core, issues CoMRA & SiMRA operations with a fixed invertal
Workloads:
    60 five-core five-core multiprogrammed workload mixes.
    Each mix is composed of
      four workloads from five major benchmark suites and
      one synthetic workload that periodically performs back-to-back one SiMRA with 32-row activation and one CoMRA operation

## Slide 48: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-Naïve
PRAC-WC
DRAM performs PuD operations in every 125ns
Normalized to no RH mitigation

## Slide 49: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-WC greatly outperforms PRAC-Naïve until 2us.
PRAC-WC incurs an average (maximum) performance overhead of 48.26% (98.83%).

## Slide 50: More in the Paper
More characterization results
    Temperature, spatial variation, timing parameters, access pattern, data pattern, aggressor row on time analyses for CoMRA and SiMRA
    Combined Read Disturbance Effect of RowHammer with PuD
      Combined pattern is more effective than RowHammer alone (e.g., 1.66x reduction in HCfirst on average)
Details and analyses on mitigating PuDHammer
    Discussion on how modifying DRAM chips could help mitigating PuDHammer
    More details on PRAC adaptation
      Challenges on adapting for PuDHammer
      An area-efficient PRAC solution
      ..
Notes: We have more content in the paper, including
…

## Slide 51: Available on arXiv
https://arxiv.org/pdf/2506.12947
Notes: The extended version of our study is available on arxiv

## Slide 52: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 53: Conclusion
We extensively study the interaction between read disturbance and multiple-row activation-based Processing-using-DRAM operations
We characterize 316 DDR4 chips from four major manufacturers
PuDHammer significantly exacerbates the DRAM read vulnerability (e.g., HCfirst reduces from 4K to 26)
PuDHammer bypasses in-DRAM RowHammer mitigation (TRR) and induces 11340x more bitflips than RowHammer
We hope our findings guide system-level and architectural solutions to enable read-disturbance-resilient future PuD systems.
We adapt Per Row Activation Counting (PRAC) for PuDHammer
Incurs 48.26% performance overhead on average across 60 multiprogrammed workload mixes
Notes: In this study,
[CLICK] We experimentally demonstrate that off-the-shelf DRAM chips can simultaneously activate up to 32 DRAM rows
[CLICK] perform MAJ3, MAJ5, MAJ7, and MAJ9 operations
[CLICK] and copy one row’s content into up to 31 different rows simultaneously
[CLICK] We characterize the success rate of in-DRAM operations on 120 DDR4 chips from two major manufacturers And we highlight three key results
[CLICK] By storing multiple copies of majority’s input operands, we can increase the success rate of majority operations
[CLICK] and operating conditions can significantly affect the robustness of in-DRAM operations
[CLICK] We conclude that these empirical results demonstrate the promising potential of using DRAM as a computation substrate

## Slide 54: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 55: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Backup Slides
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 56: Per Row Activation Counting in DDR5 (April 2024)
DRAM Rows
0xA
PRAC Counters
DRAM Command Timeline
ACT A
ACT A
1
ACT A
ACT A
2
...
ACT A
ACT A
NBO
accurately tracks activation counts of each row
requires
preventive
action
Back-off
RFM
RFM
allocates a fixed time for preventive refresh
ACT
Back-off
continue to send commands
back-off threshold

## Slide 57: Adapting PRAC for PuDHammer
A Naïve Approach
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting
Count each operation differently depending on their lowest observed HCfirst

## Slide 58: A Naïve Approach (PRAC-Naïve)
DRAM Rows
0xA
PRAC Counters
1
2
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=20
Lowest HCfirst for tested DRAM chips
RH: ~4K
CoMRA: ~400
SiMRA: ~20

## Slide 59: Weighted Counting (PRAC-WC)
DRAM Rows
0xA
PRAC Counters
1
201
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=4K
Threshold is set to 4K (RH Threshold) Each operation increases counters by
RH (ACT): 1
CoMRA: 10
SiMRA: 200

## Slide 60: Limitations of Tested COTS DRAM Chips (I)
Some COTS DRAM chips do not support all in-DRAM operations
    We do not observe simultaneous multiple-row activation in all tested Samsung chips
    Hypothesis
      Internal DRAM circuitry ignores the PRE command or the second ACT command when the timing parameters are greatly violated
    If such a limitation were not imposed, we believe these DRAM chips are also fundamentally capable of performing the operations we examine in this work

## Slide 61: Limitations of Tested COTS DRAM Chips (II)
Tested COTS DRAM chips support only consecutive two row activation and simultaneous activation of 2, 4, 8, 16, and 32 rows
    Hypothesis
      This is due to our current infrastructure limitations, where we can issue DRAM commands at intervals of only 1.5ns.
      Having fine-grained control on timing would allow us to deassert/assert desired intermediate signals in the row decoder circuitry

## Slide 62: In-DRAM Row-Copy (RowClone)
Fetch src’s content into the sense amplifiers
d
s
t
r
c
s
d
s
t
s
r
c
ACT src
Assert the src’s wordline
36ns
Notes: [CLICK] To perform RowClone, we first activate the source row by issuing ACT src command. This will assert the src’s wordline
[CLICK] and then fetch src’s content into the sense amplifiers

## Slide 63: In-DRAM Row-Copy (RowClone)
sense amplifier is still enabled
d
s
t
r
c
s
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
ACT src
ACT dst
Bitlines are still at src voltage
PRE
7.5ns
36ns
Activates dst row
Notes: After that, we activate
[CLICK] the destination row without performing precharge operation in between two activate commands
[CLICK] By doing that DRAM will keep the bitlines at src voltage
[CLICK] and keep the sense amplifier enabled
[CLICK] As a result, after some time, the source row’s content is copied to the destination row

## Slide 64: Aggressor Row On Time & RowPress
Instead of using a high hammer count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
[Luo+, ISCA’23]
hammer count = 2
Aggressor row on time (tAggON)
Minimum allowed row on time
(tRASmin)
Notes: In contrast, RowPress, instead of a high activation count, [CLICK] increases the time the that aggressor stays open.
Doing so disturbs adjacent rows enough to cause bitflips without having very high activation count.

## Slide 65: CoMRA (w/ increased tAggOn)
ACT src
ACT dst
PRE
7.5ns
36ns
36ns
Hammering with CoMRA
ACT src
ACT dst
PRE
7.5ns
36ns
tAggOn
(more than 36ns)
Pressing with CoMRA
PRE
PRE

## Slide 66: CoMRA (w/ Aggressor Row On Time) vs RowPress
For CoMRA
From 36ns to 70.2us
79x reduction
For RH/RP
From 36ns to 70.2us
31x reduction

## Slide 67: CoMRA (w/ Aggressor Row On Time) vs RowPress
Trend consistent across all four manufacturer:
Increasing tAggOn significantly reduces HCfirst for both CoMRA and RH/RP

## Slide 68: CoMRA (w/ Aggressor Row On Time) vs RowPress
Pressing with CoMRA is more effective than hammering with CoMRA
Key Takeaway 2

## Slide 69: Impact of the Data Pattern
(Victim has negated data pattern)
Aggressor Rows = 0xFF..FF
Victim Rows = 0x00..00

## Slide 70: Impact of the Data Pattern
(Victim has negated data pattern)
58x
Initializing victim rows with 0x00
increases avg. HCfirst by 58x
Dominant bitflip direction for SiMRA
1->0
Dominant bitflip direction for RH*
0->1
*not shown in the figure

## Slide 71: Impact of the Data Pattern
Trend consistent across all tested number of simultaneously activated rows
SiMRA is significantly affected by data pattern and directionality of SiMRA and RowHammer bitflips are opposite
Key Takeaway 2

## Slide 72: PuDHammer in the presence of TRR

## Slide 73: PuDHammer in the presence of TRR