## Slide 1: Architectures and Programming Models for General-Purpose Near-Data Computing
Brian C. Schwedock
Memory-Centric Computing Systems @ MICRO’24
November 2, 2024

## Slide 2: Data movement costs keep getting worse
[Efnusheva, IJCSIT’17]
1000x
[Dally, SC’10]
Performance
Energy

## Slide 3: Memory hierarchy has evolved, but the interface has not
50 years
Loads & stores
Core
Memory
LLC bank
Core & L1
L2
Memory
Memory
… but software still sees this

## Slide 4: Data movement optimizations are forced to be conservative
Shared Cache
Private Cache
Core
Shared Cache
Private Cache
Core
Shared Cache
Private Cache
Core
Shared Cache
Private Cache
Core
Memory
Software-controlled
Hardware-controlled
Replacement policies
Prefetchers
Memory
These mechanisms are not very effective

## Slide 5: Hardware doesn’t know what applications want
Shared
Private
Core
Shared
Private
Core
Shared
Private
Core
Shared
Private
Core
Memory
Software-controlled
Hardware-controlled
Memory
Tail latency
Security
Graph locality
Streaming throughput
Memory interface doesn’t allow software to customize datapath

## Slide 6: Specialized memory hierarchies (e.g., NDC, PIM) give big gains!
Graph optimizations
Security
Data placement
Remote memory operations
Sparse linear algebra / machine learning
Approximation / compression
Data marshalling / layout
Pointer chasing
Memoization
Prefetching
Relaxed coherence / consistency
Memory management
…
- Big opportunity -
Often >2x end-to-end speedup!
LLC slice
Core & L1
L2
Memory
Memory
Specialized hardware  Not scalable!!!

## Slide 7: How can we specialize the memory hierarchy without specialized hardware?

## Slide 8: The interface is the problem!
Current systems
Programmable hierarchies
Loads & stores
Core
Memory
Specialized hierarchies
Shared Cache
Memory
Private Cache
Core
Shared Cache
Memory
Private Cache
Core
Shared Cache
Memory
Private Cache
Core
ASICs
Software-controlled
Hardware-controlled
Software’s view
Programmable logic

## Slide 9: Overview
täkō
ISCA 2022
Data-triggered
Task offload
Streaming
Long-lived workload
Leviathan
MICRO 2024
* täkō is Japanese for “octopus”

## Slide 10
Memory
Memory
Programmability replaces the need for custom hardware

## Slide 11
Memory
Memory
Engine
Programmability replaces the need for custom hardware

## Slide 12: täkō exposes data movement to software
Cache
Memory
Core
Phantom Data
täkō Engine
Normal Data
Miss
Data
Load
Load
App Code
onMiss()
onEviction()
onWriteback()
App Code
Solution: Tell software when data moves! (& let it do something)
Baseline loads &
stores work normally
“Phantom” data lives
only in caches! [Carter, HPCA’99]
Software serves
misses to phantom
data (& evictions)

## Slide 13: täkō: Roadmap
Introduction
Example use case
täkō design
Evaluation

## Slide 14: Base+delta (B+Δ) lossy compression
Base
Δ
Δ
Δ
Δ
+
+
+
+
Compressed
Decompressed
Base
Δ
Δ
…
≈
≈
≈
≈
…

## Slide 15: B+Δ decompression: in the core
Private Cache
Core
Shared Cache
Memory
B
Δ
Pros: Reduced memory and cache usage
Cons: Decompress on every access
B
Δ
+
≈
Load
B
Δ
B
Δ
B
Δ

## Slide 16: B+Δ decompression: compressed caches?
B
Δ
Private Cache
Core
Shared Cache
Memory
Pros:
Reduced memory and cache usage
Reuse decomp. data in private cache
Cons:
Compression scheme fixed in hardware
Cannot support lossy compression
B
Δ
+
≈
Load
B
Δ
B
Δ
[Miguel, MICRO’15]

## Slide 17: B+Δ decompression: täkō
Load
phantom
Core
Private Cache
Shared Cache
Memory
B
Δ
Pros:
Reduced memory and cache usage
Reuse decomp. data in private cache
SW can implement any compression scheme!
… without needing new hardware for each!
✅
onMiss()
täkō Engine
B
Δ
+
≈
B
Δ

## Slide 18: Evaluation: täkō leverages cache to capture reuse
16K objects, 32K accesses, Zipfian distribution (full experimental methodology shown later)
Decompress on each access
Offload each decompression to L2
Data-movement triggers decompression on cache miss!
täkō with an ideal engine

## Slide 19: The interface is the problem
täkō
Loads & stores
Core
Memory
Shared Cache
Memory
Private Cache
Core
Software-controlled
Hardware-controlled
täkō is the solution
Engine
Software’s view

## Slide 20: täkō: Roadmap
Introduction
Example use case
täkō design
  Programming interface
  Architecture
Evaluation

## Slide 21: täkō programming interface
Callback
Description
onMiss(void* addr)
Generate & fill in cache line at addr.
onEviction(void* addr)
Handle eviction of clean data.
onWriteback(void* addr)
Handle eviction of dirty data.

## Slide 22: Registering callbacks
Address range
onMiss()
onEviction()
onWriteback()
Morph
register(Morph, L2, 4 MB)
register(Morph, LLC, 8 MB)
0x0000
0xFFFF
Normal data

## Slide 23: täkō: Roadmap
Introduction
Example use case
täkō design
  Programming interface
  Architecture
Evaluation

## Slide 24: täkō architecture
Callback Buffer
Dataflow Fabric
L1d
rTLB
TLB
Hardware Scheduler
Tile
Core
Data Array
Tag Array
L2
Engine
L1d
L1i
L3 Cache Bank

## Slide 25: onMiss callback
Callback Buffer
L1d
rTLB
TLB
Hardware Scheduler
Core
Data Array
Tags
L2
Engine
L1d
L1i
L3 Cache Bank
GET A
L3 miss
Scheduled
onMiss(A)
Response
L1 hit
1
2
3
4
6
∞
Fill A
5

## Slide 26: onWriteback callback
Callback Buffer
L1d
rTLB
TLB
Hardware Scheduler
Core
Data Array
Tags
L2
Engine
L1d
L1i
L3 Cache Bank
A evicted
(✔ = registered)
1
onWriteback(A)
A ✔
Invalidate A
2
4
Scheduled
3

## Slide 27: Additional cache and engine state
Dataflow Fabric
Data Array
L2
L3 Cache Bank
Engine
Core
L1d
L1i
TLB
Hardware Scheduler
Callback Buffer
Tag Array
L1d
rTLB
TLB
2 bits per TLB entry
1 bit per tag
Callback buffer
Engine L1d
Engine TLB
Engine reverse TLB
< 3% overhead vs. L3 cache

## Slide 28: Engine microarchitecture
Callbacks need memory-level parallelism
Callbacks are typically short
Callbacks are executed repeatedly
Multiple callbacks execute in parallel
Engine Dataflow Fabric
Engine L1d

## Slide 29: täkō: Roadmap
Introduction
Example use case
täkō design
Evaluation

## Slide 30: Evaluation methodology
Cycle-level simulation of 16-tile CMP
Tile contains: OoO main core and täkō engine
täkō dataflow fabric: 5x5 array, 1-cycle PE latency
Ideal fabric: infinite PEs, 0-cycle PE latency
Dataflow Fabric
rTLB
Core
Data Array
Tag Array
L2
L3 Cache Bank
L1d
L1i
Engine
L1d
TLB
TLB
Callback Buffer
Hardware Scheduler

## Slide 31: Commutative scatter-updates in graphs
Scatter-updates are common in graph algorithms:
But current cache hierarchies are bad at scatter-updates
  Conflict between pull vs. push semantics
   Excess bandwidth & synchronization
for src in vertices:
for dst in outNeighbors(src):
vertex(dst) += vertex(src)
1
0
2
4
3
[Mukkara, MICRO’19]

## Slide 32: Commutative scatter-updates in graphs
PHI changes the memory hierarchy to have push-based semantics
1. Updates are buffered in-cache without accessing memory
2. Updates applied on eviction:
  2a) Immediately in-place, or
  2b) Logged & deferred [Beamer, IPDPS’17]
Updates moved off critical path
Bandwidth optimized by 2a) vs 2b)
UPDATE 0xFOO, +4
Cache
Core
Memory
4
UPDATE 0xFOO, +2
6
0xFOO
0xFOO
10
2a) +6 in-place
16
0xFOO: +6
2b) Log & defer
[Mukkara, MICRO’19]

## Slide 33: Example: PHI on täkō
Memory
B
F
E
A
Core
L3
L2
Engine
Bins
{F,1}
{B,0}
{E,2}
{C,3} {D,1}
Update Vertex
1
onWriteback can a) update in-place b) log update
onMiss zeroes lines
2
3b
3a
{B,1}
C
D
{B,1} {E,2}
{F,1}
Impossible in software without täkō’s callbacks!
Morph registered at L3 cache
Vertex updates buffered in phantom data
onWriteback selectively applies updates in-place or logs updates

## Slide 34: täkō’s benefits implementing PHI
PageRank, 16 threads, graph: 8M vertices & 80M edges
In-place
Log
In-place
Log
In-place
Log
Push-based PageRank
Software update-batching (always log)
täkō implementation of PHI
täkō with an ideal engine
[Beamer, IPDPS’17]

## Slide 35: täkō: programmable specialized hierarchy
The memory interface limits software capabilities
Specialized hierarchies are beneficial but impractical
täkō provides a general-purpose architecture to enable software optimization of the cache hierarchy
Dataflow Fabric
rTLB
Core
Data Array
Tag Array
L2
L3 Cache Bank
L1d
L1i
Engine
L1d
TLB
TLB
Callback Buffer
Hardware Scheduler

## Slide 36: Overview
täkō
ISCA 2022
Data-triggered
Task offload
Streaming
Long-lived workload
Leviathan
MICRO 2024

## Slide 37: Near-data computing (NDC) paradigms
Core
Cache
Memory
NDC HW
Data
Data
Core
Cache
Memory
NDC HW
Data
App Code
Data
Core
Cache
Memory
NDC HW
Data
App Code
Data
Core
Cache
Memory
NDC HW
Data
App Code
Data
App Code
Task
Data-triggered (e.g., täkō)
Streaming
Long-lived
Task
Task
Task offload
Task
Core
Cache
Memory
NDC HW
Data
Data

## Slide 38: Prior NDC designs mostly target a single paradigm
Data-triggered
Compression [ASPLOS’19, MICRO’13, …]
Prefetching [HPCA’21, ASPLOS’18, …]
HTM [MICRO’16]
Coherence [MICRO’15, ISCA’94, …]
…
Task offload
Remote memory ops [ASPLOS’96]
Pointer chasing [PACT’16, ICCD’16]
Hash tables [MICRO’19]
Memoization [IEEE CAL’18]
…
Long-lived
Garbage collection [ISCA’18]
SerDes [MICRO’21, ASPLOS’20]
Memory deduplication [MICRO’17]
COREx [ISCA’18]
…
Streaming
Stream Dataflow [ISCA’17]
Stream ISA [ISCA’19]
SpZip [ISCA’21]
Graph traversals [MICRO’18]
…
täkō
Livia [ASPLOS’20]
Dist-DA [MICRO’22]
No prior NDC design supports all NDC paradigms

## Slide 39: Prior NDC suffers from poor hardware abstraction
Task loses locality
0
64
128
24-byte objects
Objects split over LLC lines
Task loses locality
0
64
128
96-byte objects
Objects always span cache lines
Cache line
Core
Core
NDC
Cache
Cache
Task
Core
Core
NDC
Cache
Cache
Task
Programmers shouldn’t have to worry about cache-line size

## Slide 40: Leviathan: a unified NDC system with data management
Data-triggered
Task offload
Streaming
Long-lived workload
L1d
L1i
L2
LLC Bank
Engine
Core
NoC
Task Offload
Code
Supports multiple NDC paradigms
Performs data management to ensure data locality
Scope:
HW abstraction:
Objects

## Slide 41: Leviathan: Roadmap
Motivation
Example NDC application
Design
Evaluation

## Slide 42: Example application: linked-list traversal
Traditional: Each lookup pulls data to the core
Task offload NDC: Each lookup executes near the data
NDC HW
3
2
1
Core
LLC bank
3
2
1
Reduced latency and network traffic!
1
2
3

## Slide 43: Leviathan: Roadmap
Motivation
Example NDC application
Design
  Programming interface
  Architecture
Evaluation

## Slide 44: Programming interface: futures
Mechanism to asynchronously return data from NDC actions to the core
Future<T> fut = invoke (…)
T result = fut.wait()
wait()
2
invoke()
1
invoke()
3
send()
4

## Slide 45: Programming interface: actors
class Node:
int key, value
Node* next
Node* Lookup(key):
if (this->key == key):
return value
if (next == nullptr):
return -1
return invoke next->Lookup(key)
Future<int> result = invoke node->Lookup(key)
Actor = data + action(s)
Near-data action
Example action triggered by core
Actions can trigger further actions
Data
“return” sends the value to the future

## Slide 46: Programming interface: memory allocator
class Allocator<T>:
T* allocate()
void deallocate(T* object)
0
64
128
24-byte objects
Normal array
Objects split over LLC banks
0
64
128
24-byte objects
w/ Leviathan allocator
Objects padded automatically
Leviathan only pads in cache! Data is compacted in DRAM

## Slide 47: Programming interface: paradigms
class Actor: # actor
int action1(…) # action
void action2(…) # action
Actor* a =
Allocator<Actor>::allocate()
Future<int> result =
invoke a->action1(…)
class Actor: # actor
# actions
Actor(State* s)
~Actor(State* s,
bool isDirty)
class Stream<T>: # actor
# Producer interface
void genStream() # action
void push(T entry)
# Consumer interface
Future<T> next()
Task offload & long-lived
Data-triggered
Streaming
Core
Cache
NDC HW
Data
App Code
Task
Task
Core
Cache
NDC HW
Data
App Code
Task
Core
Cache
NDC HW
Data
App Code
Task

## Slide 48: Leviathan: Roadmap
Motivation
Example NDC application
Design
  Programming interface
  Architecture
Evaluation

## Slide 49: Architecture: system
L1d
L1i
L2
LLC Bank
Engine
Core

## Slide 50: Architecture: engines
Task offload & long-lived:
  Check whether data is locally cached to execute action
  If data not cached, forward action to next level
Data-triggered:
  Maintain a buffer of currently-active actors
  Map actors to their actions
Stream:
  Track buffer size and head/tail pointers
  Stall producer when buffer is full
rTLB
Task-offload scheduler
Programmable compute logic
Engine
Execute action
Task-context buffer
L1d
TLB
Data-triggered scheduler
Stream scheduler

## Slide 51: Architecture: large object mapping
Padded 96B objects
LLC hash function
TLB
Zero out LSBs
Lines per object: 2
0
64
128
192
256
Bank id
Address
Address
Per-object address

## Slide 52: Architecture: additional support
Compress padded data in main memory
Task offload & long-lived
  Invoke instruction
  Invoke backpressure buffer
Data-triggered
  2 TLB registration bits
  1 bit per cache tag
Streaming
  Push and pop instructions
  Total HW overhead including engines: 6.4% vs LLC

## Slide 53: Leviathan: Roadmap
Motivation
Example NDC application
Design
Evaluation

## Slide 54: Evaluation methodology
Cycle-level simulation of 16-tile CMP
Tile contents: OoO main core, LLC bank, and Leviathan engine
Engine compute: dataflow fabric, 5x5 array, 1-cycle PE latency
Ideal engine: dataflow fabric, infinite PEs, 0-cycle PE latency
L1d
L1i
L2
LLC Bank
Engine
Core
rTLB
Task-offload scheduler
Dataflow fabric
Task-context buffer
L1d
TLB
Data-triggered scheduler
Stream scheduler

## Slide 55
Case Study:
Hash-table Lookups

## Slide 56: Hash-table lookups w/ task offload NDC
hash function
1
2
3
1
2
3
1
2
3
1
2
3
bucket
lookup
class Node:
Node* next
int key
int values[N]
Data size doesn’t matter

## Slide 57: Leviathan’s benefits with transparent data management
16 threads, 32-node buckets, 4 MB total, lists accessed with uniform distribution

## Slide 58
Case Study:
Multi-paradigm Accelerator

## Slide 59: PHI requires support for multiple NDC paradigms
UPDATE 0xFOO, +2
Cache
Core
Memory
6
0xFOO
0xFOO
10
Update in-place
18
0xFOO: +8
Log & defer
[Mukkara, MICRO’19]
Data-triggered:
Conditionally update or log on evictions
Task offload:
Offload remote memory operation (RMO) to cache
Core
UPDATE 0xFOO, +6
8
Leviathan is the only programmable system that supports both paradigms!
✅
Supported by täkō
NOT supported by täkō

## Slide 60: Leviathan’s benefits supporting multiple paradigms w/ PHI
PageRank, 16 threads, graph: 4M vertices & 40M edges
Push-based PageRank
täkō with normal, fenced atomics
täkō with relaxed, fenceless atomics
Leviathan implementation of PHI
Leviathan with an ideal engine

## Slide 61: Leviathan: unified system for NDC
Practical NDC systems need to support many types of NDC
Data management is vital to provide locality to near-data actions
Leviathan provides a single architecture and programming interface for near-data computing
Data-triggered
Task offload
Streaming
Long-lived workload

## Slide 62: Takeaways
Near-data computing tackles the data-movement bottleneck
Custom hardware and programming interfaces for each optimization is not scalable
General-purpose architectures enable software to implement a wide range of NDC designs
Data-triggered
Task offload
Streaming
Long-lived workload