## Slide 1: Tutorial on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
MICRO 2024
02 November 2024

## Slide 2: Agenda
Processing-Near-Memory Systems: Academia & Industry Developments
Invited Talk by Dr. Brian Schwedock: Architectures and Programming Models for General-Purpose Near-Data Computing
Processing-Using-Memory Systems for Bulk Bitwise Operations
Coffee Break
Ataberk Olgun: Infrastructure for Processing-Using-Memory Research
Invited Talk by Dr. Christina Giannoula: System Software and Libraries for Sparse Computational Kernels in PIM Architectures
Nika Mansouri Ghiasi: Storage-Centric Computing for Genomics and Metagenomics
Research Challenges for PIM & Closing Remarks

## Slide 3: Processing in Memory: Two Approaches
1. Processing near Memory
2. Processing using Memory

## Slide 4: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 5: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 6: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 7: Brief Review: Inside A DRAM Chip

## Slide 8: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array
of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
Row Buffer
Notes: A DRAM module
[CLICK] is composed of many DRAM chips
[CLICK] Each DRAM chip is composed of several banks.
[CLICK] Each bank has many subarrays, which are a 2D array of DRAM cells
[CLICK] The 2D array of DRAM cells are horizontally connected via a wordline
[CLICK] And vertically connected via a bitline
[CLICK] The bitlines are connected to an array of sense amplifiers
[CLICK] called row buffer .
[CLICK] A DRAM cell is composed of
[CLICK] A storage capacitor, which holds the data stored in DRAM as charge and
[CLICK] An access transistor, which enables and disables the charge flow from the storage capacitor to the bitline
[NEXT]

## Slide 9: DRAM Cell Operation
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
Notes: The DRAM cells operates using three main commands: ACTIVATE, READ/WRITE, and PRECHARGE.
[NEXT]

## Slide 10: DRAM Cell Operation (1/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. raise wordline
2. capacitor loses charge to bitline
4. amplify deviation
in the bitline
+ δ
3. enable
sense amplifier
VDD
5. capacitor charge is restored
Notes: To read the charge level stored in the storage capacitor, the memory controller issues an ACTIVATE command. Prior to receiving the ACTIVATE command, the bitline is held under a reference voltage, usually 1/2 VDD.
[CLICK] First, once the DRAM array receives the ACTIVE command, the wordline of the target row is asserted, which connects all cells along the row to their respective bitlines.
[CLICK] Second, the storage capacitor shares charge with its corresponding bitline
[CLICK] Third, the sense amplifier is enabled and
[CLICK] Fourth, the resulting bitline voltage shift is sensed and amplified by the bitline’s sense amplifier. Once the sense amplifiers finish amplification
[CLICK] the row buffer will contain the values originally stored within the cells along the asserted wordline. Also, the charge in the storage capacitor is fully restored. At the end of the ACTIVATE operation, the DRAM array is ready to receive read and write requests from the memory controller.
[NEXT]]

## Slide 11: DRAM Cell Operation (2/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
read/write charge
latched in sense amplifier
Notes: The memory controller then issues read or write commands to columns within the activated row.
[NEXT]

## Slide 12: DRAM Cell Operation (3/3)
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
½ VDD
2. precharge bitline for next access
1. lower
wordline
3. disable
sense amplifier
Notes: To prepare the DRAM array for future access to other DRAM rows, the memory controller issues a precharge command. It works as follows
[CLICK] First, the capacitor is disconnected from the bitline by disabling the wordline
[CLICK] Second, the bitline voltage is restored to its quiescent state. Now, the DRAM array is ready for next accesses.
[CLICK] Third, the sense amplifier is disabled.
[NEXT]

## Slide 13: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 14: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
14
Notes: copy

## Slide 15: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst
15

## Slide 16: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 17: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]
17

## Slide 18: RowClone Extensions and Follow-Up Work
Can we do faster inter-subarray copy?
  Yes, see LISA [Chang et al., HPCA 2016]
Can we enable data movement at smaller granularities within a bank?
  Yes, see FIGARO [Wang et al., MICRO 2020]
Can we do better inter-bank copy?
  Yes, see Network-on-Memory [CAL 2020]
Can similar ideas and DRAM properties be used to perform computation on data?
  Yes, see Ambit [Seshadri et al., CAL 2015, MICRO 2017]

## Slide 19: LISA: Increasing Connectivity in DRAM
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 20: Moving Data Inside DRAM?
DRAM cell
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 21: Key Idea and Applications
Low-cost Inter-linked subarrays (LISA)
  Fast bulk data movement between subarrays
  Wide datapath via isolation transistors: 0.8% DRAM chip area
LISA is a versatile substrate → new applications
Subarray 1
Subarray 2
…
  Fast bulk data copy: Copy latency 1.363ms→0.148ms (9.2x) → 66% speedup, -55% DRAM energy
  In-DRAM caching: Hot data access latency 48.7ns→21.5ns (2.2x) → 5% speedup
  Fast precharge: Precharge latency 13.1ns→5.0ns (2.6x) → 8% speedup

## Slide 22: More on LISA
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 23: FIGARO: Fine-Grained In-DRAM Copy
Yaohua Wang, Lois Orosa, Xiangjun Peng, Yang Guo, Saugata Ghose, Minesh Patel, Jeremie S. Kim, Juan Gómez Luna, Mohammad Sadrosadati, Nika Mansouri Ghiasi, and Onur Mutlu, "FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020.

## Slide 24: Network-On-Memory: Fast Inter-Bank Copy
Seyyed Hossein SeyyedAghaei Rezaei, Mehdi Modarressi, Rachata Ausavarungnirun, Mohammad Sadrosadati, Onur Mutlu, and Masoud Daneshtalab, "NoM: Network-on-Memory for Inter-Bank Data Transfer in Highly-Banked Memories" IEEE Computer Architecture Letters (CAL), to appear in 2020.

## Slide 25: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 26: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 27: Performance: In-DRAM Bitwise Operations

## Slide 28: Energy of In-DRAM Bitwise Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 29: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 30: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 31: More on Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 32: In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 33: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 34: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
34

## Slide 35: SIMDRAM Framework: Step 1
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
35

## Slide 36
Step 1: Naïve MAJ/NOT Implementation
A
B
Cin
Cout
Part 1
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
A
B
C
A
B
C
output is “1” only when A = B = “1”
  output is “0” only when A = B = “0”
Naïvely converting AND/OR/NOT-implementation to MAJ/NOT-implementation leads to an unoptimized circuit
MAJ
A
B
C
0
MAJ
A
B
C
1
36

## Slide 37
Step 1: Efficient MAJ/NOT Implementation
Part 2
Step 1 generates an optimized
MAJ/NOT-implementation of the desired operation
A
B
Cout
Cin
MAJ
Greedy
optimization
algorithm4
4 L. Amarù et al, “Majority-Inverter Graph: A Novel Data-Structure and Algorithms for Efficient Logic Optimization”, DAC, 2014.
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
37

## Slide 38: SIMDRAM Framework: Step 2
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
38

## Slide 39: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
39

## Slide 40: SIMDRAM Framework: Step 3
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
40

## Slide 41: Step 3: µProgram Execution
SIMDRAM control unit: handles the execution of the µProgram at runtime
Upon receiving a bbop instruction, the control unit:
  Loads the µProgram corresponding to SIMDRAM operation
  Issues the sequence of DRAM commands (ACT/PRE) stored in the µProgram to SIMDRAM subarrays to perform the in-DRAM operation
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
41

## Slide 42: Example: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 43: Example: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 44: Example: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← tmp
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
A
Sum
MAJ
Cout
MAJ
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 45: Example: Bulk Bitwise Arithmetic Operations
← A
← tmp
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 46: Example: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 47: Example: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 48: More in the Paper
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
48
https://people.inf.ethz.ch/omutlu/pub/SIMDRAM_asplos21.pdf

## Slide 49: SIMDRAM Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications
49

## Slide 50: More on SIMDRAM
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 51: SIMDRAM: Follow-Ups
Limitations of current substrate?
  Computing granularity
  Data layout conversion
  High-latency bit-serial operations
  Assembly-like programming model
  Application scope
  …
We are working on even better processing-using-memory substrates
  One step at a time!

## Slide 52: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 53: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 54: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 55: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 56: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 57: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 58: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 59: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 60: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 61: MIMDRAM: Modifications to DRAM Chip
inter-mat
interconnect
row decoder
global wordline
mat range
mat selector
isolation transistors
row decoder latch
IO interface
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 62: MIMDRAM: Control Unit Design
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 63: MIMDRAM: Compiler Support
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 64: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 65: More on MIMDRAM
Geraldo F. Oliveira, Ataberk Olgun, Abdullah Giray Yağlıkçı, F. Nisa Bostancı, Juan Gómez-Luna, Saugata Ghose, and Onur Mutlu " MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.19080.pdf

## Slide 66: In-DRAM Lookup-Table Based Execution
João Dinis Ferreira, Gabriel Falcao, Juan Gómez-Luna, Mohammed Alser, Lois Orosa, Mohammad Sadrosadati, Jeremie S. Kim, Geraldo F. Oliveira, Taha Shahroodi, Anant Nori, and Onur Mutlu, "pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (26 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2104.07699.pdf

## Slide 67: The Goal of pLUTo
Extend Processing-using-DRAM to support the execution of arbitrarily complex operations
Notes: STATED PLAINLY, THE GOAL OF PLUTO IS THUS, PRECISELY, TO **EXTEND**…

## Slide 68
x
pLUTo: Key Idea
?
output
x
input
x
ALU
f(x)
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 69
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 70
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 71
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
0
1
2
3
row buffer
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 72
row buffer
row decoder
0
1
2
3
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
2
3
5
7
2
3
5
7
2
3
5
7
Multiple copies of the lookup table
→ exploit DRAM parallelism
2
3
5
7
2
3
5
7
DRAM array
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 73
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
pLUTo
row sweep
DRAM array
row buffer
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 74
0
0
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 75
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
match logic
Accessing
the 2nd (1) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 76
match logic
Accessing
the 2nd (1) prime number?
input
vector
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
input
vector
row buffer
pLUTo
row sweep
0 = 1 ?
1
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 77
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
?
𝘅
input
vector
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 78
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
𝘅
input
vector
input
vector
row buffer
Accessing
the 1st (0) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 79
input
vector
Accessing
the 1st (0) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
row buffer
𝘅
0
pLUTo
row sweep
0 = 0 ?
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 80
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 81
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 82
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
input
vector
?
✓
𝘅
input
vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 83
Accessing
the 4th (3) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
?
✓
𝘅
𝘅
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 84
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
3 | 3 | 3 | 3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 85
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 86
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 87
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 88
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 89
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
3
𝘅
𝘅
1
2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
𝘅
𝘅
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 90
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
7 | 7 | 7 | 7
3 | 2 | 3 | -
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 91
0
1
2
3
output
vector
3 | 2 | 3 | -
- | - | - | -
7 | 7 | 7 | 7
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
𝘅
✓
𝘅
7
𝘅
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 92
0
1
2
3
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
7 | 7 | 7 | 7
𝘅
✓
𝘅
𝘅
3 | 2 | 3 | -
7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 93
System Integration
C-Like Code with
pLUTo API calls
Assembly Code with pLUTo ISA Extensions
Execution in the DRAM Substrate
pLUTo Compiler
pLUTo Controller
api_pluto_mul
pluto_subarray_alloc
pluto_bit_shift_l
pluto_or
pluto_op
ACT
PRE
ACT
ACT
PRE
...

## Slide 94
Average speedup normalized to area across 7 real-world workloads
Performance (normalized to area)
Chart: Average Speedup per Unit Area
| CPU | GPU | PnM
pLUTo-GSA | 426 | 441
pLUTo-BSA | 801 | 830
pLUTo-GMC | 1504 | 1558
pLUTo provides substantially higher performance per unit area than both the CPU and the GPU

## Slide 95
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 96: More Results in the Paper
Comparison with FPGA
Area Overhead Analysis
Circuit-Level Reliability & Correctness
Subarray-Level Parallelism
LUT Loading Overhead
Range of Supported Operations
https://arxiv.org/pdf/2104.07699.pdf

## Slide 97: SRC TECHCON Presentation
Geraldo F. Oliveira
  pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables
  https://arxiv.org/pdf/2104.07699.pdf
https://youtu.be/9t1FJQ6nNw4?si=bhylWCLZde2DC7os

## Slide 98: Bulk Bitwise Operations in Real DRAM Chips
Ismail Emir Yüksel, Yahya Can Tugrul Ataberk Olgun, F. Nisa Bostancı, A. Giray Yaglıkçı, Geraldo F. Oliveira, Haocong Luo, Juan Gómez-Luna, Mohammad Sadrosadati, Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis," Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, Scotland, March 2024.
https://arxiv.org/pdf/2402.18736

## Slide 99: The Capability of COTS DRAM Chips
99
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 100: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 101: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 102: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 103: Agenda
Processing-Near-Memory Systems: Academia & Industry Developments
Invited Talk by Dr. Brian Schwedock: Architectures and Programming Models for General-Purpose Near-Data Computing
Processing-Using-Memory Systems for Bulk Bitwise Operations
Coffee Break
Ataberk Olgun: Infrastructure for Processing-Using-Memory Research
Invited Talk by Dr. Christina Giannoula: System Software and Libraries for Sparse Computational Kernels in PIM Architectures
Nika Mansouri Ghiasi: Storage-Centric Computing for Genomics and Metagenomics
Research Challenges for PIM & Closing Remarks

## Slide 104: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 105: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 106: NAND Flash Basics: A Flash Cell
A flash cell stores data by adjusting the amount of charge in the cell
Erased Cell
(Low Charge Level)
1
Programmed Cell
(High Charge Level)
0
Activation
Operates as a resistor
Operates as an open switch
106
Notes: A flash cell stores data by adjusting the amount of charge in the cell. [Click]
A cell is considered to store bit data ‘1’ if its charge level is low, whereas it is considered to store ‘0’ if its charge level is high. [Click]
When activating a cell, a low-charge cell operates as a resistance, while a high-charge cell operates as as open switch. [Click]

## Slide 107: NAND Flash Basics: A NAND String
A set of flash cells are serially connected, forming a NAND string
1
0
0
1
0
Bitline (BL)
…
NAND String
107
Notes: A set of flash cells are serially connected, forming a NAND string, [Click] and to read …

## Slide 108: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
108
Notes: To read only the target cell from a NAND string, NAND flash memory makes all non-target cells in the string operate as a resistance regardless of stored data. [Click]

## Slide 109: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
109
Notes: If the cell stores ‘1’, it operates as a resistance, [Click] so the bitline current …

## Slide 110: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
BLi
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
0
1
1
0
1
BLj
…
Reads as ‘1’
if BL current
flows
Reads as ‘0’
if BL current
cannot flow
110
Notes: So the bitline current can flow through the NAND string, which reads as ‘1’ [Click]
If the cell stores ‘0’, [Click] the cell blocks the bitline current, which reads as ‘0’. [Click]

## Slide 111: NAND Flash Basics: A NAND Flash Block
NAND strings connected to different bitlines comprise a block
BL1
BL2
BL3
BL4
BL5
1
0
0
1
0
BLN
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
…
…
…
…
…
WL1
WL2
WL3
WL4
WLM
Block
111
Notes: There are a large number of bitlines in NAND flash memory, and NAND strings at the same vertical position comprise a NAND flash block. [Click]
A single wordline controls all the flash cells at the same vertical position, which enables the high bit-level parallelism of NAND flash memory [Click]

## Slide 112: Key Ideas
Multi-Wordline Sensing (MWS)
to enable in-flash bulk bitwise operations via a single sensing operation
Enhanced SLC-Mode Programming (ESP)
to eliminate raw bit errors in stored data
(and thus in computation results)
112
Notes: We introduce two techniques, Multi-Wordline Sensing, or MWS in short, that enables in-flash bulk bitwise operations via a single sensing operation, [Click] and Enhanced SLC-Mode Programming, or ESP in short, to achieve zero raw bit errors in stored data and thus no errors in computation results. [Click]

## Slide 113: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:
113
Notes: Target cells operate as either a resistance or an open switch depending the stored data. [Click]
In this example, only Bitline 4 can conduct flow, as the other bitlines have at least one cell that operates as an open switch. [Click]

## Slide 114: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
114
Notes: So, the sensing result would be ‘1’ only when all the target cells store bit data ‘1’, which is equivalent to the bitwise AND of all the target cells. [Click]

## Slide 115: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
115
Notes: It means that the sensing result would read as ‘0’ only when all the target cells store bit data ‘0’, which is equivalent to the bitwise OR of all the target cells. [Click]

## Slide 116: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
116
Notes: It means that the sensing result would read as ‘0’ only when all the target cells store bit data ‘0’, which is equivalent to the bitwise OR of all the target cells. [Click]

## Slide 117: Other Types of Bitwise Operations
Flash-Cosmos also enables other types of bitwise operations (NOT/NAND/NOR/XOR/XNOR)
leveraging existing features of NAND flash memory
https://arxiv.org/abs/2209.05566.pdf
117

## Slide 118: Summary: Flash-Cosmos
The first work that enables in-flash multi-operand bulk bitwise operations with a single sensing operation and high reliability
Improves performance by 32x/25x/3.5x over OSP/ISP/ParaBit
Improves energy efficiency by 95x/13.4x/3.3x over OSP/ISP/ParaBit
$
Low-cost & requires no changes to flash cell arrays
118

## Slide 119: More on Flash-Cosmos
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 120: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 121: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 122: Aside: In-Memory Crossbar Computation
Shafiee+, “ISAAC: A Convolutional Neural Network Accelerator
with In-Situ Analog Arithmetic in Crossbars”, ISCA 2016.

## Slide 123: Aside: In-Memory Crossbar Computation
Notes: This is a core part of ReRAM-based PIM. We use resistance of each cell to represent the value of weight, and add voltages representing values of inputs on each row.
According to the Kirchhoff‘s law, we finally obtain a current, representing the value of output. Thus, by modifying the peripheral circuit of ReRAM array, it can support a Matrix-Multiply-Vector operation in almost one read cycle. Let’s see how to do it.
We have an input vector, multiply it with a matrix, and get an output vector.
First, we write the matrix into a ReRAM array.
Then we feed inputs into the ReRAM array, through performing an analog sum, finally we obtain outputs.

## Slide 124: Tutorial on Memory-Centric Computing: Processing-Using-Memory
Geraldo F. Oliveira
https://geraldofojunior.github.io
MICRO 2024
02 November 2024

## Slide 125: Agenda
Processing-Near-Memory Systems: Academia & Industry Developments
Invited Talk by Dr. Brian Schwedock: Architectures and Programming Models for General-Purpose Near-Data Computing
Processing-Using-Memory Systems for Bulk Bitwise Operations
Coffee Break
Ataberk Olgun: Infrastructure for Processing-Using-Memory Research
Invited Talk by Dr. Christina Giannoula: System Software and Libraries for Sparse Computational Kernels in PIM Architectures
Nika Mansouri Ghiasi: Storage-Centric Computing for Genomics and Metagenomics
Research Challenges for PIM & Closing Remarks