## Slide 1
Nika Mansouri Ghiasi
n.mansorighiasi@gmail.com
Storage-Centric Computing for Genomics and Metagenomics

## Slide 2: Brief Self Introduction
A PhD student at the SAFARI Research Group @ ETH Zurich, advised by Professor Onur Mutlu
Research interests:
  Computer architecture
  Large-scale bioinformatics applications
  Storage systems
  Near data processing
  Emerging technologies such as ultra-dense 3D integrated systems
Contact information
  Email: n.mansorighiasi@gmail.com
  Personal website: https://bit.ly/nikamgh

## Slide 3: Outline
Brief Intro to (Meta)Genomics
Storage-Centric Designs for (Meta)Genomics
  GenStore
  MegIS
Conclusion

## Slide 4: Outline
Brief Intro to (Meta)Genomics
Storage-Centric Designs for (Meta)Genomics
  GenStore
  MegIS
Conclusion

## Slide 5: Genomics and Metagenomics are Critical for Many Applications
Developing personalized medicine
Predicting the presence and relative abundance of microbes in a sample
Rapid surveillance of disease outbreaks
Understanding genetic variations, species, evolution, …

## Slide 6: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell

## Slide 7
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCC
GGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTG

## Slide 8: Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 9: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION

## Slide 10: Problems with (Meta) Genome Analysis Today
Special-Purpose Machine
for Data Generation
FAST
SLOW
General-Purpose Machine
for Data Analysis
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today
Large amounts of data movement

## Slide 11: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Data Movement
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 12: Accelerating (Meta)Genome Analysis
Heuristics
Accelerators
Filters
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 13: Illumina DRAGEN Bio-IT Platform (2018)
Processes whole genome at 30x coverage in ~25 minutes with hardware support for data compression
FPGA board(s)
emea.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html
emea.illumina.com/company/news-center/press-releases/2018/2349147.html

## Slide 14: NVIDIA Clara Parabricks (2020)
https://developer.nvidia.com/clara-parabricks
GPU board(s)
A University of Michigan startup in 2018 joined NVIDIA in 2020

## Slide 15: NVIDIA Hopper DPX Instructions (2022)
https://blogs.nvidia.com/blog/2022/03/22/nvidia-hopper-accelerates-dynamic-programming-using-dpx-instructions/

## Slide 16: Bionano & NVIDIA: Accelerating Analysis for Fast Time to Results
We are accelerating the transformation in how we analyze the human genome!
New high-performance algorithms from Bionano
Technological solution to support higher throughput
Powered by NVIDIA RTX™ 6000
Ada Generation GPUs
Workflow tailored for a small lab and
IT footprint
Notes: Partnership
Designed to scale from small labs that do not have datacenters to datacenters and cloud

## Slide 17: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 18: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Overcomes the limitations of traditional genomics
  Bypasses the need for analyzing individual species in isolation
Notes: Metagenomics: Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)
Metagenomics overcomes the limitations of traditional genomics
Because it bypasses the need for culturing individual species in isolation,
which is not feasible in many important clinical and environmental use cases

## Slide 19: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
V. cholerae
E. coli
SARS-CoV-2
A large database
containing information
on many species
Presence/Absence Identification
(e.g., > 100 TBs in emerging databases)
Notes: Therefore, metagenomics has led to ground-breaking advances
In many fields such as
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases

## Slide 20: Our Goal
Improve (meta)genomic analysis performance
by reducing large data movement overhead
from the storage system

## Slide 21: Outline
Brief Intro to (Meta)Genomics
Storage-Centric Designs for (Meta)Genomics
  GenStore
  MegIS
Conclusion

## Slide 22: GenStore
[ASPLOS’22]

## Slide 23: GenStore A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 24: Genome Sequence Analysis
Genome sequence analysis is critical for many applications
  Personalized medicine
  Outbreak tracing
  Evolutionary studies
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: Genome sequence analysis (GSA) is critical for many applications [CLICK]
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads. [CLICK]

## Slide 25: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 26: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 27: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 28: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 29: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: That was a summary of my talk. So let’s start with the background on read mapping so we can dive into the talk in more detail.

## Slide 30: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters
Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Seeds
…
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 31: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters
Reference Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
…
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 32: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: We perform experimental studies to understand the potential of efficient in-storage filters for improving read mapping performance.

## Slide 33: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
The ideal in-storage filter significantly improves performance by
reducing the computation overhead
reducing the data movement overhead
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 34: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
Filtering outside SSD provides lower performance benefit since it
does not reduce the data movement overhead
2) must compete with read mapping for system resources
A HW accelerator reduces the computation bottleneck,
which makes I/O a larger bottleneck in the system
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 35: Our Goal
Design Objectives:
Design an in-storage filter for genome sequence analysis in a cost-effective manner
Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Performance
Support reads with 1) different properties and 2) different degrees of genetic variation in the compared genomes
Applicability
Do not require significant hardware overhead
Low-cost
Notes: Motivated by these observations, Our goal is to design an in-storage filter for genome sequence analysis in a cost-effective manner. [CLICK]
We have three key objectives in designing our new system. [CLICK]
First, the system should Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Second, the design should Support reads with 1) different properties and 2) different degrees of genetic variation
Third, it should not require significant additional hardware overhead

## Slide 36: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: To this end, we propose GenStore…

## Slide 37: GenStore
SSD Controller
Core
Core
Core
In-SSD DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
Host System
FTL
ACC
ACC
ACC
GenStore
Metadata
GenStore
FTL
Reads that need
substantial processing
Key idea: Filter reads that do not require alignment inside the storage system
Challenges
  Different behavior across read mapping workloads
  Limited hardware resources in the SSD
Notes: Which is the first in-storage processing system designed for genome sequence analysis
Our key idea is to Filter reads that do not require alignment inside the storage system and send the unfiltered data to the host system for further processing
However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD.

## Slide 38: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 39: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 40: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Let's take a closer look at GenStore-EM

## Slide 41: GenStore-EM
Efficient in-storage filter for reads with at least one exact match in the reference genome
Uses simple operations, without requiring alignment
Challenge: large number of random accesses per read to the reference genome and its index
Expensive random accesses to flash chips
Limited DRAM capacity inside the SSD
Notes: [CLICK] GenStore-EM accelerates read mapping by using an efficient in-storage filter to filter reads that have at least one exactly matching location in the reference genome
[CLICK] via simple operations, without requiring alignment.
The key challenge in designing GenStore-EM is the large number of random accesses to large data structures inside the SSD.
This is challenging because. [CLICK]
NAND flash memory exhibits poor performance for random access reads. [CLICK]
there is limited DRAM capacity available in SSD which is relatively small compared to the size of the data structures that need to be accessed.

## Slide 42: GenStore-EM: Data Structures
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
K-mer
Read-sized k-mers: to reduce the number of accesses per each read
Only one index lookup per read
Sorted read-sized k-mers: to avoid random accesses to the index
Sequential scan of the read set and the index
✓
✓
Notes: To reduce the **number** of accesses per each read, we introduce read-sized k-mers.
Therefore, instead of extracting several k-mers per read and performing index lookup for each of them, [CLICK] we can use the whole read as one k-mer
[CLICK] And have only one index lookup per read
[CLICK] To avoid **random** accesses to the index, we introduce the **sorted** index of read-sized k-mers.
[CLICK] This sorted index allows finding exact matches via sequential scanning of the read sets and the index

## Slide 43: GenStore-EM: Data Structures
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Sorted
Read-sized
K-mers
Read
AAAAAAAAAA
Notes: I show the key idea of GenStore-EM with a simplified example in which each short read consists of 10 characters.
Suppose that we have two data structures:
[CLICK] 1) a sorted read table, each entry of which stores a read [CLICK] and its unique ID, and
[CLICK] 2) a sorted k-mer index, which contains all unique read sized k-mers of the reference genome,
[CLICK] along with each k-mer’s corresponding locations in the reference genome.
[CLICK] Each data structure is sorted by read/k-mer in alphabetical order.

## Slide 44: GenStore-EM: Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read = K-mer
Next
Exact match  Filter the read
Next
Notes: We sequentially scan through these data structures in three different ways based on the [CLICK] comparison result of the current read and k-mer.
[CLICK] First, when the current read and k-mer are identical,
[CLICK] we record the read as an exactly-matching read that can be filtered from further read mapping process
[CLICK] Then, we move to the next element in both arrays. [CLICK]

## Slide 45: GenStore-EM: Not Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Next
Comparator
Read > K-mer
Notes: if the read is alphabetically larger than the k-mer,
we conclude that the k-mer does not match any read
and go to the next element in the index (so that we can examine if the next k-mer).

## Slide 46: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 47: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Avoids random accesses
Simple low-cost logic
✓
✓
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 48: GenStore-EM: Optimization
Read-sized k-mer index takes up a large amount of space (126 GB for human index) due to the larger number of unique k-mers
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted K-mer Index
Strong Hash Value
1
4
7
16
Using strong hash values instead of read-sized k-mers
reduces the size of the index by 3.9x
Notes: Despite the key benefits of the sorted read-sized k-mer index, this index takes up a large space (126 GB for human index) due to the large number of unique read-sized k-mers.
We further reduce the overheads of GenStore-EM, by replacing read-sized k-mers with a strong hash of each read that act as
Sorting criterion
Fingerprint of each entry
Using strong hash values instead of read-sized k-mers reduces the size of the index by 3.9x
While this index is still larger than the baseline k-mer index used in the conventional read mappers, our proposal is feasible for in-storage processing due to the large capacity and high internal bandwidth of modern NAND flash-based SSDs.

## Slide 49: GenStore-EM: Design
GenStore-Enabled SSD
Host System
Die#1
Plane#1
Plane#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
⋯
Channel#1
Channel#2
Channel#N
❷ Exact-match filtering
SSD Controller
NAND Flash Array
SRTable
SKIndex
❶ Sequential Reads
DRAM
Batch#i-1
Batch#i
Batch#j-1
Batch#j
Comparator
SRTable Buffer
SKIndex Buffer
Data is evenly distributed between channels, dies, and planes
to leverage the full internal bandwidth of the SSD
Steps 1 and 2 are pipelined.
During filtering, GenStore-EM sends the unfiltered reads
to the host system.
Notes: Now I show the overall operational flow of GenStore-EM, [CLICK]
with SRTable and SKIndex in the NAND flash memory, [CLICK]
distributed across all channels and dies. [CLICK]
And the comparator logic located on the SSD controller.
GenStore-EM consists of two steps: [CLICK]
Step 1 reads the two data structures from NAND flash chips to the SSD’s internal DRAM [CLICK] in a batched manner
Step 2 performs exact-match filtering within each read batch, using simple comparator logic.
Steps 1 and 2 are performed in a pipelined manner. During filtering, GenStore-EM sends the unfiltered reads to the host system for full read mapping.

## Slide 50: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Now, let’s take a closer look at GenStore-NM

## Slide 51: GenStore-NM
Efficient chaining-based in-storage filter to prune most of the non-matching reads
Challenge: how to perform chaining inside the SSD
  For a read with Seeds to , the chaining score for can be calculated as
i > j > 1
Costly dynamic programming on many seeds in each read
Particularly challenging for long reads with many seeds
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Notes: Using chaing, GenStore-NM filters most of the nonmatching reads, i.e., reads that would not align to any subsequence in the reference genome. Recall that chaining filter calculates a similarity score for each read (called chaining score) and filters read with no high-scoring potential matching locations.
Calculating a chaining score in the SSD is challenging
because finding the best chaining score requires performing [CLICK] many iterations of a dynamic programming algorithm for all seeds within a read,
This is particularly challenging for long reads since they have a large number of k-mers per read

## Slide 52: GenStore-NM: Mechanism
  Filters many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
✓
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 53: GenStore-NM: Mechanism
  Can filter many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
Details on GenStore-NM’s design are in the paper
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 54: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: I will now go into our results

## Slide 55: Evaluation Methodology
Read Mappers
Base: state-of-the-art software or hardware read mappers
  Minimap2 [Bioinformatics’18]: software mapper for short and long reads
  GenCache [MICRO’19]: hardware mapper for short reads
  Darwin [ASPLOS’18]: hardware mapper for long reads
GS: Base integrated with GenStore
SSD Configurations
SSD-L: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-M: with PCIe Gen3 interface (3.5 GB/s sequential read bandwidth)
SSD-H: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Notes: We valuate the following systems:
[CLICK] Base: state-of-the-art software or hardware read mappers for both short and long reads
[CLICK] GS: Base integrated with the GenStore inside the SSD
We evaluate these mappers on systems with various SSD configurations, a low-end, medium-end, and high-end SSD
For other details about our methodology, please refer to the paper.

## Slide 56: Performance – GenStore-EM
For a read set with 80% exactly-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 57: Performance – GenStore-NM
For a read set with 99.7% non-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
Notes: We analyze the benefits of GenStore-NM for a 12-GB long read set with very high genetic variation compared the the reference genome where 99.7% of reads do not match any subsequence in the reference genome.
We show the benefit of GS on software and hardware read mappers.
GS provides 22.4× – 27.9× speedup compared to the software Base
GS provides 6.8× – 19.2× speedup compared to the hardware Base
GS provides on average 27.2× energy reduction

## Slide 58: Area and Power
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 59: More in the Paper
Effect of read set features on performance
  Data size (up to 440 GB)
  Filter ratio
Performance benefit of an implementation of GenStore outside the SSD
  In some cases, it provides performance benefits due more efficient streaming accesses
  Provides significantly lower benefit compared to GenStore
More detailed characterization of non-matching reads across different read mapping use cases and species
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 60: GenStore A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 61: Outline
Brief Intro to (Meta)Genomics
Storage-Centric Designs for (Meta)Genomics
  GenStore
  MegIS
Conclusion

## Slide 62: MegIS
[ISCA’24]

## Slide 63: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
Nika Mansouri Ghiasi
Mohammed Alser Jisung Park Onur Mutlu
Mohammad Sadrosadati Harun Mustafa Arvid Gollwitzer Can Firtina
Julien Eudine Haiyu Mao Joël Lindegger Meryem Banu Cavlak
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 64: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 65: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 66: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 67: Motivation
Case study of the performance of metagenomic analysis tools
With various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
I/O data movement causes significant performance overhead
Chart: 
| 0.7 | 1.4
No I/O | 1 | 1
Performance-Optimized | 0.31054 | 0.24299
Cost-Optimized | 0.03627 | 0.025496
3.2x
4.1x
27.6x
39.2x
Notes: We perform a case study on the throughput of metagenomic analysis tools
with various state-of-the-art cost-optimized or performance-optimized SSD configurations
And normalized throughput compared to a hypothetical configuration with zero performance overhead due to storage I/O
We observe that I/O data movement causes significant performance overhead

## Slide 68: Motivation
Case study on the throughput of metagenomic analysis tools
With Various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
Chart: 
| 0.7 | 1.4
SSD-C | 0.03627 | 0.025496
SSD-P | 0.31054 | 0.24299
No-I/O | 1 | 1
I/O data movement causes significant performance overhead
Cost-Optimized
Performance-Optimized
No I/O
I/O becomes an even larger overhead (by 2.7x)
in systems where other bottlenecks are alleviated

## Slide 69: I/O Overhead is Hard to Avoid
I/O overhead due to accessing large, low-reuse data is hard to avoid
Sampling techniques to shrink database sizes
Keeping all data required by metagenomic analysis
completely and always resident in main memory
Reduce accuracy to levels unacceptable for many use cases
Energy inefficient, costly, unscalable, and unsustainable
Database sizes increase rapidly (doubling every few months)
Different analyses need different databases
[Wood+, Genome Biology’19], [Ounit+, BMC Genomics’15], [Kim+, Genome Research’16], …
Notes: I/O overhead from moving large, low-reuse data is hard to avoid
One might think it is possible to avoid this overhead by
using sampling techniques to shrink database sizes
However, this approach inevitably reduces accuracy to levels unacceptable for many use cases
Or another potential solution might seem to be
Keeping all data required by metagenomic analysis
completely and always resident in main memory
However, this is energy inefficient, costly, unscalable, and unsustainable due to two reasons
First, the sizes of metagenomic databases (which are already large, i.e., in some recent examples, exceeding a hundred terabytes) have been increasing rapidly.
For example, recent trends show the doubling of different important databases in only several months
Second, regardless of the sizes of individual databases, different analyses need different databases,
with information from different sets of genomes or with varying parameters.
Therefore, it is inefficient and unsustainable to maintain all data required by all possible analyses in main memory at all times

## Slide 70: Our Goal
Improve metagenomic analysis performance
by reducing large data movement overhead
from the storage system
in a cost-effective manner and with high accuracy
Notes: Motivated by these points, Our Goal is to Improve metagenomic analysis performance
by reducing the large data movement overhead from the storage system in a cost-effective manner

## Slide 71: Challenges of In-Storage Processing
No metagenomic analysis tools can run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While In-Storage Processing (ISP) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an ISP system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 72: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 73: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 74: MegIS’s Steps
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 1
Step 2
Step 3

## Slide 75: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 76: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 77: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 78: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 79: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 80: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 81: Step 1 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Step 2
Step 3

## Slide 82: Step 1 Overview
MegIS employs sorted data structures
to avoid expensive random accesses to the SSD
  Extract k-mers from the sample
  Sort the k-mers (database is sorted offline)
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
MegIS executes Step 1 in the host system
  Benefits from larger DRAM and more powerful computation
  Incurs fewer writes to NAND flash chips (than processing this step in the SSD)
  Enables overlapping Step 1 with Step 2
To execute Step 1 efficiently in the host system, MegIS needs to:
  Avoid significant overhead due to data transfer time between the steps
  Minimize performance and lifetime overheads even when host DRAM cannot hold all query k-mers
Notes: MegIS works with lexicographically-sorted data structures to avoid expensive random accesses to the SSD
Therefore, to prepare the input queries, MegIS 1) extracts k-mers from the sample,
2) sorts the k-mers
We execute this step in the host system for three reasons.
First, this step benefits from the relatively larger DRAM and more powerful computation resources in the host.
Second, due to the large host-side DRAM, performing this step in the host leads to significantly fewer writes to the flash chips
Third, by leveraging the host system for this step, we enable pipelining and overlapping Step 1 with Step 2 (which searches the large, low-reuse database).
To efficiently execute Step 1 on the host system, we need to ensure that
First, partitioning the application between the host and the SSD does not incur significant overheads due to data transfer time.
Second, minimize performance and lifetime overheads even when the host DRAM cannot hold all the extracted query k-mers

## Slide 83: Step 1 Design
Divide k-mers into independent partitions by their alphabetical range
  Can overlap operations on different partitions
Host DRAM
Host CPU
Read
Input Queries
ACGTTACGATT…
ACGTT
⋯
Query
K-mers
CGTTA
GTTAC
MegIS-Enabled SSD
Partition
A
ACGTC
ACTTT
ATGAT
⋯
⋯
C
CATTA
CTATG
CCGCA
⋯
G
GTTAC
GGTCC
GACAG
⋯
⋯
A
ACGTC
ACTTT
ATGAT
⋯
CATTA
CTATG
CCGCA
⋯
Overlap Step 1’s sorting
with Data transfer
and Step 2’s In-storage operations
Notes: To this end, we design an input processing scheme
That extracts k-mers from the sample and
divides the k-mers into independent partitions, each corresponding to an alphabetical range.
This enables overlapping the sorting on one partition with transfer and operations of its previous partitions.
Second, for scenarios where even host DRAM is not large enough to buffer all query k-mers,
the fact that these partitions are independent allows megis to pin some partitions to the host dram
and pin the others to the SSD. This way, megis can
avoid unnecessary movement of k-mers due to page swaps

## Slide 84: Step 2 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Step 3

## Slide 85: Step 2 Overview
  Identify the common k-mers between the query k-mers
  and the database k-mers
  Retrieve the species IDs
  of the common k-mers
MegIS executes Step 2 in the SSD
  Accesses large data with low reuse
  Involves lightweight computation
To execute Step 2 efficiently in the SSD, MegIS needs to:
  Leverage internal bandwidth efficiently
  Not require expensive hardware inside the SSD
  (e.g., large DRAM bandwidth/capacity and costly logic units)
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Notes: In Step 2, MegIS finds the species present in the sample
by 1) Identifying the intersecting k-mers between the query k-mers and the database
and 2) Retrieve the taxonomic IDs of intersecting k-mers
We perform this step inside the SSD since it requires streaming the
large database with low reuse and involves only lightweight computation.
To efficiently execute this step in the SSD,
MegIS should leverage the full internal bandwidth without requiring expensive hardware resources inside the SSD
(e.g., large internal DRAM size/bandwidth and costly logic units).

## Slide 86: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Common
K-mers
⋯
AGTTT
Database K-mers
from Flash Chips
Notes: Relying solely on the SSD’s internal DRAM to buffer
Database k-mers that are stored in the NAND flash chips and accessed at full channel bandwidth,
and
query k-mers from the host system
and buffering the results
During in-storage processing and
can pressure the valuable internal DRAM bandwidth

## Slide 87: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Intersect
Intersect
Buffer
Buffer
Compute directly on the flash data streams
Reduce buffer size based on application features
K-mer Register
K-mer Register
K-mer Register
K-mer Register
Write to DRAM
Common K-mers
[Zou+, MICRO’22]
Notes: To address this challenge, we adopt an approach that
processes data directly from flash chips without buffering it in internal DRAM.
we utilize key features of MegIS to determine the minimum required buffer size.
This approach allows MegIS to compute directly on the flash data stream using only two registers, thus maintaining a low cost.
Finally, we write the intersecting K-mers to the SSD DRAM to be analyzed in the next step

## Slide 88: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
Slow inside the SSD
due to long
NAND flash latency
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 89: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 90: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Design details are in the paper
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 91: Step 3
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3

## Slide 92: Step 3
MegIS performs additional analysis on species identified in the sample to estimate their abundance
MegIS can flexibly integrate with different approaches
Lightweight statistical approaches: Directly uses the output of Step 2
More accurate and costly read mapping: MegIS facilitates integration by preparing mapping indexes in the SSD
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3 and MegIS FTL are in the paper

## Slide 93: Outline
Conclusion
Background
Motivation and Goal
MegIS
Evaluation

## Slide 94: Evaluation Methodology Overview (I)
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1-TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 95: Evaluation Methodology Overview (II)
Metagenomic Analysis Task
Finding species present in the sample
Analysis of the abundance estimation task is in the paper
Metagenomic Samples
With varying degrees of genetic diversity
  Low
  Medium
  High

## Slide 96: Speedup over Software (with Cost-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 97: Speedup over Software (with Performance-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs

## Slide 98: Speedup over the PIM Hardware Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 99: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Same
accuracy
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 100: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 score
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2
Power: 7.658 mW
(Only 1.7% of the area and 4.6% of the power consumption
of three ARM Cortex R4 cores in an SSD controller)
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 101: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x

## Slide 102: More in the Paper
MegIS’s performance when running in-storage processing operations on the cores existing in the SSD controller
MegIS’s performance when using the same accelerators outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 103: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
https://arxiv.org/abs/2406.19113
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 104: Outline
Brief Intro to (Meta)Genomics
Storage-Centric Designs for (Meta)Genomics
  GenStore
  MegIS
Conclusion

## Slide 105: Specializing the Storage System for Genomics & Metagenomics Can Provide Large Benefits

## Slide 106: Specializing the Storage System for Genomics & Metagenomics Can Provide Large Benefits
Storage-centric designs
improve system cost-efficiency
and makes accurate (meta)genomics
more accessible for wider adoption

## Slide 107: (Co-)Optimizing Algorithm-Architecture-Device is Critical

## Slide 108: Computer Architecture (Expanded View)
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 109: More About My Research
Near-Data Processing
(Other Works)
ALP IEEE TETC’22
SIMDRAM ASPLOS’21
CODIC ISCA’21
Venice ISCA’23
CAL MICRO’18
CROW ISCA’19
Optimizing Memory
and Storage Systems
FIGARO MICRO’20
FLIN ISCA’18
Algorithms
MLA ISMB’24
RawHash ISMB’23
BLEND Bioinformatics’23
TargetCall APBC’23
Algorithm-Architecture Co-Design
Scrooge Bioinformatics’23
SeGraM ISCA’22
SMASH MICRO’19
Device-Architecture Co-Design
Understanding and Modeling Ultra-Dense 3D Memory Systems PACT SRC’24
https://bit.ly/nikamgh
My Website:
Works Described in This Talk
GenStore ASPLOS’22
MegIS ISCA’24

## Slide 110
Nika Mansouri Ghiasi
n.mansorighiasi@gmail.com
Storage-Centric Computing for Genomics and Metagenomics

## Slide 111: Backup Slides

## Slide 112: End-to-End Workflow of Genome Sequence Analysis
There are three key initial steps in a standard genome sequencing and analysis workflow
  Collection, preparation, and sequencing of a DNA sample in the laboratory
  Basecalling
  Read mapping
Genomic read sets can be obtained by
  Sequencing a DNA sample and storing the generated read set into the SSD of a sequencing machine
  Downloading read sets from publicly available repositories and storing them into an SSD
We focus on optimizing the performance of read mapping because sequencing and basecalling are performed only once per read set, whereas read mapping can be performed many times
  Analyzing the differences between a reads from an individual and many reference genomes of other individuals
  Repeating the read mapping step many times to improve the outcome of read mapping
Improving read mapping performance is critical in almost all genomic analyses that use sequencing
  45% of the execution time when discovering sequence variants in cancer genomics studies
  60% of the execution time when profiling the species composition of a multi-species (i.e., metagenomic) read

## Slide 113: Motivation
SSD-L
SSD-M
SSD-H
DRAM
Chart: 
| Base | SW-filtered | Ideal-ISF | Accelerator | Ideal-ISF+ACC
SSD-L | 97.56 | 76.6218 | 32.943 | 24.8 | 10.08
SSD-M | 78.44 | 55.588 | 25.1038 | 3.5428 | 1.44
SSD-H | 78.35 | 55.489 | 25.0669 | 2.0101 | 0.72203
DRAM | 75.16 | 51.98 | 1.6422
Chart: 
| Accelerator | ACC+Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-M | 3.5428 | 1.44
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
N/A
24.8
N/A
3.54
2.01
1.64
1.44
0.72
10.1
Execution time [sec]
ACC
SW-filter

## Slide 114: Motivation
State-of-the-art software read mapper, Minimap2
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Base integrated with a software filter
that prunes 80% of exactly-matching reads
Base integrated with an
ideal in-storage filter
N/A
Notes: This plot shows the execution time of three read mapping systems.
Base refers to a State-of-the-art software read mapper, Minimap2
SW-filter refers to Base integrated with a software filter that prunes 80% of exactly-matching reads
Ideal-ISF refers to base integrated with an ideal in-storage filter than prunes 80% exactly matching reads inside the SSD

## Slide 115: Motivation
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Low-end SSD with SATA3 interface (0.5 GB/s)
High-end SSD with PCIe Gen4 interface (7 GB/s)
Data preloaded in DRAM,
with no I/O overhead
N/A
Notes: To assess the impact of the storage subsystem, we evaluate each of the three mappers with different configurations
A low-end SSD, a high-end SSD, and DRAM which refers to an idealized scenario where all needed data is preloaded in DRAM with no I/O overhead

## Slide 116: Benefits of Ideal In-Storage Filter
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
The ideal in-storage filter significantly improves performance by
Reducing computation overhead
Reducing data movement overhead
N/A
Notes: Based on this plot, we make several observations, First…

## Slide 117: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
I/O has a significant impact on application performance
which can be alleviated at the cost of
expensive storage devices and interfaces
N/A
Notes: By comparing the high-end SSD, low-end SSD, and DRAM with no I/O overhead, we observe that
[CLICK] I/O has a significant impact on application performance
[CLICK] which can be alleviated at the cost of expensive storage devices and interfaces
However, it is challenging to scale a storage system’s capacity using only the high-end SSDs due to
[CLICK] the relatively smaller number of the PCIe slots in a server
[CLICK] And their significantly-higher prices

## Slide 118: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
SW-filter provides limited benefits compared to Base
N/A
The filtering process outside the SSD must compete
with the read mapping process for the resources in the system
Notes: Third, by comparing Base and SW-filter, we observe that despite a large number of needs that can be filtered, SW-filter does not provide significant benefits compared to base.
The limited speedup is mainly due to large number of accesses to the index structure for several k-mers per each read.
[CLICK] This shows that as opposed to the instorage filter, the filtering process outside the SSD must compete with the read mapping process for the resources in the system

## Slide 119: Overheads of Hardware Mappers
Chart: 
| Accelerator | Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
Execution time [sec]
24.8
10.1
23%
The ideal in-storage filter significantly improves performance
Even the high-end SSD does not fully alleviate the storage bottleneck
N/A
Notes: This figures shows similar analysis but with a state-of-the-art hardware read mapper, gencache, and its integration with the ideal in-storage filter.
We observe that Even the high-end SSD does not fully alleviate the storage bottleneck in this case
This is because by addressing computation overhead using the accelerator, I/O turns into a more serious bottleneck.
However, we observe that the ideal n-storage filter significantly improves performance since it addresses both the computation and data movement overheads.

## Slide 120: Ideal-OSF
Execution time of an ideal in-storage filter:
Execution time of an ideal outside-storage filter:
  60% slower than Ideal-ISF in our analysis

## Slide 121: Comparison to PIM
Even though read mapping applications could also benefit from other near-data, in-storage processing can fundamentally address the data movement problem by filtering large, low-reuse data where the data initially resides.
Even if an ideal accelerator achieved a zero execution time, there would still exist the need to bring the data from storage to the accelerator.
  2.15x slower than the execution time that Ideal-ISF+ACC provides in our motivational analysis
In-storage filter can be integrated with any read mapping accelerator, including PIM accelerators, to alleviate their data movement overhead.

## Slide 122: Long Read Use Cases

## Slide 123: FTL
GenStore-Enabled SSD
GenStore SSD Controller
Core
Core
Core
SSD-LV
ACC
DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
⋯
CH-LV
ACC#1
CH-LV
ACC#N
GenStore
Metadata
① Start analysis
⑤ Unfiltered data
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
③ Full-bandwidth read
② Preparation
Flush
Load
GenStore
FTL
④ Filtering
Host System
❷
❸
❶

## Slide 124: FTL: Metadata
GenStore metadata includes the mapping information of the data structures necessary for read mapping acceleration
In accelerator mode, GenStore also keeps in internal DRAM other metadata structures of the regular FTL
  Examples include the page status table and block read counts which need to be updated during the filtering process
We carefully design GenStore to only sequentially access the underlying NAND flash chips while operating as an accelerator
  Requires only a small amount of metadata to access the stored data

## Slide 125: FTL: Data Placement
GenStore needs to properly place its data structures to enable the full utilization of the internal SSD bandwidth
When each data structure is initially written to the SSD, GenStore sequentially and evenly distributes it across NAND flash chips
GenStore can specify the physical location of a 30-GB data structure by maintaining only the list of 1,250 (30 GB/24 MB) physical block addresses
It significantly reduces the size of the necessary mapping information from 300 MB (with conventional 4-KiB page mapping) to only 5 KB (1,250 4 bytes)

## Slide 126: FTL: SSD Management Tasks
In accelerator mode, GenStore only reads data structures to perform filtering, and does not write any new data
  GenStore does not require any write-related SSD-management tasks such as garbage collection and wear-leveling
The other tasks necessary for ensuring data reliability can be done before or after the filtering process
  GenStore significantly limits the amount of data whose retention age would exceed the manufacturer-specified threshold since GenStore’s filtering process takes a short time.
  GenStore-FTL can easily avoid read disturbance errors for data with high read counts since GenStore sequentially reads NAND flash blocks only once during filtering

## Slide 127: Data Sizes
Conventional k-mer index in Minimap2 + reference genome: 7 GB (k = 15)
Read-sized k-mer index before optimization: 126 GB (k= 150)
Read-sized k-mer index after optimization: 32 GB (k = 150)

## Slide 128: SSD Specs
SSD-L: SATA3 interface (0.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  8 channels
SSD-L: PCIe Gen3 M.2 interface (3.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels
SSD-L: PCIe Gen4 interface (7 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels

## Slide 129: Evaluation Methodology
Performance modeling
  Ramulator for DRAM timing
  MQSim for SSD timing
  We model the end-to-end throughput of GenStore based on the throughput of each GenStore pipeline stage
    Accessing NAND flash chips
    Accessing internal DRAM
    Accelerator computation
    Transferring unfiltered data to the host
Real system results
  AMD EPYC 7742 CPU
  1TB DDR4 DRAM
  AMD μProf
Notes: I won’t go into details, but you can refer to our paper for more details about our evaluation methdology.

## Slide 130: GenStore-NM
GenStore-Enabled SSD
Host System
Flash Array
Input
Read Set
SSD Controller
DRAM
KmerIndex
Seed Finder
Location Buffer
① Reads
Chaining-Based Filter
(Filters low-score reads)
❸
M ≤ # of Seeds < N
Seed Count-Based Filter
(Filters if # of Seeds < M)
❷
# of Seeds ≥ N
High chaining score
❶
④ Seeds
③ Query
K-mer Window
Hash Acc.
K-mers
②

## Slide 131: Chaining Processing Element

## Slide 132: GenStore-EM
Chart: 
| Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | SSD-L | SSD-M | SSD-H
Other | 101.8 | 128.44 | 119.24 | 52.78 | 73.98 | 81.378 | 31.69 | 31.69 | 86.17 | 94.787 | 31.92 | 31.92
Alignment | 68.37 | 16.46 | 16.46 | 16.46 | 80.67 | 43.02 | 43.02 | 43.02 | 72.9 | 41.39 | 41.39 | 41.39
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 44 | 108.4 | 8.8 | 6.2857 | 15.4857 | 2.8229 | 4.2832 | 7.7429 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
44
108
15
GS-Ext provides significant performance improvements
over both Base and SIMD in SSD-M and SSD-H.
GS-Ext provides limited benefits over SIMD in SSD-L
due to low external I/O bandwidth.
Notes: GS-Ext provides significant performance
improvements over both Base and SIMD in SSD-M and SSD-H. However,
GS-Ext provides limited benefits over SIMD in SSD-L since
its performance is bottlenecked by the low external I/O bandwidth.

## Slide 133: GenStore-NM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 30.056 | 1.564 | 5.362 | 4.2937 | 0.78198 | 5.36 | 2.1469 | 0.78198
GS-Ext performs significantly slower than Base (2.28x - 1.91x)
on all systems.
Notes: GS-Ext performs significantly slower than Base (2.28x - 1.91x) on all systems.

## Slide 134: Effect of Inputs on GenStore-EM
Normalized exec. time
Read set size:
Exact match:
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.50504 | 0.30763 | 0.27598 | 0.19436 | 0.28937 | 0.16534
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.65906 | 0.65906 | 0.33838 | 0.33838 | 0.31986 | 0.31986

## Slide 135: Effect of Inputs on GenStore-NM
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.029734 | 0.68811 | 0.03427 | 0.67399 | 0.035084 | 0.66259
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.14589 | 0.37024 | 0.14582 | 0.37002 | 0.14581 | 0.37001
Normalized exec. time
Read set size:
Align. rate:
0.69
0.67
0.66

## Slide 136
MegIS Backup Slides
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
12 mins
1 min conclusion
3 mins results
4 mins mech
+ 2 mins motivation
+ 2 mins background

## Slide 137: Motivational Analysis
Database access patterns
Random Query
Streaming Query

## Slide 138: Overview of MegIS’s Steps

## Slide 139: More Details on Step 1

## Slide 140: K-mer Sketch Data Structures

## Slide 141: K-mer Sketch Streaming Hardware Design
SSD Controller
Intersection
Curr. Register
MegIS-
Enabled
SSD
Channel#1
Channel#2
Internal
DRAM
5-mer | 5-mer ID
AAAAA | 1
AAAAC | 6
AATCC | 2
… | …
4-mer ID
-
3
…
AGTTT
⋯
Idx.
Gen
AAAAC
Next Register
AATCC
Move to
Next 4-mer
❶ Intersect 5-mers
❷ Intersect 4-mers
6
2
Curr. Register
AAAA
Next Register
AATC
-
3
AATC
Intersect
Intersect
❸ Send Tax IDs

## Slide 142: Index Generation in Step 3

## Slide 143: MegIS FTL

## Slide 144: Multi-Sample Analysis

## Slide 145: SSD Configurations

## Slide 146: Impact of Different Optimizations

## Slide 147: Impact of Different Optimizations

## Slide 148: Speedup with Different Database Sizes

## Slide 149: Speedup with Different #SSDs

## Slide 150: Speedup with Different Main Memory Capacities

## Slide 151: Speedup with Varying SSD Internal Bandwidth

## Slide 152: Speedup of Abundance Estimation

## Slide 153: Multi-Sample Use Case

## Slide 154: Area and Power
Based on synthesis of MegIS accelerators using the Synopsys Design Compiler @ 65nm technology node
Only 1.7% of the area of three 28-nm ARM Cortex R4 cores
in a SATA SSD controller
Logic Unit | # of instances | Area [mm2] | Power [mW]
Intersect (120-bit) | 1 per channel | 0.001361 | 0.284
k-mer Registers (2 x 120-bit) | 1 per channel | 0.002821 | 0.645
Index Generator (64-bit) | 1 per channel | 0.000272 | 0.025
Control Unit | 1 per SSD | 0.000188 | 0.026
Total for an 8-channel SSD | - | 0.04 | 7.658
Notes: We find area and power values of MegIS by synthesizing MegIS using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.04 mm square and the power is 7.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of MegIS is only 1.7% of the of the three ARM processors in a SATA SSD controller.

## Slide 155: Step 1 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Step 2
Step 3

## Slide 156: Step 1 Overview
MegIS employs sorted data structures
to avoid expensive random accesses to the SSD
  Extract k-mers from the sample
  Sort the k-mers (database is sorted offline)
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
MegIS executes Step 1 in the host system
  Benefits from larger DRAM and more powerful computation
  Incurs fewer writes to NAND flash chips (than processing this step in the SSD)
  Enables overlapping Step 1 with Step 2
To execute Step 1 efficiently in the host system, MegIS needs to:
  Avoid significant overhead due to data transfer time between the steps
  Minimize performance and lifetime overheads even when host DRAM cannot hold all query k-mers
Notes: MegIS works with lexicographically-sorted data structures to avoid expensive random accesses to the SSD
Therefore, to prepare the input queries, MegIS 1) extracts k-mers from the sample,
2) sorts the k-mers
We execute this step in the host system for three reasons.
First, this step benefits from the relatively larger DRAM and more powerful computation resources in the host.
Second, due to the large host-side DRAM, performing this step in the host leads to significantly fewer writes to the flash chips
Third, by leveraging the host system for this step, we enable pipelining and overlapping Step 1 with Step 2 (which searches the large, low-reuse database).
To efficiently execute Step 1 on the host system, we need to ensure that
First, partitioning the application between the host and the SSD does not incur significant overheads due to data transfer time.
Second, minimize performance and lifetime overheads even when the host DRAM cannot hold all the extracted query k-mers

## Slide 157: Step 1 Design
Divide k-mers into independent partitions by their alphabetical range
  Can overlap operations on different partitions
Host DRAM
Host CPU
Read
Input Queries
ACGTTACGATT…
ACGTT
⋯
Query
K-mers
CGTTA
GTTAC
MegIS-Enabled SSD
Partition
A
ACGTC
ACTTT
ATGAT
⋯
⋯
C
CATTA
CTATG
CCGCA
⋯
G
GTTAC
GGTCC
GACAG
⋯
⋯
A
ACGTC
ACTTT
ATGAT
⋯
CATTA
CTATG
CCGCA
⋯
Overlap Step 1’s sorting
with Data transfer
and Step 2’s In-storage operations
Notes: To this end, we design an input processing scheme
That extracts k-mers from the sample and
divides the k-mers into independent partitions, each corresponding to an alphabetical range.
This enables overlapping the sorting on one partition with transfer and operations of its previous partitions.
Second, for scenarios where even host DRAM is not large enough to buffer all query k-mers,
the fact that these partitions are independent allows megis to pin some partitions to the host dram
and pin the others to the SSD. This way, megis can
avoid unnecessary movement of k-mers due to page swaps

## Slide 158: Step 2 Overview
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Step 3

## Slide 159: Step 2 Overview
  Identify the common k-mers between the query k-mers
  and the database k-mers
  Retrieve the species IDs
  of the common k-mers
MegIS executes Step 2 in the SSD
  Accesses large data with low reuse
  Involves lightweight computation
To execute Step 2 efficiently in the SSD, MegIS needs to:
  Leverage internal bandwidth efficiently
  Not require expensive hardware inside the SSD
  (e.g., large DRAM bandwidth/capacity and costly logic units)
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Notes: In Step 2, MegIS finds the species present in the sample
by 1) Identifying the intersecting k-mers between the query k-mers and the database
and 2) Retrieve the taxonomic IDs of intersecting k-mers
We perform this step inside the SSD since it requires streaming the
large database with low reuse and involves only lightweight computation.
To efficiently execute this step in the SSD,
MegIS should leverage the full internal bandwidth without requiring expensive hardware resources inside the SSD
(e.g., large internal DRAM size/bandwidth and costly logic units).

## Slide 160: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Common
K-mers
⋯
AGTTT
Database K-mers
from Flash Chips
Notes: Relying solely on the SSD’s internal DRAM to buffer
Database k-mers that are stored in the NAND flash chips and accessed at full channel bandwidth,
and
query k-mers from the host system
and buffering the results
During in-storage processing and
can pressure the valuable internal DRAM bandwidth

## Slide 161: Step 2 Design: Identifying the Common K-mers
Challenge: Limited internal DRAM bandwidth
SSD DRAM
SSD Controller
MegIS-Enabled
SSD
Channel#1
Channel#N
AAAAA
TAACC
CAAAA
AGTTT
TTGGT
CCGTG
⋯
⋯
⋯
⋯
Database K-mers
Query K-mers
from the Host
CGTCA
⋯
Intersect
Intersect
Buffer
Buffer
Compute directly on the flash data streams
Reduce buffer size based on application features
K-mer Register
K-mer Register
K-mer Register
K-mer Register
Write to DRAM
Common K-mers
[Zou+, MICRO’22]
Notes: To address this challenge, we adopt an approach that
processes data directly from flash chips without buffering it in internal DRAM.
we utilize key features of MegIS to determine the minimum required buffer size.
This approach allows MegIS to compute directly on the flash data stream using only two registers, thus maintaining a low cost.
Finally, we write the intersecting K-mers to the SSD DRAM to be analyzed in the next step

## Slide 162: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
Slow inside the SSD
due to long
NAND flash latency
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 163: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 164: Step 2 Design: Retrieving the Species ID
Space-Inefficient
MegIS retrieves the species IDs of the common k-mers by looking up a sketch database
K-mer | ID
AAAAA | 1,5
AAAAC | 6
AATCC | 2, 9
… | …
Space-Efficient
7.5x Smaller
2.1× Larger
K-mer Sketch Streaming
K-mer Sketch Streaming is much more suitable for in-storage processing
due to its streaming accesses
Design details are in the paper
Notes: Storing this information for many species can be space-inefficient
Therefore,
some approaches provide data structures to encode the k-mer information in a space-efficient manner.
Despite the benefits, these approaches typically require many pointer-chasing operations for each lookup.
Performing these operations inside the SSD is challenging due to large latency of NAND flash chips
We provide an intermediate approach, K-mer Sketch Streaming that is optimized for in-storage processing
KSS leads to
significantly smaller data structures compared to the baseline tables
but is still larger compared to state-of-the-art compact structures
However, it is much more suitable for ISP due to its more efficient streaming accesses

## Slide 165: Step 3
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Step 1
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Step 2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3

## Slide 166: Step 3
MegIS performs additional analysis on species identified in the sample to estimate their abundance
MegIS can flexibly integrate with different approaches
Lightweight statistical approaches: Directly uses the output of Step 2
More accurate and costly read mapping: MegIS facilitates integration by preparing mapping indexes in the SSD
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 3 and MegIS FTL are in the paper