## Slide 1
Systems Software and Libraries
for Sparse Computational Kernels
in PIM Architectures
Christina Giannoula
Tutorial on Memory-Centric Computing Systems
MICRO 2024
Notes: Hello, I am Christina Giannoula and
In this talk I will introduce SparseP: the first Sparse Matrix Vector Multiplication Library for real Processing-In-Memory Architectures. [CLICK]

## Slide 2
Sparse Data is Everywhere
Road Networks
Austin
San Marcos
Round Rock
Bastrop
Georgetown
Notes: Irregular applications lie at the heart of many important fields including graph analytics, neural networks, medical imaging, and economic modeling.
Therefore, accelerating irregular applications is of vital importance nowdays. [CLICK]
In this dissertation, we identify three important characteristics of the irregular applications that highly affect their performance. [CLICK]

## Slide 3
Sparse Data is Everywhere
Sparse Tables:
Recommendation Data
Notes: Irregular applications lie at the heart of many important fields including graph analytics, neural networks, medical imaging, and economic modeling.
Therefore, accelerating irregular applications is of vital importance nowdays. [CLICK]
In this dissertation, we identify three important characteristics of the irregular applications that highly affect their performance. [CLICK]

## Slide 4
Sparse Data Processing Applications
Neural Networks
Bioinformatics
Databases
Medical Imaging
Economic Modeling
Graph Analytics
How can we accelerate the sparse kernels?
Notes: Irregular applications lie at the heart of many important fields including graph analytics, neural networks, medical imaging, and economic modeling.
Therefore, accelerating irregular applications is of vital importance nowdays. [CLICK]
In this dissertation, we identify three important characteristics of the irregular applications that highly affect their performance. [CLICK]

## Slide 5
Sparse Computational Kernels
E.g., Sparse Matrix Vector/Matrix Multiplication
Characteristics:
  Random memory accesses
    Not sequential/strided
    Input-driven
  Low arithmetic intensity
Highly memory-bound kernels in CPUs/GPUs
Arithmetic Intensity
Performance
Peak Compute Performance
Peak Memory Bandwidth
SpMV
Roofline Model

## Slide 6
Processing-In-Memory Systems
Processing-In-Memory (PIM) Systems:
High levels of parallelism
Low memory access latency
Large aggregate memory bandwidth
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
PIM Core 2
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
PIM Core 2
PIM constitutes a promising paradigm for accelerating sparse kernels

## Slide 7
The Challenge
Real Processing-In-Memory (PIM) Systems:
Different architectures
Software stacks are still in early stage
Specialized low-level programming interfaces
Programmers Need to:
Carefully distribute data across thousands of memory arrays
Have high expertise of the PIM hardware
Kwon+, [ISSCC 2021]
Lee+, [ISSCC 2022]
https://www.upmem.com
Instruction-level API
Instruction-level API
C-like API
Programming a real PIM architecture
for a high-level application is a hard task

## Slide 8
Our Goal
Bridge the programming gap
between software engineers/researchers
and real-world PIM architectures
High-Level
User-Friendly
API
UPMEM PIM
HBM PIM
Sparse Application

## Slide 9
Outline
SparseP (Sigmetrics’22) A Library of Efficient Sparse Matrix Vector Multiplication Kernels for Real PIM Systems
Sparse Linear Algebra
1
PyGim (Sigmetrics’25) An Efficient Graph Neural Network Framework for Real PIM Systems
Graph Neural Networks
2

## Slide 10
Sparse Matrix Vector Multiplication
Sparse Matrix Vector Multiplication (SpMV):
Widely-used kernel in graph processing, machine learning, scientific computing …
A highly memory-bound kernel
Operational Intensity
Performance
Peak Compute Performance
Peak Memory Bandwidth
SpMV
Roofline Model
Notes: Sparse Matrix Vector Multiplication (SpMV) is fundamental linear algebra kernel and lies at the heart of important applications from the scientific computing, machine learning, and graph analytics domains.
In commodity systems like CPUs and GPUs, it has been repeatedly reported to achieve only a small fraction of the peak performance, and it is primarily bottlenecked by the memory bandwidth of the system [CLICK].

## Slide 11
Real Near-Bank PIM Systems
Real Near-Bank Processing-In-Memory (PIM) Systems:
High levels of parallelism
Low memory access latency
Large aggregate memory bandwidth
Host CPU
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus
Notes: At the same time, several manufacturers have already started to commercialize near-bank Processing-In-Memory or (PIM) architectures.
A PIM system consists of multiple PIM-enabled memory modules connected to a host CPU via common channel-based connections.
Each PIM-enabled module supports several simple PIM cores.
Each PIM core is located close to a DRAM bank.
As a result, real PIM systems can provide high levels of parallelism, low memory access latency and large aggregate memory bandwidth, thereby being a good fit to accelerate the Sparse Matrix Vector Multiplication (SpMV) kernel. [CLICK]
A few real near-bank PIM architectures are Samsung’s FIMDRAM [CLICK], SK Hynix’s AiM [CLICK] and the UPMEM PIM system [CLICK].

## Slide 12
SparseP: SpMV Library for Real PIMs
Our Contributions:
Design efficient SpMV kernels for current and future PIM systems
  25 SpMV kernels
    4 compressed matrix formats (CSR, COO, BCSR, BCOO)
    6 data types
    4 data partitioning techniques
    Various load balancing schemes among PIM cores/threads
    3 synchronization approaches
Provide a comprehensive analysis of SpMV on the first commercially-available real PIM system
  26 sparse matrices
  Comparisons to state-of-the-art CPU and GPU systems
  Recommendations for software, system and hardware designers
Notes: To this end, we make two key contributions.
1. We design SparseP, the first SpMV library for real PIM architectures.
We propose 25 efficient SpMV kernels supporting several compressed matrix formats, data types, data partitioning techniques, load balancing schemes and synchronization approaches in order to cover a wide variety of matrices and applications. [CLICK]
2. We conduct a comprehensive study of the popular SpMV kernel on the first commercially-available real PIM system, the UpMEM system.
Our characterization study includes a wide range of sparse matrices with diverse characteristics, and comparisons to state-of-the-art CPU and GPU systems.
Our analysis provides recommendations for software, system and hardware designers [CLICK].

## Slide 13
SpMV Execution on a PIM System
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
Notes: The end-to-end SpMV execution on a real PIM system can broken down in four steps:
(1) the time to load the input vector into DRAM banks of PIM-enabled memory, [CLICK]
(2) the time to execute the SpMV kernel on PIM cores, [CLICK]
(3) the time to retrieve from DRAM banks to the host CPU results for the output vector, [CLICK]
and (4) the time to merge partial results and assemble the final output vector on the host CPU. [CLICK]
Our evaluated system does not have PIM-enabled memory as main memory, [CLICK] and thus we need to load the input vector to PIM-enabled DIMMs.
However, our kernel implementations would be the same and they can apply to an architecture where the PIM-enabled memory constitutes the main memory of the system. [CLICK]

## Slide 14
Data Partitioning Techniques
1D Partitioning
=
1x output vector
*
4x input vector
Core 1
Core 2
Core 3
Core 4
perform the complete
SpMV computation
only on PIM cores
2D Partitioning
2x output vector
=
2x input vector
*
Core 1
Core 2
Core 3
Core 4
trade-off
computation vs
data transfer costs
SparseP supports two types of data partitioning techniques:
Notes: To parallelize the SpMV kernel, SparseP supports two general types of data partitioning techniques:
1. We provide an 1D partitioning technique where the matrix is horizontally partitioned across PIM cores.
2. We provide a 2D partitioning technique where the matrix is partitioned into 2D tiles, the number of which is equal to the number of PIM cores. [CLICK]
With the 1D partitioning technique, almost the entire SpMV computation is performed using only PIM cores, since PIM cores directly compute the final elements for the output vector. However, the input vector needs to be replicated at each DRAM bank of PIM-enabled memory, and thus the number of the copies of the input vector that is transferred to PIM-enabled memory through the narrow memory bus is equal to the number of PIM cores used. [CLICK]
With the 2D partitioning technique, we aim to strive a balance between computation and data transfer costs, since only a subset of the elements of the input vector is copied into the DRAM bank of each PIM core. Thus, the number of copies of the input and output vectors that are transferred to PIM-enabled memory through the narrow memory bus depends on the number of vertical partitions used [CLICK].

## Slide 15
1D Partitioning Technique
Load-Balancing Approaches:
CSR, COO:
  Balance Rows
  Balance NNZs *
BCSR, BCOO:
  Balance Blocks ^
  Balance NNZs ^
* row-granularity for CSR
^ block-row-granularity for BCSR
Notes: In the 1D partitioning technique, we provide various load balancing schemes across multiple PIM cores for the 4 most widely-used compreseed matrix storage formats.
For CSR and COO formats, we load-balance either the number of rows or the number of non-zero elements across PIM cores.
For BCSR and BCOO formats, we load-balance either the number of blocks or the number of non-zero elements across PIM cores.
However, the load-balancing depends on characteristics of each compressed format.
[CLICK].

## Slide 16
1D Partitioning Technique
Load-Balancing Approaches:
#Rows or #NNZs
CSR (row-granularity), COO
CSR
0
1
3
5
7
7
8
8
9
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowptr
colind
values
0
1
1
2
2
3
3
5
7
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowind
colind
values
COO
row-order
nnz-order
Core 1
Core 2
Core 3
Core 1
Core 2
Core 3
row-
granularity
nnz-
granularity
Notes: For example, in the CSR format, since the matrix is stored in row-order, load-balancing of the non-zero elements across PIM cores is performed at row granularity.
Instead [CLICK], in the COO format, the matrix is stored in non-zero element order, and load-balancing of the non-zero elements can be performed by splitting a row across two neighbouring PIM cores,
Thus, providing a near-perfect non-zero element balance across cores.
Similarly [CLICK], in BCSR the load-balancing is performed at a block row granularity. [CLICK]

## Slide 17
1D Partitioning Technique
Load-Balancing of #NNZs:
CSR (row-granularity), COO
BCSR (block-row-granularity), BCOO
ΒCSR
0
1
3
5
7
7
8
8
9
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowptr
colind
values
0
1
1
2
2
3
3
5
7
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowind
colind
values
ΒCOO
block-row-order
block-order
Core 1
Core 2
Core 3
Core 1
Core 2
Core 3
block-row-
granularity
block-
granularity
Notes: For example, in the CSR format, since the matrix is stored in row-order, load-balancing of the non-zero elements across PIM cores is performed at row granularity.
Instead [CLICK], in the COO format, the matrix is stored in non-zero element order, and load-balancing of the non-zero elements can be performed by splitting a row across two neighbouring PIM cores,
Thus, providing a near-perfect non-zero element balance across cores.
Similarly [CLICK], in BCSR the load-balancing is performed at a block row granularity. [CLICK]

## Slide 18
2D Partitioning Technique
Equally-Sized Tiles
output vector
+
Core 1
Core 3
Core 2
Core 4
4x
4x
2x
input vector
4x
4x
output vector
Core 1
Core 3
Core 2
Core 4
2x
input vector
+
output vector
+
Core 1
Core 3
Core 2
Core 4
3x
5x
2x
input vector
Equally-Wide Tiles
Variable-Sized Tiles
High NNZ imbalance
across PIM cores
High NNZ balance across PIM cores of the same vertical partition
High NNZ balance
across all PIM cores
Notes: In the 2D partitioning technique, SparseP supports three schemes for all the 4 compressed matrix formats:
(1) In the equally-sized scheme: The 2D tiles are statically created to have the same height and width. This way the subsets of the elements for the input and output vectors have the same sizes across all PIM cores. However, this scheme has high non-zero element imbalance across PIM cores due to creating static partitions on sparse matrix. [CLICK]
(2) In the equally-wide scheme: The 2D tiles have the same width and variable height. For each vertical partition on the matrix, we load-balance the non-zero elements across the tiles of the same vertical partition. In this scheme, the subset of the elements for the input vector has the same size across PIM cores, while the subset of the elements for the output vector varies across PIM cores. This way we provide high non-zero element balance across PIM cores of the same vertical partition. [CLICK]
(3) In the variable-sized scheme: The 2D tiles have both variable width and height. We load-balance the non-zero elements both across the vertical partitions and across the tiles of the same vertical partition. This way we provide high non-zero element balance across all PIM cores. [CLICK]

## Slide 19
Parallelization across Threads
Multithreaded PIM Cores:
DRAM
Bank
Multithreaded
PIM Core
Core 1
Core 2
Core 4
Core 3
Core 1
Core 2
Core 4
Core 3
1D Partitioning
2D Partitioning
Thread 2
Thread 1
Thread 2
Thread 1
Various load-balance schemes across threads
Various synchronization approaches among threads
Balance NNZs
Balance NNZs
Notes: Finally, since real PIM architectures can support multithreaded PIM cores,
In both 1D and 2D partitioning techniques [CLICK],
we support various load balancing schemes and synchronization approaches among threads of a single multithreaded PIM core. [CLICK]

## Slide 20
SparseP Software Package
25 SpMV kernels for PIM Systems 
https://github.com/CMU-SAFARI/SparseP
Load-balance
across PIM cores/threads:
* row-granularity (CSR)
^ block-row-granularity (BCSR)
Synchronization
among threads of a PIM core:
▵ lb-cg, lb-fg, lf (COO, BCOO)
Data Types:
8-bit integer
16-bit integer
32-bit integer
64-bit integer
32-bit float
64-bit float
Partitioning | Matrix Format | Load-Balancing
9x 1D Kernels | CSR | rows, nnzs *
 | COO▵ | rows, nnzs *, nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnzs
4x 2D Equally-Sized Tiles | CSR | --
 | COO▵ | --
 | BCSR | --
 | BCOO▵ | --
6x 2D Equally-Wide Tiles | CSR | nnzs *
 | COO▵ | nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnzs
6x 2D Variable-Sized Tiles | CSR | nnzs *
 | COO▵ | nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnz
Notes: Overall, SparseP provides 9 1D parttioned-kernels and 16 2D-partitioned kernels,
supporting a wide range of data types, including both low-precision integer, and high-precision float data types. [CLICK]

## Slide 21
UPMEM-based PIM System
20 UPMEM PIM DIMMs with 2560 PIM cores in total
Each multithreaded PIM core supports 24 threads
Host CPU
(2-socket,
Intel Xeon)
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
160 GB PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
128 GB Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus
DISPATCH
FETCH
ALU
MERGE
14-stage
Pipeline
24 KB
Instr. Mem.
64 KB
Data Mem.
DMA Engine
64 MB
DRAM
Bank
64
bits
24x
threads
Notes: This is the real UPMEM PIM system that we use in our evaluation.
It includes 20 PIM DIMMs connected to a host CPU, having in total 2560 PIM cores. [CLICK].
Each PIM core can support up to 24 threads, which can access data from a local 64MB DRAM bank. [CLICK]

## Slide 22
Sparse Matrix Data Set
26 sparse matrices*:
Diverse sparsity patterns
Variability on irregular patterns
Variability on block patterns
Regular Matrix
Scale-Free Matrix
* Suite Sparse Matrix Collection: https://sparse.tamu.edu/
Notes: We evaluate a wide variety of sparse matrices.
When the standard deviation of the non-zero elements across rows and columns of the matrix is low, the matrix is reffered to as regular.
However, when the standard deviation of the non-zero elements across rows and columns is high, the matrix becomes very irregular and is reffered to as scale-free matrix. [CLICK]

## Slide 23
Kernel Execution on PIM Cores
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
Notes: We first examine only the kernel tme of SpMV execution. [CLICK].

## Slide 24
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: Speedup
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 0.84396 | 6.8634
BCSR | 0.57691 | 0.45252
BCOO | 0.73399 | 6.1852
6.86x
13.66x
Core 1
In scale-free matrices, COO + BCOO provide higher non-zero element balance across PIM cores than CSR + BCSR, respectively.
Core 2
Core 1
Core 2
COO
CSR
(row-granularity)
1D
Scale-free: COO, BCOO 
10.26x CSR, BCSR
Notes: We compare the 4 compressed matrix formats by normalizing their performance to that of the CSR format.
In 1D-partitioned kernels, we find that in scale-free matrices [CLICK] the COO and BCOO formats significantly outperform the CSR and BCSR formats, respectively, [CLICK]
This is because they provide higher non-zero element balance across PIM cores.
since CSR and BCSR are limited to perform load-balancing at a row- and block-row granularity, respectively. [CLICK]

## Slide 25
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: Speedup
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 1.0236 | 1.2315
BCSR | 0.75497 | 0.60928
BCOO | 0.85746 | 0.944
1.23x
1.55x
In scale-free matrices, COO + BCOO provide higher non-zero element balance across threads than CSR + BCSR, respectively.
Core 1
Core 3
Core 2
Core 4
CSR
(row-granularity)
COO
Thread 1
Thread 2
Thread 1
Thread 2
2D Equally-Sized Tiles
Scale-free:
COO, BCOO 
1.39x CSR, BCSR
Notes: Similarly, in the 2D equally-sized kernels, even though all compressed formats have the same non-zero element balance across PIM cores because of the static partitioning, [CLICK]
The non-zero element balance among multiple threads of each PIM core is affected by the compressed matrix format used. [CLICK]
Therefore, COO and BCOO outperform CSR and BCSR by providing higher non-zero element balance among threads within a multithreaded PIM core.

## Slide 26
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: 2D Equally-Wide Tiles
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 44.021 | 22.4092
BCSR | 1.1764 | 0.85832
BCOO | 46.4785 | 23.9397
Chart: 2D Variable-Sized Tiles
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 42.24 | 19.9686
BCSR | 1.1388 | 0.7889
BCOO | 40.0751 | 20.653
44x
42x
40x
46x
22x
24x
20x
21x
COO + BCOO formats provide higher non-zero element balance across PIM cores + threads than CSR + BCSR, respectively.
COO, BCOO  32.38x CSR, BCSR
Notes: Finally, in 2D equally-wide and variable-sized partitioning schemes,
we find that [CLICK] COO and BCOO significantly outperform CSR and BCSR formats respectively across all our evaluated sparse matrices, and [CLICK]
This is because COO and BCOO provide high non-zero element balance across PIM cores and threads within a PIM core. [CLICK]

## Slide 27
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: 1D
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 0.84396 | 6.8634
BCSR | 0.57691 | 0.45252
BCOO | 0.73399 | 6.1852
Chart: 2D Equally-Sized
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 1.0236 | 1.2315
BCSR | 0.75497 | 0.60928
BCOO | 0.85746 | 0.944
Chart: 2D Equally-Wide
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 44.021 | 22.4092
BCSR | 1.1764 | 0.85832
BCOO | 46.4785 | 23.9397
Chart: 2D Variable-Sized
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 42.24 | 19.9686
BCSR | 1.1388 | 0.7889
BCOO | 40.0751 | 20.653
The compressed matrix format used to store the input matrix determines the data partitioning across DRAM banks of PIM-enabled memory. As a result, it affects the load-balance across PIM cores (and threads of a PIM core) with corresponding performance implications.
Key Takeaway 1
Design compressed data structures that can be effectively partitioned across DRAM banks, with the goal of providing high computation balance across PIM cores (and threads of a PIM core).
Recommendation 1
Notes: Our main key takeaway from this analysis is that
the compressed matrix format used to store the input matrix determines the data partitioning across DRAM banks of PIM-enabled memory.
Thus, it affects the load balance across PIM cores with corresponding performance implications. [CLICK]
Therefore, we recommend software designers to propose compressed data structures for sparse kernels that can be effectively partitioned across DRAM banks, with the goal of providing high computation balance across PIM cores (and/or across threads within each PIM core). [CLICK].

## Slide 28
End-to-End Performance
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
Notes: Then, we characterize the end-to-end SpMV execution including the data transfer costs for the input and output vectors [CLICK].

## Slide 29
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
1D: #bytes to load the input vector grows linearly to #PIM cores
The scalability is limited by the load time
Notes: We evaluate the scalability of all partitioning techniques as the number of PIM cores increases.
Performance is normalized to that with 256 PIM cores. [CLICK].
We find that the scalability of the 1D partitioning technique is limited by the load data transfers, [CLICK] because the amount of bytes that is transferred to PIM-enabled memory for the input vector grows linearly with the number of PIM cores. [CLICK]

## Slide 30
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
The 1D-partitioned kernels are severely bottlenecked by the high data transfer costs to broadcast the whole input vector into DRAM banks of all PIM cores, through the narrow off-chip memory bus.
Key Takeaway 2
Optimize the broadcast collective operation in data transfers to PIM-enabled memory to efficiently copy the input data into DRAM banks in the PIM system.
Recommendation 2
Notes: We conclude the 1D-partitioned kernels are bottlecked by the high data transfers to broadcast the whole input vector into each DRAM bank of all PIM cores.[CLICK]
To this end, we suggest hardware and system designers to optimize the *broadcast* collective in data tranfers to PIM-enabled memory, such that to minimize overhead of copying input data into all DRAM banks of the PIM system [CLICK].

## Slide 31
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
2D Equally-Sized: kernel time is limited by only
a few PIM cores assigned to the 2D tiles with the largest #NNZs
The scalability is limited by the kernel time
Notes: We also find that [CLICK] in 2D equally-sized scheme the kernel time limits its scalability.
Specifically, the kernel time is limited by the PIM core (or only a few PIM cores) assigned to the 2D tile with the largest number of non-zero elements. [CLICK]

## Slide 32
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
2D Equally-Wide + 2D Variable-Sized:
high amount of zero padding to gather the output vector 
parallel transfers supported at rank granularity = 64 PIM cores
> 88% of data is zeros
The scalability is limited by the retrieve time
Notes: Finally, we find that the scalability of 2D equally-wide and 2D variable-sized kernels [CLICK] is limited by the retrieve time to transfer the results for the output vector to the host CPU [CLICK]
These scemes are severely bottlenecked by the high amount of padding with empty bytes performed in the parallel transfers to retrieve results for the output vector.
Our evaluated system supports parallel transfers at rank granularity, i.e., among 64 PIM cores, and therefore a high amount of zero padding is performed in retrieve data transfers, accounting approximately the 88% of data transferred from PIM-enabled memory to the host CPU. [CLICK]
[εισαγωγή για τα idle cores εδω! και μετα αναλυση οτι τα idle cores στα scale-free ειναι πολυ παραπανω]

## Slide 33
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
88.6%
88.0%
Optimize the gather collective operation at DRAM bank granularity in data transfers from PIM-enabled memory to efficiently retrieve the output results to the host CPU.
Recommendation 3
The 2D equally-wide and variable-sized kernels need fine-grained parallel data transfers at DRAM bank granularity (zero padding) to be supported by the PIM system to achieve high performance.
Key Takeaway 3
Notes: We conclude that the 2D equally-wide and variable-sized partitioning schemes require fine-grained parallel data transfers at DRAM bank granularity to be supported by the PIM system to achieve high performance. [CLICK]
To this end, we suggest hardware and system designers to optimize the *gather* collective operation from PIM-enabled memory to the host CPU,
and provide parallel data transfers at DRAM bank granularity (i.e., having zero padding), in order to significantly minimize overheads of retrieving the output results. [CLICK]

## Slide 34
Up to 2528 PIM Cores, 32-bit float
1D vs 2D
Chart: 
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (equally-sized) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
1.45x
1.31x
regular
scale-free
>1100 Idle Cores
>2200 Idle Cores
Best-performing SpMV execution:
trades off computation with lower data transfer costs
Notes: Finally, when we compare the end-to-end-performance all data partitioning techiques. [CLICK]
We find that the equally-sized 2D partitioning technique performs best in regular matrices, [CLICK]
While the 1D partitioning technique performst best in scale-free matrices.
However, [CLICK] in all sparse matrices the best performance is achieved using a much smaller number of PIM cores than the available PIM cores of the system.
There are many idle cores in the system because the best-perforing SpMV execution is a trade-off between computation and data transfer costs. [CLICK]

## Slide 35
2528 PIM Cores, 32-bit float
1D vs 2D
Chart: 
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (equally-sized) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
1.45x
1.31x
regular
scale-free
1329 Cores
253 Cores
Expensive data transfers to/from PIM-enabled memory performed via the narrow memory bus impose significant performance overhead to end-to-end SpMV execution. Thus, it is hard to fully exploit all available PIM cores of the system.
Key Takeaway 4
Design high-speed communication channels and optimized libraries in data transfers to/from PIM-enabled memory, provide hardware support to effectively overlap computation with data transfers in the PIM system, and/or integrate PIM-enabled memory as the main memory of the system.
Recommendation 4
Notes: We conclude that the expensive data transfers to/from PIM-enabled memory performed via the narrow memory bus impose significant performance overhead to end-to-end SpMV execution,
Therefore, it is hard to fully exploit all available PIM cores of the system. [CLICK]
To this end, we recommend software, hardware and system designers to provide high-speed communication channels and optimized libraries in data transfers to/from PIM-enabled memory modules,
provide hardware support to effectively overlap computation with data transfers in the PIM system,
And/or integrate the PIM-enabled memory modules to be the main memory of the system [CLICK].

## Slide 36
SpMV Execution on Various Systems
Real PIM
System
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute
the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
bus
Main Memory
DRAM Bank
DRAM Bank
Host CPU
Execute the kernel
1
CPU System
GPU System
SMX2
SMX2
Load the
input vector
Execute the kernel
Retrieve
the final vector
1
2
3
GPU Global Memory
DRAM Bank
DRAM Bank
Host CPU
GPU Cores
bus
Main Memory
DRAM Bank
DRAM Bank
Notes: Finally, we compare the SpMV execution on the UPMEM PIM system with that of a common CPU system [CLICK],
and GPU system CLICK].
In the GPU system, we also account for the time to transfer one instance of the input vector to the GPU global memory, and also the time to retrieve the final output vector to the host CPU. [CLICK]

## Slide 37
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Notes: Common CPU and GPU systems [CLICK] are processor-centric systems with high computation capabilities,
While real PIM systems [CLICK] are memory-centric systems with high bandwidth capabilities. [CLICK]
When considering [CLICK] only the actual kernel time (without accounting for the data transfer costs)
we find that SpMV kernel execution on a real PIM system achieves a much higher fraction of the peak performance compared that of CPU and GPU systems, thereby providing a much higher total cost of ownership and higher resource utilization.
Instead, [CLICK] when considering the end-to-end execution, i.e., including the data transfer overheads for the input and output vectors, the CPU system performs best.
However, PIM systems are still maturing and future PIM systems are expected to reduce data transfer costs
E.g., by integrating the PIM-enabled memory modules as the main memory of the system or by providing hardware support to overlap computation with data transfers. [CLICK]

## Slide 38
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Only (COO, 32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
Notes: Common CPU and GPU systems [CLICK] are processor-centric systems with high computation capabilities,
While real PIM systems [CLICK] are memory-centric systems with high bandwidth capabilities. [CLICK]
When considering [CLICK] only the actual kernel time (without accounting for the data transfer costs)
we find that SpMV kernel execution on a real PIM system achieves a much higher fraction of the peak performance compared that of CPU and GPU systems, thereby providing a much higher total cost of ownership and higher resource utilization.
Instead, [CLICK] when considering the end-to-end execution, i.e., including the data transfer overheads for the input and output vectors, the CPU system performs best.
However, PIM systems are still maturing and future PIM systems are expected to reduce data transfer costs
E.g., by integrating the PIM-enabled memory modules as the main memory of the system or by providing hardware support to overlap computation with data transfers. [CLICK]
[Add results for the energy]

## Slide 39
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Only (COO, 32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
End-to-End (COO, 32-bit float):
  CPU = 4.08 GFlop/s
  GPU = 1.92 GFlop/s
  PIM (1D) = 0.11 GFlop/s
Notes: Common CPU and GPU systems [CLICK] are processor-centric systems with high computation capabilities,
While real PIM systems [CLICK] are memory-centric systems with high bandwidth capabilities. [CLICK]
When considering [CLICK] only the actual kernel time (without accounting for the data transfer costs)
we find that SpMV kernel execution on a real PIM system achieves a much higher fraction of the peak performance compared that of CPU and GPU systems, thereby providing a much higher total cost of ownership and higher resource utilization.
Instead, [CLICK] when considering the end-to-end execution, i.e., including the data transfer overheads for the input and output vectors, the CPU system performs best.
However, PIM systems are still maturing and future PIM systems are expected to reduce data transfer costs
E.g., by integrating the PIM-enabled memory modules as the main memory of the system or by providing hardware support to overlap computation with data transfers. [CLICK]
[Add results for the energy]

## Slide 40
CPU/GPU Comparisons
Kernel-Only (COO, 32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
End-to-End (COO, 32-bit float):
  CPU = 4.08 GFlop/s
  GPU = 1.92 GFlop/s
  PIM (1D) = 0.11 GFlop/s
Many more results in the full paper: https://arxiv.org/pdf/2201.05072.pdf
Notes: Please refer to our arxiv paper for many more key insights. [CLICK]

## Slide 41
Outline
SparseP (Sigmetrics’22) A Library of Efficient Sparse Matrix Vector Multiplication Kernels for Real PIM Systems
Sparse Linear Algebra
1
PyGim (Sigmetrics’25) An Efficient Graph Neural Network Framework for Real PIM Systems
Graph Neural Networks
2

## Slide 42
Applications of Graph Neural Networks (GNNs)
Drug Discovery
Recommendation Systems
Fraud Detection

## Slide 43
A GNN Layer
Input Graph
Aggregation
Input Feature Matrix
Small
Neural
Network
Combination
Output Feature Matrix
A GNN Layer

## Slide 44
GNN Execution is Bandwidth-Bound
Input Graph
Aggregation
Input Feature Matrix
Small
Neural
Network
Combination
Output Feature Matrix
A GNN Layer
In an RTX 3090 GPU with ~900 GB/s bandwidth, GNN aggregation:
takes ~91% of the inference time
achieves ~3% core utilization
GNN execution is significantly limited by memory bandwidth in processor-centric systems

## Slide 45
The PyGim Framework: Overview
PyGim
PyGim:
An efficient GNN framework for real PIM systems
Bridges the gap between ML engineers and real PIM hardware for GNNs
Incorporates 4 key techniques:
  Cooperative Acceleration (CoA)
  Parallelism Fusion (PaF)
  Lightweight Tuner
  Python-like Programming Interface

## Slide 46
PyGim Cooperative Acceleration (CoA)
Host CPU
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
Host Cores
Shared Cache
GNN Combination
Combination runs on Host cores
Aggregation runs on PIM cores

## Slide 47
PyGim Parallelism Fusion (PaF)
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
3 parallelization levels with different strategy at each level
Across PIM Clusters: Feature- + Edge-level Parallelism
Within a PIM Cluster: Vertex-/Edge-level Parallelism
Within a PIM Core: Vertex-/Edge-level Parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 4
Cluster 3
PIM Core
Threads

## Slide 48
PyGim Parallelism Fusion (PaF)
Provides various parallelization and load balancing strategies across, within PIM clusters and within a PIM core
Strives a balance between computation and data transfer costs for various real-world graphs
Real-world graphs have different characteristics

## Slide 49
PyGim Tuner
Tuner selects the best-performing parallelization strategy based on:
  Real-world graph characteristics
  PIM hardware characteristics
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Real-world Graph
Real PIM System
PyGim Tuner
PyGim PaF Strategy

## Slide 50
PyGim Interface
A handy Python interface (currently integrated with PyTorch)

## Slide 51
Performance Evaluation
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts
PyGim outperforms PyTorch CPU and prior PIM-based schemes by 3.1x and 4.4x, respectively

## Slide 52
Energy Efficiency Evaluation
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 2564.2726 | 2587.1552 | 2442.4522 | 4433.7424 | 4279.762 | 4359.3713 | 5852.4966 | 5620.9367 | 5704.5425
SparseP1 | 4946.4061 | 4897.4054 | 4944.507 | 7214.2204 | 7086.3536 | 7154.5176 | 10135.5761 | 9977.7677 | 10039.4813
SparseP2 | 4487.6501 | 4451.2338 | 4496.3087 | 6478.7246 | 6381.0069 | 6422.2122 | 9143.2736 | 9046.1845 | 9065.546
GraNDe | 6149.8183 | 5918.9864 | 6105.7194 | 8200.6406 | 7889.4481 | 7882.9551 | 13149.1481 | 13064.0146 | 13328.4552
PyGim_CSR | 1856.5666 | 1765.8154 | 1798.3173 | 2555.2897 | 2450.003 | 2473.5083 | 3737.752 | 3570.6333 | 3628.2915
PyGim_COO | 1912.043 | 1882.2876 | 1899.8371 | 2572.9546 | 2496.2467 | 2576.2211 | 3735.719 | 3580.2291 | 3671.5764
ogbn-proteins
reddit
amazonProducts
PyGim is 2.7x and 3.3x more energy efficient than PyTorch CPU and prior PIM-based schemes

## Slide 53
Conclusion
Sparse computational kernels form the backbone of many important applications (HPC, machine learning, graph analytics… )
Sparse kernels are typically a highly memory-bound kernel in processor-centric systems (e.g., CPU and GPU systems)
Real near-bank PIM systems can tackle the data movement bottleneck (high parallelism, large aggregate memory bandwidth)
Real PIM systems typically provide specialized low-level programming interfaces and need high expertise of PIM hardware
Our Contributions:
  SparseP : first open-source SpMV library for real PIM systems
  PyGim : first open-source GNN framework for real PIM systems
  Recommendations for future PIM hardware and software
SparseP Code: https://github.com/CMU-SAFARI/SparseP
SparseP Paper: https://arxiv.org/pdf/2201.05072.pdf
PyGim Code: https://github.com/CMU-SAFARI/PyGim
PyGim Paper: https://arxiv.org/pdf/2402.16731.pdf
Our Work

## Slide 54
Systems Software and Libraries
for Sparse Computational Kernels
in PIM Architectures
Christina Giannoula
Tutorial on Memory-Centric Computing Systems
MICRO 2024
Notes: Hello, I am Christina Giannoula and
In this talk I will introduce SparseP: the first Sparse Matrix Vector Multiplication Library for real Processing-In-Memory Architectures. [CLICK]