## Slide 1: Infrastructure for Processing-Using-Memory Research
Ataberk Olgun
PPoPP 2025
1st March 2025

## Slide 2: Brief Self Introduction
Ataberk Olgun
  4th year PhD Student @ SAFARI Research Group
    ETH Zurich, Switzerland (Jan 2022 – ongoing)
    BSc + MSc, TOBB ETU, Turkey
  https://ataberkolgun.com
  olgunataberk@gmail.com
  https://safari.ethz.ch
Research interests:
  Computer architecture
  Memory systems:
    Security, safety, reliability, availability, performance, energy efficiency
  Processing in memory

## Slide 3: Papers We Will Discuss
Ataberk Olgun, Juan Gomez Luna, Konstantinos Kanellopoulos, Behzad Salami, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "PiDRAM: A Holistic End-to-end FPGA-based Framework for Processing-in-DRAM" ACM Transactions on Architecture and Code Optimization (TACO), March 2023. [arXiv version] Presented at the 18th HiPEAC Conference, Toulouse, France, January 2023. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (40 minutes)] [PiDRAM Source Code]
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips” IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024. [Slides (pptx) (pdf)] [arXiv version] [FCDRAM Source Code]
Ismail Emir Yuksel, Yahya Can Tugrul, F. Nisa Bostanci, Geraldo F. Oliveira, A. Giray Yaglikci, Ataberk Olgun, Melina Soysal, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 54th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Brisbane, Australia, June 2024. [Slides (pptx) (pdf)] [arXiv version] [SiMRA-DRAM Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as both code and dataset available, reviewed and reproducible.

## Slide 4: Recall: Processing using DRAM
We can support
  Bulk bitwise AND, OR, NOT, MAJ
  Bulk bitwise COPY and INIT/ZERO
  True Random Number Generation; Physical Unclonable Functions
  Lookup Table based more complex computation
At low cost
Using analog computation capability of DRAM
  Idea: activating (multiple) rows performs computation
    Even in commodity off-the-shelf DRAM chips!

## Slide 5: PiDRAM An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques
Ataberk Olgun
Juan Gomez Luna
Konstantinos Kanellopoulos
Hasan Hassan
Behzad Salami
Oğuz Ergin
Onur Mutlu
Notes: Hi, I am Ataberk and I will present PiDRAM: An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques. This work was done in a collaboration of SAFARI and Kasirga Research groups in ETH Zurich and TOBB University of Economics and technology.

## Slide 6: PiDRAM Summary
Motivation: Commodity DRAM based PiM techniques improve the performance and energy efficiency of computing systems at no additional DRAM hardware cost
Problem: Challenges of integrating these PiM techniques into real systems are not solved
General-purpose computing systems, special-purpose testing platforms, and system simulators cannot be used to efficiently study system integration challenges
Goal: Design and implement a flexible framework that can be used to:
solve system integration challenges
analyze trade-offs of end-to-end implementations of commodity DRAM-based-PiM techniques
Key idea: PiDRAM, an FPGA-based framework that enables:
system integration studies
end-to-end evaluations of PIM techniques using real unmodified DRAM chips
Evaluation: End-to-end integration of two PiM techniques on PiDRAM’s FPGA prototype
Case Study #1 – RowClone: In-DRAM bulk data copy operations
119x speedup for copy operations compared to CPU-copy with system support
198 lines of Verilog and 565 lines of C++ code over PiDRAM’s flexible codebase
Case Study #2 – D-RaNGe: DRAM-based random number generation technique
8.30 Mb/s true random number generator (TRNG) throughput, 220 ns TRNG latency
190 lines of Verilog and 78 lines of C++ code over PiDRAM’s flexible codebase
PiDRAM: https://github.com/CMU-SAFARI/PiDRAM
Notes: I will start with an executive summary
[CLICK] Commodity DRAM-based PIM techniques improve the performance and energy efficiency of computing systems without incurring any DRAM hardware cost
[CLICK] However, challenges of integrating these techniques into real systems are not yet solved.
[CLICK] Moreover, these challenges cannot be efficiently studied using existing computing systems, special-purpose DRAM testing platforms or system simulators
[CLICK] Our goal is to design and implement a flexible framework that can be used to [CLICK] solve the important system integration challenges and [CLICK] analyze the trade-offs of end-to-end implementations of commodity DRAM based PiM techniques
[CLICK] Our key idea is to develop PiDRAM, an FPGA-based framework that enables such studies using real unmodified DRAM chips
[CLICK] Using our framework, we conduct two case studies on two recent commodity DRAM based PiM techniques on a real FPGA prototype of a full system
[CLICK] In our first case study about in-DRAM bulk data copy operations, we show that in-DRAM data copy operations provide 119 times speedup over CPU-copy operations including system support. To conduct this case study over PiDRAM’s extensible code base, we add only 198 lines of Verilog and only 565 lines of C++ code.
[CLICK] In our second case study about an in-DRAM true random number generation technique, we show that an end-to-end implementation of a DRAM-based true random number generator can provide high throughput true random numbers at low latency. Implementing the true random number generator takes us only 190 additional lines of Verilog and 78 additional lines of C++ code over PiDRAM’s code base.

## Slide 7: Outline
Background
  DRAM Organization and Operation
  Commodity DRAM Based PiM Techniques
PiDRAM
  Overview
  Hardware & Software Components
  FPGA Prototype
Case Studies
  Case Study #1 – RowClone Case Study #2 – D-RaNGe
Conclusion
Notes: Here is the outline of my talk. I will start with a background on DRAM organization and operation

## Slide 8: DRAM Organization
…
…
…
[Olgun+ ISCA’21]
Notes: A processor’s memory controller
[CLICK] communicates with a set of DRAM chips within a DRAM module through a memory channel.
[CLICK] Each DRAM chip contains multiple banks that share a common chip I/O interface.
[CLICK] DRAM banks are organized into subarrays that consists of a set of wordline drivers and sense amplifiers
[CLICK] Subarrays are partitioned into DRAM MATs which are collections of DRAM cells that are separated from each other by wordline drivers.
[CLICK] DRAM cells are laid out onto a two-dimensional array of wordlines and bitlines within
a DRAM MAT. A row of DRAM cells is a DRAM row.
[CLICK] Here is a simplified diagram of a DRAM cell.

## Slide 9: DRAM Operation
…
…
…
…
…
Sense Amplifiers
Sense Amplifiers
Cache line
READ
…
READ
READ
Wordline Drivers
Sense Amplifiers
READ
READ
READ
ACT R0
RD
PRE R0
RD
RD
ACT R1
RD
RD
RD
time
DRAM Command Sequence
(Activation Latency)
(Precharge Latency)
[Kim+ HPCA’19]
(Access Latency)
Notes: Now we will look at how DRAM operates at the scope of a single subarray.
[CLICK] Because memory controllers typically access DRAM cells in the granularity of a cache line or a cache block we combine consecutive DRAM cells to form cache lines in this diagram.
[CLICK] On the bottom we have a timeline of DRAM commands.
[CLICK] First, we activate the first row to [CLICK] copy its cache lines to the sense amplifiers
[CLICK] At this point we can read data [CLICK] in cache line granularity from the sense [CLICK] amplifiers by sending READ commands
[CLICK] To access another row, we must first precharge the DRAM bank which closes the open DRAM row and sets the bitline voltage to half Vdd.
[CLICK] We can now activate the [CLICK] second row before [CLICK] [CLICK] [CLICK] reading data from it.
[CLICK] To ensure correct operation, we must obey certain timing parameters that define intervals between DRAM command pairs.
Three important timing parameters are tRAS, tRP, and tRCD
[CLICK] tRAS is the time required for the charge to become restored in the capacitors on the open row. tRAS dictates the amount of time we need to wait between successive activate and precharge commands
[CLICK] tRP is the time it takes for a bitline to become precharged to half Vdd such that a new activate command can be issued to open a DRAM row. Successive precharge and activate commands must be separated on the command bus by at least a tRP amount of time.
[CLICK] tRCD is the time it takes for sense amplifiers to amplify the bitline voltage to an I/O readable value. Successive activate and read commands must be separated by a tRCD amount of time.

## Slide 10: Processing-in-Memory Techniques
Use operational principles of memory to perform bulk data movement and computation
Commodity DRAM chips can already perform:
Row-copy: In-DRAM bulk data copy (or initialization) at DRAM row granularity
True random number generation
Physical uncloneable functions
Majority operation
[Gao+, MICRO’19]-[Gao+, MICRO’22]
(e.g., [Kim+, HPCA’19]-[Olgun+, ISCA’21])
(e.g., [Kim+, HPCA’18])
[Gao+, MICRO’19]-[Gao+, MICRO’22]
Notes: Commodity DRAM based PiM techniques use operational principles of commodity DRAM chips to move data and perform computation inside the DRAM chip.
[CLICK] Two examples of such techniques relevant to our work are in-DRAM data copy or initialization and [CLICK] in-DRAM true random number generation.

## Slide 11: Row-Copy: Key Idea (RowClone)
r
c
r
o
w
s
s
t
o
w
d
r
1. Source row to sense amplifiers
2. Sense amplifiers to destination row
Sense Amplifiers
r
c
r
o
w
s
s
r
c
r
o
w
?

[Seshadri+ MICRO’13]
Notes: I will describe the key idea of in-DRAM copy operations over this diagram. The diagram shows a simplified view of a DRAM subarray with a set of DRAM rows and sense amplifiers. To copy the orange source row to the gray destination row:
[CLICK] First, we copy the source row to row buffer
[CLICK] Second, we move the data from the sense amplifiers to the destination row
[CLICK] Current DRAM chips already support the first step of this operation. We can use activate commands to copy the source row to the destination row
[CLICK] I will describe how we can move data back from the sense amplifiers to the destination row later in my presentation

## Slide 12: RowClone in Real DRAM Chips
Key Idea: Use carefully created DRAM command sequences
ACT  PRE  ACT command sequence with greatly reduced DRAM timing parameters
ComputeDRAM [Gao+, MICRO’19] demonstrates in-DRAM copy operations in real DDR3 chips
ACT S
PRE
ACT D
ACT S
PRE
ACT D
Standard DRAM Timings
Violated DRAM Timings
“activate row S, precharge, then activate row D”
“activate row S, then activate row D”
Notes: The key idea in our RowClone implementation is to perform in-DRAM copy operations by using carefully crafted DRAM command sequences
[CLICK] We use the command sequences proposed by the ComputeDRAM paper, which demonstrates in-DRAM copy operations in real DDR3 chips
[CLICK] We send an ACTivate precharge activate command sequence with greatly violated DRAM timing parameters
[CLICK] This operation allows us to [CLICK] copy a source row to a destination row in the same DRAM subarray.
[CLICK] We target the source row with the first activate command [CLICK] wait for 10 nanoseconds and [CLICK] send a precharge command, [CLICK] and then wait for another 10 nanoseconds [CLICK] and target the destination row with the second activate command.

## Slide 13: In-DRAM TRNG: Key Idea (D-RaNGe)
Row Decoder
High % chance to fail with reduced access latency
Low % chance to fail with reduced access latency
SA
SA
SA
SA
SA
SA
SA
[Kim+ HPCA’19]
Commodity DRAM chips can already perform D-RaNGe
50% chance to fail
Notes: The key idea of D-RaNGe, or the in-DRAM true random number generation technique that we are interested in is to reduce DRAM read access latency below manufacturer-recommended values and exploit the resulting error patterns as true random numbers. I will describe this over a diagram:
[CLICK] This diagram depicts a DRAM bank. We color and size the cells according to their failure probabilities when they are accessed with reduced access latency values.
[CLICK] Red cells fail with a high probability
[CLICK] and green cells fail with a low probability when accessed with reduced latency
[CLICK] D-RaNGe identifies cells that fail with a probability close to 50% and repeatedly accesses these cells with reduced access latency to generate true random numbers in DRAM

## Slide 14: System Support for PiM
bulk data initialization
DRAM Chip
support for custom timing parameters
control logic for PiM operations
software interface to execute PiM ops.
supervisor for basic system support
Micro-architecture
SW/HW Interface
Program/Language
Application
Logic
Devices
System Software
Electrons

## Slide 15: PiDRAM
bulk data initialization
DRAM Chip
support for custom timing parameters
control logic for PiM operations
software interface to execute PiM ops.
supervisor for basic system support
Bridge the “system gap” with customizable HW/SW components
rapidly implement PiM techniques,
solve system integration challenges,
analyze end-to-end implementations
in doing so, allow users to

## Slide 16: PiDRAM: Key Components
Hardware
Software
Control PiM operation
Memory controller for
custom timing parameters
Interface for
Applications
Supervisor software
for basic system support
Notes: PiDRAM’s goal is to provide a flexible framework that is useful for studies on commodity DRAM based PiM techniques, such as the ones I described in the previous slides.
[CLICK] To guide our design, we look at the system requirements shared by the PiM techniques that we are interested in.
[CLICK] Then, we develop these key components as customizable modules to provide modularity and enhance the extensibility of PiDRAM
[CLICK] Overall, these components provide a common basis for developers of the framework to implement and enable system support for PiM techniques

## Slide 17: PiDRAM: System Design
Key components attached to a real computing system
Notes: We attach the key components to a real RISC-V based computing system to develop PiDRAM’s system design.
[CLICK] In the system, we implement PiM Operations Controller and PiDRAM memory controller as hardware modules in the hardware system
[CLICK] the custom supervisor software runs on the hardware system
[CLICK] and the extensible software library is used by the supervisor software and runs on the hardware system

## Slide 18: PiDRAM’s FPGA Prototype
Full system prototype on Xilinx ZC706 FPGA board
RISC-V System: In-order, pipelined RISC-V Rocket CPU core, L1D/I$, TLB
PiM-Enabled DIMM (Commodity): Micron MT8JTF12864, 1 GiB, 8 banks
Notes: We develop a prototype of PiDRAM’s full system on a Xilinx ZC706 FPGA board
[CLICK] The RISC-V system comprises an in-order pipelined RISC-V core and level 1 data and instruction caches as well as a translation lookaside buffer
[CLICK] and we enable PIM operations in the DRAM module under the metal cage in the photograph

## Slide 19: RowClone Implementation
Extend the PiDRAM memory controller to support the DRAM command sequence
Expose the operation to pimolib by implementing the copy() PiDRAM instruction
1
2
Only 198 lines of Verilog code
ACT S
PRE
ACT D
ACT S
PRE
ACT D
Standard DRAM Timings
“activate row S, precharge, then activate row D”
“activate row S, then activate row D”
Violated DRAM Timings
Notes: [CLICK] We extend the PiDRAM memory controller with a new state machine that controls the activate precharge activate command sequence
[CLICK] and expose the operation to pimolib by implementing the copy() PiDRAM instruction in the pim operations controller
[CLICK] These modifications take us only 198 lines of Verilog code over PiDRAM’s flexible code base

## Slide 20: RowClone System Integration
Identify two challenges in end-to-end RowClone
1
Memory allocation (intra-subarray operation)
2
Memory coherency (computation in DRAM)
Implement CLFLUSH instruction in the RISC-V CPU Evict a cache block from the CPU caches to the DRAM module
Notes: We then study the challenges in integrating RowClone end-to-end in a real system
[CLICK] The first challenge we identify is proper memory allocation for RowClone operations. Because RowClone operations can only copy data inside a subarray, the data structures must be allocated properly to benefit from fast bulk-data copy operations in DRAM.
[CLICK] The second challenge is maintaining memory coherency. Because data movement, or computation is done inside memory, any cached copies of the data we operate on needs to be evicted and the data must be up to date in DRAM.
[CLICK] To address the second challenge, we implement the CLFLUSH instruction in the RISC-V CPU. This instruction allows us to evict a cache block, given its address as an argument, from CPU caches to the DRAM module. We use CLFLUSH instructions to evict data to DRAM prior to ROwClone operations.
[CLICK] I will now explain the first challenge in more detail

## Slide 21: RowClone Memory Allocation (I)
Memory allocation requirements
Granularity: Operands must occupy DRAM rows fully
1
Notes: We identify three memory allocation requirements for operands of RowClone operations
[CLICK] This is a simplified diagram of a DRAM chip with two banks on two columns and two subarrays (depicted as SA W and SA Z) on two rows.
[CLICK] The first requirement is the granularity requirement. Operands must occupy their DRAM rows fully. Otherwise, RowClone operations may overwrite data on the destination row.

## Slide 22: RowClone Memory Allocation (I)
Memory allocation requirements
Alignment: Operands must be placed at the same offset
2
Notes: The second requirement is called alignment. Operands must be placed at the same offsets in their respective DRAM rows. This is because in-DRAM the operand can be copied to the other operand only if their bits share the same set of sense amplifiers.

## Slide 23: RowClone Memory Allocation (I)
Memory allocation requirements
Mapping: Operands must be placed in the same subarray
3
Notes: The third requirement is called mapping. Because ROwClone operations can only be performed within a DRAM subarray, the operands must be placed or allocated in the same DRAM subarray in the same DRAM bank.

## Slide 24: RowClone Memory Allocation (I)
Memory allocation requirements
Satisfies all three requirements
4
Notes: In contrast to previous operand allocations, the allocation for source four and target four satisfy all three requirements and can be used in RowClone operations.

## Slide 25: RowClone Memory Allocation (II)
Implement a new memory allocation function to overcome the memory allocation challenges
Goal: Allocate virtual memory pages that are mapped to the same DRAM subarray and aligned with each other
virtual_address = alloc_align(int size, int id) size: # of bytes allocated id: allocations with the same id go to the same subarray
alloc_align( 4 KiB, “Subarray 0”)
Subarray Mapping Table
Page Table
1
2
Get physical address pointing to a DRAM row in subarray 0
Update the page table to map virtual address to subarray 0
1
2
Notes: We implement a new memory allocation function in the custom supervisor software to overcome the memory allocation challenges of RowClone
[CLICK] The goal of this function is to allow programmers to allocate virtual memory pages that are mapped to the same DRAM subarray in an aligned way
[CLICK] The key mechanism of our function is to distribute the allocated virtual pages to different banks, but also map the virtual pages to different rows in the same DRAM subarray in those banks.
[CLICK] We implement alloc_align with the semantics I show here. It takes two arguments. The size arguments tells it the amount of data it needs to allocate in bytes, and the id argument is supplied by the programmer to collect data structures that are allocated with different alloc_align calls under the same subarray, such that they can be copied to and from each other.

## Slide 26: RowClone Memory Allocation (II)
Implement a new memory allocation function to overcome the memory allocation challenges
Goal: Allocate virtual memory pages that are mapped to the same DRAM subarray and aligned with each other
virtual_address = alloc_align(int size, int id) size: # of bytes allocated id: allocations with the same id go to the same subarray
alloc_align( 4 KiB, “Subarray 0”)
Subarray Mapping Table
Page Table
1
2
Get physical address pointing to a DRAM row in subarray 0
Update the page table to map virtual address to subarray 0
1
2
https://arxiv.org/abs/2111.00082

## Slide 27: Evaluation: Methodology
Microbenchmarks
CPU-Copy (using LOAD/STORE instructions)
RowClone-Copy (using in-DRAM copy operations) with and without CLFLUSH
Copy/Initialization Heavy Workloads
forkbench (copy)
compile (initialization)
SPEC2006 libquantum: replace “calloc()” with in-DRAM initialization
in-DRAM copy/initialization granularity
Notes: We evaluate the performance of RowClone operations with system support in our PiDRAM prototype.
[CLICK] This table shows the configuration of our prototyped system
[CLICK] We run two sets of microbenchmarks called CPU-Copy and RowClone-Copy. To perform bulk data copy, in the CPU-Copy microbenchmark we execute load and store instructions in the RISC-V core, and in the RowCLone-Copy microbenchmark we execute in-DRAM copy instructions
[CLICK] We estimate the performance improvements provided by RowClone-Copy and Initialization operations using two copy/initialization heavy workloads
[CLICK] and we run the libquantum workload from SPEC2006 end-to-end on our prototype

## Slide 28: Microbenchmark Copy/Initialization Throughput Improvement
In-DRAM Copy and Initialization improve throughput by 119x and 89x, respectively
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 29: CLFLUSH Overhead
CLFLUSH dramatically reduces the potential throughput improvement
Notes: Now I will discuss the overheads of CLFLUSH operations. The plot shows the throughput improvement provided by in-DRAM copy and initialization over CPU-based copy and initialization when we copy 8 megabytes of data and all data is cached. The x-axis shows the proportion of the modified cache blocks among all cache blocks of the data being copied.
[CLICK] We observe that CLFLUSH operations dramatically reduce the potential copy throughput improvement provided by in-DRAM copy operations.

## Slide 30: Other Workloads
forkbench (copy-heavy workload)
compile (initialization-heavy workload)
9% execution time reduction by in-DRAM initialization
  17% of compile’s execution time is spent on initialization
SPEC2006 libquantum
1.3% end-to-end execution time reduction
  2.3% of libquantum’s time is spent on initialization
Performance improvement increases
Notes: I will summarize our results for other workloads in this slide
[CLICK] This plot shows the Speedup provided by rowclone-copy operations for the forkbench workload when the rowclone copy operations are used instead of CPU-based copy operations. The x-axis shows different configurations of the forkbench workload where the number after the hyphen indicates the amount of 4 KiB pages copied after each fork call.
We observe that as the fraction of time spent on copy operations increase, indicated by the blue curve, the speedup provided by RowClone increases, up to 42.9% for the fork-2K configuration
[CLICK] We observe 9% reduction in execution time for the initialization-heavy compile workload, which is expected as compile spends 17% of its execution time on initialization.
[CLICK] Finally, we observe 1.3% end-to-end execution time reduction for libquantum. Similarly this is because in our experiments libquantum spends only 2.3% of its time on bulk data initialization.

## Slide 31: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.
Notes: Maybe not processing using memory but can enable interesting pum workloads

## Slide 32: Recall: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced access latency
Low % chance to fail with reduced access latency
SA
SA
SA
SA
SA
SA
SA
[Kim+ HPCA’19]
Commodity DRAM chips can already perform D-RaNGe
50% chance to fail
Notes: The key idea of D-RaNGe, or the in-DRAM true random number generation technique that we are interested in is to reduce DRAM read access latency below manufacturer-recommended values and exploit the resulting error patterns as true random numbers. I will describe this over a diagram:
[CLICK] This diagram depicts a DRAM bank. We color and size the cells according to their failure probabilities when they are accessed with reduced access latency values.
[CLICK] Red cells fail with a high probability
[CLICK] and green cells fail with a low probability when accessed with reduced latency
[CLICK] D-RaNGe identifies cells that fail with a probability close to 50% and repeatedly accesses these cells with reduced access latency to generate true random numbers in DRAM

## Slide 33: D-RaNGe Implementation
Identify four DRAM cells that fail randomly in a cache block
1 0 1 0 1 0 0 1 0 0
1 0010110100110011101000110101
1
RNG Cell
SA
[Kim+ HPCA’19]
Notes: To implement the D-RaNGe true random number generation technique
[CLICK] We first identify a DRAM cache block that contains four cells with a failure probability of 50% when accessed with a reduced access latency value.
[CLICK] Then, we use these cells to produce true random numbers as accessing them with a reduced access latency will output random values.

## Slide 34: D-RaNGe Implementation
Periodically generate true random numbers by accessing the identified cache block
Reduce access latency
1 KiB random number buffer in POC
Programmers read random numbers from the data register using the rand_dram() function call
190 lines of Verilog code 74 lines of C++ code
Notes: We periodically generate true random numbers by accessing these four cells.
[CLICK] To store the periodically generated random numbers, we implement a one kilobyte random number buffer in the pim operations controller
[CLICK] The programmer reads a random number from the data register using the rand_dram() function call
[CLICK] Modifying PiDRAM to implement D-RaNGe takes us only 190 lines of Verilog and 74 lines of C++ code

## Slide 35: Evaluation
Methodology: Microbenchmark that reads true random numbers
PiDRAM’s D-RaNGe generates true random numbers at 8.30 Mb/s throughput
Notes: To evaluate our implementation of D-RaNGe, we run a microbenchmark that continuously reads true random numbers using the rand_dram() function.
[CLICK] This plot shows the true random number generation throughput we observe. On the x-axis, we show the true random number generation period which we can dynamically configure for PiDRAM’s D-RaNGe implementation.
[CLICK] We observe that our D-RaNGE implementation can generate true random numbers at high throughput.

## Slide 36: PiDRAM Summary
Motivation: Commodity DRAM based PiM techniques improve the performance and energy efficiency of computing systems at no additional DRAM hardware cost
Problem: Challenges of integrating these PiM techniques into real systems are not solved
General-purpose computing systems, special-purpose testing platforms, and system simulators cannot be used to efficiently study system integration challenges
Goal: Design and implement a flexible framework that can be used to:
solve system integration challenges
analyze trade-offs of end-to-end implementations of commodity DRAM-based-PiM techniques
Key idea: PiDRAM, an FPGA-based framework that enables:
system integration studies
end-to-end evaluations of PIM techniques using real unmodified DRAM chips
Evaluation: End-to-end integration of two PiM techniques on PiDRAM’s FPGA prototype
Case Study #1 – RowClone: In-DRAM bulk data copy operations
119x speedup for copy operations compared to CPU-copy with system support
198 lines of Verilog and 565 lines of C++ code over PiDRAM’s flexible codebase
Case Study #2 – D-RaNGe: DRAM-based random number generation technique
8.30 Mb/s true random number generator (TRNG) throughput, 220 ns TRNG latency
190 lines of Verilog and 74 lines of C++ code over PiDRAM’s flexible codebase
PiDRAM: https://github.com/CMU-SAFARI/PiDRAM
Notes: I will start with an executive summary
[CLICK] Commodity DRAM-based PIM techniques improve the performance and energy efficiency of computing systems without incurring any DRAM hardware cost
[CLICK] However, challenges of integrating these techniques into real systems are not yet solved.
[CLICK] Moreover, these challenges cannot be efficiently studied using existing computing systems, special-purpose DRAM testing platforms or system simulators
[CLICK] Our goal is to design and implement a flexible framework that can be used to [CLICK] solve the important system integration challenges and [CLICK] analyze the trade-offs of end-to-end implementations of commodity DRAM based PiM techniques
[CLICK] Our key idea is to develop PiDRAM, an FPGA-based framework that enables such studies using real unmodified DRAM chips
[CLICK] Using our framework, we conduct two case studies on two recent commodity DRAM based PiM techniques on a real FPGA prototype of a full system
[CLICK] In our first case study about in-DRAM bulk data copy operations, we show that in-DRAM data copy operations provide 119 times speedup over CPU-copy operations including system support. To conduct this case study over PiDRAM’s extensible code base, we add only 198 lines of Verilog and only 565 lines of C++ code.
[CLICK] In our second case study about an in-DRAM true random number generation technique, we show that an end-to-end implementation of a DRAM-based true random number generator can provide high throughput true random numbers at low latency. Implementing the true random number generator takes us only 190 additional lines of Verilog and 78 additional lines of C++ code over PiDRAM’s code base.

## Slide 37: PiDRAM is Open Source
https://github.com/CMU-SAFARI/PiDRAM
Notes: PiDRAM is openly and freely available on Github. If you are interested in PiDRAM, please use it and feel free to contribute to it.

## Slide 38: Extended Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 39: Long Talk + Tutorial on Youtube
https://youtu.be/s_z_S6FYpC8
Notes: I also describe PiDRAM in more detail and give a tutorial on how to use our framework in this SAFARI live seminar talk.

## Slide 40: PiDRAM An FPGA-based Framework for End-to-end Evaluation of Processing-in-DRAM Techniques
Ataberk Olgun
Juan Gomez Luna
Konstantinos Kanellopoulos
Hasan Hassan
Behzad Salami
Oğuz Ergin
Onur Mutlu

## Slide 41: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu

## Slide 42: Factors Affecting DRAM Reliability and Latency
We need to perform experimental studies
of real DRAM chips
DRAM timing violation
Inter-cell interference
Voltage
Temperature
Manufacturing process
Factors affecting DRAM reliability and latency cannot be properly modeled in simulation or analytically

## Slide 43: DRAM Testing Infrastructure
Allow experimental studies of real DRAM chips
Open-source FPGA-based testing infrastructure
Publicly-available: Start using today
Relatively low cost: An FPGA board + DRAM modules
SoftMC
Litex Tester

## Slide 44: Limitations of Existing Infrastructure
Impose restrictions on the DDR4 interface.
Restrictions limit various characterization experiments.
Difficult to set up (based on discontinued HW/SW) and use (require developing HW)
Monolithic hardware design makes extensions (new standards, prototypes) relatively difficult
Notes: They have several limitations that make it difficult to use them as flexible, accessible, extensible platforms.

## Slide 45: DRAM Bender: Design Goals
Flexibility
  Ability to test any DRAM operation
  Ability to test any combination of DRAM operations and custom timing parameters
Ease of use
  Simple programming interface (C++)
  Minimal programming effort and time
  Accessible to a wide range of users
    who may lack experience in hardware design
Extensibility
  Modular design
  Well-defined interfaces between hardware modules

## Slide 46: DRAM Bender: Overview
Publicly-available FPGA-based DDR4/3 (and HBM2) characterization infrastructure
Easily programmable using the DRAM Bender C++ API
[Yaglikci+, DSN’22]

## Slide 47: DRAM Bender: Prototypes
Five out of the box FPGA-based prototypes

## Slide 48: DRAM Bender: Three Case Studies
RowHammer: Interleaving Pattern of Activations
  Interleaving pattern significantly affects the number of RowHammer bitflips
RowHammer: Random Data Patterns
  Use 512-bit random data patterns
  Uncover more bitflips than 8-bit SoftMC random patterns
In-DRAM Bitwise Operations
  Demonstrate in-DRAM bitwise AND/OR capability in real DDR4 chips
DRAM Bender is flexible: supports many different types of experiments

## Slide 49: DRAM Bender: Ease of Use
RowHammer: Interleaving Pattern of Activations
Easy to devise new experiments to uncover new insights.
one iteration of the RowHammer test
Easily programmable using the DRAM Bender C++ API

## Slide 50: More in the paper (II)
DRAM Bender design details
  DRAM Bender instruction set architecture
  Hardware & software modules
  Prototype design
  Temperature controller setup
DRAM Bender application programming interface
Detailed results for three case studies
Future work & improvements

## Slide 51: More in the paper (II)
https://arxiv.org/abs/2211.05838

## Slide 52: Research DRAM Bender Enabled
[HPCA’25] Olgun+, “Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance“
[HPCA’25] Tugrul+, “Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[DSN’24] Olgun+, “Read Disturbance in High Bandwidth Memory: A Detailed Experimental Study on HBM2 DRAM Chips”
[DSN’24] Yuksel+, “Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis”
[DSN’24 Disrupt] Luo+, “An Experimental Characterization of Combined RowHammer and RowPress Read Disturbance in Modern DRAM Chips”
[HPCA’24] Yaglikci+, ”Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[HPCA’24] Yuksel+, “Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis"
[ISCA’23] Luo+, “RowPress: Amplifying Read Disturbance in Modern DRAM Chips”
[DSN’23 Disrupt] Olgun+, ”An Experimental Analysis of RowHammer on HBM2 DRAM Chips”
[arXiv Preprint, 2023] Orosa+, ”SpyHammer: Using RowHammer to Remotely Spy on Temperature”
[MICRO’22] Yaglikci+, “HIRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips”
[DSN’22] Yaglikci+, “Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices”
[MICRO’21] Orosa+, “A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses”
[MICRO’21] Hassan+, “Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications”
[ISCA’21] Olgun+, “QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips”

## Slide 53: More Research DRAM Bender Enabled
[ISCA’21] Orosa+, “CODIC: A Low-Cost Substrate for Enabling Custom In-DRAM Functionalities and Optimizations”
[ISCA’20] Kim+, “Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques”
[S&P’20] Frigo+, “TRRespass: Exploiting the Many Sides of Target Row Refresh”
[HPCA’19] Kim+, “D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput”
[MICRO’19] Koppula+, “EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM”
[SIGMETRICS’18] Ghose+, “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study”
[SIGMETRICS’17] Chang+, “Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms”
[MICRO’17] Khan+, “Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content”
[SIGMETRICS’16] Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization”

## Slide 54: Even More Research DRAM Bender Enabled
[ISCA’24] Nam+, ”DRAMScope: Uncovering DRAM Microarchitecture and Characteristics by Issuing Memory Commands”
[DATE’24] Zhou+, “DRAM-Locker: A General-Purpose DRAM Protection Mechanism Against Adversarial DNN Weight Attacks”
[DRAMSec’23] Lang+, “BLASTER: Characterizing the Blast Radius of Rowhammer”
[IEEE CAL’23] Nam+ ”X-ray: Discovering DRAM Internal Structure and Error Characteristics by Issuing Memory Commands”
[MICRO’22] Gao+, “FracDRAM: Fractional Values in Off-the-Shelf DRAM”
[Applied Sciences’22] Bepary+, “DRAM Retention Behavior with Accelerated Aging in Commercial Chips”
[ETS’21] Farmani+, “RHAT: Efficient RowHammer-Aware Test for Modern DRAM Modules”
[HOST’20] Talukder+, “Towards the Avoidance of Counterfeit Memory: Identifying the DRAM Origin”
[MICRO’19] Gao+, “ComputeDRAM: In-Memory Compute Using Off-the-Shelf DRAMs”
[IEEE Access’19] Talukder+, “PreLatPUF: Exploiting DRAM Latency Variations for Generating Robust Device Signatures”
[ICCE’18] Talukder+, “Exploiting DRAM Latency Variations for Generating True Random Numbers”
Notes: SoftMC has also contributed to research from other research groups.

## Slide 55: DRAM Chips Are Already (Quite) Capable!
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18736.pdf

## Slide 56: DRAM Chips Are Already (Quite) Capable!
Appears at DSN 2024
https://arxiv.org/pdf/2405.06081

## Slide 57: The Capability of COTS DRAM Chips
57
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 58: Finding: SiMRA Across Subarrays
36ns
58
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Activating two rows in quick succession
can simultaneously activate
multiple rows in neighboring subarrays
Neighboring Subarrays
Subarray X
Subarray Y
Row A
Row B
DRAM Bank
Shared Sense Amplifiers
14ns
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate multiple rows in neighboring subarrays
[CLICK] You may remember this pictorial example where Subarray X and Subarray Y are neighbor subarrays and Row A is in Subarray X and Row B is in Subarray Y.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT, we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate multiple rows at once in neighboring subarrays

## Slide 59: Key Idea: NOT Operation
59
Connect rows in neighboring subarrays
through a NOT gate by simultaneously activating rows
SA
A
src
dst
ACT src
ACT dst
SA
A
src
dst
SA
A
src
dst
~A
NOT gate
Notes: Our key idea is to leverage the connection between neighboring subarrays,
[CLICK] the NOT gate in the sense amplifier.
[CLICK] By simultaneously activating rows in neighboring subarrays, we can connect these rows through a NOT gate
[CLICK] As an example, source and destination in neighboring subarrays and if we first activate src
[CLICK] and then activate destination, this result in sense amplifier to drive the negated src value to the dst

## Slide 60: Key Idea: NAND, NOR, AND, OR
60
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in X and Y and the bitline at the top subarray becomes the function of voltages in A and B
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 61: Two-Input AND and NAND Operations
61
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
VDD
VDD/2*
Notes: Now let me show you the basic intuition to perform two-input AND and NAND operations.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2 as a side note we store VDD/2,using FracDRAM’s technique.
[CLICK] and in the compute subarray we have X and Y.
With this setup, if we activate all these four cells
[CLICK] using ACT-PRE-ACT sequence, we will get AND of X and Y in the compute subarray and NAND of X and Y in the reference subarray.
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half.
Now let me prove that that is the case. I am going to cover all combinations of X and Y values.

## Slide 62: Two-Input AND and NAND Operations
VDD=1 & GND = 0
X
Y
COM
0
0
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
62
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
GND
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
Notes: In the first row of truth table, X and Y are GND.
[CLICK] This results in bitline in the compute subarray to be GND and the reference bitline is 3 vdd over 4.
[CLICK] Sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than GND, reference cells store VDD and compute cells store GND

## Slide 63: Two-Input AND and NAND Operations
VDD=1 & GND = 0
63
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
0
1
0
0
0
1
Notes: In the second row of truth table, X is GND and Y is VDD
[CLICK] As the bitline voltage in compute subarray is lower than reference subarray’s bitline voltage
[CLICK] reference cells store VDD and compute cells store GND

## Slide 64: Two-Input AND and NAND Operations
VDD=1 & GND = 0
64
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
sense amp.
compares
the voltages on the bitlines
VDD
GND
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
1
0
0
1
0
0
0
1
0
1
0
1
Notes: In the third row of truth table, X is VDD and Y is GND
[CLICK] This results in bitline in the compute subarray to be VDD half and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than vdd half, reference cells store VDD and compute cells store GND

## Slide 65: Two-Input AND and NAND Operations
VDD=1 & GND = 0
65
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
GND
VDD
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1
Notes: In the last row of truth table, X and Y are both VDD
[CLICK] This results in bitline in the compute subarray to be VDD and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference. However, this time compute subarray’s bitline is greater than. As a results reference cells store GND and compute cells store VDD
Consequently, this example shows compute subarray stores the result of the and operation of X and Y. and reference subarray cells store the result of the nand of operation of X and Y.

## Slide 66: Two-Input AND and NAND Operations
VDD=1 & GND = 0
66
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1

## Slide 67: Many-Input AND, NAND, OR, and NOR Operations
VDD=1 & GND = 0
X
Y
AND
0
0
0
0
1
0
1
0
0
1
1
1
NAND
1
1
1
0
67
Reference Subarray (REF)
Compute Subarray (COM)
VDD/2
VDD
X
Y
ACT REF
PRE
ACT COM
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
We can express AND, NAND, OR, and NOR operations
by carefully manipulating the reference voltage
(More details in the paper)
https://arxiv.org/pdf/2402.18736.pdf
Notes: By carefully choosing the voltage levels of the cells in the reference subarray, we can express many-input AND, NAND, OR, and NOR operations
[CLICK] As our time is limited, please check our paper for more details.

## Slide 68: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
68
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 69: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
69
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 70: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
70
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations
Success rate is the number of correctly performed bitwise operations

## Slide 71: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
16-input AND, NAND, OR, and NOR operations
with very high success rate (>94%)
71
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 72: Impact of Data Pattern
72
1.98% variation in average success rate
across all number of input operands
Notes: Our second analysis the impact of data pattern
[CLICK] This plot depicts the effect of data pattern on the NOR operation’s success rate: x-axis shows the number of input operands and y-axis shows the success rate distribution and hue shows the tested data patterns: either all 1s/0s in a row and random data pattern.
[CLICK] We observe a 1.97% variation in average success rate across all tested number of input operands

## Slide 73: Impact of Data Pattern
73
Impact of data pattern is consistent
across all tested operations
Notes: Here we show AND, NAND, OR, and NOR operations and
[CLICK] We observe that the impact of data pattern is consistent across all tested operations

## Slide 74: Impact of Data Pattern
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
74
Notes: Our takeaway from this experiment is data pattern slightly affects the reliability of AND, NAND, OR, and NOR operations.

## Slide 75: More in the Paper
Detailed hypotheses & key ideas to perform
  NOT operation
  Many-input AND, NAND, OR, and NOR operations
How the reliability of bitwise operations are affected by
  The location of activated rows
  Temperature (for AND, NAND, OR, and NOR)
  DRAM speed rate
  Chip density and die revision
Discussion on the limitations of COTS DRAM chips
75
Notes: You can find the following in the paper
[CLICK] The key ideas and hypotheses on how a COTS DRAM chip is capable of performing these operations
[CLICK] How the reliability of tested operations are affected by: Spatial Variation, more temperature results, DRAM Speed Rate and Chip density and Die revision
[CLICK] And what are the limitations that we face in off-the-shelf DRAM chips and a broad discussion on this topic

## Slide 76: Available on arXiv
https://arxiv.org/pdf/2402.18736.pdf
76
Notes: The extended version of our study is available on arxiv

## Slide 77: Summary
We experimentally demonstrate that commercial off-the-shelf (COTS) DRAM chips can perform:
  Functionally-complete Boolean operations: NOT, NAND, and NOR
  Up to 16-input AND, NAND, OR, and NOR operations
We characterize the success rate of these operations on 256 COTS DDR4 chips from two major manufacturers
We highlight two key results:
  We can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations on COTS DRAM chips with very high success rates (>94%)
  Data pattern and temperature only slightly affect the reliability of these operations
77
We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate

## Slide 78: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 79: Executive Summary
Experimental Study: 120 DDR4 chips from two major manufacturers
COTS DRAM chips can perform MAJ5, MAJ7, and MAJ9 operations and copy one DRAM row to up to 31 different rows at once
Storing multiple redundant copies of MAJ’s input operands (i.e., input replication) drastically increases robustness (>30% higher success rate)
Operating conditions (temperature, voltage, and data pattern) affect the robustness of in-DRAM operations (by up to 11.52% success rate)
Goal: To experimentally analyze and understand
The computational capability of COTS DRAM chips beyond that of prior works
The robustness of such capability under various operating conditions
Motivation:
Processing-Using-DRAM (PUD) alleviates data movement bottlenecks
Commercial off-the-shelf (COTS) DRAM chips can perform three-input majority (MAJ3) and in-DRAM copy operations
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: Let’s start with an executive summary
[CLICK] Processing-Using-DRAM is a promising paradigm to alleviate performance and energy overheads caused by frequent data movement between main memory and processing unit
[CLICK] Prior works show that off-the-shelf DRAM chips are capable of performing three-input majority and in-DRAM copy operations
[CLICK] In this study, our goal is to experimentally analyze and understand the computational capability of off-the-shelf DRAM chips beyond what prior works have demonstrated
[CLICK] and the robustness of such capability under various operating conditions
[CLICK] To this end, we conduct our experimental study on 120 DDR4 DRAM chips from two major manufacturers and
[CLICK] We show that off-the-shelf DRAM chips can perform MAJ5, MAJ7, and MAJ7 operations and copy one row’s content to up to 31 different rows simultaneously
[CLICK] We show that storing multiple redundant copies of majority operations’ input operands drastically increases robustness, more than 30% increase in success rate, which is our robustness metric
[CLICK] Finally, we observe that operating conditions (such as temperature, voltage, and data pattern) can affect the robustness of in-DRAM operations by up to 11.52% on average
[CLICK] Our work is artifact evaluated and fully open sourced, you can access our repository from this link here
-----
Whitespace is broken

## Slide 80: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: By leveraging simultaneous many-row activation, we can
[CLICK] Perform majority operations with more than three inputs
[CLICK] We can increase the robustness of majority operations
[CLICK] And we can copy one row’s content to multiple rows

## Slide 81: In-DRAM Multiple Row Copy (Multi-RowCopy)
d
s
t
r
c
s
Simultaneously activate many rows to copy one row’s content to multiple destination rows
d
s
t
s
r
c
RowClone
s
r
c
r
c
s
s
r
c
d
s
t
d
s
t
d
s
t
Multi-RowCopy
s
r
c
s
r
c
s
r
c
[Seshadri+ MICRO’13]
Notes: [CLICK] Our key idea is since we can activate many rows simultaneously, we can copy one row’s content to other simultaneously activated rows
[CLICK] Let’s recall the RowClone example where we copy source to destination
[CLICK] In RowClone, we first activate the source row which will copy its content to sense amplifiers
[CLICK] And then, we activate destination row to drive the sense amplifier’s content to destination row
[CLICK] In our mechanism, which we call Multi-RowCopy, we have several destination rows
[CLICK] Here we activate many destination rows simultaneously
[CLICK] and thus sense amplifier drives its content to these destination rows.

## Slide 82: Key Takeaways from Multi-RowCopy
COTS DRAM chips are capable of copying one row’s data to 1, 3, 7, 15, and 31 other rows at very high success rates
Key Takeaway 1
Multi-RowCopy in COTS DRAM chips is highly resilient to changes in data pattern, temperature, and wordline voltage
Key Takeaway 2
Notes: Our analysis provides two key takeaway lessons:
[CLICK] First, off-the-shelf DRAM chips are capable of copying one row’s data to 1, 3, 7, 15, and 31 other rows at very high success rates
[CLICK] Multi-RowCopy in COTS DRAM chips is highly resilient to changes in data pattern, temperature, and wordline voltage

## Slide 83: Robustness of Multi-RowCopy
COTS DRAM chips can copy one row’s content to up to 31 rows with a very high success rate
Average: >99.98%
Notes: Now let me show you the first result
[CLICK] In this plot, y-axis shows the success rate
[CLICK] x-axis shows the number of destination rows from 1 to 31
[CLICK] And we plot the success rate distribution as a box-and-whiskers plot
[CLICK] We observe that the average success rate is higher than 99.98% across all tested number of destination rows
[CLICK] Hence, we conclude that off-the-shelf DRAM chips can copy one row’s content to up to 31 rows with a very high success rate

## Slide 84: Impact of Data Pattern
Data pattern has a small effect on the success rate of the Multi-RowCopy operation
At most 0.79% decrease in average success rate
Notes: Now let’s analyze the impact of data pattern
[CLICK] We plot the average success rate for each number of destination rows and show the trend using a lineplot. Each colered line represent a different data pattern
[CLICK] We observe that data pattern decreases the average success rate at most by 0.79%
[CLICK] We conclude that data pattern has a small effect on the success rate

## Slide 85: Also in the Paper: Impact of Temperature & Voltage
Increasing temperature up to 90◦C has a very small effect on the success rate of the Multi-RowCopy operation
Reducing the wordline voltage
only slightly affects the success rate of the Multi-RowCopy operation
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V

## Slide 86: More in the Paper
Detailed hypotheses and key ideas on
    Hypothetical row decoder circuitry
    Input Replication
More characterization results
    Power consumption of simultaneous many-row activation
    Effect of timing delays between ACT-PRE and PRE-ACT commands
    Effect of temperature and wordline voltage
Circuit-level (SPICE) experiments for input replication
Potential performance benefits of enabling new in-DRAM operations
    Majority-based computation
    Content destruction-based cold-boot attack prevention
Discussions on the limitations of tested COTS DRAM chips
Notes: We have more content in the paper, including
…

## Slide 87: Available on arXiv
https://arxiv.org/pdf/2405.06081
Notes: The extended version of our study is available on arxiv

## Slide 88: Our Work is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: And our work is artifact evaluated and got every badges
[CLICK] You can download our code from github and start testing right away!

## Slide 89: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 90: DRAM Bender Summary
DRAM Bender
The first publicly-available DDR4 characterization infrastructure
github.com/CMU-SAFARI/DRAMBender
[Yaglikci+, DSN’22]
Flexible and Easy to Use
Source code available:
DRAM Bender enables many studies, ideas, and methodologies in the design of future memory systems
Notes: [CLICK] In summary, SoftMC is the first publicly-available DRAM characterization infrastructure
[CLICK] It is flexible and easy to use
[CLICK] The source code of SoftMC is available on GitHub
[CLICK] SoftMC enables many new studies, ideas, and methodologies in the design of future memory systems

## Slide 91: DRAM Bender Paper, Slides, Videos, Code
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 92: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu

## Slide 93: BACKUP SLIDES

## Slide 94: Accessing a DRAM Cell
Sense Amp
enable
bitline
wordline
capacitor
access transistor
[Seshadri+ MICRO’17]
Notes: Here is how we access this DRAM cell. This is a diagram showing how a DRAM cell is connected to a sense amplifier.
[CLICK] A DRAM cell contains two components, the capacitor stores data and the access transistor determines if the cell is being accessed.
[CLICK] The access transistor is controlled by the wordline, which is enabled to
[CLICK] connect the DRAM cell to its bitline
[CLICK] The bitline bar is esentially the inverse of the bitline
[CLICK] The DRAM sense amplifier has an enable signal which determines if the sense amplifier is currently active.

## Slide 95: Accessing a DRAM Cell
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
½ VDD
VDD
enable wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell charge restored
Sense Amp
deviation in bitline voltage
[Seshadri+ MICRO’17]
1
2
3
4
5
6
Notes: Initially, both the access transistor and the sense amplifier are disabled and both ends of the sense amplifier are maintained at half vdd. In this example, the capacitor is fully charged. To access the cell
[CLICK] we first enable the wordline, [CLICK] this connects the capacitor to its bitline.
[CLICK] Since the capacitor has a voltage level higher than the bitline, the charge starts flowing from the capacitor to the bitline, [CLICK] resulting in the bitline voltage to deviate slightly towards Vdd.
[CLICK] When we enable the sense amplifier, it will compare the voltage levels of bitline and bitline bar, and [CLICK] amplify the deviation until bitline voltage reaches Vdd.
[CLICK] Since the capacitor is still connected to the bitline, the amplification process also restores the charge in the capacitor.

## Slide 96: alloc_align() function
SubArray Mapping Table (SAMT) enables alloc_align()
SAMT
Subarray 0
Subarray 1
Subarray N
…
SAMT Entry
Physical addresses of DRAM rows
alloc_align( 4 KiB, “Subarray 0”)
SAMT
Page Table
1
2
Retrieve a physical address pointing to a DRAM row in subarray 0
Update the page table to map programmer-allocated address to subarray 0
1
2
Notes: We implement a key structure in the supervisor software called subarray mapping table, to enable alloc_align().
[CLICK] SAMT is organized as a table of entries per DRAM subarray
[CLICK] Each SAMT entry contains a list of physical addresses that point to the DRAM rows in that subarray
[CLICK] An example alloc align call to allocate four kibs of data in subarray 0 [CLICK] accesses SAMT to retrieve a physical address pointing to a DRAM row in subarray 0, and then [CLICK] updates the page table to map the virtual address allocated for the programmer to subarray 0
This way, we allocate different virtual pages to the same DRAM subarray, such that we can use in-DRAM copy operations to copy data from and to these pages

## Slide 97: Initializing SAMT
SAMT
Subarray 0
Subarray 1
Subarray N
…
SAMT Entry
Physical addresses of DRAM rows
?
Perform in-DRAM copy using every DRAM row address as source and destination rows
If the in-DRAM copy operation succeeds source and destination rows are in the same subarray
Notes: [CLICK] To find physical addresses of the DRAM rows that map to a subarray,
[CLICK] We perform an experiment in our prototype where we try to copy data in-DRAM from every row address to every other row address.
[CLICK] We conclude that if the operation succeeds, the source and the destination row addresses we used must belong in the same subarray.
[CLICK] Please read our full paper in arXiv for more details on how our allocation mechanism works

## Slide 104: PiM Operations Controller (POC)
Decode & execute PiDRAM instructions (e.g., in-DRAM copy)
Receive instructions over memory-mapped interface
Simple interface to the PiDRAM memory controller (i) send request, (ii) wait until completion, (iii) read results
Notes: The PiM Operations Controller
[CLICK] decodes and executes PiDRAM instructions to perform PiM operations
[CLICK] It is connected to the hardware system as a memory mapped module, meaning that it receives the PiDRAM instructions over the memory bus from the RISC-V CPU core. The three registers, depicted as instruction, flag, and data registers in the figure are accessible over the memory bus. This makes it easy to port PiM operations controller to another system that uses a different CPU ISA.
[CLICK] PiM operations controller communicates with the PiDRAM memory controller over a simple interface where it sends a request for a PiM operation to the memory controller, waits until the operation is complete, and reads the results from the memory controller to perform a PiM operation.

## Slide 105: PiDRAM Memory Controller
Perform PiM operations by violating DRAM timing parameters
Support conventional memory operations (e.g., LOAD/STORE) One state machine per operation (e.g., LOAD/STORE, in-DRAM copy)
Easily replicate a state machine to implement a new operation
Controls the physical DDR3 interface Receives commands from command scheduler & operates DDR3 pins
Notes: The PiDRAM memory controller performs PiM operations by using timing parameters smaller than manufacturer-recommended values.
[CLICK] The command scheduler supports conventional memory operations like stores and loads. We implement one state machine in its command scheduler to control the execution per each memory operation. [CLICK] This makes PiDRAM memory controller easy to extend to support new PiM operations or new DRAM commands by replicating the state machines.
[CLICK] The physical interface controls the physical signals on the DDR3 interface. It receives DRAM commands from the command scheduler and drives the DDR3 interface signals.

## Slide 106: PiM Operations Library (pimolib)
Contains customizable functions that interface with the POC Software interface for performing PiM operations
Executes LOAD & STORE requests to communicate with the POC
Notes: The PiM operations library or pimolib encapsulates customizable functions that interface with the pim operations controller to perform pim operations. We expose the PIM functionality to software using pimolib.
[CLICK] To perform a PiM operation, a typical function in pimolib executes LOAD&STORE requests to access the memory mapped registers of the Pim operations controller
I will later describe the communication protocol that pimolib obeys while communicating with the pim operations controller

## Slide 107: Custom Supervisor Software
Exposes PiM operations to the user application via system calls
Contains the necessary OS primitives to develop end-to-end PiM techniques (e.g., memory management and allocation for RowClone)
Notes: The last component, custom supervisor software, exposes PiM oeprations to user applications via system calls
[CLICK] We implement the necessary OS primitivies to develop end-to-end PiM techniques in the custom supervisor software such as memory management and allocation for in-DRAM copy or RowClone operations)

## Slide 108: PiM Operation Execution Flow
Copy() function called by the user to perform a RowClone-Copy operation in DRAM
1
Application makes a system call: Copy(A, B, N bytes)
2
Custom Supervisor Software calls the Copy() pimolib function
Copy (S, D)
S: source DRAM row
D: destination DRAM row
Notes: I will describe the execution flow for a PiM operation in our PiDRAM framework
As an example, we will look at what happens when the user calls the copy() function to perform an in-DRAM copy operation
[CLICK] The user first makes a system call to the copy function to copy N bytes from array A to array B
[CLICK] The custom supervisor software find the physical addresses corresponding to arrays A and B, and then calls the copy() function in the pimolib with the semantics that I show here
[CLICK] It takes two arguments, S is the address of the source DRAM row, and D is the address of the destination DRAM row

## Slide 109: PiM Operation Execution Flow
3
Copy(S, D) executes two store instructions in the CPU
4
The first store updates the instruction register with Copy(S, D)
5
The second store sets the “Start” flag in the flag register
1
Start (S)
Start the execution of PiM operation
Notes: The Copy function executes two store instrutions in the CPU
[CLICK] The first store instruction updates the instruction register with a PiDRAM instruction that instructs the Pim operations controller to perform in-DRAM copy from row S to row D
[CLICK] The second store instruction sets the start flag in the flag register [CLICK] to initiate the PiM operation

## Slide 110: PiM Operation Execution Flow
6
POC instructs the memory controller to perform RowClone
7
POC resets the “Start” flag, and sets the “Ack” flag
8
PiDRAM memory controller issues commands with violated timing parameters to the DDR3 module
Notes: When the start flag is set, the Pim operations controller instructs the memory controller to perform an in-DRAM copy operation from row S to row D
[CLICK] When the memory controller acknowledges the Pim operations controller’s request, the Pim operations controller resets the start flag and sets the ack. flag. This indicates that the PiDRAM memory controller has started executing the last valid PiM operation.
[CLICK] To execute the PiM operation, the PiDRAM memory controller issues DRAM commands with violated timing parameters to the DDR3 module

## Slide 111: PiM Operation Execution Flow
9
The memory controller sets the “Fin.” flag
10
Copy(S, D) periodically checks either “Ack” or “Fin.” flags using LOAD instructions
Copy(S, D)returns when the periodically checked flag is set
Notes: When the memory controller issues the last DRAM command to perform the operation, it sets the Fin. Flag. This indicates that the memory controller has finished executing the last valid PiM operation
[CLICK] The pimolib copy function periodically checks either the ACK or the FIN flags, based on a user-specified argument, to block until either the start or the end of the PiM operation. [CLICK] In other words, the pimolib function returns when either the ACK or the FIN flag is set.

## Slide 112: PiM Operation Execution Flow
Data Register is not used in RowClone operations because the result is stored in memory
It is used to read true random numbers generated by D-RaNGe
Notes: In this example, we did not make use of the data register in the pim operations controller. This register was not useful because the in-DRAM copy operation’s result is already stored in memory.
[CLICK] However, we use this register in our in-DRAM true random number generator implementation in which case the random number generation function in the pimolib accesses the data register using LOAD instructions

## Slide 113: PiDRAM Components Summary
Four key components orchestrate PiM operation execution
Notes: [CLICK] In short, we implement four key components that together orchestrate the execution of PiM operations.