## Slide 1
Dr. Juan Gómez Luna
Professor Onur Mutlu
Processing-Near-Memory
Real PNM Architectures
Programming General-purpose PIM
HPCA 2023 Tutorial
Real-world Processing-in-Memory Architectures
Sunday, February 26, 2023

## Slide 2: Two PIM Approaches
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021. [Tutorial Video on "Memory-Centric Computing Systems" (1 hour 51 minutes)]
https://people.inf.ethz.ch/omutlu/pub/ModernPrimerOnPIM_springer-emerging-computing-bookchapter21.pdf

## Slide 3: PIM Becomes Real
UPMEM, founded in January 2015, announces the first real-world PIM architecture in 2016
UPMEM’s PIM-enabled DIMMs start getting commercialized in 2019
In early 2021, Samsung announces FIMDRAM at ISSCC conference
Samsung’s LP-DDR5 and DIMM-based PIM announced a few months later
In early 2022, SK Hynix announces AiM and Alibaba announces HB-PNM at ISSCC conference
https://www.eenewsautomotive.com/news/startup-plans-embed-processors-dram-0#

## Slide 4: UPMEM PIM

## Slide 5: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/
CPU
(x86, ARM, RV…)
DDR
Data bus

## Slide 6: UPMEM DIMMs
E19: 8 chips/DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips/DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 7: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 8: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 9: UPMEM Patent
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 10: UPMEM PIM System Organization (I)
FIG. 1 schematically illustrates a computing system comprising DRAM circuits having integrated processors according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 11: UPMEM PIM System Organization (II)
In a UPMEM-based PIM system UPMEM DIMMs coexist with regular DDR4 DIMMs
Notes: P21 DIMMs.
DPUs cannot be shared. There is a large number of DPUs.
No need for OS.
This simplifies security implications. No side channels.

## Slide 12: UPMEM PIM System Organization (III)
A UPMEM DIMM contains 8 or 16 chips
  Thus, 1 or 2 ranks of 8 chips each
Inside each PIM chip there are:
  8 64MB banks per chip: Main RAM (MRAM) banks
  8 DRAM Processing Units (DPUs) in each chip, 64 DPUs per rank

## Slide 13: DRAM Processing Unit (I)
FIG. 4 schematically illustrates part of the computing system of FIG. 1 in more detail according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 14: DRAM Processing Unit (II)

## Slide 15: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 16: Fine-grained Multithreading

## Slide 17: Fine-Grained Multithreading (I)
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 18: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependence latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964
Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978

## Slide 19: Lecture on Fine-Grained Multithreading
https://www.youtube.com/watch?v=6e5KZcCGBYw&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN&index=16

## Slide 20: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 21: DPU Instruction Set Architecture
Specific 32-bit ISA
  Aiming at scalar, in-order, and multithreaded implementation
  Allowing compilation of 64-bit C code
  LLVM/Clang compiler
https://sdk.upmem.com/2021.2.0/201_IS.html#

## Slide 22: Microbenchmark for INT32 ADD Throughput
C-based code
Compiled code (UPMEM DPU ISA)
1 #define SIZE 256
2 int* bufferA = mem_alloc(SIZE * sizeof(int));
3 for(int i = 0; i < SIZE; i++){
4 int temp = bufferA[i];
5 temp += scalar;
6 bufferA[i] = temp;
7 }
1 move r2, 0
2 .LBB0_1: // Loop header
3 lsl_add r3, r0, r2, 2 // Address calculation
4 lw r4, r3, 0 // Load from WRAM
5 add r4, r4, r1 // Add
6 sw r3, 0, r4 // Store to WRAM
7 add r2, r2, 1 // Index update
8 jneq r2, 256, .LBB0_1 // Conditional jump

## Slide 23: More on the UPMEM PIM Architecture
https://youtu.be/6dwV_RBjK2c
https://youtu.be/myG-H_8oN8A

## Slide 24: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 25: Key Takeaway 1
Chart: Operational Intensity (OP/B)
Memory-bound region
Compute-bound region
The throughput saturation point is as low as ¼ OP/B,
i.e., 1 integer addition per every 32-bit element fetched
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound.
As a result, the most suitable workloads are memory-bound.

## Slide 26: CPU/GPU: Performance Comparison
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY OBSERVATION
The UPMEM-based PIM system can outperform a state-of-the-art GPU on workloads with three key characteristics:
Streaming memory accesses
No or little inter-DPU synchronization
No or little use of integer multiplication, integer division, or floating point operations
These three key characteristics make a workload potentially suitable to the UPMEM PIM architecture.

## Slide 27: Key Takeaway 2
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 2
The most well-suited workloads for the UPMEM PIM architecture use no arithmetic operations or use only simple operations (e.g., bitwise operations and integer addition/subtraction).

## Slide 28: Key Takeaway 3
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 3
The most well-suited workloads for the UPMEM PIM architecture require little or no communication across DPUs (inter-DPU communication).

## Slide 29: Key Takeaway 4
KEY TAKEAWAY 4
• UPMEM-based PIM systems outperform state-of-the-art CPUs in terms of performance (by 23.2× on 2,556 DPUs for 16 PrIM benchmarks) and energy efficiency on most of PrIM benchmarks.
• UPMEM-based PIM systems outperform state-of-the-art GPUs on a majority of PrIM benchmarks (by 2.54× on 2,556 DPUs for 10 PrIM benchmarks), and the outlook is even more positive for future PIM systems.
• UPMEM-based PIM systems are more energy-efficient than state-of-the-art CPUs and GPUs on workloads that they provide performance improvements over the CPUs and the GPUs.

## Slide 30: PrIM Repository
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 31: Samsung FIMDRAM (aka HBM-PIM)

## Slide 32: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 33: Samsung Function-in-Memory DRAM (2021)

## Slide 34: Samsung Function-in-Memory DRAM (2021)

## Slide 35: FIMDRAM: System Organization
PIM units respond to standard DRAM column commands (RD or WR)
  Compliant with unmodified JEDEC controllers
They execute one wide-SIMD operation commanded by a PIM instruction with deterministic latency in a lock-step manner
A PIM unit can get 16 16-bit operands from IOSAs, a register, and/or the result bus
Lee et al., Hardware Architecture and Software Stack for PIM Based on Commercial DRAM Technology, ISCA 2021

## Slide 36: Lecture on FIMDRAM/HBM-PIM
https://youtu.be/_CpWJGK9N04

## Slide 37: Samsung AxDIMM

## Slide 38: Samsung AxDIMM (2021)
DIMM-based PIM
  DLRM recommendation system
Baseline System
AxDIMM System
Ke et al. "Near-Memory Processing in Action: Accelerating Personalized Recommendation with AxDIMM", IEEE Micro (2021)

## Slide 39: AxDIMM Design: Hardware Architecture
DDR4 slave PHY receives DRAM commands and NMP instructions
(via DQ pins) from the host side

## Slide 40: AxDIMM Design: Execution Flow

## Slide 41: Lecture on AxDIMM
https://youtu.be/J_prUKfnv7Q

## Slide 42: SK Hynix AiM

## Slide 43: SK Hynix Accelerator-in-Memory (2022)
https://news.skhynix.com/sk-hynix-develops-pim-next-generation-ai-accelerator/

## Slide 44: SK Hynix Accelerator-in-Memory (2022)
4 Gb AiM die with 16 processing units (PUs)
Lee et al., A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications, ISSCC 2022
Notes: * The operating voltage is 1.25V: - Lowered from 1.35V of the normal GDDR6, for bank parallel operation.
* 16Gb/s is reached at 1.25V in DL operation.
Flat-lid package for lower thermal resistance.
Tested in a prototype system with an FPGA (connected to host CPU via PCIe).

## Slide 45: SK Hynix AiM: System Organization (2022)
GDDR6-based AiM architecture
Lee et al., A 1ynm 1.25V 8Gb, 16Gb/s/pin GDDR6-based Accelerator-in-Memory supporting 1TFLOPS MAC Operation and Various Activation Functions for Deep-Learning Applications, ISSCC 2022

## Slide 46: Lecture on Accelerator-in-Memory
https://youtu.be/NDL77Xdccbs?t=159

## Slide 47: Alibaba HB-PNM

## Slide 48: Alibaba HB-PNM: Overall Architecture (2022)
3D-stacked logic die and DRAM die vertically bonded by hybrid bonding (HB)
Niu et al., 184QPS/W 64Mb/mm2 3D Logic-to-DRAM Hybrid Bonding with Process-Near-Memory Engine for Recommendation System, ISSCC 2022

## Slide 49: Alibaba HB-PNM: Compute Engines
Match engine and neural engine for matching and ranking in a recommendation system
Niu et al., 184QPS/W 64Mb/mm2 3D Logic-to-DRAM Hybrid Bonding with Process-Near-Memory Engine for Recommendation System, ISSCC 2022

## Slide 50: Lecture on HB-PNM
https://youtu.be/OZjKnn-DbwA

## Slide 51: More Real PIM

## Slide 52: NeuroBlade
https://blocksandfiles.com/2021/10/06/neurobladers-build-a-processing-in-memory-analytics-chip-and-server/

## Slide 53: NeuroBlade Patent (I)
Sity et al., “Memory-based Distributed Processor Architecture,” US 10,762,034 B2

## Slide 54: NeuroBlade Patent (II)
Sity et al., “Memory-based Distributed Processor Architecture,” US 10,762,034 B2

## Slide 55: NeuroBlade: Xiphos
PIM XRAM chip
  IMPU (Intensive Memory Processing Unit)
x86 CPU, 32 NVMe SSDs
PCIe fabric: “Everything is connected on top of PCIe fabric.”
Wide I/O bus: multiple x16 PCIe buses
https://www.neuroblade.com

## Slide 56: Variety of Current Real PIM Architectures
Differences
  Near-bank (UPMEM, FIMDRAM, AiM, HB-PNM) vs. near-chip (AxDIMM)
  General-purpose (UPMEM) vs. special-function (FIMDRAM, AiM, HB-PNM)
  FGMT (UPMEM) vs. SIMD (FIMDRAM, AiM, AxDIMM) vs. systolic array (HB-PNM)
  Natively integer (UPMEM, HB-PNM) vs. floating point (FIMDRAM)
    FP16 (FIMDRAM) vs. BF16 (AiM) vs. FP32 (AxDIMM)
  DDR4 (UPMEM, AxDIMM) vs. LPDDR4 (HB-PNM) vs. HBM2 (FIMDRAM) vs. GDDR6 (AiM)

## Slide 57: Common Characteristics
These PIM systems have some common characteristics:
  There is a host processor (CPU or GPU) with access to (1) standard main memory, and (2) PIM-enabled memory
  PIM-enabled memory contains multiple PIM processing elements (PEs) with high bandwidth and low latency memory access
  PIM PEs run only at a few hundred MHz and have a small number of registers and small (or no) cache/scratchpad
  PEs may need to communicate via the host processor

## Slide 58: A State-of-the-Art PIM (PNM) System
These PIM systems have some common characteristics:
  There is a host processor (CPU or GPU) with access to (1) standard main memory, and (2) PIM-enabled memory
  PIM-enabled memory contains multiple PIM processing elements (PEs) with high bandwidth and low latency memory access
  PIM PEs run only at a few hundred MHz and have a small number of registers and small (or no) cache/scratchpad
  PEs may need to communicate via the host processor

## Slide 59: Programming a General-purpose PIM System

## Slide 60: Accelerator Model (I)
UPMEM DIMMs coexist with conventional DIMMs
Integration of UPMEM DIMMs in a system follows an accelerator model
UPMEM DIMMs can be seen as a loosely coupled accelerator
  Explicit data movement between the main processor (host CPU) and the accelerator (UPMEM)
  Explicit kernel launch onto the UPMEM processors
This resembles GPU computing

## Slide 61: GPU Computing
Computation is offloaded to the GPU
Three steps
  CPU-GPU data transfer (1)
  GPU kernel execution (2)
  GPU-CPU data transfer (3)
https://www.youtube.com/watch?v=y40-tY5WJ8A
https://safari.ethz.ch/digitaltechnik/spring2018/lib/exe/fetch.php?media=digitaldesign-2018-lecture22-gpuprogramming-afterlecture.pdf

## Slide 62: Accelerator Model (II)
FIG. 6 is a flow diagram representing operations in a method of delegating a processing task to a DRAM processor according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 63: System Organization
FIG. 1 schematically illustrates a computing system comprising DRAM circuits having integrated processors according to an example embodiment
Fabrice Devaux, Jean-François Roy. “Memory circuit with integrated processor.” US 10,324,870 B2.

## Slide 64: First Programming Example: Vector Addition

## Slide 65: Observations, Recommendations, Takeaways
GENERAL PROGRAMMING RECOMMENDATIONS
Execute on the DRAM Processing Units (DPUs) portions of parallel code that are as long as possible.
Split the workload into independent data blocks, which the DPUs operate on independently.
Use as many working DPUs in the system as possible.
Launch at least 11 tasklets (i.e., software threads) per DPU.
PROGRAMMING RECOMMENDATION 1
For data movement between the DPU’s MRAM bank and the WRAM, use large DMA transfer sizes when all the accessed data is going to be used.
KEY OBSERVATION 7
Larger CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks result in higher sustained bandwidth.
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound. As a result, the most suitable work- loads are memory-bound.

## Slide 66: Vector Addition (VA)
Our first programming example
We partition the input arrays across:
  DPUs
  Tasklets, i.e., software threads running on a DPU
DPU 0
DPU 1
DPU 2
DPU 3
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1

## Slide 67: UPMEM SDK Documentation
https://sdk.upmem.com/2023.1.0/

## Slide 68: General Programming Recommendations
From UPMEM programming guide✻, presentations★, and white papers☆
✻ https://sdk.upmem.com/2021.1.1/index.html
★ F. Devaux, "The true Processing In Memory accelerator," HotChips 2019. doi: 10.1109/HOTCHIPS.2019.8875680
☆ UPMEM, “Introduction to UPMEM PIM. Processing-in-memory (PIM) on DRAM Accelerator,” White paper
GENERAL PROGRAMMING RECOMMENDATIONS
Execute on the DRAM Processing Units (DPUs) portions of parallel code that are as long as possible.
Split the workload into independent data blocks, which the DPUs operate on independently.
Use as many working DPUs in the system as possible.
Launch at least 11 tasklets (i.e., software threads) per DPU.

## Slide 69: DPU Allocation
dpu_alloc() allocates a number of DPUs
  Creates a dpu_set
Can we allocate different DPU sets
over the course of a program?
Yes, we can. We show an example next
We deallocate a DPU set with dpu_free()

## Slide 70: DPU Allocation: Needleman-Wunsch (NW)
In NW we change the number of DPUs in the DPU set as computation progresses

## Slide 71: Load DPU Binary
dpu_load() loads a program in all DPUs of a dpu_set
Is it possible to launch different kernels onto different DPUs?
Yes, it is possible. This enables:
Workloads with task-level parallelism
Different programs using different DPU sets

## Slide 72: CPU-DPU/DPU-CPU Data Transfers
CPU-DPU and DPU-CPU transfers
  Between host CPU’s main memory and DPUs’ MRAM banks
Serial CPU-DPU/DPU-CPU transfers:
  A single DPU (i.e., 1 MRAM bank)
Parallel CPU-DPU/DPU-CPU transfers:
  Multiple DPUs (i.e., many MRAM banks)
Broadcast CPU-DPU transfers:
  Multiple DPUs with a single buffer

## Slide 73: Serial Transfers
dpu_copy_to();
dpu_copy_from();
We transfer (part of) a buffer to/from each DPU in the dpu_set
DPU_MRAM_HEAP_POINTER_NAME: Start of the MRAM range that can be freely accessed by applications
  We do not allocate MRAM explicitly
Offset within MRAM
Pointer to main memory
Transfer size

## Slide 74: Parallel Transfers
We push different buffers to/from a DPU set in one transfer
  All buffers need to be of the same size
First, prepare (dpu_prepare_xfer);
then, push (dpu_push_xfer)
Direction:
  DPU_XFER_TO_DPU
  DPU_XFER_FROM_DPU
Pointer to main memory
Offset within MRAM
Transfer size
Direction

## Slide 75: Broadcast Transfers
dpu_broadcast_to();
  Only CPU to DPU
We transfer the same buffer to all DPUs in the dpu_set
Pointer to main memory
Transfer size

## Slide 76: Different Types of Transfers in a Program
An example benchmark that uses both parallel and serial transfers
Select (SEL)
  Remove even values
DPU 0
DPU 1
DPU 2
DPU 0
DPU 1
DPU 2
Parallel transfers
Serial transfers

## Slide 77: Inter-DPU Communication
There is no direct communication channel between DPUs
Inter-DPU communication takes place via the host CPU using CPU-DPU and DPU-CPU transfers
Example communication patterns:
  Merging of partial results to obtain the final result
    Only DPU-CPU transfers
  Redistribution of intermediate results for further computation
    DPU-CPU transfers and CPU-DPU transfers

## Slide 78: How Fast are these Data Transfers?
With a microbenchmark, we obtain the sustained bandwidth of all types of CPU-DPU and DPU-CPU transfers
Two experiments:
  1 DPU: variable CPU-DPU and DPU-CPU transfer size (8 bytes to 32 MB)
  1 rank: 32 MB CPU-DPU and DPU-CPU transfers to/from a set of 1 to 64 MRAM banks within the same rank
Preliminary experiments with more than one rank
  Channel-level parallelism
DDR4 bandwidth bounds the maximum transfer bandwidth
The cost of the transfers can be amortized,
if enough computation is run on the DPUs

## Slide 79: CPU-DPU/DPU-CPU Transfers: 1 DPU
Data transfer size varies between 8 bytes and 32 MB
Chart: Data transfer size (bytes)
| 8 | 32 | 128 | 512 | 2K | 8K | 32K | 128K | 512K | 2M | 8M | 32M
CPU-DPU | 0.000155 | 0.000652 | 0.002771 | 0.010059 | 0.036637 | 0.10489 | 0.20328 | 0.29402 | 0.60928 | 0.66017 | 0.38165 | 0.33248
DPU-CPU | 0.000155 | 0.000668 | 0.002795 | 0.009094 | 0.027453 | 0.052312 | 0.072383 | 0.08808 | 0.11749 | 0.12198 | 0.12252 | 0.12209
KEY OBSERVATION 7
Larger CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks result in higher sustained bandwidth.

## Slide 80: CPU-DPU/DPU-CPU Transfers: 1 Rank (I)
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)
The number of DPUs varies between 1 and 64
Chart: #DPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64
CPU-DPU (serial) | 0.33248 | 0.33347 | 0.33201 | 0.33127 | 0.30251 | 0.30048 | 0.27371
DPU-CPU (serial) | 0.12209 | 0.12213 | 0.12212 | 0.12211 | 0.11496 | 0.11515 | 0.11561
CPU-DPU (parallel) | 0.33204 | 0.54059 | 0.73245 | 0.87673 | 1.8109 | 4.2349 | 6.6828
DPU-CPU (parallel) | 0.12227 | 0.22521 | 0.42437 | 0.63153 | 1.4964 | 3.1702 | 4.7395
CPU-DPU (broadcast) | 0.33281 | 0.66768 | 1.3535 | 2.5643 | 5.0996 | 10.1432 | 16.8846
KEY OBSERVATION 8
The sustained bandwidth of parallel CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks increases with the number of DRAM Processing Units inside a rank.

## Slide 81: CPU-DPU/DPU-CPU Transfers: 1 Rank (II)
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)
The number of DPUs varies between 1 and 64
Chart: #DPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64
CPU-DPU (serial) | 0.33248 | 0.33347 | 0.33201 | 0.33127 | 0.30251 | 0.30048 | 0.27371
DPU-CPU (serial) | 0.12209 | 0.12213 | 0.12212 | 0.12211 | 0.11496 | 0.11515 | 0.11561
CPU-DPU (parallel) | 0.33204 | 0.54059 | 0.73245 | 0.87673 | 1.8109 | 4.2349 | 6.6828
DPU-CPU (parallel) | 0.12227 | 0.22521 | 0.42437 | 0.63153 | 1.4964 | 3.1702 | 4.7395
CPU-DPU (broadcast) | 0.33281 | 0.66768 | 1.3535 | 2.5643 | 5.0996 | 10.1432 | 16.8846
KEY OBSERVATION 9
The sustained bandwidth of parallel CPU-DPU transfers is higher than the sustained bandwidth of parallel DPU-CPU transfers due to different implementations of CPU-DPU and DPU-CPU transfers in the UPMEM runtime library.
The sustained bandwidth of broadcast CPU-DPU transfers (i.e., the same buffer is copied to multiple MRAM banks) is higher than that of parallel CPU-DPU transfers (i.e., different buffers are copied to different MRAM banks) due to higher temporal locality in the CPU cache hierarchy.
Notes: Load uses AVX write instructions, which are asynchronous.
However, AVX read instructions are synchronous

## Slide 82: “Transposing” Library
F. Devaux, "The true Processing In Memory accelerator," HotChips 2019. doi: 10.1109/HOTCHIPS.2019.8875680

## Slide 83: Microbenchmark: CPU-DPU
CPU-DPU (serial/parallel/broadcast) and DPU-CPU (serial/parallel)

## Slide 84: DPU Kernel Launch
dpu_launch() launches a kernel on a dpu_set
  DPU_SYNCHRONOUS suspends the application until the kernel finishes
  DPU_ASYNCHRONOUS returns the control to the application
    dpu_sync or dpu_status to check kernel completion
What does the asynchronous execution enable?
Some ideas:
Task-level parallelism: concurrent execution of different kernels on different DPU sets
Concurrent heterogeneous computation on CPU and DPUs

## Slide 85: How to Pass Parameters to the Kernel?
We can use serial and parallel transfers
We pass them directly to the scratchpad memory of the DPU
  Working RAM (WRAM): 64KB per DPU
This is useful for input parameters and some results

## Slide 86: Recall: Vector Addition (VA)
Our first programming example
We partition the input arrays across:
  DPUs
  Tasklets, i.e., software threads running on a DPU
DPU 0
DPU 1
DPU 2
DPU 3
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1
Tasklet 0
Tasklet 1

## Slide 87: Programming a DPU Kernel (I)
Vector addition
Tasklet ID
Size of vector tile processed by a DPU
MRAM addresses of arrays A and B
WRAM allocation
MRAM-WRAM DMA transfers
Vector addition (see next slide)
WRAM-MRAM DMA transfer

## Slide 88: Programming a DPU Kernel (II)
Vector addition

## Slide 89: Intra-DPU Synchronization

## Slide 90: Synchronization Primitives
A tasklet is the software abstraction of a hardware thread
Each tasklet can have its own memory space in WRAM
  Tasklets can also share data in WRAM by sharing pointers
Tasklets within the same DPU can synchronize
  Mutual exclusion
    mutex_lock(); mutex_unlock();
  Handshakes
    handshake_wait_for(); handshake_notify();
  Barriers
    barrier_wait();
  Semaphores
    sem_give(); sem_take();

## Slide 91: Parallel Reduction (I)
Tasklets in a DPU can work together on a parallel reduction
Tasklet 0
Tasklet 1
Tasklet 2
Tasklet 3

## Slide 92: Parallel Reduction (II)
Each tasklet computes a local sum
Tasklet 0
Tasklet 1
Tasklet 2
Tasklet 3

## Slide 93: Parallel Reduction (III)
Each tasklet computes a local sum
Accumulate in a local sum
Copy local sum into WRAM

## Slide 94: Final Reduction
A single tasklet can perform the final reduction
Accumulate in a local sum
Copy local sum into WRAM
Sequential accumulation
Barrier synchronization

## Slide 95: Vector Reduction: Naïve Mapping
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
Slide credit: Hwu & Kirk
…

## Slide 96: Using Barriers: Tree-Based Reduction
Multiple tasklets can perform a tree-based reduction
  After every iteration tasklets synchronize with a barrier
  Half of the tasklets retire at the end of an iteration
“offset” tasklets working
Barrier synchronization
A handshake-based tree-based reduction is also possible.
We can compare single-tasklet, barrier-based,
and handshake-based versions*
*Gómez-Luna et al., “Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture,”
https://arxiv.org/pdf/2105.03814.pdf

## Slide 97: Parallel Reduction on GPU
https://youtu.be/Xp0HHpcDwUc

## Slide 98: UPMEM SDK Documentation
https://sdk.upmem.com/2023.1.0/

## Slide 99: Microbenchmarking of UPMEM PIM

## Slide 100: DPU Pipeline
In-order pipeline
  Up to 425 MHz
Fine-grain multithreaded
  24 hardware threads
14 pipeline stages
  DISPATCH: Thread selection
  FETCH: Instruction fetch
  READOP: Register file
  FORMAT: Operand formatting
  ALU: Operation and WRAM
  MERGE: Result formatting
To the DMA engine

## Slide 101: Arithmetic Throughput: Microbenchmark
Goal
  Measure the maximum arithmetic throughput for different datatypes and operations
Microbenchmark
  We stream over an array in WRAM and perform read-modify-write operations
  Experiments on one DPU
  We vary the number of tasklets from 1 to 24
  Arithmetic operations: add, subtract, multiply, divide
  Datatypes: int32, int64, float, double
We measure cycles with an accurate cycle counter that the SDK provides
  We include WRAM accesses (including address calculation) and arithmetic operation

## Slide 102: Microbenchmark for INT32 ADD Throughput
C-based code
Compiled code (UPMEM DPU ISA)
1 #define SIZE 256
2 int* bufferA = mem_alloc(SIZE * sizeof(int));
3 for(int i = 0; i < SIZE; i++){
4 int temp = bufferA[i];
5 temp += scalar;
6 bufferA[i] = temp;
7 }
1 move r2, 0
2 .LBB0_1: // Loop header
3 lsl_add r3, r0, r2, 2 // Address calculation
4 lw r4, r3, 0 // Load from WRAM
5 add r4, r4, r1 // Add
6 sw r3, 0, r4 // Store to WRAM
7 add r2, r2, 1 // Index update
8 jneq r2, 256, .LBB0_1 // Conditional jump

## Slide 103: Arithmetic Throughput: 11 Tasklets
Chart: (d) DOUBLE (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.30234 | 0.60468 | 0.90681 | 1.2093 | 1.511 | 1.8131 | 2.1151 | 2.4186 | 2.7185 | 3.0201 | 3.3243 | 3.3244 | 3.3214 | 3.3221 | 3.3207 | 3.3267 | 3.3257 | 3.3207 | 3.3204 | 3.324 | 3.3198 | 3.3216 | 3.3191 | 3.321
SUB | 0.28329 | 0.56662 | 0.84983 | 1.1332 | 1.4159 | 1.6989 | 1.9818 | 2.2662 | 2.5476 | 2.8298 | 3.1149 | 3.1147 | 3.112 | 3.1121 | 3.1117 | 3.117 | 3.1162 | 3.1111 | 3.1113 | 3.1144 | 3.1116 | 3.1126 | 3.1103 | 3.1117
MUL | 0.047832 | 0.095664 | 0.14349 | 0.19132 | 0.23907 | 0.28684 | 0.33461 | 0.38264 | 0.43014 | 0.47786 | 0.52598 | 0.52581 | 0.52542 | 0.52545 | 0.52531 | 0.52615 | 0.526 | 0.5251 | 0.52516 | 0.5257 | 0.52533 | 0.5253 | 0.52491 | 0.52514
DIV | 0.01482 | 0.029637 | 0.044454 | 0.059279 | 0.074078 | 0.088875 | 0.10367 | 0.11857 | 0.13326 | 0.14806 | 0.16296 | 0.16294 | 0.1628 | 0.16279 | 0.16277 | 0.16302 | 0.16298 | 0.1627 | 0.1627 | 0.16286 | 0.16276 | 0.16275 | 0.16265 | 0.1627
Chart: (c) FLOAT (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.44709 | 0.89417 | 1.3411 | 1.7884 | 2.2348 | 2.6815 | 3.1278 | 3.5767 | 4.0206 | 4.4664 | 4.9157 | 4.9162 | 4.9123 | 4.912 | 4.9123 | 4.92 | 4.9188 | 4.911 | 4.9117 | 4.9166 | 4.9107 | 4.9135 | 4.9108 | 4.9129
SUB | 0.41767 | 0.83533 | 1.2528 | 1.6707 | 2.0875 | 2.5047 | 2.922 | 3.3409 | 3.7553 | 4.1729 | 4.5925 | 4.5927 | 4.5894 | 4.589 | 4.5882 | 4.5956 | 4.595 | 4.5874 | 4.5884 | 4.5927 | 4.588 | 4.5898 | 4.5873 | 4.589
MUL | 0.17353 | 0.34709 | 0.52052 | 0.69408 | 0.86731 | 1.0407 | 1.2138 | 1.3882 | 1.5603 | 1.7336 | 1.9081 | 1.908 | 1.9065 | 1.9064 | 1.9057 | 1.9093 | 1.9084 | 1.9053 | 1.9053 | 1.9075 | 1.9057 | 1.9061 | 1.9046 | 1.9058
DIV | 0.030772 | 0.061547 | 0.092309 | 0.12309 | 0.15381 | 0.18457 | 0.21529 | 0.2462 | 0.27674 | 0.30745 | 0.33839 | 0.33835 | 0.33808 | 0.33805 | 0.338 | 0.33852 | 0.33846 | 0.33789 | 0.33786 | 0.33821 | 0.33795 | 0.33796 | 0.33775 | 0.33787
Chart: (b) INT64 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 4.5316 | 9.063 | 13.5936 | 18.1243 | 22.6478 | 27.1718 | 31.6957 | 36.2453 | 40.7367 | 45.256 | 49.8099 | 49.8564 | 49.8476 | 49.8958 | 49.9275 | 50.0333 | 50.0643 | 49.9768 | 50.0108 | 50.1101 | 50.0564 | 50.098 | 50.1188 | 50.1606
SUB | 4.532 | 9.063 | 13.5932 | 18.1259 | 22.6476 | 27.173 | 31.6952 | 36.2388 | 40.7364 | 45.2517 | 49.8028 | 49.8507 | 49.8588 | 49.8829 | 49.9274 | 50.0375 | 50.0546 | 49.9797 | 50.0235 | 50.1058 | 50.0202 | 50.1042 | 50.1203 | 50.1661
MUL | 0.23352 | 0.46704 | 0.70044 | 0.93403 | 1.1671 | 1.4003 | 1.6335 | 1.8681 | 2.0997 | 2.3328 | 2.5678 | 2.5673 | 2.5654 | 2.5657 | 2.565 | 2.5689 | 2.5689 | 2.5642 | 2.5643 | 2.5672 | 2.5647 | 2.5654 | 2.5638 | 2.5645
DIV | 0.12702 | 0.25402 | 0.38093 | 0.50793 | 0.63489 | 0.76166 | 0.88826 | 1.0157 | 1.1419 | 1.2691 | 1.3961 | 1.398 | 1.3991 | 1.3992 | 1.4005 | 1.4019 | 1.4026 | 1.4015 | 1.4017 | 1.4028 | 1.402 | 1.4029 | 1.4024 | 1.4031
Chart: (a) INT32 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 5.2847 | 10.5723 | 15.8563 | 21.1427 | 26.4212 | 31.6944 | 36.9718 | 42.274 | 47.5146 | 52.7876 | 58.0936 | 58.1545 | 58.1639 | 58.2096 | 58.2769 | 58.3889 | 58.4221 | 58.3892 | 58.3661 | 58.513 | 58.4882 | 58.5088 | 58.5235 | 58.5582
SUB | 5.2861 | 10.5721 | 15.8554 | 21.1417 | 26.4167 | 31.6963 | 36.9708 | 42.2762 | 47.5111 | 52.7785 | 58.103 | 58.1663 | 58.174 | 58.2244 | 58.2631 | 58.3671 | 58.4217 | 58.3768 | 58.3686 | 58.4812 | 58.4819 | 58.52 | 58.5111 | 58.5165
MUL | 0.93379 | 1.8678 | 2.8014 | 3.7354 | 4.6672 | 5.6003 | 6.532 | 7.4704 | 8.3964 | 9.3291 | 10.2673 | 10.2689 | 10.2622 | 10.2631 | 10.2627 | 10.2796 | 10.2799 | 10.2636 | 10.2661 | 10.2752 | 10.2639 | 10.2733 | 10.2653 | 10.2687
DIV | 1.024 | 2.0483 | 3.0719 | 4.096 | 5.1194 | 6.1409 | 7.1632 | 8.1917 | 9.2088 | 10.2316 | 11.2587 | 11.262 | 11.2569 | 11.2598 | 11.2615 | 11.2771 | 11.2786 | 11.2635 | 11.2657 | 11.274 | 11.2634 | 11.2706 | 11.2689 | 11.2755
KEY OBSERVATION 1
The arithmetic throughput of a DRAM Processing Unit saturates at 11 or more tasklets.
This observation is consistent for different datatypes (INT32, INT64, UINT32, UINT64, FLOAT, DOUBLE) and operations (ADD, SUB, MUL, DIV).

## Slide 104: Arithmetic Throughput: ADD/SUB
Chart: (d) DOUBLE (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.30234 | 0.60468 | 0.90681 | 1.2093 | 1.511 | 1.8131 | 2.1151 | 2.4186 | 2.7185 | 3.0201 | 3.3243 | 3.3244 | 3.3214 | 3.3221 | 3.3207 | 3.3267 | 3.3257 | 3.3207 | 3.3204 | 3.324 | 3.3198 | 3.3216 | 3.3191 | 3.321
SUB | 0.28329 | 0.56662 | 0.84983 | 1.1332 | 1.4159 | 1.6989 | 1.9818 | 2.2662 | 2.5476 | 2.8298 | 3.1149 | 3.1147 | 3.112 | 3.1121 | 3.1117 | 3.117 | 3.1162 | 3.1111 | 3.1113 | 3.1144 | 3.1116 | 3.1126 | 3.1103 | 3.1117
MUL | 0.047832 | 0.095664 | 0.14349 | 0.19132 | 0.23907 | 0.28684 | 0.33461 | 0.38264 | 0.43014 | 0.47786 | 0.52598 | 0.52581 | 0.52542 | 0.52545 | 0.52531 | 0.52615 | 0.526 | 0.5251 | 0.52516 | 0.5257 | 0.52533 | 0.5253 | 0.52491 | 0.52514
DIV | 0.01482 | 0.029637 | 0.044454 | 0.059279 | 0.074078 | 0.088875 | 0.10367 | 0.11857 | 0.13326 | 0.14806 | 0.16296 | 0.16294 | 0.1628 | 0.16279 | 0.16277 | 0.16302 | 0.16298 | 0.1627 | 0.1627 | 0.16286 | 0.16276 | 0.16275 | 0.16265 | 0.1627
Chart: (c) FLOAT (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.44709 | 0.89417 | 1.3411 | 1.7884 | 2.2348 | 2.6815 | 3.1278 | 3.5767 | 4.0206 | 4.4664 | 4.9157 | 4.9162 | 4.9123 | 4.912 | 4.9123 | 4.92 | 4.9188 | 4.911 | 4.9117 | 4.9166 | 4.9107 | 4.9135 | 4.9108 | 4.9129
SUB | 0.41767 | 0.83533 | 1.2528 | 1.6707 | 2.0875 | 2.5047 | 2.922 | 3.3409 | 3.7553 | 4.1729 | 4.5925 | 4.5927 | 4.5894 | 4.589 | 4.5882 | 4.5956 | 4.595 | 4.5874 | 4.5884 | 4.5927 | 4.588 | 4.5898 | 4.5873 | 4.589
MUL | 0.17353 | 0.34709 | 0.52052 | 0.69408 | 0.86731 | 1.0407 | 1.2138 | 1.3882 | 1.5603 | 1.7336 | 1.9081 | 1.908 | 1.9065 | 1.9064 | 1.9057 | 1.9093 | 1.9084 | 1.9053 | 1.9053 | 1.9075 | 1.9057 | 1.9061 | 1.9046 | 1.9058
DIV | 0.030772 | 0.061547 | 0.092309 | 0.12309 | 0.15381 | 0.18457 | 0.21529 | 0.2462 | 0.27674 | 0.30745 | 0.33839 | 0.33835 | 0.33808 | 0.33805 | 0.338 | 0.33852 | 0.33846 | 0.33789 | 0.33786 | 0.33821 | 0.33795 | 0.33796 | 0.33775 | 0.33787
Chart: (b) INT64 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 4.5316 | 9.063 | 13.5936 | 18.1243 | 22.6478 | 27.1718 | 31.6957 | 36.2453 | 40.7367 | 45.256 | 49.8099 | 49.8564 | 49.8476 | 49.8958 | 49.9275 | 50.0333 | 50.0643 | 49.9768 | 50.0108 | 50.1101 | 50.0564 | 50.098 | 50.1188 | 50.1606
SUB | 4.532 | 9.063 | 13.5932 | 18.1259 | 22.6476 | 27.173 | 31.6952 | 36.2388 | 40.7364 | 45.2517 | 49.8028 | 49.8507 | 49.8588 | 49.8829 | 49.9274 | 50.0375 | 50.0546 | 49.9797 | 50.0235 | 50.1058 | 50.0202 | 50.1042 | 50.1203 | 50.1661
MUL | 0.23352 | 0.46704 | 0.70044 | 0.93403 | 1.1671 | 1.4003 | 1.6335 | 1.8681 | 2.0997 | 2.3328 | 2.5678 | 2.5673 | 2.5654 | 2.5657 | 2.565 | 2.5689 | 2.5689 | 2.5642 | 2.5643 | 2.5672 | 2.5647 | 2.5654 | 2.5638 | 2.5645
DIV | 0.12702 | 0.25402 | 0.38093 | 0.50793 | 0.63489 | 0.76166 | 0.88826 | 1.0157 | 1.1419 | 1.2691 | 1.3961 | 1.398 | 1.3991 | 1.3992 | 1.4005 | 1.4019 | 1.4026 | 1.4015 | 1.4017 | 1.4028 | 1.402 | 1.4029 | 1.4024 | 1.4031
Chart: (a) INT32 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 5.2847 | 10.5723 | 15.8563 | 21.1427 | 26.4212 | 31.6944 | 36.9718 | 42.274 | 47.5146 | 52.7876 | 58.0936 | 58.1545 | 58.1639 | 58.2096 | 58.2769 | 58.3889 | 58.4221 | 58.3892 | 58.3661 | 58.513 | 58.4882 | 58.5088 | 58.5235 | 58.5582
SUB | 5.2861 | 10.5721 | 15.8554 | 21.1417 | 26.4167 | 31.6963 | 36.9708 | 42.2762 | 47.5111 | 52.7785 | 58.103 | 58.1663 | 58.174 | 58.2244 | 58.2631 | 58.3671 | 58.4217 | 58.3768 | 58.3686 | 58.4812 | 58.4819 | 58.52 | 58.5111 | 58.5165
MUL | 0.93379 | 1.8678 | 2.8014 | 3.7354 | 4.6672 | 5.6003 | 6.532 | 7.4704 | 8.3964 | 9.3291 | 10.2673 | 10.2689 | 10.2622 | 10.2631 | 10.2627 | 10.2796 | 10.2799 | 10.2636 | 10.2661 | 10.2752 | 10.2639 | 10.2733 | 10.2653 | 10.2687
DIV | 1.024 | 2.0483 | 3.0719 | 4.096 | 5.1194 | 6.1409 | 7.1632 | 8.1917 | 9.2088 | 10.2316 | 11.2587 | 11.262 | 11.2569 | 11.2598 | 11.2615 | 11.2771 | 11.2786 | 11.2635 | 11.2657 | 11.274 | 11.2634 | 11.2706 | 11.2689 | 11.2755
INT32 ADD/SUB are 17% faster than INT64 ADD/SUB
17%
Can we explain the peak throughput?
Peak throughput at 11 tasklets.
One instruction retires every cycle when the pipeline is full

## Slide 105: Arithmetic Throughput: #Instructions
Compiler explorer: https://dpu.dev
6 instructions in the 32-bit ADD/SUB microbenchmark
7 instructions in the 64-bit ADD/SUB microbenchmark

## Slide 106: Arithmetic Throughput: ADD/SUB
32-bit ADD/SUB: 6 instructions → 58.33 MOPS
64-bit ADD/SUB: 7 instructions → 50.00 MOPS
at frequencyDPU = 350 MHz
Chart: (b) INT64 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 4.5316 | 9.063 | 13.5936 | 18.1243 | 22.6478 | 27.1718 | 31.6957 | 36.2453 | 40.7367 | 45.256 | 49.8099 | 49.8564 | 49.8476 | 49.8958 | 49.9275 | 50.0333 | 50.0643 | 49.9768 | 50.0108 | 50.1101 | 50.0564 | 50.098 | 50.1188 | 50.1606
SUB | 4.532 | 9.063 | 13.5932 | 18.1259 | 22.6476 | 27.173 | 31.6952 | 36.2388 | 40.7364 | 45.2517 | 49.8028 | 49.8507 | 49.8588 | 49.8829 | 49.9274 | 50.0375 | 50.0546 | 49.9797 | 50.0235 | 50.1058 | 50.0202 | 50.1042 | 50.1203 | 50.1661
MUL | 0.23352 | 0.46704 | 0.70044 | 0.93403 | 1.1671 | 1.4003 | 1.6335 | 1.8681 | 2.0997 | 2.3328 | 2.5678 | 2.5673 | 2.5654 | 2.5657 | 2.565 | 2.5689 | 2.5689 | 2.5642 | 2.5643 | 2.5672 | 2.5647 | 2.5654 | 2.5638 | 2.5645
DIV | 0.12702 | 0.25402 | 0.38093 | 0.50793 | 0.63489 | 0.76166 | 0.88826 | 1.0157 | 1.1419 | 1.2691 | 1.3961 | 1.398 | 1.3991 | 1.3992 | 1.4005 | 1.4019 | 1.4026 | 1.4015 | 1.4017 | 1.4028 | 1.402 | 1.4029 | 1.4024 | 1.4031
Chart: (a) INT32 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 5.2847 | 10.5723 | 15.8563 | 21.1427 | 26.4212 | 31.6944 | 36.9718 | 42.274 | 47.5146 | 52.7876 | 58.0936 | 58.1545 | 58.1639 | 58.2096 | 58.2769 | 58.3889 | 58.4221 | 58.3892 | 58.3661 | 58.513 | 58.4882 | 58.5088 | 58.5235 | 58.5582
SUB | 5.2861 | 10.5721 | 15.8554 | 21.1417 | 26.4167 | 31.6963 | 36.9708 | 42.2762 | 47.5111 | 52.7785 | 58.103 | 58.1663 | 58.174 | 58.2244 | 58.2631 | 58.3671 | 58.4217 | 58.3768 | 58.3686 | 58.4812 | 58.4819 | 58.52 | 58.5111 | 58.5165
MUL | 0.93379 | 1.8678 | 2.8014 | 3.7354 | 4.6672 | 5.6003 | 6.532 | 7.4704 | 8.3964 | 9.3291 | 10.2673 | 10.2689 | 10.2622 | 10.2631 | 10.2627 | 10.2796 | 10.2799 | 10.2636 | 10.2661 | 10.2752 | 10.2639 | 10.2733 | 10.2653 | 10.2687
DIV | 1.024 | 2.0483 | 3.0719 | 4.096 | 5.1194 | 6.1409 | 7.1632 | 8.1917 | 9.2088 | 10.2316 | 11.2587 | 11.262 | 11.2569 | 11.2598 | 11.2615 | 11.2771 | 11.2786 | 11.2635 | 11.2657 | 11.274 | 11.2634 | 11.2706 | 11.2689 | 11.2755
INT32 ADD/SUB are 17% faster than INT64 ADD/SUB
17%
Can we explain the peak throughput?
Peak throughput at 11 tasklets.
One instruction retires every cycle when the pipeline is full

## Slide 107: Arithmetic Throughput: MUL/DIV
Chart: (d) DOUBLE (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.30234 | 0.60468 | 0.90681 | 1.2093 | 1.511 | 1.8131 | 2.1151 | 2.4186 | 2.7185 | 3.0201 | 3.3243 | 3.3244 | 3.3214 | 3.3221 | 3.3207 | 3.3267 | 3.3257 | 3.3207 | 3.3204 | 3.324 | 3.3198 | 3.3216 | 3.3191 | 3.321
SUB | 0.28329 | 0.56662 | 0.84983 | 1.1332 | 1.4159 | 1.6989 | 1.9818 | 2.2662 | 2.5476 | 2.8298 | 3.1149 | 3.1147 | 3.112 | 3.1121 | 3.1117 | 3.117 | 3.1162 | 3.1111 | 3.1113 | 3.1144 | 3.1116 | 3.1126 | 3.1103 | 3.1117
MUL | 0.047832 | 0.095664 | 0.14349 | 0.19132 | 0.23907 | 0.28684 | 0.33461 | 0.38264 | 0.43014 | 0.47786 | 0.52598 | 0.52581 | 0.52542 | 0.52545 | 0.52531 | 0.52615 | 0.526 | 0.5251 | 0.52516 | 0.5257 | 0.52533 | 0.5253 | 0.52491 | 0.52514
DIV | 0.01482 | 0.029637 | 0.044454 | 0.059279 | 0.074078 | 0.088875 | 0.10367 | 0.11857 | 0.13326 | 0.14806 | 0.16296 | 0.16294 | 0.1628 | 0.16279 | 0.16277 | 0.16302 | 0.16298 | 0.1627 | 0.1627 | 0.16286 | 0.16276 | 0.16275 | 0.16265 | 0.1627
Chart: (c) FLOAT (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.44709 | 0.89417 | 1.3411 | 1.7884 | 2.2348 | 2.6815 | 3.1278 | 3.5767 | 4.0206 | 4.4664 | 4.9157 | 4.9162 | 4.9123 | 4.912 | 4.9123 | 4.92 | 4.9188 | 4.911 | 4.9117 | 4.9166 | 4.9107 | 4.9135 | 4.9108 | 4.9129
SUB | 0.41767 | 0.83533 | 1.2528 | 1.6707 | 2.0875 | 2.5047 | 2.922 | 3.3409 | 3.7553 | 4.1729 | 4.5925 | 4.5927 | 4.5894 | 4.589 | 4.5882 | 4.5956 | 4.595 | 4.5874 | 4.5884 | 4.5927 | 4.588 | 4.5898 | 4.5873 | 4.589
MUL | 0.17353 | 0.34709 | 0.52052 | 0.69408 | 0.86731 | 1.0407 | 1.2138 | 1.3882 | 1.5603 | 1.7336 | 1.9081 | 1.908 | 1.9065 | 1.9064 | 1.9057 | 1.9093 | 1.9084 | 1.9053 | 1.9053 | 1.9075 | 1.9057 | 1.9061 | 1.9046 | 1.9058
DIV | 0.030772 | 0.061547 | 0.092309 | 0.12309 | 0.15381 | 0.18457 | 0.21529 | 0.2462 | 0.27674 | 0.30745 | 0.33839 | 0.33835 | 0.33808 | 0.33805 | 0.338 | 0.33852 | 0.33846 | 0.33789 | 0.33786 | 0.33821 | 0.33795 | 0.33796 | 0.33775 | 0.33787
Chart: (b) INT64 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 4.5316 | 9.063 | 13.5936 | 18.1243 | 22.6478 | 27.1718 | 31.6957 | 36.2453 | 40.7367 | 45.256 | 49.8099 | 49.8564 | 49.8476 | 49.8958 | 49.9275 | 50.0333 | 50.0643 | 49.9768 | 50.0108 | 50.1101 | 50.0564 | 50.098 | 50.1188 | 50.1606
SUB | 4.532 | 9.063 | 13.5932 | 18.1259 | 22.6476 | 27.173 | 31.6952 | 36.2388 | 40.7364 | 45.2517 | 49.8028 | 49.8507 | 49.8588 | 49.8829 | 49.9274 | 50.0375 | 50.0546 | 49.9797 | 50.0235 | 50.1058 | 50.0202 | 50.1042 | 50.1203 | 50.1661
MUL | 0.23352 | 0.46704 | 0.70044 | 0.93403 | 1.1671 | 1.4003 | 1.6335 | 1.8681 | 2.0997 | 2.3328 | 2.5678 | 2.5673 | 2.5654 | 2.5657 | 2.565 | 2.5689 | 2.5689 | 2.5642 | 2.5643 | 2.5672 | 2.5647 | 2.5654 | 2.5638 | 2.5645
DIV | 0.12702 | 0.25402 | 0.38093 | 0.50793 | 0.63489 | 0.76166 | 0.88826 | 1.0157 | 1.1419 | 1.2691 | 1.3961 | 1.398 | 1.3991 | 1.3992 | 1.4005 | 1.4019 | 1.4026 | 1.4015 | 1.4017 | 1.4028 | 1.402 | 1.4029 | 1.4024 | 1.4031
Chart: (a) INT32 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 5.2847 | 10.5723 | 15.8563 | 21.1427 | 26.4212 | 31.6944 | 36.9718 | 42.274 | 47.5146 | 52.7876 | 58.0936 | 58.1545 | 58.1639 | 58.2096 | 58.2769 | 58.3889 | 58.4221 | 58.3892 | 58.3661 | 58.513 | 58.4882 | 58.5088 | 58.5235 | 58.5582
SUB | 5.2861 | 10.5721 | 15.8554 | 21.1417 | 26.4167 | 31.6963 | 36.9708 | 42.2762 | 47.5111 | 52.7785 | 58.103 | 58.1663 | 58.174 | 58.2244 | 58.2631 | 58.3671 | 58.4217 | 58.3768 | 58.3686 | 58.4812 | 58.4819 | 58.52 | 58.5111 | 58.5165
MUL | 0.93379 | 1.8678 | 2.8014 | 3.7354 | 4.6672 | 5.6003 | 6.532 | 7.4704 | 8.3964 | 9.3291 | 10.2673 | 10.2689 | 10.2622 | 10.2631 | 10.2627 | 10.2796 | 10.2799 | 10.2636 | 10.2661 | 10.2752 | 10.2639 | 10.2733 | 10.2653 | 10.2687
DIV | 1.024 | 2.0483 | 3.0719 | 4.096 | 5.1194 | 6.1409 | 7.1632 | 8.1917 | 9.2088 | 10.2316 | 11.2587 | 11.262 | 11.2569 | 11.2598 | 11.2615 | 11.2771 | 11.2786 | 11.2635 | 11.2657 | 11.274 | 11.2634 | 11.2706 | 11.2689 | 11.2755
Huge throughput difference between ADD/SUB and MUL/DIV
DPUs do not have
a 32-bit multiplier
MUL/DIV implementation is based on an instruction that performs bit shifting and addition in 1 cycle
(MUL/DIV take a maximum of 32 instructions)

## Slide 108: Arithmetic Throughput: Native Support
Chart: (d) DOUBLE (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.30234 | 0.60468 | 0.90681 | 1.2093 | 1.511 | 1.8131 | 2.1151 | 2.4186 | 2.7185 | 3.0201 | 3.3243 | 3.3244 | 3.3214 | 3.3221 | 3.3207 | 3.3267 | 3.3257 | 3.3207 | 3.3204 | 3.324 | 3.3198 | 3.3216 | 3.3191 | 3.321
SUB | 0.28329 | 0.56662 | 0.84983 | 1.1332 | 1.4159 | 1.6989 | 1.9818 | 2.2662 | 2.5476 | 2.8298 | 3.1149 | 3.1147 | 3.112 | 3.1121 | 3.1117 | 3.117 | 3.1162 | 3.1111 | 3.1113 | 3.1144 | 3.1116 | 3.1126 | 3.1103 | 3.1117
MUL | 0.047832 | 0.095664 | 0.14349 | 0.19132 | 0.23907 | 0.28684 | 0.33461 | 0.38264 | 0.43014 | 0.47786 | 0.52598 | 0.52581 | 0.52542 | 0.52545 | 0.52531 | 0.52615 | 0.526 | 0.5251 | 0.52516 | 0.5257 | 0.52533 | 0.5253 | 0.52491 | 0.52514
DIV | 0.01482 | 0.029637 | 0.044454 | 0.059279 | 0.074078 | 0.088875 | 0.10367 | 0.11857 | 0.13326 | 0.14806 | 0.16296 | 0.16294 | 0.1628 | 0.16279 | 0.16277 | 0.16302 | 0.16298 | 0.1627 | 0.1627 | 0.16286 | 0.16276 | 0.16275 | 0.16265 | 0.1627
Chart: (c) FLOAT (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 0.44709 | 0.89417 | 1.3411 | 1.7884 | 2.2348 | 2.6815 | 3.1278 | 3.5767 | 4.0206 | 4.4664 | 4.9157 | 4.9162 | 4.9123 | 4.912 | 4.9123 | 4.92 | 4.9188 | 4.911 | 4.9117 | 4.9166 | 4.9107 | 4.9135 | 4.9108 | 4.9129
SUB | 0.41767 | 0.83533 | 1.2528 | 1.6707 | 2.0875 | 2.5047 | 2.922 | 3.3409 | 3.7553 | 4.1729 | 4.5925 | 4.5927 | 4.5894 | 4.589 | 4.5882 | 4.5956 | 4.595 | 4.5874 | 4.5884 | 4.5927 | 4.588 | 4.5898 | 4.5873 | 4.589
MUL | 0.17353 | 0.34709 | 0.52052 | 0.69408 | 0.86731 | 1.0407 | 1.2138 | 1.3882 | 1.5603 | 1.7336 | 1.9081 | 1.908 | 1.9065 | 1.9064 | 1.9057 | 1.9093 | 1.9084 | 1.9053 | 1.9053 | 1.9075 | 1.9057 | 1.9061 | 1.9046 | 1.9058
DIV | 0.030772 | 0.061547 | 0.092309 | 0.12309 | 0.15381 | 0.18457 | 0.21529 | 0.2462 | 0.27674 | 0.30745 | 0.33839 | 0.33835 | 0.33808 | 0.33805 | 0.338 | 0.33852 | 0.33846 | 0.33789 | 0.33786 | 0.33821 | 0.33795 | 0.33796 | 0.33775 | 0.33787
Chart: (b) INT64 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 4.5316 | 9.063 | 13.5936 | 18.1243 | 22.6478 | 27.1718 | 31.6957 | 36.2453 | 40.7367 | 45.256 | 49.8099 | 49.8564 | 49.8476 | 49.8958 | 49.9275 | 50.0333 | 50.0643 | 49.9768 | 50.0108 | 50.1101 | 50.0564 | 50.098 | 50.1188 | 50.1606
SUB | 4.532 | 9.063 | 13.5932 | 18.1259 | 22.6476 | 27.173 | 31.6952 | 36.2388 | 40.7364 | 45.2517 | 49.8028 | 49.8507 | 49.8588 | 49.8829 | 49.9274 | 50.0375 | 50.0546 | 49.9797 | 50.0235 | 50.1058 | 50.0202 | 50.1042 | 50.1203 | 50.1661
MUL | 0.23352 | 0.46704 | 0.70044 | 0.93403 | 1.1671 | 1.4003 | 1.6335 | 1.8681 | 2.0997 | 2.3328 | 2.5678 | 2.5673 | 2.5654 | 2.5657 | 2.565 | 2.5689 | 2.5689 | 2.5642 | 2.5643 | 2.5672 | 2.5647 | 2.5654 | 2.5638 | 2.5645
DIV | 0.12702 | 0.25402 | 0.38093 | 0.50793 | 0.63489 | 0.76166 | 0.88826 | 1.0157 | 1.1419 | 1.2691 | 1.3961 | 1.398 | 1.3991 | 1.3992 | 1.4005 | 1.4019 | 1.4026 | 1.4015 | 1.4017 | 1.4028 | 1.402 | 1.4029 | 1.4024 | 1.4031
Chart: (a) INT32 (1 DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
ADD | 5.2847 | 10.5723 | 15.8563 | 21.1427 | 26.4212 | 31.6944 | 36.9718 | 42.274 | 47.5146 | 52.7876 | 58.0936 | 58.1545 | 58.1639 | 58.2096 | 58.2769 | 58.3889 | 58.4221 | 58.3892 | 58.3661 | 58.513 | 58.4882 | 58.5088 | 58.5235 | 58.5582
SUB | 5.2861 | 10.5721 | 15.8554 | 21.1417 | 26.4167 | 31.6963 | 36.9708 | 42.2762 | 47.5111 | 52.7785 | 58.103 | 58.1663 | 58.174 | 58.2244 | 58.2631 | 58.3671 | 58.4217 | 58.3768 | 58.3686 | 58.4812 | 58.4819 | 58.52 | 58.5111 | 58.5165
MUL | 0.93379 | 1.8678 | 2.8014 | 3.7354 | 4.6672 | 5.6003 | 6.532 | 7.4704 | 8.3964 | 9.3291 | 10.2673 | 10.2689 | 10.2622 | 10.2631 | 10.2627 | 10.2796 | 10.2799 | 10.2636 | 10.2661 | 10.2752 | 10.2639 | 10.2733 | 10.2653 | 10.2687
DIV | 1.024 | 2.0483 | 3.0719 | 4.096 | 5.1194 | 6.1409 | 7.1632 | 8.1917 | 9.2088 | 10.2316 | 11.2587 | 11.262 | 11.2569 | 11.2598 | 11.2615 | 11.2771 | 11.2786 | 11.2635 | 11.2657 | 11.274 | 11.2634 | 11.2706 | 11.2689 | 11.2755
KEY OBSERVATION 2
DPUs provide native hardware support for 32- and 64-bit integer addition and subtraction, leading to high throughput for these operations.
DPUs do not natively support 32- and 64-bit multiplication and division, and floating point operations. These operations are emulated by the UPMEM runtime library, leading to much lower throughput.

## Slide 109: Microbenchmark: Arithmetic Throughput
Arithmetic throughput for different operations and datatypes

## Slide 110: DPU: WRAM Bandwidth

## Slide 111: WRAM Bandwidth: Microbenchmark
Goal
  Measure the WRAM bandwidth for the STREAM benchmark
Microbenchmark
  We implement the four versions of STREAM: COPY, ADD, SCALE, and TRIAD
  The operations performed in ADD, SCALE, and TRIAD are addition, multiplication, and addition+multiplication, respectively
  We vary the number of tasklets from 1 to 16
  We show results for 1 DPU
We do not include accesses to MRAM

## Slide 112: STREAM Benchmark in WRAM
8 bytes read, 8 bytes written,
no arithmetic operations
16 bytes read, 8 bytes written,
ADD
8 bytes read, 8 bytes written,
MUL
16 bytes read, 8 bytes written,
MUL, ADD
// COPY
for(int i = 0; i < SIZE; i++){
bufferB[i] = bufferA[i];
}
// ADD
for(int i = 0; i < SIZE; i++){
bufferC[i] = bufferA[i] + bufferB[i];
}
// SCALE
for(int i = 0; i < SIZE; i++){
bufferB[i] = scalar * bufferA[i];
}
// TRIAD
for(int i = 0; i < SIZE; i++){
bufferC[i] = bufferA[i] + scalar * bufferB[i];
}

## Slide 113: WRAM Bandwidth: STREAM
How can we estimate the bandwidth?
Chart: STREAM (WRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY | 252.0799 | 504.1772 | 755.964 | 1008.0385 | 1259.7345 | 1511.352 | 1762.7094 | 2014.4239 | 2265.4988 | 2516.4835 | 2767.1737 | 2779.6834 | 2790.2899 | 2798.9216 | 2808.5738 | 2818.9827
ADD | 151.961 | 303.9141 | 455.7988 | 607.7779 | 759.6116 | 911.3948 | 1063.1564 | 1215.1616 | 1366.4453 | 1518.1038 | 1669.8969 | 1672.7035 | 1675.169 | 1676.8911 | 1679.401 | 1682.4645
SCALE | 3.8204 | 7.6407 | 11.4596 | 15.2813 | 19.1005 | 22.9189 | 26.7368 | 30.5619 | 34.3727 | 38.1884 | 42.0071 | 42.0045 | 42.0041 | 42.0112 | 42.0036 | 42.0336
TRIAD | 5.6041 | 11.2082 | 16.8102 | 22.4162 | 28.0178 | 33.6202 | 39.2209 | 44.8312 | 50.4201 | 56.0187 | 61.6205 | 61.6171 | 61.6166 | 61.6263 | 61.6156 | 61.6596
Assuming that the pipeline is full, and Bytes is the number of bytes read and written:

## Slide 114: WRAM Bandwidth: COPY
Chart: STREAM (WRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY | 252.0799 | 504.1772 | 755.964 | 1008.0385 | 1259.7345 | 1511.352 | 1762.7094 | 2014.4239 | 2265.4988 | 2516.4835 | 2767.1737 | 2779.6834 | 2790.2899 | 2798.9216 | 2808.5738 | 2818.9827
ADD | 151.961 | 303.9141 | 455.7988 | 607.7779 | 759.6116 | 911.3948 | 1063.1564 | 1215.1616 | 1366.4453 | 1518.1038 | 1669.8969 | 1672.7035 | 1675.169 | 1676.8911 | 1679.401 | 1682.4645
SCALE | 3.8204 | 7.6407 | 11.4596 | 15.2813 | 19.1005 | 22.9189 | 26.7368 | 30.5619 | 34.3727 | 38.1884 | 42.0071 | 42.0045 | 42.0041 | 42.0112 | 42.0036 | 42.0336
TRIAD | 5.6041 | 11.2082 | 16.8102 | 22.4162 | 28.0178 | 33.6202 | 39.2209 | 44.8312 | 50.4201 | 56.0187 | 61.6205 | 61.6171 | 61.6166 | 61.6263 | 61.6156 | 61.6596
COPY executes 2 instructions (WRAM load and store).
With 11 tasklets, 11 × 16 bytes in 22 cycles:

## Slide 115: WRAM Bandwidth: ADD
Chart: STREAM (WRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY | 252.0799 | 504.1772 | 755.964 | 1008.0385 | 1259.7345 | 1511.352 | 1762.7094 | 2014.4239 | 2265.4988 | 2516.4835 | 2767.1737 | 2779.6834 | 2790.2899 | 2798.9216 | 2808.5738 | 2818.9827
ADD | 151.961 | 303.9141 | 455.7988 | 607.7779 | 759.6116 | 911.3948 | 1063.1564 | 1215.1616 | 1366.4453 | 1518.1038 | 1669.8969 | 1672.7035 | 1675.169 | 1676.8911 | 1679.401 | 1682.4645
SCALE | 3.8204 | 7.6407 | 11.4596 | 15.2813 | 19.1005 | 22.9189 | 26.7368 | 30.5619 | 34.3727 | 38.1884 | 42.0071 | 42.0045 | 42.0041 | 42.0112 | 42.0036 | 42.0336
TRIAD | 5.6041 | 11.2082 | 16.8102 | 22.4162 | 28.0178 | 33.6202 | 39.2209 | 44.8312 | 50.4201 | 56.0187 | 61.6205 | 61.6171 | 61.6166 | 61.6263 | 61.6156 | 61.6596
ADD executes 5 instructions (2 ld, add, addc, sd).
With 11 tasklets, 11 × 24 bytes in 55 cycles:

## Slide 116: WRAM Bandwidth: Access Patterns
All 8-byte WRAM loads and stores take one cycle when the DPU pipeline is full
Microbenchmark: c[a[i]]=b[a[i]];
  Unit-stride: a[i]=a[i-1]+1;
  Strided: a[i]=a[i-1]+stride;
  Random: a[i]=rand();
KEY OBSERVATION 3
The sustained bandwidth provided by the DPU’s internal Working memory (WRAM) is independent of the memory access pattern (either streaming, strided, or random access pattern).
All 8-byte WRAM loads and stores take one cycle, when the DPU’s pipeline is full (i.e., with 11 or more tasklets).

## Slide 117: Microbenchmark: STREAM and WRAM
STREAM benchmark and WRAM access patterns

## Slide 118: DPU: MRAM Latency and Bandwidth

## Slide 119: MRAM Bandwidth
Goal
  Measure MRAM bandwidth for different access patterns
Microbenchmarks
  Latency of a single DMA transfer for different transfer sizes
    mram_read(); // MRAM-WRAM DMA transfer
    mram_write(); // WRAM-MRAM DMA transfer
  STREAM benchmark
    COPY, COPY-DMA
    ADD, SCALE, TRIAD
  Strided access pattern
    Coarse-grain strided access
    Fine-grain strided access
  Random access pattern (GUPS)
We do include accesses to MRAM

## Slide 120: MRAM Read and Write Latency (I)
We can model the MRAM latency with a linear expression
Chart: MRAM Read
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 34.3749 | 63.742 | 113.0185 | 201.2656 | 308.8345 | 419.14 | 534.2382 | 605.0304 | 628.2264
Latency | 81.4548 | 87.8541 | 99.0988 | 111.2957 | 145.0615 | 213.7711 | 335.4309 | 592.3669 | 1140.99
 | 81.4548 | 85.4548 | 93.4548 | 109.4548 | 141.4548 | 205.4548 | 333.4548 | 589.4548 | 1101.4548
Chart: MRAM Write
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 42.6136 | 79.3959 | 142.7862 | 239.4263 | 355.329 | 467.0049 | 555.5843 | 616.7485 | 633.2199
Latency | 65.7067 | 70.5326 | 78.4389 | 93.557 | 126.0803 | 191.861 | 322.5433 | 581.1121 | 1131.9922
 | 65.7067 | 69.7067 | 77.7067 | 93.7067 | 125.7067 | 189.7067 | 317.7067 | 573.7067 | 1085.7067
In our measurements, equals 0.5 cycles/byte.
Theoretical maximum MRAM bandwidth = 700 MB/s at 350 MHz

## Slide 121: MRAM Read and Write Latency (II)
KEY OBSERVATION 4
The DPU’s Main memory (MRAM) bank access latency increases linearly with the transfer size.
The maximum theoretical MRAM bandwidth is 2 bytes per cycle.
Chart: MRAM Read
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 34.3749 | 63.742 | 113.0185 | 201.2656 | 308.8345 | 419.14 | 534.2382 | 605.0304 | 628.2264
Latency | 81.4548 | 87.8541 | 99.0988 | 111.2957 | 145.0615 | 213.7711 | 335.4309 | 592.3669 | 1140.99
 | 81.4548 | 85.4548 | 93.4548 | 109.4548 | 141.4548 | 205.4548 | 333.4548 | 589.4548 | 1101.4548
Chart: MRAM Write
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 42.6136 | 79.3959 | 142.7862 | 239.4263 | 355.329 | 467.0049 | 555.5843 | 616.7485 | 633.2199
Latency | 65.7067 | 70.5326 | 78.4389 | 93.557 | 126.0803 | 191.861 | 322.5433 | 581.1121 | 1131.9922
 | 65.7067 | 69.7067 | 77.7067 | 93.7067 | 125.7067 | 189.7067 | 317.7067 | 573.7067 | 1085.7067

## Slide 122: MRAM Read and Write Latency (III)
Read and write accesses to MRAM are symmetric
Chart: MRAM Read
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 34.3749 | 63.742 | 113.0185 | 201.2656 | 308.8345 | 419.14 | 534.2382 | 605.0304 | 628.2264
Latency | 81.4548 | 87.8541 | 99.0988 | 111.2957 | 145.0615 | 213.7711 | 335.4309 | 592.3669 | 1140.99
 | 81.4548 | 85.4548 | 93.4548 | 109.4548 | 141.4548 | 205.4548 | 333.4548 | 589.4548 | 1101.4548
Chart: MRAM Write
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 42.6136 | 79.3959 | 142.7862 | 239.4263 | 355.329 | 467.0049 | 555.5843 | 616.7485 | 633.2199
Latency | 65.7067 | 70.5326 | 78.4389 | 93.557 | 126.0803 | 191.861 | 322.5433 | 581.1121 | 1131.9922
 | 65.7067 | 69.7067 | 77.7067 | 93.7067 | 125.7067 | 189.7067 | 317.7067 | 573.7067 | 1085.7067
The sustained MRAM bandwidth increases
with data transfer size
PROGRAMMING RECOMMENDATION 1
For data movement between the DPU’s MRAM bank and the WRAM, use large DMA transfer sizes when all the accessed data is going to be used.

## Slide 123: MRAM Read and Write Latency (IV)
MRAM latency changes slowly between 8 and 128 bytes
Chart: MRAM Read
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 34.3749 | 63.742 | 113.0185 | 201.2656 | 308.8345 | 419.14 | 534.2382 | 605.0304 | 628.2264
Latency | 81.4548 | 87.8541 | 99.0988 | 111.2957 | 145.0615 | 213.7711 | 335.4309 | 592.3669 | 1140.99
 | 81.4548 | 85.4548 | 93.4548 | 109.4548 | 141.4548 | 205.4548 | 333.4548 | 589.4548 | 1101.4548
Chart: MRAM Write
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 42.6136 | 79.3959 | 142.7862 | 239.4263 | 355.329 | 467.0049 | 555.5843 | 616.7485 | 633.2199
Latency | 65.7067 | 70.5326 | 78.4389 | 93.557 | 126.0803 | 191.861 | 322.5433 | 581.1121 | 1131.9922
 | 65.7067 | 69.7067 | 77.7067 | 93.7067 | 125.7067 | 189.7067 | 317.7067 | 573.7067 | 1085.7067
For small transfers, the fixed cost () dominates the variable cost ()
PROGRAMMING RECOMMENDATION 2
For small transfers between the MRAM bank and the WRAM, fetch more bytes than necessary within a 128-byte limit. Doing so increases the likelihood of finding data in WRAM for later accesses (i.e., the program can check whether the desired data is in WRAM before issuing a new MRAM access).

## Slide 124: MRAM Read and Write Latency (V)
2,048-byte transfers are only 4% faster than 1,024-byte transfers
Chart: MRAM Read
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 34.3749 | 63.742 | 113.0185 | 201.2656 | 308.8345 | 419.14 | 534.2382 | 605.0304 | 628.2264
Latency | 81.4548 | 87.8541 | 99.0988 | 111.2957 | 145.0615 | 213.7711 | 335.4309 | 592.3669 | 1140.99
 | 81.4548 | 85.4548 | 93.4548 | 109.4548 | 141.4548 | 205.4548 | 333.4548 | 589.4548 | 1101.4548
Chart: MRAM Write
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
 | 42.6136 | 79.3959 | 142.7862 | 239.4263 | 355.329 | 467.0049 | 555.5843 | 616.7485 | 633.2199
Latency | 65.7067 | 70.5326 | 78.4389 | 93.557 | 126.0803 | 191.861 | 322.5433 | 581.1121 | 1131.9922
 | 65.7067 | 69.7067 | 77.7067 | 93.7067 | 125.7067 | 189.7067 | 317.7067 | 573.7067 | 1085.7067
Larger transfers require more WRAM, which may limit the number of tasklets
PROGRAMMING RECOMMENDATION 3
Choose the data transfer size between the MRAM bank and the WRAM based on the program’s WRAM usage, as it imposes a tradeoff between the sustained MRAM bandwidth and the number of tasklets that can run in the DPU (which is dictated by the limited WRAM capacity).

## Slide 125: MRAM Bandwidth
Goal
  Measure MRAM bandwidth for different access patterns
Microbenchmarks
  Latency of a single DMA transfer for different transfer sizes
    mram_read(); // MRAM-WRAM DMA transfer
    mram_write(); // WRAM-MRAM DMA transfer
  STREAM benchmark
    COPY, COPY-DMA
    ADD, SCALE, TRIAD
  Strided access pattern
    Coarse-grain strided access
    Fine-grain strided access
  Random access pattern (GUPS)
We do include accesses to MRAM

## Slide 126: STREAM Benchmark in MRAM
// COPY
// Load current MRAM block to WRAM
mram_read((__mram_ptr void const*)mram_address_A, bufferA,
SIZE * sizeof(uint64_t));
for(int i = 0; i < SIZE; i++){
bufferB[i] = bufferA[i];
}
// Write WRAM block to MRAM
mram_write(bufferB, (__mram_ptr void*)mram_address_B,
SIZE * sizeof(uint64_t));
// COPY-DMA
// Load current MRAM block to WRAM
mram_read((__mram_ptr void const*)mram_address_A, bufferA,
SIZE * sizeof(uint64_t));
// Write WRAM block to MRAM
mram_write(bufferA, (__mram_ptr void*)mram_address_B,
SIZE * sizeof(uint64_t));

## Slide 127: STREAM Benchmark: COPY-DMA
Chart: STREAM (MRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY-DMA | 596.0419 | 624.2088 | 624.388 | 624.4544 | 624.6304 | 623.8208 | 624.2254 | 624.3448 | 624.0396 | 624.0496 | 623.9136 | 623.8971 | 623.9335 | 623.5294 | 623.6519 | 624.023
COPY | 178.436 | 356.5621 | 534.1774 | 622.4553 | 623.3176 | 623.2944 | 622.8515 | 623.3176 | 623.4367 | 623.0332 | 623.0729 | 623.0629 | 623.1952 | 622.9671 | 622.9043 | 623.2977
ADD | 121.6017 | 243.1098 | 364.467 | 485.8173 | 604.0971 | 622.0015 | 622.1421 | 622.1728 | 622.1047 | 622.0761 | 621.9136 | 621.9488 | 622.0059 | 622.1838 | 622.2168 | 622.386
SCALE | 3.7965 | 7.5929 | 11.3878 | 15.1851 | 18.9799 | 22.7748 | 26.568 | 30.3692 | 34.1543 | 37.9461 | 41.74 | 41.9844 | 41.9823 | 41.978 | 41.9784 | 42.0067
TRIAD | 5.5523 | 11.1044 | 16.654 | 22.2081 | 27.7585 | 33.3075 | 38.8557 | 44.4133 | 49.948 | 55.4921 | 61.0389 | 61.5637 | 61.5607 | 61.5493 | 61.5525 | 61.5947
The sustained bandwidth of COPY-DMA is close to
the theoretical maximum (700 MB/s): ~1.6 TB/s for 2,556 DPUs
COPY-DMA saturates with two tasklets, even though
the DMA engine can perform only one transfer at a time
Using two or more tasklets guarantees that there is always
a DMA request enqueued to keep the DMA engine busy

## Slide 128: STREAM Benchmark: Bandwidth Saturation (I)
Chart: STREAM (MRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY-DMA | 596.0419 | 624.2088 | 624.388 | 624.4544 | 624.6304 | 623.8208 | 624.2254 | 624.3448 | 624.0396 | 624.0496 | 623.9136 | 623.8971 | 623.9335 | 623.5294 | 623.6519 | 624.023
COPY | 178.436 | 356.5621 | 534.1774 | 622.4553 | 623.3176 | 623.2944 | 622.8515 | 623.3176 | 623.4367 | 623.0332 | 623.0729 | 623.0629 | 623.1952 | 622.9671 | 622.9043 | 623.2977
ADD | 121.6017 | 243.1098 | 364.467 | 485.8173 | 604.0971 | 622.0015 | 622.1421 | 622.1728 | 622.1047 | 622.0761 | 621.9136 | 621.9488 | 622.0059 | 622.1838 | 622.2168 | 622.386
SCALE | 3.7965 | 7.5929 | 11.3878 | 15.1851 | 18.9799 | 22.7748 | 26.568 | 30.3692 | 34.1543 | 37.9461 | 41.74 | 41.9844 | 41.9823 | 41.978 | 41.9784 | 42.0067
TRIAD | 5.5523 | 11.1044 | 16.654 | 22.2081 | 27.7585 | 33.3075 | 38.8557 | 44.4133 | 49.948 | 55.4921 | 61.0389 | 61.5637 | 61.5607 | 61.5493 | 61.5525 | 61.5947
COPY and ADD saturate at 4 and 6 tasklets, respectively
SCALE and TRIAD saturate at 11 tasklets
The latency of MRAM accesses becomes longer than the pipeline latency after 4 and 6 tasklets for COPY and ADD, respectively
The pipeline latency of SCALE and TRIAD is longer than the MRAM latency for any number of tasklets (both use costly MUL)

## Slide 129: STREAM Benchmark: Bandwidth Saturation (II)
Chart: STREAM (MRAM, INT64, 1DPU)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
COPY-DMA | 596.0419 | 624.2088 | 624.388 | 624.4544 | 624.6304 | 623.8208 | 624.2254 | 624.3448 | 624.0396 | 624.0496 | 623.9136 | 623.8971 | 623.9335 | 623.5294 | 623.6519 | 624.023
COPY | 178.436 | 356.5621 | 534.1774 | 622.4553 | 623.3176 | 623.2944 | 622.8515 | 623.3176 | 623.4367 | 623.0332 | 623.0729 | 623.0629 | 623.1952 | 622.9671 | 622.9043 | 623.2977
ADD | 121.6017 | 243.1098 | 364.467 | 485.8173 | 604.0971 | 622.0015 | 622.1421 | 622.1728 | 622.1047 | 622.0761 | 621.9136 | 621.9488 | 622.0059 | 622.1838 | 622.2168 | 622.386
SCALE | 3.7965 | 7.5929 | 11.3878 | 15.1851 | 18.9799 | 22.7748 | 26.568 | 30.3692 | 34.1543 | 37.9461 | 41.74 | 41.9844 | 41.9823 | 41.978 | 41.9784 | 42.0067
TRIAD | 5.5523 | 11.1044 | 16.654 | 22.2081 | 27.7585 | 33.3075 | 38.8557 | 44.4133 | 49.948 | 55.4921 | 61.0389 | 61.5637 | 61.5607 | 61.5493 | 61.5525 | 61.5947
KEY OBSERVATION 5
When the access latency to an MRAM bank for a streaming benchmark (COPY-DMA, COPY, ADD) is larger than the pipeline latency (i.e., execution latency of arithmetic operations and WRAM accesses), the performance of the DPU saturates at a number of tasklets smaller than 11. This is a memory-bound workload.
When the pipeline latency for a streaming benchmark (SCALE, TRIAD) is larger than the MRAM access latency, the performance of a DPU saturates at 11 tasklets. This is a compute-bound workload.

## Slide 130: MRAM Bandwidth
Goal
  Measure MRAM bandwidth for different access patterns
Microbenchmarks
  Latency of a single DMA transfer for different transfer sizes
    mram_read(); // MRAM-WRAM DMA transfer
    mram_write(); // WRAM-MRAM DMA transfer
  STREAM benchmark
    COPY, COPY-DMA
    ADD, SCALE, TRIAD
  Strided access pattern
    Coarse-grain strided access
    Fine-grain strided access
  Random access pattern (GUPS)
We do include accesses to MRAM

## Slide 131: Strided and Random Access to MRAM
// COARSE-GRAINED STRIDED ACCESS
// Load current MRAM block to WRAM
mram_read((__mram_ptr void const*)mram_address_A, bufferA,
SIZE * sizeof(uint64_t));
mram_read((__mram_ptr void const*)mram_address_B, bufferB,
SIZE * sizeof(uint64_t));
for(int i = 0; i < SIZE; i += stride){
bufferB[i] = bufferA[i];
}
// Write WRAM block to MRAM
mram_write(bufferB, (__mram_ptr void*)mram_address_B,
SIZE * sizeof(uint64_t));
// FINE-GRAINED STRIDED & RANDOM ACCESS
for(int i = 0; i < SIZE; i += stride){
int index = i * sizeof(uint64_t);
// Load current MRAM element to WRAM
mram_read((__mram_ptr void const*)(mram_address_A + index), bufferA, sizeof(uint64_t));
// Write WRAM element to MRAM
mram_write(bufferA, (__mram_ptr void*)(mram_address_B + index), sizeof(uint64_t));
}
Notes: For random accesses we implement the GUPS benchmark.

## Slide 132: Strided and Random Accesses (I)
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
Large difference in maximum sustained bandwidth between coarse-grained and fine-grained DMA
Coarse-grained DMA uses 1,024-byte transfers,
while fine-grained DMA uses 8-byte transfers
Random access achieves very similar maximum sustained bandwidth to fine-grained strided approach

## Slide 133: Strided and Random Accesses (II)
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
The sustained MRAM bandwidth of coarse-grained DMA decreases as the stride increases
The effective utilization of the transferred data decreases
as the stride becomes larger (e.g., a stride 4 means that only one fourth of the transferred data is used)

## Slide 134: Strided and Random Accesses (III)
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
For a stride of 16 or larger, the fine-grained DMA approach achieves higher bandwidth
With stride 16, only one sixteenth of the maximum sustained bandwidth (622.36 MB/s) of coarse-grained DMA
is effectively used, which is lower than
the bandwidth of fine-grained DMA (72.58 MB/s)

## Slide 135: Strided and Random Accesses (IV)
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
Chart: (a) Coarse-grained Strided (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Coarse-grained DMA - 1 tasklet | 104.4411 | 88.6824 | 68.0677 | 46.5167 | 28.4726 | 16.0308 | 8.5606 | 4.4253 | 2.26 | 1.1421 | 0.57485 | 0.28775 | 0.1439
Coarse-grained DMA - 2 tasklets | 208.82 | 177.2605 | 136.0353 | 76.7112 | 38.8607 | 19.4647 | 9.7362 | 4.8676 | 2.4336 | 1.2167 | 0.60835 | 0.30423 | 0.15209
Coarse-grained DMA - 4 tasklets | 417.2883 | 307.4048 | 155.5432 | 77.8409 | 38.9703 | 19.4812 | 9.7414 | 4.8705 | 2.4349 | 1.2175 | 0.60879 | 0.30441 | 0.1522
Coarse-grained DMA - 8 tasklets | 622.584 | 311.0985 | 155.5712 | 77.8863 | 38.9394 | 19.4761 | 9.7362 | 4.8683 | 2.4343 | 1.217 | 0.60856 | 0.30429 | 0.15213
Coarse-grained DMA - 16 tasklets | 622.3575 | 311.1809 | 155.6686 | 77.8648 | 38.9487 | 19.4764 | 9.7364 | 4.8672 | 2.434 | 1.217 | 0.6085 | 0.30425 | 0.15212
Chart: (b) Fine-grained Strided & Random (MRAM, 1 DPU)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | GUPS
Fine-grained DMA - 1 tasklet | 34.9599 | 34.9527 | 35.0044 | 34.9545 | 34.9605 | 34.9629 | 34.981 | 34.9829 | 34.9544 | 34.965 | 34.9148 | 34.874 | 34.8503 | 14.7424
Fine-grained DMA - 2 tasklets | 65.5561 | 65.5495 | 65.5539 | 65.5524 | 65.5746 | 65.5663 | 65.5648 | 65.5426 | 65.5315 | 65.4911 | 65.3776 | 65.1045 | 64.9275 | 28.9639
Fine-grained DMA - 4 tasklets | 72.2013 | 72.1963 | 72.1968 | 72.2018 | 72.2082 | 72.2436 | 72.1677 | 72.1705 | 72.249 | 72.1599 | 71.8885 | 71.6513 | 71.7661 | 54.3524
Fine-grained DMA - 8 tasklets | 72.9231 | 72.9148 | 74.4314 | 74.4176 | 71.5138 | 72.9208 | 74.409 | 72.886 | 73.0069 | 71.2596 | 71.1111 | 72.6241 | 71.1676 | 72.6604
Fine-grained DMA - 16 tasklets | 74.0384 | 72.5676 | 73.2904 | 73.2842 | 73.2904 | 73.3163 | 74.0227 | 73.2205 | 73.2906 | 73.24 | 73.2999 | 72.8752 | 72.58 | 72.5815
PROGRAMMING RECOMMENDATION 4
For strided access patterns with a stride smaller than 16 8-byte elements, fetch a large contiguous chunk (e.g., 1,024 bytes) from a DPU’s MRAM bank.
For strided access patterns with larger strides and random access patterns, fetch only the data elements that are needed from an MRAM bank.

## Slide 136: Microbenchmark: Strided and Random
Strided and random accesses to MRAM

## Slide 137: DPU: Arithmetic Throughput vs. Operational Intensity

## Slide 138: Arithmetic Throughput vs. Operational Intensity (I)
Goal
  Characterize memory-bound regions and compute-bound regions for different datatypes and operations
Microbenchmark
  We load one chunk of an MRAM array into WRAM
  Perform a variable number of operations on the data
  Write back to MRAM
The experiment is inspired by the Roofline model*
We define operational intensity (OI) as the number of arithmetic operations performed per byte accessed from MRAM (OP/B)
The pipeline latency changes with the operational intensity, but the MRAM access latency is fixed
*S. Williams et al., “Roofline: An Insightful Visual Performance Model for Multi-core Architectures,” CACM, 2009

## Slide 139: Arithmetic Throughput vs. Operational Intensity (II)
int repetitions = input_repeat >= 1.0 ? (int)input_repeat : 1;
int stride = input_repeat >= 1.0 ? 1 : (int)(1 / input_repeat);
// Load current MRAM block to WRAM
mram_read((__mram_ptr void const*)mram_address_A, bufferA, SIZE * sizeof(T));
// Update
for(int r = 0; r < repetitions; r++){
for(int i = 0; i < SIZE; i+=stride){
#ifdef ADD
bufferA[i] += scalar; // ADD
#elif SUB
bufferA[i] -= scalar; // SUB
#elif MUL
bufferA[i] *= scalar; // MUL
#elif DIV
bufferA[i] /= scalar; // DIV
#endif
}
}
// Write WRAM block to MRAM
mram_write(bufferA, (__mram_ptr void*)mram_address_B, SIZE * sizeof(T));
input_repeat greater or equal to 1 indicates the (integer) number of repetitions per input element
input_repeat smaller than 1 indicates the fraction of elements that are updated

## Slide 140: Arithmetic Throughput vs. Operational Intensity (III)
We show results of arithmetic throughput vs. operational intensity for
(a) 32-bit integer ADD, (b) 32-bit integer MUL,
(c) 32-bit floating-point ADD, and (d) 32-bit floating-point MUL
(results for other datatypes and operations show similar trends)

## Slide 141: Arithmetic Throughput vs. Operational Intensity (IV)
Chart: Operational Intensity (OP/B)
Memory-bound region
Compute-bound region
In the memory-bound region, the arithmetic throughput increases with the operational intensity
In the compute-bound region, the arithmetic throughput is flat at its maximum
The throughput saturation point is the operational intensity
where the transition between
the memory-bound region and the compute-bound region happens
The throughput saturation point is as low as ¼ OP/B,
i.e., 1 integer addition per every 32-bit element fetched

## Slide 142: Arithmetic Throughput vs. Operational Intensity (V)
KEY OBSERVATION 6
The arithmetic throughput of a DRAM Processing Unit (DPU) saturates at low or very low operational intensity (e.g., 1 integer addition per 32-bit element). Thus, the DPU is fundamentally a compute-bound processor.
We expect most real-world workloads be compute-bound in the UPMEM PIM architecture.

## Slide 143: Microbenchmark: Arithmetic Throughput vs. Operational Intensity
Arithmetic Throughput versus Operational Intensity

## Slide 144: Benchmarking and Workload Suitability

## Slide 145: PrIM Benchmarks
Goal
  A common set of workloads that can be used to
    evaluate the UPMEM PIM architecture,
    compare software improvements and compilers,
    compare future PIM architectures and hardware
Two key selection criteria:
  Selected workloads from different application domains
  Memory-bound workloads on processor-centric architectures
14 different workloads, 16 different benchmarks*
*There are two versions for two of the workloads (HST, SCAN).

## Slide 146: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 147: Roofline Model
Chart: Arithmetic Intensity (OP/B)
| 0.14799999999999999 | 8.3000000000000004E-2 | 8.7999999999999995E-2 | 0.107 | 0.1 | 0.11 | 9.7000000000000003E-2 | 0.125 | 0.15 | 0.14299999999999999 | 0.25 | 0.125 | 0.25 | 0.16300000000000001
Performance (GOPS) | 0.791 | 2.749 | 4.774 | 8.988 | 0.693 | 0.95 | 2.331 | 1.525 | 5.551 | 2.119 | 0.741 | 0.762 | 1.68 | 1.067
Peak compute performance
Intel Advisor on an Intel Xeon E3-1225 v6 CPU
DRAM
L3
All workloads fall in the memory-bound area of the Roofline

## Slide 148: PrIM Benchmarks: Diversity
PrIM benchmarks are diverse:
  Memory access patterns
  Operations and datatypes
  Communication/synchronization

## Slide 149: PrIM Benchmarks: Inter-DPU Communication
Inter-DPU communication
  Result merging:
    SEL, UNI, HST-S, HST-L, RED
    Only DPU-CPU transfers
  Redistribution of intermediate results:
    BFS, MLP, NW, SCAN-SSA, SCAN-RSS
    DPU-CPU and CPU-DPU transfers

## Slide 150: PrIM Benchmarks
16 benchmarks and scripts for evaluation
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 151: Outline
Introduction
  Accelerator Model
  UPMEM-based PIM System Overview
UPMEM PIM Programming
  Vector Addition
  CPU-DPU Data Transfers
  Inter-DPU Communication
  CPU-DPU/DPU-CPU Transfer Bandwidth
DRAM Processing Unit
  Arithmetic Throughput
  WRAM and MRAM Bandwidth
PrIM Benchmarks
  Roofline Model
  Benchmark Diversity
Evaluation
  Strong and Weak Scaling
  Comparison to CPU and GPU
Key Takeaways

## Slide 152: Evaluation Methodology
We evaluate the 16 PrIM benchmarks on two UPMEM-based systems:
  2,556-DPU system
  640-DPU system
Strong and weak scaling experiments on the 2,556-DPU system
  1 DPU with different numbers of tasklets
  1 rank (strong and weak)
  Up to 32 ranks
Strong scaling refers to how the execution time of a program solving a particular problem varies with the number of processors for a fixed problem size
Weak scaling refers to how the execution time of a program solving a particular problem varies
with the number of processors for a fixed problem size per processor

## Slide 153: Evaluation Methodology
We evaluate the 16 PrIM benchmarks on two UPMEM-based systems:
  2,556-DPU system
  640-DPU system
Strong and weak scaling experiments on the 2,556-DPU system
  1 DPU with different numbers of tasklets
  1 rank (strong and weak)
  Up to 32 ranks
Comparison of both UPMEM-based PIM systems to state-of-the-art CPU and GPU
  Intel Xeon E3-1240 CPU
  NVIDIA Titan V GPU

## Slide 154: 2,560-DPU System
UPMEM-based PIM system with 20 UPMEM DIMMs of 16 chips each (40 ranks)
  P21 DIMMs
  Dual x86 socket
    UPMEM DIMMs coexist with regular DDR4 DIMMs
    2 memory controllers/socket (3 channels each)
    2 conventional DDR4 DIMMs on one channel of one controller
2560 DPUs*
* There are 4 faulty DPUs in the system that we use in our experiments. Thus, the maximum number of DPUs we can use is 2,556.
160 GB

## Slide 155: 640-DPU System
UPMEM-based PIM system with 10 UPMEM DIMMs of 8 chips each (10 ranks)
  E19 DIMMs
  x86 socket
    2 memory controllers (3 channels each)
    2 conventional DDR4 DIMMs on one channel of one controller
640 DPUs
40 GB

## Slide 156: Datasets
Strong and weak scaling experiments
The PrIM benchmarks repository includes
all datasets and scripts used in our evaluation
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 157: Strong Scaling: 1 DPU (I)
Strong scaling experiments on 1 DPU
  We set the number of tasklets to 1, 2, 4, 8, and 16
  We show the breakdown of execution time:
    DPU: Execution time on the DPU
    Inter-DPU: Time for inter-DPU communication via the host CPU
    CPU-DPU: Time for CPU to DPU transfer of input data
    DPU-CPU: Time for DPU to CPU transfer of final results
  Speedup over 1 tasklet
Chart: VA
| 1 | 2 | 4 | 8 | 16
DPU | 883.812 | 443.165 | 228.265 | 114.315 | 76.323
Inter-DPU | 0 | 0 | 0 | 0 | 0
CPU-DPU | 94.1904 | 94.1904 | 94.1904 | 94.1904 | 94.1904
DPU-CPU | 87.7304 | 87.7304 | 87.7304 | 87.7304 | 87.7304
Speedup | 1 | 1.9943 | 3.8719 | 7.7314 | 11.5799

## Slide 158: Strong Scaling: 1 DPU (II)
VA, GEMV, SpMV, SEL, UNI, TS, MLP, NW, HST-S, RED, SCAN-SSA (Scan kernel), SCAN-RSS (both kernels), and TRNS (Step 2 kernel), the best performing number of tasklets is 16
Speedups 1.5-2.0x as we double the number of tasklets from 1 to 8.
Speedups 1.2-1.5x from 8 to 16, since the pipeline throughput saturates at 11 tasklets
KEY OBSERVATION 10
A number of tasklets greater than 11 is a good choice for most real-world workloads we tested (16 kernels out of 19 kernels from 16 benchmarks), as it fully utilizes the DPU’s pipeline.

## Slide 159: Strong Scaling: 1 DPU (III)
VA, GEMV, SpMV, BS, TS, MLP, HST-S do not use intra-DPU synchronization primitives
BFS, HST-L, TRNS (Step 3) use mutexes, which cause contention when accessing shared data structures
In SEL, UNI, NW, RED, SCAN-SSA (Scan kernel), SCAN-RSS (both kernels), synchronization is lightweight

## Slide 160: Strong Scaling: 1 DPU (IV)
Chart: HST-L
| 1 | 2 | 4 | 8 | 16
DPU | 1631.278 | 819.023 | 411.71 | 303.674 | 436.309
Inter-DPU | 0.185 | 0.127 | 0.151 | 0.144 | 0.142
CPU-DPU | 19.9726 | 19.9726 | 19.9726 | 19.9726 | 19.9726
DPU-CPU | 0 | 0 | 0 | 0 | 0
Speedup | 1 | 1.9917 | 3.9622 | 5.3718 | 3.7388
VA, GEMV, SpMV, BS, TS, MLP, HST-S do not use intra-DPU synchronization primitives
BFS, HST-L, TRNS (Step 3) use mutexes, which cause contention when accessing shared data structures
KEY OBSERVATION 11
Intensive use of intra-DPU synchronization across tasklets (e.g., mutexes, barriers, handshakes) may limit scalability, sometimes causing the best performing number of tasklets to be lower than 11.
In SEL, UNI, NW, RED, SCAN-SSA (Scan kernel), SCAN-RSS (both kernels), synchronization is lightweight

## Slide 161: Strong Scaling: 1 DPU (V)
Chart: SCAN-SSA
| 1 | 2 | 4 | 8 | 16
DPU (Add) | 602.751 | 301.534 | 150.881 | 101.075 | 101.071
DPU (Scan) | 1123.974 | 617.625 | 359.495 | 230.09 | 179.014
Inter-DPU | 0.151 | 0.091 | 0.107 | 0.138 | 0.201
CPU-DPU | 141.4454 | 141.4454 | 141.4454 | 141.4454 | 141.4454
DPU-CPU | 265.3682 | 265.3682 | 265.3682 | 265.3682 | 265.3682
Speedup (Scan) | 1 | 1.8198 | 3.1265 | 4.8849 | 6.2787
Speedup (Add) | 1 | 1.9989 | 3.9949 | 5.9634 | 5.9636
SCAN-SSA (Add kernel) is not compute-intensive. Thus, performance saturates with less that 11 tasklets (recall STREAM ADD).
BS shows similar behavior
KEY OBSERVATION 12
Most real-world workloads are in the compute-bound region of the DPU (all kernels except SCAN-SSA (Add kernel) and BS), i.e., the pipeline latency dominates the MRAM access latency.

## Slide 162: Strong Scaling: 1 DPU (VI)
TRNS performs step 1 of the matrix transposition via the CPU-DPU transfer.
Using small transfers (8 elements) does not exploit full CPU-DPU bandwidth
KEY OBSERVATION 13
Transferring large data chunks from/to the host CPU is preferred for input data and output results due to higher sustained CPU-DPU/DPU-CPU bandwidths.
The amount of time spent on CPU-DPU and DPU-CPU transfers is low compared to the time spent on DPU execution
Chart: TRNS
| 1 | 2 | 4 | 8 | 16
DPU (Step 2) | 2632.501 | 1319.618 | 659.935 | 330.185 | 236.16
DPU (Step 3) | 1158.888 | 581.713 | 292.734 | 156.289 | 169.425
Inter-DPU | 0 | 0 | 0 | 0 | 0
CPU-DPU (Step 1) | 10590.0262 | 10590.0262 | 10590.0262 | 10590.0262 | 10590.0262
DPU-CPU | 113.507 | 113.507 | 113.507 | 113.507 | 113.507
Speedup (Step 3) | 1 | 1.9922 | 3.9588 | 7.415 | 6.8401
Speedup (Step 2) | 1 | 1.9949 | 3.989 | 7.9728 | 11.1471
Notes: Fifth
TRNS

## Slide 163: Strong Scaling: 1 Rank (I)
Strong scaling experiments on 1 rank
  We set the number of tasklets to the best performing one
  The number of DPUs is 1, 4, 16, 64
  We show the breakdown of execution time:
    DPU: Execution time on the DPU
    Inter-DPU: Time for inter-DPU communication via the host CPU
    CPU-DPU: Time for CPU to DPU transfer of input data
    DPU-CPU: Time for DPU to CPU transfer of final results
  Speedup over 1 DPU
Chart: NW
| 1 | 4 | 16 | 64
DPU | 1379.001 | 615.103 | 187.609 | 80.096
Inter-DPU | 0.566 | 189.892 | 243.127 | 288.782
CPU-DPU | 213.6558 | 258.8882 | 260.3884 | 287.0798
DPU-CPU | 318.872 | 318.9462 | 299.822 | 309.9938
Speedup | 1 | 2.2419 | 7.3504 | 17.2169

## Slide 164: Strong Scaling: 1 Rank (II)
VA, GEMV, SpMV, SEL, UNI, BS, TS, MLP, HST-S, HSTS-L, RED, SCAN-SSA (both kernel), SCAN-RSS (both kernels), and TRNS (both kernels) scale linearly with the number of DPUs
Scaling is sublinear for BFS and NW
BFS suffers load imbalance due to irregular graph topology
NW computes a diagonal of a 2D matrix in each iteration.
More DPUs does not mean more parallelization in shorter diagonals.

## Slide 165: Strong Scaling: 1 Rank (III)
VA, GEMV, SpMV, BS, TS, TRNS do not need inter-DPU synchronization
SEL, UNI, HST-S, HST-L, RED, SCAN-SSA, SCAN-RSS need inter-DPU synchronization but 64 DPUs still obtain the best performance
BFS, MLP, NW require heavy inter-DPU synchronization, involving DPU-CPU and CPU-DPU transfers

## Slide 166: Strong Scaling: 1 Rank (IV)
VA, GEMV, TS, MLP, HST-S, HST-L, RED, SCAN-SSA, SCAN-RSS, TRNS use parallel transfers.
CPU-DPU and DPU-CPU transfer times decrease as we increase the number of DPUs
BS, NW use parallel transfers but do not reduce transfer times:
BS transfers a complete array to all DPUs.
NW does not use all DPUs in all iterations
SpMV, SEL, UNI, BFS cannot use parallel transfers, as the transfer size per DPU is not fixed
PROGRAMMING RECOMMENDATION 5
Parallel CPU-DPU/DPU-CPU transfers inside a rank of DPUs are recommended for real-world workloads when all transferred buffers are of the same size.

## Slide 167: Strong Scaling: 32 Ranks (I)
Strong scaling experiments on 32 rank
  We set the number of tasklets to the best performing one
  The number of DPUs is 256, 512, 1024, 2048
  We show the breakdown of execution time:
    DPU: Execution time on the DPU
    Inter-DPU: Time for inter-DPU communication via the host CPU
    We do not show CPU-DPU/DPU-CPU transfer times
  Speedup over 256 DPUs
Chart: MLP
| 256 | 512 | 1024 | 2048
DPU | 286.0227 | 143.4857 | 72.2427 | 39.7453
Inter-DPU | 828.3117 | 940.8107 | 705.393 | 502.6177
Speedup | 1 | 1.9934 | 3.9592 | 7.1964

## Slide 168: Strong Scaling: 32 Ranks (II)
SpMV, BFS, NW do not scale linearly due to load imbalance
KEY OBSERVATION 14
Load balancing across DPUs ensures linear reduction of the execution time spent on the DPUs for a given problem size, when all available DPUs are used (as observed in strong scaling experiments).
VA, GEMV, SEL, UNI, BS, TS, MLP, HST-S, HSTS-L, RED, SCAN-SSA (both kernel), SCAN-RSS (both kernels), and TRNS (both kernels) scale linearly with the number of DPUs

## Slide 169: Strong Scaling: 32 Ranks (III)
KEY OBSERVATION 15
The overhead of merging partial results from DPUs in the host CPU is tolerable across all PrIM benchmarks that need it.
SEL, UNI, HST-S, HST-L, RED only need to merge final results
KEY OBSERVATION 16
Complex synchronization across DPUs (i.e., inter-DPU synchronization involving two-way communication with the host CPU) imposes significant overhead, which limits scalability to more DPUs.
BFS, MLP, NW, SCAN-SSA, SCAN-RSS have more complex communication

## Slide 170: Weak Scaling: 1 Rank
KEY OBSERVATION 17
Equally-sized problems assigned to different DPUs and little/no inter-DPU synchronization lead to linear weak scaling of the execution time spent on the DPUs (i.e., constant execution time when we increase the number of DPUs and the dataset size accordingly).
KEY OBSERVATION 18
Sustained bandwidth of parallel CPU-DPU/DPU-CPU transfers inside a rank of DPUs increases sublinearly with the number of DPUs.
Chart: VA
| 1 | 4 | 16 | 64
DPU | 76.323 | 76.336 | 76.245 | 76.204
Inter-DPU | 0 | 0 | 0 | 0
CPU-DPU | 94.1904 | 145.6756 | 221.9448 | 298.3084
DPU-CPU | 87.7304 | 103.5604 | 156.1164 | 282.0878

## Slide 171: CPU/GPU: Evaluation Methodology
Comparison of both UPMEM-based PIM systems to state-of-the-art CPU and GPU
  Intel Xeon E3-1240 CPU
  NVIDIA Titan V GPU
We use state-of-the-art CPU and GPU counterparts of PrIM benchmarks
  https://github.com/CMU-SAFARI/prim-benchmarks
We use the largest dataset that we can fit in the GPU memory
We show overall execution time, including DPU kernel time and inter DPU communication

## Slide 172: CPU/GPU: Performance Comparison (I)
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
The 2,556-DPU and the 640-DPU systems outperform the CPU for all benchmarks except SpMV, BFS, and NW
The 2,556-DPU and the 640-DPU are, respectively, 93.0x and 27.9x faster than the CPU for 13 of the PrIM benchmarks

## Slide 173: CPU/GPU: Performance Comparison (II)
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
The 2,556-DPU outperforms the GPU
for 10 PrIM benchmarks with an average of 2.54x
The performance of the 640-DPU is within 65%
the performance of the GPU for the same 10 PrIM benchmarks

## Slide 174: CPU/GPU: Performance Comparison (III)
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY OBSERVATION 19
The UPMEM-based PIM system can outperform a state-of-the-art GPU on workloads with three key characteristics:
Streaming memory accesses
No or little inter-DPU synchronization
No or little use of integer multiplication, integer division, or floating point operations
These three key characteristics make a workload potentially suitable to the UPMEM PIM architecture.

## Slide 175: CPU/GPU: Energy Comparison (I)
The 640-DPU system consumes on average 1.64x less energy than the CPU for all 16 PrIM benchmarks
For 12 benchmarks, the 640-DPU system provides energy savings
of 5.23x over the CPU
Chart: Energy savings over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 23.54 | 93.55 | 120.25 | 0.06 | 13.74 | 13.74 | 6.56 | 6.73 | 6.73 | 9.75 | 156.18 | 6.23 | 243.97 | 0.36 | 79.24 | 15.82 | 9.8605 | 21.793 | 13.2101
640 DPUs | 5.22 | 28.54 | 39.14 | 1.6306 | 16.35 | 4.13 | 1.28 | 1.79 | 2.47 | 6.57 | 4.855 | 0.06 | 3.5886 | 0.0037 | 0.8168 | 0.0366 | 5.4675 | 0.22072 | 1.6354

## Slide 176: CPU/GPU: Energy Comparison (II)
Chart: Energy savings over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 23.54 | 93.55 | 120.25 | 0.06 | 13.74 | 13.74 | 6.56 | 6.73 | 6.73 | 9.75 | 156.18 | 6.23 | 243.97 | 0.36 | 79.24 | 15.82 | 9.8605 | 21.793 | 13.2101
640 DPUs | 5.22 | 28.54 | 39.14 | 1.6306 | 16.35 | 4.13 | 1.28 | 1.79 | 2.47 | 6.57 | 4.855 | 0.06 | 3.5886 | 0.0037 | 0.8168 | 0.0366 | 5.4675 | 0.22072 | 1.6354
KEY OBSERVATION 20
The UPMEM-based PIM system provides large energy savings over a state-of-the-art CPU due to higher performance (thus, lower static energy) and less data movement between memory and processors.
The UPMEM-based PIM system provides energy savings over a state-of-the-art CPU/GPU on workloads where it outperforms the CPU/GPU.
This is because the source of both performance improvement and energy savings is the same: the significant reduction in data movement between the memory and the processor cores, which the UPMEM-based PIM system can provide for PIM-suitable workloads.

## Slide 177: Outline
Introduction
  Accelerator Model
  UPMEM-based PIM System Overview
UPMEM PIM Programming
  Vector Addition
  CPU-DPU Data Transfers
  Inter-DPU Communication
  CPU-DPU/DPU-CPU Transfer Bandwidth
DRAM Processing Unit
  Arithmetic Throughput
  WRAM and MRAM Bandwidth
PrIM Benchmarks
  Roofline Model
  Benchmark Diversity
Evaluation
  Strong and Weak Scaling
  Comparison to CPU and GPU
Key Takeaways

## Slide 178: Key Takeaway 1
Chart: Operational Intensity (OP/B)
Memory-bound region
Compute-bound region
The throughput saturation point is as low as ¼ OP/B,
i.e., 1 integer addition per every 32-bit element fetched
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound.
As a result, the most suitable workloads are memory-bound.

## Slide 179: Key Takeaway 2
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 2
The most well-suited workloads for the UPMEM PIM architecture use no arithmetic operations or use only simple operations (e.g., bitwise operations and integer addition/subtraction).

## Slide 180: Key Takeaway 3
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 3
The most well-suited workloads for the UPMEM PIM architecture require little or no communication across DPUs (inter-DPU communication).

## Slide 181: Key Takeaway 4
KEY TAKEAWAY 4
• UPMEM-based PIM systems outperform state-of-the-art CPUs in terms of performance (by 23.2× on 2,556 DPUs for 16 PrIM benchmarks) and energy efficiency on most of PrIM benchmarks.
• UPMEM-based PIM systems outperform state-of-the-art GPUs on a majority of PrIM benchmarks (by 2.54× on 2,556 DPUs for 10 PrIM benchmarks), and the outlook is even more positive for future PIM systems.
• UPMEM-based PIM systems are more energy-efficient than state-of-the-art CPUs and GPUs on workloads that they provide performance improvements over the CPUs and the GPUs.

## Slide 182: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 183: Short arXiv Version
https://arxiv.org/pdf/2110.01709.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 184: Long arXiv Version
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 185: PrIM Repository
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 186
Dr. Juan Gómez Luna
Professor Onur Mutlu
Processing-Near-Memory
Real PNM Architectures
Programming General-purpose PIM
HPCA 2023 Tutorial
Real-world Processing-in-Memory Architectures
Sunday, February 26, 2023